# 1,1,1-TRICHLOROETHANE
UN Number: 2831 - CAS Number: 71-55-6 Also known as: CHLOROETHANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2831 CAS number 71-55-6
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1310 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 133.41 Density of gas (kg/m3) 5.934 Boiling Point (°C) 74 Melting Point (°C) -38 Vapour Pressure (Pa) 13330 [Pa] at a temperature of 20°C Ignition Temperature (°C) 537 Upper explosivity limit (UEL) (volume %) 16
### Behaviour at sea
### Additional data
Colour colourless Odour chemical odour
### Transportation data
Package group III State liquid Temperature (°C) ambient Pressure (Pa) under pressure IMO class 6.1
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 1000 TLV-TWA 350 ERPG-1 (ppm) 350 ERPG-2 (ppm) 700 ERPG-3 (ppm) 3500
### Ecotoxicity
# 1,1,2-TRICHLORO-1,2,2-TRIFLUOROETHANE
CAS Number: 76-13-1
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 76-13-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1400 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 187.37 Density of gas (kg/m3) 8.34 Boiling Point (°C) 48 Melting Point (°C) -35 Vapour Pressure (Pa) 36000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 680
### Behaviour at sea
### Additional data
Colour colourless Odour sweet, ether-like
### Transportation data
Cargo group 36 State liquid Temperature (°C) ambient Family name halogenated hydrocarbons
### Reactivity data
Water No Base(s) Yes Metal(s) and alloys Yes (powder) Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
IDHL 2000 TLV-TWA 1000 TEEL-1 (mg/m3) 1250 ppm TEEL-2 (mg/m3) 1500 ppm TEEL-3 (mg/m3) 2000 ppm
### Ecotoxicity
# 1,1,2-TRICHLOROETHANE
UN Number: 3082 - CAS Number: 70-00-5
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082 CAS number 70-00-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1440 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 133.4 Density of gas (kg/m3) 5.93 Boiling Point (°C) 114 Melting Point (°C) -36 Vapour Pressure (Pa) 2500 [Pa] at a temperature of 20°C Ignition Temperature (°C) 410 Upper explosivity limit (UEL) (volume %) 15.5
### Behaviour at sea
### Additional data
Colour colourless Odour characteristic
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 36 State liquid Family name halogenated hydrocarbons
### Reactivity data
Water No Metal(s) and alloys Yes (Al) Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 100 TLV-TWA 10
### Ecotoxicity
# 1,1-DICHLOROETHANE
UN Number: 2362 - CAS Number: 75-34-3 Also known as: CHLORINATED HYDROCHLORIC ETHER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2362 CAS number 75-34-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1174 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 98.97 Density of gas (kg/m3) 4.41 Boiling Point (°C) 57.3 Melting Point (°C) -97.4 Vapour Pressure (Pa) 40534 [Pa] at a temperature of 20°C Ignition Temperature (°C) 458 Flash Point (°C) -5.5 Lower explosivity limit (LEL) (volume %) 5.6 Upper explosivity limit (UEL) (volume %) 11.4
### Behaviour at sea
### Additional data
Colour colourless Odour etheral, chloroform-like Standard behavior classification SD/DE
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 36 State liquid Temperature (°C) cool Family name halogenated hydrocarbons IMO class 3.2
### Reactivity data
Water No Metal(s) and alloys Yes Oxidizing agents Yes Reducing agents No Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 3000 TLV-TWA 100 TEEL-1 (mg/m3) 300 ppm TEEL-2 (mg/m3) 3000 ppm TEEL-3 (mg/m3) 3000 ppm
### Ecotoxicity
# 1,1-DICHLOROPROPANE
UN Number: 1993 - CAS Number: 78-99-9
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1993 CAS number 78-99-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1132 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 112.99 Density of gas (kg/m3) 5.03 Boiling Point (°C) 88.1 Melting Point (°C) -35 Vapour Pressure (Pa) 24890 [Pa] at a temperature of 20°C Ignition Temperature (°C) 557 Flash Point (°C) 15.56 Lower explosivity limit (LEL) (volume %) 3.4 (E) Upper explosivity limit (UEL) (volume %) 14.5 (E)
### Behaviour at sea
### Additional data
Colour colourless Odour sweet
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 36 State liquid Temperature (°C) ambient Family name halogenated hydrocarbons IMO class 3.2
### Reactivity data
Water No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
TEEL-1 (mg/m3) 12.5 ppm TEEL-2 (mg/m3) 75 ppm TEEL-3 (mg/m3) 400 ppm
### Ecotoxicity
# 1,2,3-Trichlorobenzene
UN Number: 2810 - CAS Number: 87-61-6 Also known as: 1,2,6-Trichlorobenzene, Vic-Trichlorobenzene, 1,2,3-Tcb, 1,2,3-Trcb, 1,2,3-Trichlorobenzene, Trichloro-1,2,3 Benzene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2810 CAS number 87-61-6 Formula C 6 H 3 Cl 3
### Physical chemical data
Physical State (25°C) Solid Kinematic viscosity (cSt) 1.16 [cSt] at a temperature of 50°C Molar mass (g/mol) 181.46 Solubility (g/L) 18 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 218.5 Melting Point (°C) 51.3 Critical temperature (°C) 762.5 Critical pressure (Pa) 3010000 Flash Point (Pensky-Martens closed cup) (°C) 113 Henry's constant (mol/(m³·Pa)) 126.7
### Behaviour at sea
Log kow 4.05 Log koc 3.14 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 1300
### Additional data
MARPOL pollution category Category Description X Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a major hazard to either marine resources or human health and, therefore, justify the prohibition of the discharge into the marine environment.
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 2 - Moderate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
Hazard statements Health H317 May cause an allergic skin reaction. Environmental H410 Very toxic to aquatic life with long lasting effects. Precautionary statements Prevention P262 Do not get in eyes, on skin, or on clothing. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection.
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 0.08 Lowest median lethal concentration (LC50) on fishes (mg/l) 0.348 Highest no observed effect concentration (NOEC) on fishes (mg/l) 0.9
# 1,2,3-TRICHLOROPROPANE
CAS Number: 96-18-4 Also known as: ALLYL TRICHLORIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 96-18-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1390 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 147.43 Density of gas (kg/m3) 6.45 Boiling Point (°C) 156 Melting Point (°C) -15 Vapour Pressure (Pa) 200 [Pa] at a temperature of 20°C Ignition Temperature (°C) 304 Flash Point (°C) 73 Lower explosivity limit (LEL) (volume %) 3.2 Upper explosivity limit (UEL) (volume %) 12.6
### Behaviour at sea
### Additional data
Colour colourless Odour strong acid
### Transportation data
Cargo group 36 Temperature (°C) out of sunlight Family name halogenated hydrocarbons
### Reactivity data
Water No Base(s) Yes Metal(s) and alloys Yes (Al) Oxidizing agents Yes Combustibles Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Specific Health Concern (D3) C - Carcinogenicity Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 100 TLV-TWA 10 TEEL-1 (mg/m3) 10 ppm TEEL-2 (mg/m3) 10 ppm TEEL-3 (mg/m3) 100 ppm
### Ecotoxicity
# 1,2,4-TRICHLOROBENZENE
UN Number: 2321 - CAS Number: 120-82-1 Also known as: BENZENE, 1,2,4-TRICHLORO-
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2321 CAS number 120-82-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1450 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 181,5 Density of gas (kg/m3) 8.06 Boiling Point (°C) 213 Melting Point (°C) 16.5 Vapour Pressure (Pa) 130 (38�C) [Pa] at a temperature of 20°C Ignition Temperature (°C) 571 Flash Point (°C) 99
### Behaviour at sea
### Additional data
Colour white Odour sharp, chlorobenzene-like
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 36 Temperature (°C) ambient Family name halogenated hydrocarbons IMO class 6.1
### Reactivity data
Water No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation in BCF (A1B) 5 - ≥ 4000 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Specific Health Concern (D3) M - Mutagenicity Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 5 ppm TEEL-2 (mg/m3) 5ppm TEEL-3 (mg/m3) 40 ppm
### Ecotoxicity
# 1,2-BUTYLENE OXIDE stabilized
UN Number: 3022 - CAS Number: 106-88-7 Also known as: BUTANE, 1,2-EPOXY, 1-BUTENE OXIDE, BUTYLENE OXIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3022 CAS number 106-88-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 826 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 72 Density of gas (kg/m3) 3.225 Boiling Point (°C) 63 Melting Point (°C) -150 Vapour Pressure (Pa) 19329 [Pa] at a temperature of 20°C Ignition Temperature (°C) 550 Flash Point (°C) -15 Lower explosivity limit (LEL) (volume %) 1.5 Upper explosivity limit (UEL) (volume %) 25.1
### Behaviour at sea
### Additional data
Colour colourless Odour sharp odour Standard behavior classification ED
### Transportation data
Package group II Cargo group 16 State liquid Temperature (°C) ambient Pressure (Pa) pressure - vacuum Family name alkylene oxides IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 75 TEEL-2 (mg/m3) 200 TEEL-3 (mg/m3) 200
### Ecotoxicity
# 1,2-DICHLOROETHANE
UN Number: 1184 - CAS Number: 107-06-2 Also known as: BORER SOL, BROCIDE, 1,2-DCE, DESTRUXOL BORER SOL, DICHLOREMULSION, alpha,beta-DICHLORO ETHANE, DICHLORO-1,2-ETHANE, sym- DICHLOROETHANE, DICHLORURE D'ETHYLENE, DICHLORURE D'ETHYLENE, DUTCH LIQUID, DUTCH OIL, 1,2-Dichloroethane, 1,2-Ethylene Dichloride, Ethane Dichloride, Ethylene Chloride, Bichlorure D'Ethylene, Chlorure D'Ethylene, Sym-Dichloroethane, Edc, Ethylene Dichloride
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1184 CAS number 107-06-2 Formula C 2 H 4 Cl 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1253 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.67 [cSt] at a temperature of 20°C 0.62 [cSt] at a temperature of 25°C Molar mass (g/mol) 98.96 Density of gas (kg/m3) 4.386 Solubility (g/L) 8690 [g/L] at a temperature of 20°C and salinity of 0‰ 8600 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 83.7 Melting Point (°C) -36 Critical molar volume (m³/mol) 0.000225 Critical temperature (°C) 561 Critical pressure (Pa) 5400000 Surface tension (mN/m) 32.2 [mN/m] at a temperature of 20°C 31.86 [mN/m] at a temperature of 25°C Interfacial tension (mN/m) 30 [mN/m] at a temperature of 25°C and salinity of 0‰ Vapour Pressure (Pa) 8700 [Pa] at a temperature of 20°C 10546 [Pa] at a temperature of 25°C Ignition Temperature (°C) 440 Flash Point (°C) 13 Flash Point (Pensky- Martens closed cup) (°C) 13 Flash Point (Cleveland open cup) (°C) 18 Lower explosivity limit (LEL) (volume %) 6.2 Upper explosivity limit (UEL) (volume %) 16 Vapor enthalpy (J/Kg) 323160 [J/Kg] at a temperature of 83.5°C 355295 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 11200000 Specific heat capacity (J/(Kg·K)) 1297.5 Combustion efficiency (%) 50 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.04 Rad fraction (%) 40 Henry's constant (mol/(m³·Pa)) 111.46
### Behaviour at sea
Log kow 1.48 Log koc 1.45 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) Not biodegradable Bioconcentration factor (BCF) 2.75
### Additional data
Colour colourless Odour sweet odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification SD
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 36 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name halogenated hydrocarb IMO class 3.2
### Reactivity data
Static electricity Yes Notable risks On combustion, forms toxic and corrosive fumes Reacts with oxidizers.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Specific Health Concern (D3) C - Carcinogenicity Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 1000 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H302 Harmful if swallowed. H315 Causes skin irritation. H319 Causes serious eye irritation. H335 May cause respiratory irritation. H350 May cause cancer. Precautionary statements Prevention P201 Obtain special instructions before use. P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. Response P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P311 Call a POISON CENTER or doctor/physician. ERPG-1 (ppm) 50 ERPG-2 (ppm) 200 ERPG-3 (ppm) 300
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 166 Lowest median lethal concentration (LC50) on crustacean (mg/l) 85 Lowest median lethal concentration (LC50) on fishes (mg/l) 11.8 Highest no observed effect concentration (NOEC) on algae (mg/l) 53 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 10.6 Highest no observed effect concentration (NOEC) on fishes (mg/l) 14 Assessment factor (AF) 10 on the Short term 10 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 1180 [µg/l] on the Short term 1060 [µg/l] on the Long term
# 1,2-DICHLOROETHYLENE
UN Number: 1150 Also known as: ACETYLENE DICHLORIDE, DICHLORO-1,2 ETHYLENE, 1,2 -DICHLORO-ETHYLENE, DIOFORM
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1150
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1270 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 97 Density of gas (kg/m3) 4.386 Boiling Point (°C) 60 Melting Point (°C) -80 Vapour Pressure (Pa) 8000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 460 Lower explosivity limit (LEL) (volume %) 9.7 Upper explosivity limit (UEL) (volume %) 13
### Behaviour at sea
### Additional data
Colour colourless Odour sweet, pleasant odour
### Transportation data
Package group II State liquid Temperature (°C) ambient Pressure (Pa) under pressure IMO class 3.2
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 4000 TLV-TWA 200
### Ecotoxicity
# 1,2-DICHLOROPROPANE
UN Number: 1279 - CAS Number: 78-87-5 Also known as: DICHLOROPROPANE, Propylene Dichloride, 1,2-Dichloropropane
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1279 CAS number 78-87-5 Formula C 3 H 6 Cl 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1150 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 112.99 Density of gas (kg/m3) 5.04 Solubility (g/L) 2.8 [g/L] at a temperature of 20°C and salinity of 0‰ 2.7 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 96 Melting Point (°C) -100 Critical temperature (°C) 578.5 Critical pressure (Pa) 4154325 Surface tension (mN/m) 33.93 [mN/m] at a temperature of 20°C Vapour Pressure (Pa) 5600 [Pa] at a temperature of 20°C 6666 [Pa] at a temperature of 25°C Ignition Temperature (°C) 555 Flash Point (°C) 15 Flash Point (Pensky-Martens closed cup) (°C) 13 Flash Point (Cleveland open cup) (°C) 21 Lower explosivity limit (LEL) (volume %) 3.4 Upper explosivity limit (UEL) (volume %) 14.5 Vapor enthalpy (J/Kg) 300235 [J/Kg] at a temperature of 96.4°C 321540 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 17000000 Specific heat capacity (J/(Kg·K)) 1320 Henry's constant (mol/(m³·Pa)) 274
### Behaviour at sea
Log kow 2 Log koc 1.6 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) 5771 Biodegradation in marine environment (Half-life) (days) Not biodegradable Bioconcentration factor (BCF) 1
### Additional data
Colour colourless Odour sweet, chloroform odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification SD
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 36 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name halogenated hydrocarbons IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 2000 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H302 Harmful if swallowed. H332 Harmful if inhaled. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P241 Use explosion- proof electrical/ventilating/lighting/.../equipment. P260 Do not breathe dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P312 IF SWALLOWED: Call a POISON CENTER or doctor/physician if you feel unwell. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. TLV-TWA 75 TEEL-1 (mg/m3) 300 ppm TEEL-2 (mg/m3) 400 ppm TEEL-3 (mg/m3) 400 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 38 Lowest median lethal concentration (LC50) on crustacean (mg/l) 24.79 Lowest median lethal concentration (LC50) on fishes (mg/l) 240 Highest no observed effect concentration (NOEC) on algae (mg/l) 38 Highest no observed effect concentration (NOEC) on crustacean (mg/l) > 100 Highest no observed effect concentration (NOEC) on fishes (mg/l) 4.09 Assessment factor (AF) 500 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 8 [µg/l] on the Short term
# 1,3,5-TRIMETHYL BENZENE
UN Number: 2325 - CAS Number: 526-73-8
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2325 CAS number 526-73-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 800 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 120 Density of gas (kg/m3) 5.354 Vapour Pressure (Pa) 10100 [Pa] at a temperature of 20°C Flash Point (°C) 44
### Behaviour at sea
### Additional data
Colour green Odour ammonia, fish odour Standard behavior classification DE, D
### Transportation data
Package group III State liquid IMO class 3.3
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 3 - ≥100 and <500 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 2 - Irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 140 TEEL-2 (mg/m3) 360 TEEL-3 (mg/m3) 500
### Ecotoxicity
# 1,3,5-TRIOXANE
CAS Number: 110-88-3
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 110-88-3
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1200 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 90.1 Boiling Point (°C) 115 (sublim.) Melting Point (°C) 61 Vapour Pressure (Pa) 1700 (25�C [Pa] at a temperature of 20°C Ignition Temperature (°C) 410 Flash Point (°C) 44 Lower explosivity limit (LEL) (volume %) 3.6 Upper explosivity limit (UEL) (volume %) 29
### Behaviour at sea
### Additional data
Colour white Odour sweet, ether-like Standard behavior classification SD
### Transportation data
Cargo group 41 State solid Family name ethers
### Reactivity data
Water No Acid(s) Yes Metal(s) and alloys Yes (mild steel) Static electricity Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Specific Health Concern (D3) R - Reprotoxicity Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# 1,3-CYCLOPENTADIENE DIMER molten
CAS Number: 77-73-6 Also known as: BICYCLOPENTADIENE, BISCYCLOPENTADIENE, 1,3-CYCLOPENTADIENE dimère, fondu, DICYCLOPENTADIENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 77-73-6
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 980 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 132.22 Boiling Point (°C) 172 Melting Point (°C) 33 Vapour Pressure (Pa) 180000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 503 Flash Point (°C) 26 Lower explosivity limit (LEL) (volume %) 0.8 Upper explosivity limit (UEL) (volume %) 6.3
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Cargo group 30 State solid Family name olefins
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 3 - ≥100 and <500 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# 1,3-DICHLOROPROPANE
UN Number: 1993 - CAS Number: 142-28-9
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1993 CAS number 142-28-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1188 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 112.99 Density of gas (kg/m3) 5.03 Boiling Point (°C) 120.4 Melting Point (°C) -99.5 Vapour Pressure (Pa) 8425 [Pa] at a temperature of 20°C Flash Point (°C) 15 Lower explosivity limit (LEL) (volume %) 3.4 (E) Upper explosivity limit (UEL) (volume %) 14.5 (E)
### Behaviour at sea
### Additional data
Colour colourless Odour sweet
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 36 State liquid Temperature (°C) ambient Family name halogenated hydrocarbons IMO class 3.2/3.3
### Reactivity data
Water No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Interference with coastal amenities (E2) SD - Sinker/Dissolver
### Human toxicity threshold
TEEL-1 (mg/m3) 15 ppm TEEL-2 (mg/m3) 100 ppm TEEL-3 (mg/m3) 350 ppm
### Ecotoxicity
# 1,3-DIISOPROPYLBENZENE
UN Number: 3082 - CAS Number: 25321-09-9 Also known as: BENZENE, DIISOPROPYL, BIS(1-METHYLETHYL)-BENZENE, CUMENE BOTTOMS, DIPB
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082 CAS number 25321-09-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 856 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 162.3 Density of gas (kg/m3) 7.22 Boiling Point (°C) 203 Melting Point (°C) -63 Vapour Pressure (Pa) 133 (34�C) [Pa] at a temperature of 20°C Ignition Temperature (°C) 449 Flash Point (°C) 76 Lower explosivity limit (LEL) (volume %) 0.9 Upper explosivity limit (UEL) (volume %) 6.5
### Behaviour at sea
### Additional data
Colour clear amber Odour odourless Standard behavior classification F/FD
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 32 State liquid Temperature (°C) ambient Family name aromatic hydrocarbons
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# 1,3-PENTADIENE
CAS Number: 504-60-9
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 504-60-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 680 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 68.12 Density of gas (kg/m3) 3.1 Boiling Point (°C) 42 Melting Point (°C) -87.5 Vapour Pressure (Pa) 46000 [Pa] at a temperature of 20°C Flash Point (°C) -29 Upper explosivity limit (UEL) (volume %) 8.3
### Behaviour at sea
### Additional data
Colour colourless Odour faint
### Transportation data
Cargo group 30 State liquid Family name olefins
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# 1,4-BUTYNEDIOL
UN Number: 2716 Also known as: BUTYNE-2 DIOL-1,4
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2716
### Physical chemical data
Physical State (20°C) Solid Molar mass (g/mol) 86.09 Density of gas (kg/m3) 2.83 Melting Point (°C) 58 Vapour Pressure (Pa) 0.2 [Pa] at a temperature of 20°C Ignition Temperature (°C) 335 Flash Point (°C) 152
### Behaviour at sea
### Additional data
Colour white to light yellow
### Transportation data
Package group III State solid IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-2 (mg/m3) 20 TEEL-3 (mg/m3) 30
### Ecotoxicity
# 1,5,9-CYCLODODECATRIENE
UN Number: 2518 - CAS Number: 4904-61-4 Also known as: CYCLODODECATRIENE, Cdt, Cyclododeca-1,5,9-Triene, 1,5,9-Cyclododecatriene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2518 CAS number 4904-61-4 Formula C 1 2 H 1 8
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 890 [Kg/m³] at a temperature of 20°C 840 [Kg/m³] at a temperature of 100°C Molar mass (g/mol) 162.28 Solubility (g/L) 5 [g/L] at a temperature of 20°C and salinity of 0‰ 0.34 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 231 Melting Point (°C) -17 Vapour Pressure (Pa) 12265 (160�C) [Pa] at a temperature of 20°C Flash Point (°C) 80 Flash Point (Pensky-Martens closed cup) (°C) 88 Lower explosivity limit (LEL) (volume %) 1 Upper explosivity limit (UEL) (volume %) 4 Henry's constant (mol/(m³·Pa)) 2847.2
### Behaviour at sea
Log kow 5.1 Log koc 3.73 Biodegradation in estuary environment (Half- life) (days) Not hydrolysable Bioconcentration factor (BCF) 2000
### Additional data
Colour white to slightly yellow Odour pungent MARPOL pollution category Category Description X Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a major hazard to either marine resources or human health and, therefore, justify the prohibition of the discharge into the marine environment. Marine pollutant P Standard behavior classification F/FE/E
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 30 State liquid Temperature (°C) ambient Family name olefins IMO class 6.1
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation in BCF (A1B) 5 - ≥ 4000 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Specific Health Concern (D3) A - Aspiration Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
Hazard statements Health H304 May be fatal if swallowed and enters airways. Environmental H410 Very toxic to aquatic life with long lasting effects.
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 0.47 Lowest median lethal concentration (LC50) on fishes (mg/l) 2.0
# 1-DECENE
UN Number: 3295 - CAS Number: 872-05-9 Also known as: DECENE-1, N-DECYLENE, Decene, Decylene, 1-Decene, Dec-1-Ene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3295 CAS number 872-05-9 Formula C 1 0 H 2 0
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 741 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.75 [cSt] at a temperature of 20°C 1.0205 [cSt] at a temperature of 25°C Molar mass (g/mol) 140.2 Solubility (g/L) 0.115 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 170 Melting Point (°C) -66 Critical molar volume (m³/mol) 0.000584 Critical temperature (°C) 617 Critical pressure (Pa) 2220000 Surface tension (mN/m) 24 [mN/m] at a temperature of 20°C Vapour Pressure (Pa) 150 [Pa] at a temperature of 20°C Ignition Temperature (°C) 210 Flash Point (°C) 46 Flash Point (Pensky-Martens closed cup) (°C) 45 Lower explosivity limit (LEL) (volume %) 0.5 Upper explosivity limit (UEL) (volume %) 5.4 Vapor enthalpy (J/Kg) 359530 [J/Kg] at a temperature of 25°C Specific heat capacity (J/(Kg·K)) 2144 Henry's constant (mol/(m³·Pa)) 54715
### Behaviour at sea
Log kow 4.7 Log koc 1.724 Biodegradation in estuary environment (Half- life) (days) Not hydrolysable Bioconcentration factor (BCF) 488
### Additional data
Colour colourless Odour pleasant odour MARPOL pollution category Category Description X Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a major hazard to either marine resources or human health and, therefore, justify the prohibition of the discharge into the marine environment. Standard behavior classification D, FD, F
### Transportation data
Cargo group 30 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name olefins
### Reactivity data
Water No Acid(s) Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 2 - Moderate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 0 - Not irritating Specific Health Concern (D3) A - Aspiration Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
Hazard statements Physical H226 Flammable liquid and vapour. Health H304 May be fatal if swallowed and enters airways. Environmental H400 Very toxic to aquatic life. H410 Very toxic to aquatic life with long lasting effects. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P243 Take precautionary measures against static discharge. P273 Avoid release to the environment. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P331 Do NOT induce vomiting. P391 Collect spillage.
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 22 Lowest median lethal concentration (LC50) on crustacean (mg/l) 480 Lowest median lethal concentration (LC50) on fishes (mg/l) > 1000
# 1-DODECENE
UN Number: 2850 - CAS Number: 6842-15-5 Also known as: DODECENE-1, Propylene Tetramer, Tetrapropylene, Dodecene, 1-Dodecene, Dodec-1-Ene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2850 CAS number 6842-15-5 Formula C 1 2 H 2 4
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 758 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 1.18 [cSt] at a temperature of 20°C 1.5823 [cSt] at a temperature of 25°C Molar mass (g/mol) 168.31 Density of gas (kg/m3) 7.495 Solubility (g/L) 0.113 [g/L] at a temperature of 20°C and salinity of 0‰ 0.203 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 213 Melting Point (°C) -32 Critical temperature (°C) 658 Critical pressure (Pa) 1930000 Surface tension (mN/m) 25.6 [mN/m] at a temperature of 20°C Vapour Pressure (Pa) 133 [Pa] at a temperature of 20°C 220 [Pa] at a temperature of 25°C Ignition Temperature (°C) 255 Flash Point (°C) 100 Flash Point (Cleveland open cup) (°C) 79 Lower explosivity limit (LEL) (volume %) 0.6 Vapor enthalpy (J/Kg) 361100 [J/Kg] at a temperature of 25°C Specific heat capacity (J/(Kg·K)) 2143
### Behaviour at sea
Log kow 6.1 Log koc 5.864 Bioconcentration factor (BCF) 310
### Additional data
Colour colourless Odour mild pleasant odour MARPOL pollution category Category Description X Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a major hazard to either marine resources or human health and, therefore, justify the prohibition of the discharge into the marine environment.
### Transportation data
Cargo group 30 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name olefins IMO class 3.3
### Reactivity data
Water No Acid(s) Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 22 Lowest median lethal concentration (LC50) on crustacean (mg/l) 480 Lowest median lethal concentration (LC50) on fishes (mg/l) > 1000 Assessment factor (AF) 1 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 1 [µg/l] on the Short term
# 1-HEXENE
UN Number: 2370 - CAS Number: 592-41-6 Also known as: 1-Hexene, Butylethylene, Hex-1-Ene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2370 CAS number 592-41-6 Formula C 6 H 1 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 673 [Kg/m³] at a temperature of 20°C 668.5 [Kg/m³] at a temperature of 25°C Kinematic viscosity (cSt) 0.35 [cSt] at a temperature of 20°C 0.37696 [cSt] at a temperature of 25°C Molar mass (g/mol) 84.16 Density of gas (kg/m3) 3.87 Solubility (g/L) 50 [g/L] at a temperature of 20°C and salinity of 0‰ 50 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 63.7 Melting Point (°C) -140 Critical temperature (°C) 504 Surface tension (mN/m) 17.9 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 41320 [Pa] at a temperature of 20°C 24531 [Pa] at a temperature of 25°C Ignition Temperature (°C) 253 Flash Point (°C) -18 Flash Point (Pensky-Martens closed cup) (°C) -25 Lower explosivity limit (LEL) (volume %) 1.2 Upper explosivity limit (UEL) (volume %) 6.9 Vapor enthalpy (J/Kg) 363712 [J/Kg] at a temperature of 25°C Specific heat capacity (J/(Kg·K)) 2178 Henry's constant (mol/(m³·Pa)) 41543
### Behaviour at sea
Log kow 3.4 Log koc 2.17 Bioconcentration factor (BCF) 81
### Additional data
Colour colourless Odour mild pleasant odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 30 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name olefins IMO class 3.1
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
Hazard statements Physical H225 Highly flammable liquid and vapour. Health H304 May be fatal if swallowed and enters airways. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P243 Take precautionary measures against static discharge. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P331 Do NOT induce vomiting. TLV-TWA 500 ERPG-2 (ppm) 500 ERPG-3 (ppm) 5000
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 2.4 Lowest median lethal concentration (LC50) on crustacean (mg/l) 30 Lowest median lethal concentration (LC50) on fishes (mg/l) 1.3 Assessment factor (AF) 1 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 111 [µg/l] on the Short term
# 1-METHYL-2-PYRROLIDONE
CAS Number: 872-50-4
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 872-50-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1030 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 99 Density of gas (kg/m3) 4.39 Boiling Point (°C) 202 Melting Point (°C) -17 Vapour Pressure (Pa) 66000 (25C) [Pa] at a temperature of 20°C Ignition Temperature (°C) 270 Flash Point (°C) 96 Lower explosivity limit (LEL) (volume %) 0.99 Upper explosivity limit (UEL) (volume %) 3.9
### Behaviour at sea
### Additional data
Colour white Odour mild fishy Standard behavior classification D/DE
### Transportation data
State liquid Temperature (°C) ambient Family name aromatic amines
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 10 ppm TEEL-2 (mg/m3) 25 ppm TEEL-3 (mg/m3) 25 ppm
### Ecotoxicity
# 1-METHYLNAPHTALENE molten
UN Number: 3082
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1020 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 142.2 Density of gas (kg/m3) 6.33 Boiling Point (°C) 240/243 Melting Point (°C) -3.6 Ignition Temperature (°C) 529 Flash Point (°C) 82
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 32 State liquid Temperature (°C) ambient Family name aromatic hydrocarbons
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# 1-METHYLPYRROLIDONE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1030 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 99 Density of gas (kg/m3) 1030 Boiling Point (°C) 202 Melting Point (°C) -24 Ignition Temperature (°C) 270 Flash Point (°C) 96 Lower explosivity limit (LEL) (volume %) 0.99 Upper explosivity limit (UEL) (volume %) 3.9
### Behaviour at sea
### Additional data
Colour white Odour mild fish odour
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 10 TEEL-2 (mg/m3) 25 TEEL-3 (mg/m3) 25
### Ecotoxicity
# 1-NITROPROPANE
UN Number: 2608 - CAS Number: 108-03-2
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2608 CAS number 108-03-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1000 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 89.09 Density of gas (kg/m3) 3.94 Boiling Point (°C) 120 Melting Point (°C) -91 Vapour Pressure (Pa) 1700 [Pa] at a temperature of 20°C Ignition Temperature (°C) 404 Flash Point (°C) 28 Lower explosivity limit (LEL) (volume %) 2.5
### Behaviour at sea
### Additional data
Colour colourless Odour mild fruity Standard behavior classification FED
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 42 State liquid Temperature (°C) ambient Family name nitro compounds IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 1000 TLV-TWA 25
### Ecotoxicity
# 1-Nonene
UN Number: 1993 - CAS Number: 27215-95-8 Also known as: Propylene Trimer, Propene Trimer, Pt 3, Olefin Mixture, Nonene, 1-Nonene, Non-1-Ene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1993 CAS number 27215-95-8 Formula C 9 H 1 8
### Physical chemical data
Physical State (25°C) Liquid Kinematic viscosity (cSt) 0.851 [cSt] at a temperature of 20°C 0.80794 [cSt] at a temperature of 25°C Molar mass (g/mol) 126.239 Solubility (g/L) 3.6 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 146.9 Melting Point (°C) -81.3 Critical molar volume (m³/mol) 0.000526 Critical temperature (°C) 594 Critical pressure (Pa) 2431800 Surface tension (mN/m) 22.56 [mN/m] at a temperature of 25°C Flash Point (Cleveland open cup) (°C) 26 Lower explosivity limit (LEL) (volume %) 0.7 Upper explosivity limit (UEL) (volume %) 3.9 Vapor enthalpy (J/Kg) 287629 [J/Kg] at a temperature of 146.9°C 360586 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 44146000 Specific heat capacity (J/(Kg·K)) 2142 Henry's constant (mol/(m³·Pa)) 100312
### Behaviour at sea
Log kow 4.55 Log koc 2.9 Biodegradation in estuary environment (Half- life) (days) Not hydrolysable Bioconcentration factor (BCF) 1843
### Additional data
MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Specific Health Concern (D3) A - Aspiration Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
Hazard statements Physical H226 Flammable liquid and vapour. Health H304 May be fatal if swallowed and enters airways. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P233 Keep container tightly closed. P240 Ground/bond container and receiving equipment. P241 Use explosion- proof electrical/ventilating/lighting/.../equipment. P242 Use only non-sparking tools. P243 Take precautionary measures against static discharge. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P331 Do NOT induce vomiting. P370 + P378 In case of fire: Use ... for extinction. Storage P403 + P235 Store in a well-ventilated place. Keep cool. P405 Store locked up. Disposal P501 Dispose of contents/container to ...
### Ecotoxicity
Lowest median lethal concentration (LC50) on fishes (mg/l) 3 Highest no observed effect concentration (NOEC) on algae (mg/l) 3.2 Highest no observed effect concentration (NOEC) on fishes (mg/l) 1
# 1-OCTENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 715 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 112.22 Density of gas (kg/m3) 5.03 Boiling Point (°C) 121.5 Melting Point (°C) -101 Vapour Pressure (Pa) 400 [Pa] at a temperature of 20°C Ignition Temperature (°C) 256 Flash Point (°C) -7 Lower explosivity limit (LEL) (volume %) 0.7 Upper explosivity limit (UEL) (volume %) 3.9
### Behaviour at sea
Persistence (days) 0.8
### Additional data
Colour colourless Odour gasoline odour Standard behavior classification E, FE, F
### Transportation data
Cargo group 30 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name olefins
### Reactivity data
Water No Acid(s) Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Specific Health Concern (D3) A - Aspiration Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
ERPG-1 (ppm) 40 ERPG-2 (ppm) 800 ERPG-3 (ppm) 2000
### Ecotoxicity
# 1-PENTENE
UN Number: 1108 - CAS Number: 109-67-1 Also known as: alpha-n-AMYLENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1108 CAS number 109-67-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 600 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 70.13 Density of gas (kg/m3) 3.1 Boiling Point (°C) 30 Melting Point (°C) -165 Vapour Pressure (Pa) 66000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 273 Flash Point (°C) -20 Lower explosivity limit (LEL) (volume %) 1.4 Upper explosivity limit (UEL) (volume %) 8.7
### Behaviour at sea
### Additional data
Colour colourless Odour gasoline
### Transportation data
Transport mode Bulk,Packaged Cargo group 30 State liquid Temperature (°C) ambient Family name olefins IMO class 3.1
### Reactivity data
Water No Acid(s) Yes Static electricity Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 750 ppm TEEL-2 (mg/m3) 6000 ppm TEEL-3 (mg/m3) 75000 ppm
### Ecotoxicity
# 1-PHENYL-1-XYLYLETHANE
CAS Number: 40766-31-2
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 40766-31-2
### Physical chemical data
Density (kg/m3) 983 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 210.3 Flash Point (°C) 143
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification FD/FED/E
### Transportation data
Cargo group 32 Family name aromatic hydrocarbons
### Reactivity data
Water No Acid(s) Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
### Ecotoxicity
# 1-UNDECENE
CAS Number: 821-95-4
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 821-95-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 750 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 154.2 Boiling Point (°C) 192.9 Vapour Pressure (Pa) 400 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless Odour gasoline odour
### Transportation data
Cargo group 30 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name olefins
### Reactivity data
Water No Acid(s) Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Specific Health Concern (D3) A - Aspiration Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# 1.6-DICHLOROHEXANE
UN Number: 3082 - CAS Number: 2163-00-0
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082 CAS number 2163-00-0
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1070 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 155.07 Melting Point (°C) -13 Vapour Pressure (Pa) 500 [Pa] at a temperature of 20°C Flash Point (°C) 74
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification S/SD/D
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 36 State liquid Temperature (°C) ambient Family name halogenated hydrocarbons
### Reactivity data
Water No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 0 - Is not a floater; and does not pose any known health hazards
### Human toxicity threshold
### Ecotoxicity
# 2,2'-DICHLOROISOPROPYL ETHER
UN Number: 2490 Also known as: BIS,(2-CHLOROISOPROPYL)ETHER, di-(2-CHLOROISPROPYL)ETHER, 2,2'-DICHLOROISOPROPYL ETHER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2490
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1112 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 171.07 Density of gas (kg/m3) 7.6 Boiling Point (°C) 187.3 Melting Point (°C) 1.051652893 Vapour Pressure (Pa) < 200 [Pa] at a temperature of 20°C Flash Point (°C) 77
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification SD
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 36 State liquid Temperature (°C) ambient Family name halogenated hydrocarbons IMO class 6.1
### Reactivity data
Water No Oxidizing agents Yes
### GESAMP Hazard profile
Biodegradation (A2) NR - Not readily biodegradable
### Human toxicity threshold
TEEL-1 (mg/m3) 10 ppm TEEL-2 (mg/m3) 75 ppm TEEL-3 (mg/m3) 350 ppm
### Ecotoxicity
# 2,2,4-Trimethyl-1,3-Pentanediol-1-Isobutyrate
CAS Number: 25265-77-4 Also known as: Texanol, 2,2,4-Trimethyl-1,3-Pentanediol Monoisobutyrate, Propanoic Acid, 2-Methyl-, 3-Hydroxy-2,2,4-Trimethylpentyl Ester, Propanoic Acid, 2-Methyl-, Monoester With 2,2,4-Trimethyl-1,3-Pentanediol, 2,2,4-Trimethyl-1,3-Pentanediol-1-Isobutyrate
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 25265-77-4 Formula C 1 2 H 2 4 O 3
### Physical chemical data
Physical State (25°C) Liquid Density (kg/m3) 957.7 [Kg/m³] at a temperature of 5°C 954.2 [Kg/m³] at a temperature of 10°C 947.7 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 45.625 [cSt] at a temperature of 5°C 34.972 [cSt] at a temperature of 10°C 19.996 [cSt] at a temperature of 20°C Molar mass (g/mol) 216.32 Solubility (g/L) 858 [g/L] at a temperature of 25°C and salinity of 0‰ 970 [g/L] at a temperature of 20°C and salinity of 0‰ 870 [g/L] at a temperature of 20°C and salinity of 5‰ 660 [g/L] at a temperature of 20°C and salinity of 30‰ Boiling Point (°C) 244 Melting Point (°C) -50 Surface tension (mN/m) 28.6 [mN/m] at a temperature of 22°C 29.46 [mN/m] at a temperature of 6.2°C 28.73 [mN/m] at a temperature of 12.4°C 28.12 [mN/m] at a temperature of 19.5°C Flash Point (Pensky- Martens closed cup) (°C) 122 Flash Point (Cleveland open cup) (°C) 120 Henry's constant (mol/(m³·Pa)) 0.01
### Behaviour at sea
Log kow 3.47 Log koc 1.47 Biodegradation in estuary environment (Half- life) (days) 16.5
### Additional data
MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 18.4 Lowest median lethal concentration (LC50) on crustacean (mg/l) > 95 Lowest median lethal concentration (LC50) on fishes (mg/l) 30 Highest no observed effect concentration (NOEC) on algae (mg/l) 3.28 Assessment factor (AF) 10000 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 2 [µg/l] on the Short term
# 2,2-DICHLOROPROPIONIC ACID
CAS Number: 75-99-0 Also known as: ACIDE 2,2-DICHLOROPROPIONIQUE, 2,2-DICHLOROPROPANOIC ACID
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 75-99-0
### Physical chemical data
Physical State (20°C) Liquid Molar mass (g/mol) 142.97 Boiling Point (°C) 500/900 Melting Point (°C) 185/190 Vapour Pressure (Pa) < 10 [Pa] at a temperature of 20°C Flash Point (°C) > 110
### Behaviour at sea
### Additional data
### Transportation data
State liquid
### Reactivity data
Water Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# 2,2-DIMETHYLPROPANE-1,3-DIOL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1060 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 104.14 Boiling Point (°C) 208 Melting Point (°C) 123/127 Flash Point (°C) 107
### Behaviour at sea
### Additional data
### Transportation data
State solid
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 600 ppm TEEL-2 (mg/m3) 600 ppm TEEL-3 (mg/m3) 600 ppm
### Ecotoxicity
# 2,4-DICHLOROPHENOL solid
UN Number: 2020 - CAS Number: 120-83-2 Also known as: DICHLOROPHENOL(S) solide
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2020 CAS number 120-83-2
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1400 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 163.01 Density of gas (kg/m3) 1400 Boiling Point (°C) 216 Melting Point (°C) 45 Vapour Pressure (Pa) 100 [Pa] at a temperature of 20°C Ignition Temperature (°C) 500 Flash Point (°C) 113
### Behaviour at sea
Persistence (days) 1.9
### Additional data
Colour colourless Odour medicine odour
### Transportation data
Transport mode Bulk,Packaged Package group III State solid IMO class 6.1
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 2 - Moderate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
ERPG-1 (ppm) 0.2 ERPG-3 (ppm) 20
### Ecotoxicity
# 2,4-DICHLOROPHENOXY ACETIC ACID solid
UN Number: 3077 Also known as: ACIDE DICHLORO-2,4 PHENOXYACETIQUE solide, AGRIBEN, AGROTECT, AMIDOX, AMOXONE, AQUA-KEEN, CLOFIBRAAT, 2,4-D, DACAMINE, DECAMINE, DICITOX, DIOTOX
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3077
### Physical chemical data
Physical State (20°C) Solid Molar mass (g/mol) 221 Melting Point (°C) 140 Vapour Pressure (Pa) 99 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour white to tan Odour odourless
### Transportation data
State solid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 50
### Ecotoxicity
# 2,6-DIETHYLANILINE
Also known as: ANILINE, 2,6-DIEHYL, BENZENEAMINO, 2,6-DIETHYL-(ACL)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 959 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 149.24 Density of gas (kg/m3) 6.64 Boiling Point (°C) 242 Vapour Pressure (Pa) < 13 [Pa] at a temperature of 20°C Flash Point (°C) 99
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification FD/F
### Transportation data
State liquid Temperature (°C) ambient Family name aromatic amines
### Reactivity data
Water No Acid(s) Yes Metal(s) and alloys Yes (Cu) Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 3 - ≥100 and <500 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 10 TEEL-2 (mg/m3) 60 TEEL-3 (mg/m3) 350
### Ecotoxicity
# 2-(2-AMINOETHOXY)ETHANOL
UN Number: 3055 - CAS Number: 929-06-6 Also known as: DGA, DIGLYCOLAMINE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3055 CAS number 929-06-6
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1060 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 105.14 Boiling Point (°C) 221 Melting Point (°C) -12 Vapour Pressure (Pa) 2000 [Pa] at a temperature of 20°C Flash Point (°C) 127
### Behaviour at sea
### Additional data
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Family name alkanolamines
### Reactivity data
Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 35 TEEL-2 (mg/m3) 250 TEEL-3 (mg/m3) 500
### Ecotoxicity
# 2-AMINO-2-METHYL-1-PROPANOL (90% or less)
CAS Number: 124-68-5 Also known as: 2-AMINODIMETHYLETHANOL, beta-AMINOISOBUTANOL, AMP 95
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 124-68-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 935 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 89.14 Density of gas (kg/m3) > 1.29 Boiling Point (°C) 165 Melting Point (°C) -2 Vapour Pressure (Pa) 10400 [Pa] at a temperature of 20°C Ignition Temperature (°C) 446 Flash Point (°C) 87 Lower explosivity limit (LEL) (volume %) 1.1/1.5 Upper explosivity limit (UEL) (volume %) 9.2/10.1
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification D/DE
### Transportation data
State liquid Temperature (°C) ambient Family name alkanolamines
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys Yes (Al, Cu) Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 0.075 TEEL-2 (mg/m3) 0.6 TEEL-3 (mg/m3) 500
### Ecotoxicity
# 2-Butoxyethanol
CAS Number: 111-76-2 Also known as: 2-Be, 2-Butoxy-1-Ethanol, Egbe, Ethylene Glycol Monobutyl Ether, Ethylene Glycol Mono-N-Butyl Ether, Ethylene Glycol N-Butyl Ether, Glycol Monobutyl Ether, Glycol Ether Eb, Monobutyl Glycol Ether, Butoxyethanol, O-Butyl Ethylene Glycol, Butylglycol, 3-Oxa-1-Heptanol, Monobutyl Ethylene Glycol Ether, Ether Monobutylique De L'Ethylene Glycol, 2-Butoxyethanol, 2-Butoxy Ethanol
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 111-76-2 Formula C 6 H 1 4 O 2
### Physical chemical data
Physical State (25°C) Liquid Kinematic viscosity (cSt) 3.62 [cSt] at a temperature of 20°C 3.15 [cSt] at a temperature of 25°C Molar mass (g/mol) 118.17 Solubility (g/L) 900000 [g/L] at a temperature of 20°C and salinity of 0‰ 900000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 168.4 Melting Point (°C) -72.5 Critical molar volume (m³/mol) 0.000424 Critical temperature (°C) 634 Critical pressure (Pa) 3270000 Surface tension (mN/m) 26.55 [mN/m] at a temperature of 20°C 26.14 [mN/m] at a temperature of 25°C Flash Point (Pensky-Martens closed cup) (°C) 60 Flash Point (Cleveland open cup) (°C) 69 Lower explosivity limit (LEL) (volume %) 1.1 Upper explosivity limit (UEL) (volume %) 10.1 Vapor enthalpy (J/Kg) 478886 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 30100000 Specific heat capacity (J/(Kg·K)) 312.22 Combustion efficiency (%) 98 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.04 Rad fraction (%) 23 Henry's constant (mol/(m³·Pa)) 0.16
### Behaviour at sea
Log kow 0.84 Log koc 1.81 Biodegradation in estuary environment (Half- life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 10 Bioconcentration factor (BCF) 0.97
### Additional data
MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Interference with coastal amenities (E2) G - Gas
### Human toxicity threshold
IDHL 700 Hazard statements Health H302 Harmful if swallowed. H312 Harmful in contact with skin. H315 Causes skin irritation. H319 Causes serious eye irritation. H332 Harmful if inhaled. Precautionary statements Prevention P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P264 Wash ... thoroughly after handling. P270 Do no eat, drink or smoke when using this product. P271 Use only outdoors or in a well-ventilated area. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P312 IF SWALLOWED: Call a POISON CENTER or doctor/physician if you feel unwell. P302 + P352 IF ON SKIN: Wash with plenty of soap and water. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P321 Specific treatment (see ... on this label). P332 + P313 If skin irritation occurs: Get medical advice/attention. P337 + P313 If eye irritation persists: Get medical advice/attention. P362 Take off contaminated clothing and wash before reuse.
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 911 Lowest median lethal concentration (LC50) on crustacean (mg/l) 540 Lowest median lethal concentration (LC50) on fishes (mg/l) 983 Highest no observed effect concentration (NOEC) on algae (mg/l) 286 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 100 Highest no observed effect concentration (NOEC) on fishes (mg/l) > 100 Assessment factor (AF) 100 on the Short term 100 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 5400 [µg/l] on the Short term 1000 [µg/l] on the Long term
# 2-CHLOROPROPIONIC ACID
UN Number: 2511 Also known as: ACIDE 2-CHLOROPROPIONIQUE, 2-CHLOROPROPANOIC ACID, alpha-CHLOROPROPIONIC ACID
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2511
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1258 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 108.53 Density of gas (kg/m3) 4.77 Boiling Point (°C) 186 Vapour Pressure (Pa) < 200 [Pa] at a temperature of 20°C Ignition Temperature (°C) 500 Flash Point (°C) 107.2 Lower explosivity limit (LEL) (volume %) 3.6 (E)
### Behaviour at sea
### Additional data
Colour pale yellow Odour slight
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) ambient Family name organic acids
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 3A - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TLV-TWA 0.1
### Ecotoxicity
# 2-ETHYL-3-PROPYL ACROLEIN
UN Number: 1191 - CAS Number: 645-62-5
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1191 CAS number 645-62-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 857 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 126.2 Boiling Point (°C) 175 Vapour Pressure (Pa) < 345 [Pa] at a temperature of 20°C Ignition Temperature (°C) 200 Flash Point (°C) 68
### Behaviour at sea
### Additional data
Colour yellow Odour odourless Standard behavior classification F/FE
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 19 Temperature (°C) ambient Family name aldehydes
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# 2-ETHYLHEXANOIC ACID
CAS Number: 149-57-5 Also known as: ACIDE 2-ETHYLHEXANOIQUE, BUTYLETHYLACETIC ACID, 2-Ethylcaproic Acid, 2-Ethyl-Hexanoic Acid, Ethylhexoic Acid, Ethylhexanoic Acid, 2-Ethylhexanoic Acid, Acide 2-EthylhexanoÏQue
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 149-57-5 Formula C 8 H 1 6 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 908 [Kg/m³] at a temperature of 20°C 903.1 [Kg/m³] at a temperature of 25°C 917.3 [Kg/m³] at a temperature of 5°C 914.2 [Kg/m³] at a temperature of 10°C 906.1 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 8.64 [cSt] at a temperature of 20°C 17.911 [cSt] at a temperature of 5°C 14.034 [cSt] at a temperature of 10°C 9.2815 [cSt] at a temperature of 20°C Molar mass (g/mol) 144.21 Density of gas (kg/m3) 6.45 Solubility (g/L) 2000 [g/L] at a temperature of 20°C and salinity of 0‰ 1400 [g/L] at a temperature of 25°C and salinity of 0‰ 1640 [g/L] at a temperature of 20°C and salinity of 0‰ 1680 [g/L] at a temperature of 20°C and salinity of 5‰ 960 [g/L] at a temperature of 20°C and salinity of 30‰ Boiling Point (°C) 227 Melting Point (°C) -83 Critical molar volume (m³/mol) 0.000528 Critical temperature (°C) 674 Critical pressure (Pa) 2780000 Surface tension (mN/m) 28.42 [mN/m] at a temperature of 6.9°C 27.62 [mN/m] at a temperature of 11.2°C 26.86 [mN/m] at a temperature of 19.5°C Ignition Temperature (°C) 440 Flash Point (°C) 118 Flash Point (Pensky-Martens closed cup) (°C) 114 Flash Point (Cleveland open cup) (°C) 118 Lower explosivity limit (LEL) (volume %) 1.4 Upper explosivity limit (UEL) (volume %) 8.64 Vapor enthalpy (J/Kg) 524563 [J/Kg] at a temperature of 25°C Henry's constant (mol/(m³·Pa)) 0.28
### Behaviour at sea
Log kow 2.64 Log koc 1.43 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 3
### Additional data
Colour colourless Odour mild MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification FD
### Transportation data
State liquid Temperature (°C) ambient Family name organic acids
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
Hazard statements Health H361 Suspected of damaging fertility or the unborn child. TEEL-1 (mg/m3) 15 TEEL-2 (mg/m3) 125 TEEL-3 (mg/m3) 500
### Ecotoxicity
Lowest median lethal concentration (LC50) on fishes (mg/l) 70 Highest no observed effect concentration (NOEC) on algae (mg/l) 0.45 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 18 Assessment factor (AF) 500 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 36 [µg/l] on the Short term
# 2-ETHYLHEXANOL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 834 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 130.23 Density of gas (kg/m3) 5.79 Boiling Point (°C) 184.9 Melting Point (°C) < -76 Ignition Temperature (°C) 231 Flash Point (°C) 73 Lower explosivity limit (LEL) (volume %) 1.1 Upper explosivity limit (UEL) (volume %) 7.4
### Behaviour at sea
### Additional data
Colour colourless Odour weak odour
### Transportation data
Cargo group 20 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alcohols, glycols
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
ERPG-1 (ppm) 0.1 ERPG-2 (ppm) 100 ERPG-3 (ppm) 200
### Ecotoxicity
# 2-ETHYLHEXYL ACRYLATE inhibited
CAS Number: 103-11-7 Also known as: ACRYLATE D'ETHYL-2 HEXYLE, ACRYLIC ACID, 2-ETHYLHEXYL ESTER, 2-Ethyl-1-Hexyl Acrylate, 2-Ethylhexyl 2-Propenoate, 2-Propenoic Acid, 2-Ethylhexyl Ester, Acrylic Acid, 2-Ethylhexyl Ester, Ethylhexyl Acrylate, 2-Ethylhexylprop-2-Enoate, 2-Ethylhexyl Acrylate, Acrylate D'Ethyl 2-Hexyle
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 103-11-7 Formula C 1 1 H 2 0 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 885 [Kg/m³] at a temperature of 20°C 897 [Kg/m³] at a temperature of 5°C 891.8 [Kg/m³] at a temperature of 10°C 886.1 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 4.4482 [cSt] at a temperature of 5°C 4.1826 [cSt] at a temperature of 10°C 6.2634 [cSt] at a temperature of 20°C Molar mass (g/mol) 184.2 Density of gas (kg/m3) 8.192 Solubility (g/L) 100 [g/L] at a temperature of 25°C and salinity of 0‰ 36 [g/L] at a temperature of 20°C and salinity of 0‰ 35 [g/L] at a temperature of 20°C and salinity of 5‰ 21 [g/L] at a temperature of 20°C and salinity of 30‰ Boiling Point (°C) 214 Melting Point (°C) -90 Surface tension (mN/m) 26 [mN/m] at a temperature of 20°C 27.91 [mN/m] at a temperature of 5.4°C 27.68 [mN/m] at a temperature of 11.3°C 26.82 [mN/m] at a temperature of 19.3°C Interfacial tension (mN/m) 30 [mN/m] at a temperature of 20°C and salinity of 0‰ Vapour Pressure (Pa) 13 [Pa] at a temperature of 20°C 24 [Pa] at a temperature of 25°C Ignition Temperature (°C) 384 Flash Point (°C) 82 Flash Point (Pensky-Martens closed cup) (°C) 87.5 Lower explosivity limit (LEL) (volume %) 0.87 Upper explosivity limit (UEL) (volume %) 6.4 Combus enthalpy (J/Kg) 33800000 Combustion efficiency (%) 96 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.05 Rad fraction (%) 23 Henry's constant (mol/(m³·Pa)) 45
### Behaviour at sea
Log kow 4.09 Log koc 3.73 Biodegradation in estuary environment (Half- life) (days) 6205 Biodegradation in marine environment (Half-life) (days) 10 Bioconcentration factor (BCF) 412
### Additional data
Colour colourless Odour sharp odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Package group II Cargo group 14 State liquid Temperature (°C) < 38� Pressure (Pa) ambient Family name acrylates
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
Hazard statements Health H315 Causes skin irritation. H317 May cause an allergic skin reaction. H335 May cause respiratory irritation. TEEL-1 (mg/m3) 1.5 TEEL-2 (mg/m3) 10 TEEL-3 (mg/m3) 10
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 1.71 Lowest median lethal concentration (LC50) on crustacean (mg/l) 1.3 Lowest median lethal concentration (LC50) on fishes (mg/l) 1.8 Highest no observed effect concentration (NOEC) on algae (mg/l) 0.8 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.19 Assessment factor (AF) 100 on the Short term 10000 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 13 [µg/l] on the Short term 0.13 [µg/l] on the Long term
# 2-ETHYLHEXYLAMINE
UN Number: 2276 Also known as: ALKYLAMINES, 1-AMINO-2-ETHYLHEXANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2276
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 800 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 129.25 Density of gas (kg/m3) 5.805 Boiling Point (°C) 169 Melting Point (°C) < -76 Vapour Pressure (Pa) 27 [Pa] at a temperature of 20°C Ignition Temperature (°C) 265 Flash Point (°C) 50
### Behaviour at sea
### Additional data
Colour colourless Odour musky ammonia Standard behavior classification FD
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) ambient Family name aliphatic amines IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Metal(s) and alloys Yes (Al, Cu, Zn) Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# 2-HYDROXY-4-(METHYLTHIO)-BUTANOIC ACID
CAS Number: 583-91-5 Also known as: ACIDE 2-HYDROXY-4-(METHYLTHIO)-BUTANOIQUE, BUTYRIC ACID, 2-HYDROXY-4-METHYLTHIO-
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 583-91-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1220 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 150.2 Density of gas (kg/m3) 6.7 Ignition Temperature (°C) 160 Flash Point (°C) 121
### Behaviour at sea
### Additional data
Colour light brown Odour odourless Standard behavior classification SD/D/DE
### Transportation data
Family name organic acids
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# 2-HYDROXYETHYL ACRYLATE inhibited
CAS Number: 818-61-1 Also known as: ACRYLATE D'HYDROXY-2 ETHYLE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 818-61-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1100 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 116.1 Boiling Point (°C) 310 Melting Point (°C) -60.2 Vapour Pressure (Pa) 10100 [Pa] at a temperature of 20°C Flash Point (°C) 101 Lower explosivity limit (LEL) (volume %) 1.8
### Behaviour at sea
### Additional data
Colour colourless Odour sweet, pleasant odour Standard behavior classification DE, D
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-3 (mg/m3) 50
### Ecotoxicity
# 2-METHYL-5-ETHYL PYRIDINE
UN Number: 2300 - CAS Number: 104-90-5
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2300 CAS number 104-90-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 922 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 122.19 Vapour Pressure (Pa) 120 [Pa] at a temperature of 20°C
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Standard behavior classification FD
### Transportation data
Package group III IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# 2-METHYL-6-ETHYL ANILINE
CAS Number: 24549-06-2
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 24549-06-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 969 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 135.2 Boiling Point (°C) 231 Melting Point (°C) -33 Flash Point (°C) 102
### Behaviour at sea
### Additional data
Colour colourless Odour pungent Standard behavior classification FD/FED/E
### Transportation data
State liquid Temperature (°C) ambient Family name aromatic amines
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# 2-METHYLPYRIDINE
UN Number: 2313 - CAS Number: 109-06-8
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2313 CAS number 109-06-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 944 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 93.13 Density of gas (kg/m3) 4.13 Boiling Point (°C) 128.8 Melting Point (°C) -66.8 Vapour Pressure (Pa) 1200 [Pa] at a temperature of 20°C Ignition Temperature (°C) 538 Flash Point (°C) 26 Lower explosivity limit (LEL) (volume %) 1.4 Upper explosivity limit (UEL) (volume %) 8.6
### Behaviour at sea
### Additional data
Colour colourless Odour strong, unpleasant
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) ambient Family name aromatic amines IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 5 ppm TEEL-2 (mg/m3) 5 ppm TEEL-3 (mg/m3) 300 ppm
### Ecotoxicity
# 2-NITROPROPANE
UN Number: 2608
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2608
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1000 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 89.09 Density of gas (kg/m3) 3.94 Boiling Point (°C) 132 Melting Point (°C) -108 Vapour Pressure (Pa) 1000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 428 Flash Point (°C) 36 Lower explosivity limit (LEL) (volume %) 2.2
### Behaviour at sea
### Additional data
Colour colourless Odour mild fruity Standard behavior classification FED
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 42 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name nitro compounds IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 0 - Not irritating Specific Health Concern (D3) C - Carcinogenicity Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 1000 TLV-TWA 25 TEEL-1 (mg/m3) 30 ppm TEEL-2 (mg/m3) 50 ppm TEEL-3 (mg/m3) 100 ppm
### Ecotoxicity
# 3,4-DICHLORO-1-BUTENE
CAS Number: 760-23-6 Also known as: 3,4 DCB, 3,4-DICHLOROBUTENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 760-23-6
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1150 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 125 Density of gas (kg/m3) 5.48 Boiling Point (°C) 119 Melting Point (°C) -61 Vapour Pressure (Pa) 1866 [Pa] at a temperature of 20°C Ignition Temperature (°C) 450 Flash Point (°C) 29 Lower explosivity limit (LEL) (volume %) 2.4 Upper explosivity limit (UEL) (volume %) 13.3
### Behaviour at sea
### Additional data
Colour colourless to brown Odour characteristic pungent Standard behavior classification S/SD
### Transportation data
Cargo group 36 State liquid Family name halogenated hydrocarbons
### Reactivity data
Water No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# 3-METHOXY-1-BUTANOL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 928 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 104.14 Boiling Point (°C) 161 Melting Point (°C) -85 Flash Point (°C) 46
### Behaviour at sea
### Additional data
### Transportation data
State liquid
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# 3-METHOXYBUTYL ACETATE
CAS Number: 1809-19-4 Also known as: ACETATE DE 3-METHOXYBUTYLE, 1-BUTANOL, 3-METHOXYACETATE, BUTOXYL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 1809-19-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 960 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 146.19 Density of gas (kg/m3) 6.51 Boiling Point (°C) 135 Flash Point (°C) 77
### Behaviour at sea
### Additional data
Colour colourless Odour acrid
### Transportation data
Cargo group 34 Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# 3-METHYLPYRIDINE
UN Number: 2313 - CAS Number: 108-99-6
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2313 CAS number 108-99-6
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 957 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 93.13 Boiling Point (°C) 144 Melting Point (°C) -18.3 Vapour Pressure (Pa) 586 [Pa] at a temperature of 20°C Ignition Temperature (°C) 538 Flash Point (°C) 36 Lower explosivity limit (LEL) (volume %) 1.3 Upper explosivity limit (UEL) (volume %) 8.7
### Behaviour at sea
### Additional data
Colour colourless Odour sweetish, not unpleasant
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) ambient Family name aromatic amines IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 5 ppm TEEL-2 (mg/m3) 125 ppm TEEL-3 (mg/m3) 600 ppm
### Ecotoxicity
# 4-METHYLPYRIDINE
UN Number: 2313 - CAS Number: 108-89-4
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2313 CAS number 108-89-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 957 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 93.13 Density of gas (kg/m3) 4.13 Boiling Point (°C) 145 Melting Point (°C) 2.4 Vapour Pressure (Pa) 530 [Pa] at a temperature of 20°C Ignition Temperature (°C) 538 Flash Point (°C) 57 Lower explosivity limit (LEL) (volume %) 1.3 Upper explosivity limit (UEL) (volume %) 8.7
### Behaviour at sea
### Additional data
Colour colourless to brown Odour sweetish, obnoxious
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) ambient Family name aromatic amines IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# ACETALDEHYDE
UN Number: 1089 Also known as: ACETIC ALDEHYDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1089
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 780 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 44.05 Density of gas (kg/m3) 1.032 Boiling Point (°C) 20.6 Melting Point (°C) -123 Vapour Pressure (Pa) 99900 [Pa] at a temperature of 20°C Ignition Temperature (°C) 185 Flash Point (°C) -38 Upper explosivity limit (UEL) (volume %) 57
### Behaviour at sea
### Additional data
Colour colourless Odour sharp, fruit odour Standard behavior classification DE
### Transportation data
Transport mode Gas,Packaged Ship type 2G,2PG Cargo group 19 State liquid Temperature (°C) ambient Pressure (Pa) safety relief Family name aldehydes IMO class 3.1
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Static electricity Yes Oxidizing agents Yes Reducing agents Yes Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 10000 TLV-TWA 100 ERPG-1 (ppm) 10 ERPG-2 (ppm) 200 ERPG-3 (ppm) 1000
### Ecotoxicity
# ACETIC ACID (>80 wt% acid)
UN Number: 2789 - CAS Number: 64-19-7 Also known as: ACIDE ACETIQUE (teneur en acide >80% mass.), AZINZUUR, Ethanoic Acid, Ethylic Acid, Methanecarboxylic Acid, Vinegar, Vinegar Acid, Acetic Acid, Acide Acetique
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2789 CAS number 64-19-7 Formula C 2 H 4 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1051 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 1.16 [cSt] at a temperature of 20°C 1 [cSt] at a temperature of 25°C Molar mass (g/mol) 60.05 Density of gas (kg/m3) 2.709 Solubility (g/L) 1050000 [g/L] at a temperature of 20°C and salinity of 0‰ 1050000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 118.1 Melting Point (°C) 17 Critical molar volume (m³/mol) 0.000171 Critical temperature (°C) 590.7 Critical pressure (Pa) 5780000 Surface tension (mN/m) 27.59 [mN/m] at a temperature of 20°C 27.1 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 1599 [Pa] at a temperature of 20°C 2093 [Pa] at a temperature of 25°C Ignition Temperature (°C) 485 Flash Point (°C) 40 Flash Point (Pensky-Martens closed cup) (°C) 39.4 Flash Point (Cleveland open cup) (°C) 44.4 Lower explosivity limit (LEL) (volume %) 5.4 Upper explosivity limit (UEL) (volume %) 16 Vapor enthalpy (J/Kg) 394670 [J/Kg] at a temperature of 117.9°C 389010 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 13100000 Specific heat capacity (J/(Kg·K)) 2053 Combustion efficiency (%) 98 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.03 Rad fraction (%) 23 Henry's constant (mol/(m³·Pa)) 0.01
### Behaviour at sea
Log kow 0.17 Log koc 1.02 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 10 Bioconcentration factor (BCF) 1
### Additional data
Colour colourless Odour strong vinegar odour MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name organic acids
### Reactivity data
Water No Abilities Miscible in water. Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents No Organic substance Yes Notable risks Reacts violently with strong oxidants and strong bases.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 1000 Hazard statements Physical H226 Flammable liquid and vapour. Health H314 Causes severe skin burns and eye damage. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P241 Use explosion-proof electrical/ventilating/lighting/.../equipment. P260 Do not breathe dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. Disposal P501 Dispose of contents/container to ... TLV-TWA 10 ERPG-2 (ppm) 35 ERPG-3 (ppm) 250
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 20 Lowest median lethal concentration (LC50) on crustacean (mg/l) 18.9 Lowest median lethal concentration (LC50) on fishes (mg/l) 43.8 Highest no observed effect concentration (NOEC) on algae (mg/l) 10.6 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 22.7 Highest no observed effect concentration (NOEC) on fishes (mg/l) 34.3 Assessment factor (AF) 100 on the Short term 100 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 189 [µg/l] on the Short term 106 [µg/l] on the Long term
# ACETIC ANHYDRIDE
UN Number: 1715 - CAS Number: 108-24-7 Also known as: ACETIC ACID ANHYDRIDE, ACETIC OXIDE, ACETYL, ACETYL ANHYDRIDE, ACETYL ETHER, ACETYL OXIDE, ANHYDRIDE ACETIQUE, AZINZUUR ANHYDRIDE, Acetanhydride, Ethanoic Anhydrate, Ethanoic Anhydride, Ethanoic Acid Anhydride, Acetic Anhydride, Anhydryde Acetique
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1715 CAS number 108-24-7 Formula C 4 H 6 O 3
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1080 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.84 [cSt] at a temperature of 20°C 0.78 [cSt] at a temperature of 25°C Molar mass (g/mol) 102.09 Density of gas (kg/m3) 4.541 Solubility (g/L) 113500 [g/L] at a temperature of 20°C and salinity of 0‰ 262000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 139 Melting Point (°C) -73 Critical temperature (°C) 606 Critical pressure (Pa) 4000000 Surface tension (mN/m) 32.7 [mN/m] at a temperature of 20°C 31.93 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 533 [Pa] at a temperature of 20°C 680 [Pa] at a temperature of 25°C Ignition Temperature (°C) 330 Flash Point (°C) 49 Flash Point (Pensky-Martens closed cup) (°C) 49 Flash Point (Cleveland open cup) (°C) 54 Lower explosivity limit (LEL) (volume %) 2.7 Upper explosivity limit (UEL) (volume %) 10 Combus enthalpy (J/Kg) 16400000 Specific heat capacity (J/(Kg·K)) 1648 Combustion efficiency (%) 98 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.03 Rad fraction (%) 23 Henry's constant (mol/(m³·Pa)) 0.57
### Behaviour at sea
Log kow -0.58 Log koc 1.11 Biodegradation in estuary environment (Half-life) (days) 1 Biodegradation in marine environment (Half-life) (days) 10 Bioconcentration factor (BCF) 1
### Additional data
Colour colourless Odour strong vinegar odour MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 11 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name organic anhydrides
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Specific Health Concern (D3) A - Aspiration Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 1000 Hazard statements Physical H226 Flammable liquid and vapour. Health H302 Harmful if swallowed. H314 Causes severe skin burns and eye damage. H332 Harmful if inhaled. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P233 Keep container tightly closed. P235 Keep cool. P240 Ground/bond container and receiving equipment. P241 Use explosion- proof electrical/ventilating/lighting/.../equipment. P242 Use only non-sparking tools. P243 Take precautionary measures against static discharge. P260 Do not breathe dust/fume/gas/mist/vapours/spray. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P264 Wash ... thoroughly after handling. P270 Do no eat, drink or smoke when using this product. P271 Use only outdoors or in a well-ventilated area. P284 Wear respiratory protection. Response P301 + P312 IF SWALLOWED: Call a POISON CENTER or doctor/physician if you feel unwell. P303 IF ON SKIN (or hair): P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P310 Immediately call a POISON CENTER or doctor/physician. P320 Specific treatment is urgent (see ... on this label). P330 Rinse mouth. P370 In case of fire: P378 Use ... for extinction. Storage P403 + P233 Store in a well-ventilated place. Keep container tightly closed. P405 Store locked up. Disposal P501 Dispose of contents/container to ... ERPG-1 (ppm) 0.5 ERPG-2 (ppm) 15 ERPG-3 (ppm) 100
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 9 Lowest median lethal concentration (LC50) on crustacean (mg/l) 55 Lowest median lethal concentration (LC50) on fishes (mg/l) 265 Highest no observed effect concentration (NOEC) on algae (mg/l) 9 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 31.4 Highest no observed effect concentration (NOEC) on fishes (mg/l) 34.3 Assessment factor (AF) 1000 on the Short term 1000 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 9 [µg/l] on the Short term 9 [µg/l] on the Long term
# ACETOCHLOR
CAS Number: 34256-82-1 Also known as: ACETOCHLORE, 2-CHLORO-N-ETHOXYMETHYL-N-(2-ETHYL-6-METHYLPHENYL)ACETAMIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 34256-82-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1117 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 270 Density of gas (kg/m3) > 1.29 Boiling Point (°C) 162 (933 Pa) Melting Point (°C) < 0 Vapour Pressure (Pa) 0.002 [Pa] at a temperature of 20°C Flash Point (°C) > 100
### Behaviour at sea
### Additional data
Colour light amber to violet Odour sweet Standard behavior classification SD
### Transportation data
State liquid
### Reactivity data
Metal(s) and alloys Yes (Cu, mild steel)
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# ACETONE
UN Number: 1090 - CAS Number: 67-64-1 Also known as: DIMETHYL FORMALDEHYDE, DIMETHYL KETAL, DIMETHYL KETONE, Dimethylketal, Ketone Propane, Beta-Ketopropane, Methyl Ketone, 2-Propanone, Pyroacetic Acid, Pyroacetic Ether, Propanone, Acetone
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1090 CAS number 67-64-1 Formula C 3 H 6 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 791 [Kg/m³] at a temperature of 20°C 807 [Kg/m³] at a temperature of 5°C 801.8 [Kg/m³] at a temperature of 10°C 791.8 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.4 [cSt] at a temperature of 20°C 0.39 [cSt] at a temperature of 25°C 1.5861 [cSt] at a temperature of 5°C 1.4467 [cSt] at a temperature of 10°C 1.7176 [cSt] at a temperature of 20°C Molar mass (g/mol) 58.08 Density of gas (kg/m3) 2.58 Solubility (g/L) 790000 [g/L] at a temperature of 20°C and salinity of 0‰ 790000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 56 Melting Point (°C) -95 Critical molar volume (m³/mol) 0.000213 Critical temperature (°C) 508.1 Critical pressure (Pa) 4700000 Surface tension (mN/m) 23.7 [mN/m] at a temperature of 20°C 23.46 [mN/m] at a temperature of 25°C 24.9 [mN/m] at a temperature of 5.1°C 21.14 [mN/m] at a temperature of 9.8°C 23.44 [mN/m] at a temperature of 18°C Vapour Pressure (Pa) 22599 [Pa] at a temperature of 20°C 30930 [Pa] at a temperature of 25°C Ignition Temperature (°C) 540 Flash Point (°C) -19 Flash Point (Pensky-Martens closed cup) (°C) -20 Flash Point (Cleveland open cup) (°C) -15.6 Lower explosivity limit (LEL) (volume %) 2.5 Upper explosivity limit (UEL) (volume %) 12.8 Vapor enthalpy (J/Kg) 501033 [J/Kg] at a temperature of 56.2°C 533574 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 28600000 Specific heat capacity (J/(Kg·K)) 2174.59 Combustion efficiency (%) 96 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.05 Rad fraction (%) 27 Henry's constant (mol/(m³·Pa)) 4.31
### Behaviour at sea
Log kow -0.24 Log koc 0.73 Aqueous photolysis (Half-life) 1.67 Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 10 Bioconcentration factor (BCF) 0.69
### Additional data
Colour colourless Odour sweet odour MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment. Standard behavior classification DE
### Transportation data
Package group II Cargo group 18 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name ketones IMO class 3.1
### Reactivity data
Water No Abilities Miscible in water. Acid(s) Yes Base(s) Yes Static electricity Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 20000 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H319 Causes serious eye irritation. H336 May cause drowsiness or dizziness. TLV-TWA 750 TEEL-1 (mg/m3) 200 TEEL-2 (mg/m3) 3200 TEEL-3 (mg/m3) 5700
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) > 10000 Lowest median lethal concentration (LC50) on crustacean (mg/l) 2100 Lowest median lethal concentration (LC50) on fishes (mg/l) 6070 Highest no observed effect concentration (NOEC) on algae (mg/l) 3400 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 1660 Assessment factor (AF) 1000 on the Short term 500 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 2100 [µg/l] on the Short term 3320 [µg/l] on the Long term
# ACETONE CYANOHYDRIN stabilized
UN Number: 1541 - CAS Number: 75-86-5 Also known as: CYANHYDRINE D'ACETONE stabilisé, 2-Hydroxy-2-Methylpropanenitrile, 2-Hydroxy-2-Methylpropionitrile, Acetonecyanhydrine, Cyanhydrine D'Acetone, 2-Methyllacetonitrile, 2-Cyano-2-Propanol, 2-Hydroxyisobutyronitrile, Alpha- Hydroxyisobutyronitrile, Acetone Cyanohydrin, Acetone Cyanohydrine, α-Hydroxyisobutyronitrile
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1541 CAS number 75-86-5 Formula C 4 H 7 NO
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 925 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 85.11 Density of gas (kg/m3) 3.741 Solubility (g/L) 930000 [g/L] at a temperature of 20°C and salinity of 0‰ 930000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 82 Melting Point (°C) -20 Vapour Pressure (Pa) 110 [Pa] at a temperature of 20°C Ignition Temperature (°C) 685 Flash Point (°C) 74 Flash Point (Pensky-Martens closed cup) (°C) 73.9 Flash Point (Cleveland open cup) (°C) 74 Lower explosivity limit (LEL) (volume %) 2.25 Upper explosivity limit (UEL) (volume %) 11 Combus enthalpy (J/Kg) 26300000 Combustion efficiency (%) 95 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.03 Rad fraction (%) 22 Henry's constant (mol/(m³·Pa)) 0.34
### Behaviour at sea
Log kow -0.03 Log koc 1.08 Biodegradation in estuary environment (Half-life) (days) 1 Bioconcentration factor (BCF) 1
### Additional data
Colour colourless Odour mild almond odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged State liquid Temperature (°C) ambient Pressure (Pa) under pressure IMO class 6.1
### Reactivity data
Abilities Miscible in water. Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 4 - High Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 45 (as CN) Hazard statements Health H300 Fatal if swallowed. H310 Fatal in contact with skin. H330 Fatal if inhaled. H370 Causes damage to organs. Environmental H400 Very toxic to aquatic life. H410 Very toxic to aquatic life with long lasting effects. Precautionary statements Prevention P280 Wear protective gloves/protective clothing/eye protection/face protection. P284 Wear respiratory protection. Response P302 + P350 IF ON SKIN: Gently wash with plenty of soap and water. Storage P403 + P233 Store in a well-ventilated place. Keep container tightly closed. Disposal P501 Dispose of contents/container to ... TLV-TWA 4.5 (CN) TEEL-2 (mg/m3) 7.1 TEEL-3 (mg/m3) 15
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 1.25 Lowest median lethal concentration (LC50) on crustacean (mg/l) 0.13 Lowest median lethal concentration (LC50) on fishes (mg/l) 0.22 Assessment factor (AF) 1000 on the Short term 10000 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 0.13 [µg/l] on the Short term 0.013 [µg/l] on the Long term
# ACETONITRILE
UN Number: 1648 - CAS Number: 75-05-8 Also known as: CYANOMETHANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1648 CAS number 75-05-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 787 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 41.05 Density of gas (kg/m3) 1.83 Boiling Point (°C) 81 Melting Point (°C) -45 Vapour Pressure (Pa) 11143 [Pa] at a temperature of 20°C Ignition Temperature (°C) 525 Lower explosivity limit (LEL) (volume %) 4.4 Upper explosivity limit (UEL) (volume %) 16
### Behaviour at sea
### Additional data
Colour colourless Odour sweet odour Standard behavior classification DE
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 37 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name nitriles IMO class 3.2
### Reactivity data
Acid(s) Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 4000 TLV-TWA 40 TEEL-1 (mg/m3) 13 TEEL-2 (mg/m3) 320 TEEL-3 (mg/m3) 670
### Ecotoxicity
# ACETOPHENONE
Also known as: ACETYLBENZENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1028 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 120.15 Boiling Point (°C) 201.9 Melting Point (°C) 20 Vapour Pressure (Pa) 140 [Pa] at a temperature of 20°C Ignition Temperature (°C) 571 Flash Point (°C) 999
### Behaviour at sea
### Additional data
Colour colourless Odour sweet, flower odour
### Transportation data
State liquid
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 30 TEEL-2 (mg/m3) 50 TEEL-3 (mg/m3) 350
### Ecotoxicity
# ACETYL CHLORIDE
UN Number: 1717 Also known as: ACETIC ACID CHLORIDE, ACETIC CHLORIDE, CHLORURE D'ACETYLE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1717
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1103.9 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 78.5 Density of gas (kg/m3) 3.483 Boiling Point (°C) 51 Melting Point (°C) -112 Vapour Pressure (Pa) 28000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 390 Flash Point (°C) -4 Lower explosivity limit (LEL) (volume %) 7.3 Upper explosivity limit (UEL) (volume %) 19
### Behaviour at sea
### Additional data
Colour colourless Odour sharp odour Standard behavior classification DE, SD
### Transportation data
Package group II State liquid Temperature (°C) ambient Pressure (Pa) under pressure IMO class 3.2
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 0.0075 TEEL-2 (mg/m3) 0.05 TEEL-3 (mg/m3) 125
### Ecotoxicity
# ACROLEIN inhibited
UN Number: 1092 Also known as: ACRALDEHYDE, ACROLEINE, ALLYL ALDEHYDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1092
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 843 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 56.1 Density of gas (kg/m3) 2.451 Boiling Point (°C) 53 Melting Point (°C) -88 Vapour Pressure (Pa) 29681 [Pa] at a temperature of 20°C Ignition Temperature (°C) 278 Flash Point (°C) -20 Lower explosivity limit (LEL) (volume %) 2.8 Upper explosivity limit (UEL) (volume %) 31
### Behaviour at sea
### Additional data
Colour colourless to light yellow Odour sharp, irritating odour Standard behavior classification DE
### Transportation data
Cargo group 19 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name aldehydes IMO class 6.1
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.1 ERPG-1 (ppm) 0.05 ERPG-2 (ppm) 0.15 ERPG-3 (ppm) 1.5
### Ecotoxicity
# ACRYLAMIDE
UN Number: 2074 - CAS Number: 79-06-1 Also known as: ACRYLIC AMIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2074 CAS number 79-06-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1050 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 71 Density of gas (kg/m3) 1.29 Melting Point (°C) 84 Vapour Pressure (Pa) 2527 [Pa] at a temperature of 20°C Ignition Temperature (°C) 424 Flash Point (°C) 999
### Behaviour at sea
### Additional data
### Transportation data
Transport mode Bulk,Packaged Package group III IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TLV-TWA 0.01 TEEL-1 (mg/m3) 7.5 TEEL-2 (mg/m3) 60 TEEL-3 (mg/m3) 60
### Ecotoxicity
# ACRYLIC ACID inhibited
UN Number: 2218 - CAS Number: 79-10-7 Also known as: ACIDE ACRYLIQUE, ACROLEIC ACID, Acrylic Acid, Inhibited, Ethylenecarboxylic Acid, Glacial Acrylic Acid, Propene Acid, 2-Propenoic Acid, Propenoic Acid, Vinylformic Acid, Acrylic Acid
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2218 CAS number 79-10-7 Formula C 3 H 4 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1049.7 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 1.24 [cSt] at a temperature of 20°C Molar mass (g/mol) 72.06 Density of gas (kg/m3) 3.225 Solubility (g/L) 1060000 [g/L] at a temperature of 20°C and salinity of 0‰ 1060000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 141.5 Melting Point (°C) 13 Surface tension (mN/m) 28.1 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 1399 [Pa] at a temperature of 20°C 530 [Pa] at a temperature of 25°C Ignition Temperature (°C) 374 Flash Point (°C) 47 Flash Point (Pensky-Martens closed cup) (°C) 48 Flash Point (Cleveland open cup) (°C) 50 Lower explosivity limit (LEL) (volume %) 5.3 Upper explosivity limit (UEL) (volume %) 26 Combus enthalpy (J/Kg) 18400000 Specific heat capacity (J/(Kg·K)) 2021.9 Combustion efficiency (%) 98 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.03 Rad fraction (%) 23 Henry's constant (mol/(m³·Pa)) 0.04
### Behaviour at sea
Log kow 0.39 Log koc 1.42 Biodegradation in estuary environment (Half- life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 10 Bioconcentration factor (BCF) 1
### Additional data
Colour colourless Odour irritating odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) 16�- 24� Family name organic acid
### Reactivity data
Water No Abilities Miscible in water. Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
Hazard statements Physical H226 Flammable liquid and vapour. Health H302 Harmful if swallowed. H312 Harmful in contact with skin. H332 Harmful if inhaled. H335 May cause respiratory irritation. Environmental H400 Very toxic to aquatic life. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P273 Avoid release to the environment. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. TLV-TWA 10 ERPG-2 (ppm) 50 ERPG-3 (ppm) 750
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 0.13 Lowest median lethal concentration (LC50) on crustacean (mg/l) 47 Lowest median lethal concentration (LC50) on fishes (mg/l) 27 Highest no observed effect concentration (NOEC) on algae (mg/l) 0.03 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 7 Assessment factor (AF) 100 on the Short term 100 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 1.3 [µg/l] on the Short term 0.3 [µg/l] on the Long term
# ACRYLONITRILE inhibited
UN Number: 1093 - CAS Number: 107-13-1 Also known as: ACRYLON, CARBACRYL, CYANOETHYLENE, Acrylonitrile Monomer, 2-Propenenitrile, Propenoic Acid Nitrile, Vinyl Cyanide, Cyanure De Vinyle, Nitrile Acrylique, Acrylonitrile
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1093 CAS number 107-13-1 Formula C 3 H 3 N
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 807.5 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.43 [cSt] at a temperature of 20°C 0.42 [cSt] at a temperature of 25°C Molar mass (g/mol) 53.06 Density of gas (kg/m3) 2.322 Solubility (g/L) 79000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 77 Melting Point (°C) -82 Critical molar volume (m³/mol) 0.000173 Critical temperature (°C) 540 Critical pressure (Pa) 4660000 Surface tension (mN/m) 27.22 [mN/m] at a temperature of 20°C 26.63 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 11143 [Pa] at a temperature of 20°C 14470 [Pa] at a temperature of 25°C Ignition Temperature (°C) 480 Flash Point (°C) -5 Flash Point (Pensky-Martens closed cup) (°C) -1 Lower explosivity limit (LEL) (volume %) 3 Upper explosivity limit (UEL) (volume %) 17 Vapor enthalpy (J/Kg) 616000 [J/Kg] at a temperature of 77.4°C Combus enthalpy (J/Kg) 31900000 Specific heat capacity (J/(Kg·K)) 2050 Combustion efficiency (%) 98 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.05 Rad fraction (%) 26 Henry's constant (mol/(m³·Pa)) 8.7
### Behaviour at sea
Log kow -0.92 Log koc -0.07 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) Not biodegradable Bioconcentration factor (BCF) 1
### Additional data
Colour colourless to light yellow Odour irritating odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification DE
### Transportation data
Transport mode Bulk,Packaged Cargo group 15 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name substituted allyls IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Static electricity No Oxidizing agents Yes Notable risks Oxidizer. Polymerization.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 500 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H301 Toxic if swallowed. H311 Toxic in contact with skin. H317 May cause an allergic skin reaction. H318 Causes serious eye damage. H331 Toxic if inhaled. H335 May cause respiratory irritation. H350 May cause cancer. Environmental H411 Toxic to aquatic life with long lasting effects. Precautionary statements Prevention P201 Obtain special instructions before use. P202 Do not handle until all safety precautions have been read and understood. P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P231 Handle under inert gas. P242 Use only non-sparking tools. P243 Take precautionary measures against static discharge. P260 Do not breathe dust/fume/gas/mist/vapours/spray. P262 Do not get in eyes, on skin, or on clothing. P270 Do no eat, drink or smoke when using this product. P272 Contaminated work clothing should not be allowed out of the workplace. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. P284 Wear respiratory protection. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P302 + P352 IF ON SKIN: Wash with plenty of soap and water. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P331 Do NOT induce vomiting. P370 + P378 In case of fire: Use ... for extinction. Storage P403 + P233 Store in a well-ventilated place. Keep container tightly closed. P405 Store locked up. Disposal P501 Dispose of contents/container to ... ERPG-1 (ppm) 10 ERPG-2 (ppm) 35 ERPG-3 (ppm) 75
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 1.63 Lowest median lethal concentration (LC50) on crustacean (mg/l) 6 Lowest median lethal concentration (LC50) on fishes (mg/l) 5.16 Highest no observed effect concentration (NOEC) on algae (mg/l) 0.8 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.5 Highest no observed effect concentration (NOEC) on fishes (mg/l) 0.17 Assessment factor (AF) 100 on the Short term 100 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 16.3 [µg/l] on the Short term 1.7 [µg/l] on the Long term
# ACRYLONITRILE-STYRENE COPOLYMER dispersion in polyether polyol
Also known as: COPOLYMERE D'ACRYLONITRILE-STYRENE dispersion dans polyether polyol
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1050 [Kg/m³] at a temperature of 20°C Boiling Point (°C) decomp. Melting Point (°C) < -25 Vapour Pressure (Pa) 6665 [Pa] at a temperature of 20°C Flash Point (°C) 182
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
State liquid
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 0 - Is not a floater; and does not pose any known health hazards
### Human toxicity threshold
### Ecotoxicity
# ADIPONITRILE
UN Number: 2205 - CAS Number: 111-69-3 Also known as: ADIPIC ACID, ADIPIC ACID DINITRILE, 1,4-CYANOBUTANE, 1,4-DICYANOBUTANE, DINITRILE, Hexanedinitrile, Hexanedioic Acid Nitrile, Adipynitrile, Tetramethylenedicyanide, Adiponitrile
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2205 CAS number 111-69-3 Formula C 6 H 8 N 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 961.1 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 9.4 [cSt] at a temperature of 20°C Molar mass (g/mol) 108 Density of gas (kg/m3) 4.77 Solubility (g/L) 83000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 290 Melting Point (°C) 1 Critical temperature (°C) 507 Critical pressure (Pa) 2800000 Surface tension (mN/m) 45.45 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 10 [Pa] at a temperature of 20°C 0.33 [Pa] at a temperature of 25°C Ignition Temperature (°C) 460 Flash Point (°C) 93 Flash Point (Cleveland open cup) (°C) 93 Lower explosivity limit (LEL) (volume %) 1.7 Upper explosivity limit (UEL) (volume %) 4.9 Vapor enthalpy (J/Kg) 703382 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 40400000 Specific heat capacity (J/(Kg·K)) 1190 Henry's constant (mol/(m³·Pa)) 0.00012
### Behaviour at sea
Persistence (days) 1.6 Log kow -0.32 Log koc 1.3 Bioconcentration factor (BCF) 3
### Additional data
Colour colourless to light yellow Odour odourless MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment. Standard behavior classification FD
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 37 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name nitriles IMO class 6.1
### Reactivity data
Acid(s) Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
Hazard statements Health H301 Toxic if swallowed. H332 Harmful if inhaled. Precautionary statements Prevention P233 Keep container tightly closed. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P330 Rinse mouth. Storage P403 Store in a well-ventilated place. TLV-TWA 50 TEEL-1 (mg/m3) 3.85 TEEL-2 (mg/m3) 3.85 TEEL-3 (mg/m3) 150
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) > 100 Lowest median lethal concentration (LC50) on crustacean (mg/l) 445 Lowest median lethal concentration (LC50) on fishes (mg/l) 384 Highest no observed effect concentration (NOEC) on algae (mg/l) > 100 Highest no observed effect concentration (NOEC) on fishes (mg/l) 720 Assessment factor (AF) 1000 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 384 [µg/l] on the Short term
# ALACHLOR technical (90% or more)
CAS Number: 15972-60-8 Also known as: ALACHLORE technique (> 90%), 2-CHLORO-2',6'-DIETHYL-N-METHOXYMETHYLACETANILIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 15972-60-8
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1130 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 269.8 Boiling Point (°C) 100 (2.66 Pa) Melting Point (°C) 38 Vapour Pressure (Pa) < 10 [Pa] at a temperature of 20°C Flash Point (°C) 137
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
State solid
### Reactivity data
Metal(s) and alloys Yes (steel, black iron)
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 3 - ≥100 and <500 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# ALCOHOLIC BEVERAGES
UN Number: 3065 Also known as: AQUEOUS ETHANOLIC SOLUTIONS, BOISSONS ALCOOLISEES
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3065
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 790 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 46.1 Boiling Point (°C) 78 Melting Point (°C) 0.974358974
### Behaviour at sea
### Additional data
Colour miscellaneous Odour alcoholic odour
### Transportation data
Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alcohols, glycols IMO class 3.2
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents Yes Reducing agents No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
### Ecotoxicity
# ALDRIN solid
UN Number: 2761 Also known as: ALDREX, ALDRINE solide, ALDRINE, ALDRITE, ALDROSOL, ALTOX, DRINOX
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2761
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1600 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 364.93 Melting Point (°C) 95 Vapour Pressure (Pa) 0.009 [Pa] at a temperature of 20°C Flash Point (°C) 65
### Behaviour at sea
### Additional data
Colour light to dark brown Odour mild chemical odour Marine pollutant P
### Transportation data
Transport mode Bulk,Packaged Package group II State solid IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.015 TEEL-1 (mg/m3) 0.25 TEEL-2 (mg/m3) 10 TEEL-3 (mg/m3) 25
### Ecotoxicity
# ALKARYL POLYETHER (C9-C20)
Also known as: ALKARYL POLYETHERS (C9-C20)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1100 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 230/290 Melting Point (°C) 11.11111111 Vapour Pressure (Pa) < 10000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 260/370 Flash Point (°C) 150
### Behaviour at sea
### Additional data
Colour yellow-brown Odour lub-oil odour Standard behavior classification S/SD
### Transportation data
Cargo group 33 State liquid Family name miscell. hydroc. mixt
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# ALKYLBENZENESULFONIC ACID (>5% free H2SO4)
UN Number: 2584 Also known as: ACIDE ALKYLSULFONIQUE (H2SO4 libre >5%)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2584
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1200 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 310 Boiling Point (°C) 637 Melting Point (°C) 277 Vapour Pressure (Pa) 10100 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour white to yellow Odour odourless Standard behavior classification DE, D
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# ALKYLBENZENESULPHONIC ACID sodium salt solution
CAS Number: 42615-29-2 Also known as: ACIDE ALKYLBENZENESULFONIQUE sel de sodium, en solution, DECYLBENZENSULFONIC ACID
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 42615-29-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1000/1400 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 310 to 394 Boiling Point (°C) decomp. Flash Point (°C) 201
### Behaviour at sea
### Additional data
Colour white to yellow Odour odourless
### Transportation data
State liquid Temperature (°C) ambient
### Reactivity data
Water No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 3 - ≥100 and <500 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# ALLYL ALCOHOL
UN Number: 1098 - CAS Number: 107-18-6 Also known as: ALCOOL ALLYLIQUE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1098 CAS number 107-18-6
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 852 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 58.08 Density of gas (kg/m3) 2.58 Boiling Point (°C) 97.1 Melting Point (°C) -129 Vapour Pressure (Pa) 2400 [Pa] at a temperature of 20°C Ignition Temperature (°C) 375 Flash Point (°C) 21 Lower explosivity limit (LEL) (volume %) 2.5 Upper explosivity limit (UEL) (volume %) 18
### Behaviour at sea
### Additional data
Colour colourless Odour sharp, mustard odour
### Transportation data
Transport mode Bulk,Packaged Cargo group 15 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name substituted allyls IMO class 6.1
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Specific Health Concern (D3) A - Aspiration Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 150 TEEL-1 (mg/m3) 2.1 TEEL-2 (mg/m3) 4.2 TEEL-3 (mg/m3) 20
### Ecotoxicity
# ALLYL CHLORIDE
UN Number: 1100 - CAS Number: 107-05-1 Also known as: CHLORALLYLENE, 3-CHLOROPROPENE, alpha-CHLOROPROPYLENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1100 CAS number 107-05-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 938 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 76.53 Density of gas (kg/m3) 3.354 Boiling Point (°C) 45 Melting Point (°C) -136 Vapour Pressure (Pa) 40014 [Pa] at a temperature of 20°C Ignition Temperature (°C) 390 Flash Point (°C) -30 Lower explosivity limit (LEL) (volume %) 3.3 Upper explosivity limit (UEL) (volume %) 11.9
### Behaviour at sea
### Additional data
Colour colourless to yellow-brown Odour sharp, irritating odour
### Transportation data
Transport mode Bulk,Packaged Cargo group 15 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name substituted allyls IMO class 3.1
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 300 ERPG-2 (ppm) 40 ERPG-3 (ppm) 300
### Ecotoxicity
# alpha-PINENE
UN Number: 2368 Also known as: ACINTENE A
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2368
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 860 [Kg/m³] at a temperature of 20°C Density of gas (kg/m3) 6.089 Vapour Pressure (Pa) 665 [Pa] at a temperature of 20°C Flash Point (°C) 33
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour colourless Odour turpentine odour Standard behavior classification D, FE, FED
### Transportation data
Package group III State liquid IMO class 3.3
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Specific Health Concern (D3) Ss - Skin Sensitization Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 0.0005 TEEL-2 (mg/m3) 0.0035 TEEL-3 (mg/m3) 0.015
### Ecotoxicity
# ALUMINIUM PHOSPHIDE
UN Number: 1397 Also known as: AIP, ALUMINIUM MONOPHOSPHIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1397
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2850 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 57.96 Melting Point (°C) > 1000
### Behaviour at sea
### Additional data
Colour dark gray or dark yellow Odour fishy
### Transportation data
State solid IMO class 4.3
### Reactivity data
Water Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 0.907 ppm TEEL-2 (mg/m3) 2 ppm TEEL-3 (mg/m3) 3.6 ppm
### Ecotoxicity
# ALUMINIUM SULFATE solution
Also known as: ALUMINIUM TRISULPHATE Solution, DIALUMINIUM SULPHATE Solution
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1270 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 342.1 Boiling Point (°C) 101 Melting Point (°C) -15.6
### Behaviour at sea
### Additional data
Colour white Odour odourless
### Transportation data
Cargo group 43 State liquid Temperature (°C) ambient Family name miscell. water solut.
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes (carbon steel) Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# AMINOETHYLETHANOLAMINE
CAS Number: 111-41-1 Also known as: N-AMONOETHYLETHANOLAMINE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 111-41-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1028 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 104.15 Density of gas (kg/m3) 4.644 Boiling Point (°C) 243 Ignition Temperature (°C) 368 Flash Point (°C) 135 Lower explosivity limit (LEL) (volume %) 15 Upper explosivity limit (UEL) (volume %) 27
### Behaviour at sea
### Additional data
Colour colourless Odour mild ammonia odour
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alkanolamines
### Reactivity data
Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 3B - Corrosive Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 35 TEEL-2 (mg/m3) 250 TEEL-3 (mg/m3) 500
### Ecotoxicity
# AMMONIA anhydrous
UN Number: 1005 - CAS Number: 7664-41-7 Also known as: AMMONIAC anhydre, Ammonia Gas, Ammonia Anhydrous, Ammoniac
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1005 CAS number 7664-41-7 Formula NH 3
### Physical chemical data
Physical State (20°C) Gas Physical State (25°C) Gas Density (kg/m3) 0.75 [Kg/m³] at a temperature of 20°C 681.8 [Kg/m³] at a temperature of -33.33°C Kinematic viscosity (cSt) 0.255 [cSt] at a temperature of -33.5°C Molar mass (g/mol) 17.03 Density of gas (kg/m3) 0.75 Solubility (g/L) 531000 [g/L] at a temperature of 20°C and salinity of 0‰ 440000 [g/L] at a temperature of 28°C and salinity of 0‰ Boiling Point (°C) -33.2 Melting Point (°C) -78 Critical molar volume (m³/mol) 6.98e-05 Critical temperature (°C) 405.56 Critical pressure (Pa) 1135700 Vapour Pressure (Pa) 861050 [Pa] at a temperature of 20°C 1013250 [Pa] at a temperature of 25°C Ignition Temperature (°C) 630 Flash Point (Pensky-Martens closed cup) (°C) 132 Lower explosivity limit (LEL) (volume %) 16 Upper explosivity limit (UEL) (volume %) 25 Vapor enthalpy (J/Kg) 1228334 [J/Kg] at a temperature of -33.33°C Combus enthalpy (J/Kg) 22476660 Henry's constant (mol/(m³·Pa)) 1.63
### Behaviour at sea
Log kow 0.23 Log koc 1.155 Biodegradation in estuary environment (Half-life) (days) Not hydrolysable
### Additional data
Colour colourless Odour ammonia odour MARPOL pollution category Category Description Other Substances Substances which have been evaluated and found to fall outside Category X, Y or Z because they are considered to present no harm to marine resources, human health, amenities or other legitimate uses of the sea when discharged into the sea from tank cleaning of deballasting operations. The discharge of bilge or ballast water or other residues or mixtures containing these substances are not subject to any requirements of MARPOL Annex II. Standard behavior classification GD
### Transportation data
Transport mode Gas,Packaged Ship type 2G,2PG State liq.compr.gas Temperature (°C) ambient Pressure (Pa) under pressure Family name ammonia IMO class 2(2.3)
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Static electricity Yes Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 2 - Moderate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 500 Hazard statements Physical H221 Flammable gas. H280 Contains gas under pressure, may explode if heated. Health H314 Causes severe skin burns and eye damage. H331 Toxic if inhaled. Environmental H410 Very toxic to aquatic life with long lasting effects. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P260 Do not breathe dust/fume/gas/mist/vapours/spray. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P377 Leaking gas fire: Do not extinguish, unless leak can be stopped safely. Storage P403 + P233 Store in a well-ventilated place. Keep container tightly closed. TLV-TWA 25 ERPG-1 (ppm) 25 ERPG-2 (ppm) 150 ERPG-3 (ppm) 750 10 min 30 min 60 min 4 hrs 8 hrs AEGL-1 (ppm) 30 30 30 30 30 AEGL-2 (ppm) 220 220 160 110 110 AEGL-3 (ppm) 2700 1600 1100 550 390
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 17 Lowest median lethal concentration (LC50) on crustacean (mg/l) 0.13 Lowest median lethal concentration (LC50) on fishes (mg/l) 0.5 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.79 Assessment factor (AF) 20 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 1 [µg/l] on the Short term
# AMMONIA aqueous solution (28% or less)
UN Number: 2672 - CAS Number: 7664-41-7 Also known as: AMMONIA LIQUOR, AMMONIAQUE solution aqueuse (< 28%), AMMONIA WATER, AMMONIUM HYDROXIDE, AQUA AMMONIA, Ammonia Aqueous, Ammonia Solution, Ammonia Monohydrate, Ammonium Monohydrate, Aqueous Ammonia, Ammonium Hydroxide ((Nh4)(Oh)), Ammonia, Aqueous Solution, Ammoniac Water, Ammonium Hydroxide (25%), Ammoniaque (25%)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2672 CAS number 7664-41-7 Formula NH 5 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 900 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 35.05 Density of gas (kg/m3) 0.77 Solubility (g/L) 305000 [g/L] at a temperature of 20°C and salinity of 0‰ 280000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 36 Melting Point (°C) -97 Surface tension (mN/m) 23.4 [mN/m] at a temperature of 20°C 18.1 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 30000 [Pa] at a temperature of 20°C 47400 [Pa] at a temperature of 21.1°C Ignition Temperature (°C) > 600 Lower explosivity limit (LEL) (volume %) 16 Upper explosivity limit (UEL) (volume %) 25
### Behaviour at sea
Log kow -0.17 Log koc 1.16 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 10
### Additional data
Colour colourless Odour odourless MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification DE
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Family name ammonia
### Reactivity data
Water No Abilities Solution. Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Combustibles Yes Organic substance Yes Notable risks Reacts with oxides and peroxides.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 2 - Moderate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 300 Hazard statements Health H314 Causes severe skin burns and eye damage. H335 May cause respiratory irritation. Environmental H400 Very toxic to aquatic life. Precautionary statements Prevention P260 Do not breathe dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P330 + P331 IF SWALLOWED: rinse mouth. Do NOT induce vomiting. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P391 Collect spillage. Disposal P501 Dispose of contents/container to ... TLV-TWA 25 TEEL-1 (mg/m3) 6 ppm TEEL-2 (mg/m3) 40 ppm TEEL-3 (mg/m3) 100 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 1300 Lowest median lethal concentration (LC50) on crustacean (mg/l) 9 Lowest median lethal concentration (LC50) on fishes (mg/l) 2.4 Highest no observed effect concentration (NOEC) on algae (mg/l) 0.234 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 2 Highest no observed effect concentration (NOEC) on fishes (mg/l) 0.06 Assessment factor (AF) 1000 on the Short term 100 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 2.4 [µg/l] on the Short term 0.6 [µg/l] on the Long term
# AMMONIUM DIHYDROGENPHOSPHATE
Also known as: AMMONIUM DIHYDROGEN ORTHOPHOSPHATE, AMMONIUM PHOSPHATE, DIHYDROGENOPHOSPHATE D'AMMONIUM
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1803 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 115.02 Melting Point (°C) 190/205
### Behaviour at sea
### Additional data
### Transportation data
State solid
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# AMMONIUM NITRATE (>0.2% combustible substances)
UN Number: 1942
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1942
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1700 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 80.05 Melting Point (°C) 170
### Behaviour at sea
### Additional data
Colour white to grey or brown Odour odourless
### Transportation data
Transport mode Bulk,Packaged Package group III State solid Family name organic acids IMO class 5.1
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 10 TEEL-2 (mg/m3) 10 TEEL-3 (mg/m3) 500
### Ecotoxicity
# AMMONIUM NITRATE solution (93% or less)
UN Number: 2426 - CAS Number: 6484-52-2 Also known as: Nitric Acid Ammonium Salt, Ammonium Nitrate, Ammonium Nitrate Solution (93% Or Less), Solutions De Nitrate D'Ammonium (93% Ou Moins)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2426 CAS number 6484-52-2 Formula NH 4 NO 3 (H 2 O)
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1720 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 80.1 Solubility (g/L) 10000000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 390, decomp. Melting Point (°C) 170 Vapour Pressure (Pa) 2000 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless Odour odourless MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged IMO class 5.1
### Reactivity data
Water No Abilities Solution. Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Reducing agents Yes Combustibles Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
Hazard statements Physical H272 May intensify fire, oxidiser. Health H319 Causes serious eye irritation. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P220 Keep/Store away from clothing/.../combustible materials. P264 Wash ... thoroughly after handling. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P370 + P378 In case of fire: Use ... for extinction. TEEL-1 (mg/m3) 10 TEEL-2 (mg/m3) 10 TEEL-3 (mg/m3) 500
### Ecotoxicity
# AMMONIUM POLYPHOSPHATE solution
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1400 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 106 Vapour Pressure (Pa) 2000 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour green Odour odourless
### Transportation data
Cargo group 43 State liquid Family name miscell. water solut.
### Reactivity data
Acid(s) Yes Metal(s) and alloys Yes (Cu, Zn) Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
### Ecotoxicity
# AMMONIUM SULPHATE solution
CAS Number: 7783-20-2 Also known as: DIAMMONIUM SULPHATE, DOLAMIN (TR)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 7783-20-2
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1200 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 132.14 Boiling Point (°C) 105
### Behaviour at sea
### Additional data
Colour white Odour odourless
### Transportation data
State solid
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 0 - Is not a floater; and does not pose any known health hazards
### Human toxicity threshold
### Ecotoxicity
# AMMONIUM SULPHIDE solution (45% or less)
UN Number: 2683 - CAS Number: 12124-99-1 Also known as: AMMONIUM HYDROGEN SULPHIDE SOLUTION, AMMONIUM MONOSULFIDE, AMMONIUM SULFHYDRATE, DIAMMONIUM SULPHIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2683 CAS number 12124-99-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 990/1010 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 68.14 Boiling Point (°C) 38/100 Melting Point (°C) -18 Vapour Pressure (Pa) 2000 [Pa] at a temperature of 20°C Flash Point (°C) 22 Upper explosivity limit (UEL) (volume %) 46
### Behaviour at sea
### Additional data
Colour greenich to yellow Odour ammonia-like
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient
### Reactivity data
Water No Acid(s) Yes Metal(s) and alloys Yes (Cu, Zn)
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 10 ppm TEEL-2 (mg/m3) 15 ppm TEEL-3 (mg/m3) 15 ppm
### Ecotoxicity
# AMMONIUM THIOSULPHATE solution (60% or less)
CAS Number: 7783-18-8 Also known as: AMMONIUM HYPO SOLUTIONS, AMMONIUM HYPOSULPHITE, DIAMMONIUM THIOSULPHATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 7783-18-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1340 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 148.2 Density of gas (kg/m3) < 1.29 Boiling Point (°C) 99/104 Melting Point (°C) -0.7 Vapour Pressure (Pa) 2000 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless to pale green-yello Odour ammonia-like
### Transportation data
Cargo group 43 State liquid Temperature (°C) ambient Family name miscell. water solut.
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
### Ecotoxicity
# AMYL ACETATES all isomers
UN Number: 1104 - CAS Number: 628-63-7 Also known as: ACETATES D'AMYLE mélange d'isomères, ACETIC ACID, n-AMYL ESTER, n-AMYLACETATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1104 CAS number 628-63-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 876 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 130.19 Density of gas (kg/m3) 5.805 Boiling Point (°C) 142/149 Melting Point (°C) 0.91025641 Vapour Pressure (Pa) 600 [Pa] at a temperature of 20°C Ignition Temperature (°C) 375/380 Flash Point (°C) -0.276923077 Upper explosivity limit (UEL) (volume %) 10
### Behaviour at sea
### Additional data
Colour colourless to yellow Odour banana-like Standard behavior classification FED
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 34 State liquid Temperature (°C) ambient (cool) Family name esters IMO class 3.3
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 1000 TLV-TWA 100 TEEL-1 (mg/m3) 100 ppm TEEL-2 (mg/m3) 100 ppm TEEL-3 (mg/m3) 1000 ppm
### Ecotoxicity
# AMYL ALCOHOL primary
UN Number: 1105 Also known as: ALCOOL AMYLIQUE primaire, n-AMYL ALCOHOL, 1-AMYL ALCOHOL, AMYLOL, n-BUTYL CARBINOL, 1-BUTYLCARBINOL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1105
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 810 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 88.15 Density of gas (kg/m3) 3.93 Boiling Point (°C) 112/138 Melting Point (°C) -79 Vapour Pressure (Pa) 407 [Pa] at a temperature of 20°C Ignition Temperature (°C) 300/400 Flash Point (°C) -0.276923077 Lower explosivity limit (LEL) (volume %) 1.1 Upper explosivity limit (UEL) (volume %) 10.5
### Behaviour at sea
### Additional data
Colour colourless Odour sweet, mild
### Transportation data
Package group II Cargo group 20 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alcohols, glycols IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents Yes Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 100 ppm TEEL-2 (mg/m3) 100 ppm TEEL-3 (mg/m3) 100 ppm
### Ecotoxicity
# ANILINE
UN Number: 1547 - CAS Number: 62-53-3 Also known as: AMINOBENZENE, AMIOPHEN, ANILINE OIL, ANYIRIM (TR), BENZENEAMINE, BENZENE, AMINO-, BENZIDAM, BLUE OIL (TR), CYANOL (TR), Aminophen, Benzenamine, Phenylamine, Aniline
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1547 CAS number 62-53-3 Formula C 6 H 7 N
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1022 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 4.26 [cSt] at a temperature of 20°C 3.76 [cSt] at a temperature of 25°C Molar mass (g/mol) 93.13 Density of gas (kg/m3) 4.128 Solubility (g/L) 35000 [g/L] at a temperature of 20°C and salinity of 0‰ 33000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 184.4 Melting Point (°C) -6 Critical molar volume (m³/mol) 0.000291 Critical temperature (°C) 705 Critical pressure (Pa) 5630000 Surface tension (mN/m) 42.9 [mN/m] at a temperature of 20°C 42.12 [mN/m] at a temperature of 25°C Interfacial tension (mN/m) 5.8 [mN/m] at a temperature of 20°C and salinity of 0‰ Vapour Pressure (Pa) 40 [Pa] at a temperature of 20°C 90 [Pa] at a temperature of 25°C Ignition Temperature (°C) 530 Flash Point (°C) 76 Flash Point (Pensky- Martens closed cup) (°C) 70 Flash Point (Cleveland open cup) (°C) 75.6 Lower explosivity limit (LEL) (volume %) 1.3 Upper explosivity limit (UEL) (volume %) 11 Vapor enthalpy (J/Kg) 455707 [J/Kg] at a temperature of 184.4°C 599585 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 34800000 Specific heat capacity (J/(Kg·K)) 2060.6 Combustion efficiency (%) 75 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.05 Rad fraction (%) 53 Henry's constant (mol/(m³·Pa)) 2.04
### Behaviour at sea
Persistence (days) 1.6 Log kow 0.9 Log koc 1.84 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 10 Bioconcentration factor (BCF) 2.6
### Additional data
Colour colourless to yellow-brown Odour weak odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification FD
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name aromatic amines IMO class 6.1
### Reactivity data
Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 2 - Moderate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 100 Hazard statements Health H301 Toxic if swallowed. H311 Toxic in contact with skin. H317 May cause an allergic skin reaction. H318 Causes serious eye damage. H331 Toxic if inhaled. H341 Suspected of causing genetic defects. H351 Suspected of causing cancer. H372 Causes damage to organs through prolonged or repeated exposure, exposure cause the hazard: Environmental H400 Very toxic to aquatic life. H410 Very toxic to aquatic life with long lasting effects. Precautionary statements Prevention P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P302 + P352 IF ON SKIN: Wash with plenty of soap and water. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. 10 min 30 min 60 min 4 hrs 8 hrs AEGL-1 (ppm) 48 16 AEGL-2 (ppm) 72 24 12 1.5 AEGL-3 (ppm) 120 40 20 2.5
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 19 Lowest median lethal concentration (LC50) on crustacean (mg/l) 0.1 Lowest median lethal concentration (LC50) on fishes (mg/l) 10.6 Highest no observed effect concentration (NOEC) on algae (mg/l) 2 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.015 Highest no observed effect concentration (NOEC) on fishes (mg/l) 0.39 Assessment factor (AF) 100 on the Short term 100 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 1 [µg/l] on the Short term 0.15 [µg/l] on the Long term
# ANTIMONY PENTACHLORIDE liquid
UN Number: 1730 Also known as: ANTIMONY CHLORIDE, ANTIMONY PERCHLORIDE, BUTTER OF ANTIMONY
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1730
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 2354 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 299.05 Boiling Point (°C) 175 Melting Point (°C) -3 Vapour Pressure (Pa) 130 [Pa] at a temperature of 20°C
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour colourless to brown Odour unpleasant odour Standard behavior classification D, SD
### Transportation data
Package group II State liquid Temperature (°C) ambient Pressure (Pa) under pressure
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 16 (as Sb) TLV-TWA 0.1 (Sb) TEEL-1 (mg/m3) 3.68 TEEL-2 (mg/m3) 6.14 TEEL-3 (mg/m3) 123
### Ecotoxicity
# ANTIMONY PENTAFLUORIDE
UN Number: 1732 Also known as: ANTIMONY (V) FLUORIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1732
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 2340 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 216.7 Boiling Point (°C) 143 Melting Point (°C) 8.3 Vapour Pressure (Pa) 130 [Pa] at a temperature of 20°C
### Behaviour at sea
Persistence (days) 2.7
### Additional data
Colour colourless Odour sharp odour Standard behavior classification D, SD
### Transportation data
Package group II State liquid Temperature (°C) ambient Pressure (Pa) under pressure
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles Yes Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 16 (as Sb) TLV-TWA 0.1 (Sb) TEEL-1 (mg/m3) 0.89 TEEL-2 (mg/m3) 2.7 TEEL-3 (mg/m3) 89
### Ecotoxicity
# ANTIMONY POTASSIUM TARTRATE
UN Number: 1551
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1551
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2600 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 334
### Behaviour at sea
### Additional data
Colour white Odour odourless
### Transportation data
Package group III State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 16 (as Sb) TLV-TWA 0.1 (Sb) TEEL-1 (mg/m3) 3.92 TEEL-2 (mg/m3) 6.53 TEEL-3 (mg/m3) 131
### Ecotoxicity
# ANTIMONY TRICHLORIDE solid
UN Number: 1733 Also known as: ANTIMONOUS CHLORIDE, ANTIMONY BUTTER, ANTIMONY CHLORIDE, BUTTER OF ANTIMONY, CAUSTIC ANTIMONY
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1733
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 3100 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 228 Boiling Point (°C) 223 Melting Point (°C) 73 Vapour Pressure (Pa) 130 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour white to pale yellow Odour sharp, unpleasant odour Standard behavior classification D, SD
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) under pressure
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 16 (as Sb) TLV-TWA 0.1 (Sb) TEEL-1 (mg/m3) 0.937 TEEL-2 (mg/m3) 0.937 TEEL-3 (mg/m3) 93.7
### Ecotoxicity
# ARSENIC ACID solid
UN Number: 1554 Also known as: ACIDE ARSENIQUE solide
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1554
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2200 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 229.8 Boiling Point (°C) 120
### Behaviour at sea
### Additional data
Colour white or colourless Odour odourless Standard behavior classification SD
### Transportation data
State solid Temperature (°C) ambient Pressure (Pa) under pressure IMO class 6.1
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 32 (as As) TLV-TWA 0.003 (As) TEEL-1 (mg/m3) 0.4 TEEL-3 (mg/m3) 9.5
### Ecotoxicity
# ARSENIC TRICHLORIDE
UN Number: 1560 Also known as: ARESENIOUS CHLORIDE, ARSENIC BUTTER, ARSENIC CHLORIDE, ARSENIC CHLORIDE (fuming), ARSENOUS CHLORIDE, BUTTER OF ARSENIC
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1560
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 2156 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 181.3 Boiling Point (°C) 130.4 Melting Point (°C) -16 Vapour Pressure (Pa) 1300 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless Odour unpleasant odour Standard behavior classification D, SD
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) under pressure IMO class 6.1
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 32 (as As) TLV-TWA 0.003 (As) TEEL-1 (mg/m3) 0.0726 ppm TEEL-2 (mg/m3) 1.35 ppm TEEL-3 (mg/m3) 12.1 ppm
### Ecotoxicity
# ARSENIC TRIOXIDE
UN Number: 1561 Also known as: ARSENOUS SESQUIOXIDE, ARSENOUS ACID, ARSENOUS ACID ANHYDRIDE, ARSENOUS OXIDE, ARSODENT, CLAUDERITE, DIARSENIC TRIOXIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1561
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 3700 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 197.8 Boiling Point (°C) 457 Melting Point (°C) 315
### Behaviour at sea
### Additional data
Colour white Odour odourless
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) under pressure IMO class 6.1
### Reactivity data
Water No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 0.56 TLV-TWA 0.0012(As) TEEL-1 (mg/m3) 0.4 TEEL-3 (mg/m3) 9.1
### Ecotoxicity
# AVIATION ALKYLATES (C8 paraffins & isoparaffins, BPt 95-120 �C)
Also known as: ALKYLATES D'AVIATION paraffines & isoparaffines en C8, Teb 95 °C
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 700 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 114 Boiling Point (°C) 95/120 Melting Point (°C) 1.833333333 Flash Point (°C) -0.923076923
### Behaviour at sea
### Additional data
Standard behavior classification F/FE/E
### Transportation data
Cargo group 33 Family name miscell. hydroc. mixt
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# AZINPHOS-METHYL
UN Number: 2783 Also known as: AZINPHOS-METHYLE, CARFENE, CORTENE (TR), COTNEON, COTNION METHYL (TR), CRYSTHION 2L (TR), DBD
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2783
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1400 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 317 Melting Point (°C) 74 Vapour Pressure (Pa) <0.001 [Pa] at a temperature of 20°C
### Behaviour at sea
Persistence (days) 2.7
### Additional data
Colour brown Marine pollutant P Standard behavior classification D, SD, S
### Transportation data
Transport mode Bulk,Packaged Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 1.5 TLV-TWA 0.015 TEEL-1 (mg/m3) 0.6 TEEL-2 (mg/m3) 0.7 TEEL-3 (mg/m3) 10
### Ecotoxicity
# BENZALDEHYDE
UN Number: 1990 Also known as: ARTIFICIAL ESSENTIAL OIL OF ALMOND, BENZENE CARBALDEHYDE, BENZENE CARBONAL, BENZOIC ALDEHYDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1990
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1046 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 106.12 Density of gas (kg/m3) 4.773 Boiling Point (°C) 179 Melting Point (°C) -26 Vapour Pressure (Pa) 130 [Pa] at a temperature of 20°C Ignition Temperature (°C) 190 Flash Point (°C) 64 Lower explosivity limit (LEL) (volume %) 1.4
### Behaviour at sea
Persistence (days) 0.8
### Additional data
Colour colourless to pale yellow Odour bitter, almond odour Standard behavior classification SD
### Transportation data
State liquid Temperature (°C) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 4 ppm TEEL-2 (mg/m3) 4 ppm TEEL-3 (mg/m3) 150 ppm
### Ecotoxicity
# BENZENE
UN Number: 1114 - CAS Number: 71-43-2 Also known as: 6-ANNULENE, BENZINE (T), BENZOL, BENZOL (T), BENZOLE (T), BENZOLENE, BICARBURET OF HYDROGEN, CARBON OIL, COAL NAPHTA (T), CYCLOHEXATRIENE (trace 1), CYCLOHEXATRIENE (trace 2), Coal Naphtha, Cyclohexatriene, Phenyl Hydride, (6)Annulene, Benzole, Pyrobenzol, Pyrobenzole, Benzene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1114 CAS number 71-43-2 Formula C 6 H 6
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 879 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.74 [cSt] at a temperature of 20°C 0.69 [cSt] at a temperature of 25°C Molar mass (g/mol) 78.11 Density of gas (kg/m3) 3.483 Solubility (g/L) 1780 [g/L] at a temperature of 20°C and salinity of 0‰ 1800 [g/L] at a temperature of 25°C and salinity of 0‰ 1360 [g/L] at a temperature of 25°C and salinity of 35‰ Boiling Point (°C) 80.3 Melting Point (°C) 5.5 Critical molar volume (m³/mol) 0.000265 Critical temperature (°C) 562.05 Critical pressure (Pa) 4895000 Surface tension (mN/m) 28.9 [mN/m] at a temperature of 20°C 28.22 [mN/m] at a temperature of 25°C Interfacial tension (mN/m) 35 [mN/m] at a temperature of 20°C and salinity of 0‰ Vapour Pressure (Pa) 10130 [Pa] at a temperature of 20°C 12700 [Pa] at a temperature of 25°C Ignition Temperature (°C) 550 Flash Point (°C) -11 Flash Point (Pensky-Martens closed cup) (°C) -11 Lower explosivity limit (LEL) (volume %) 1.4 Upper explosivity limit (UEL) (volume %) 8 Vapor enthalpy (J/Kg) 393292 [J/Kg] at a temperature of 80.1°C 433107 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 40100000 Specific heat capacity (J/(Kg·K)) 1745 Combustion efficiency (%) 70 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.09 Rad fraction (%) 60 Henry's constant (mol/(m³·Pa)) 545
### Behaviour at sea
Log kow 2.13 Log koc 1.85 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 50 Bioconcentration factor (BCF) 11
### Additional data
Colour colourless Odour gasoline odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 32 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name aromatic hydrocarbons IMO class 3.2
### Reactivity data
Acid(s) Yes Static electricity No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 3000 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H304 May be fatal if swallowed and enters airways. H315 Causes skin irritation. H319 Causes serious eye irritation. H340 May cause genetic defects. Exposure cause the hazard: H350 May cause cancer. H372 Causes damage to organs through prolonged or repeated exposure, exposure cause the hazard: Precautionary statements Prevention P202 Do not handle until all safety precautions have been read and understood. P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P243 Take precautionary measures against static discharge. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P331 Do NOT induce vomiting. ERPG-1 (ppm) 50 ERPG-2 (ppm) 150 ERPG-3 (ppm) 1000
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 29 Lowest median lethal concentration (LC50) on crustacean (mg/l) 10 Lowest median lethal concentration (LC50) on fishes (mg/l) 4.9 Highest no observed effect concentration (NOEC) on algae (mg/l) 9.6 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 3 Highest no observed effect concentration (NOEC) on fishes (mg/l) 0.8 Assessment factor (AF) 100 on the Short term 100 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 49 [µg/l] on the Short term 8 [µg/l] on the Long term
# BENZENE SULPHONYL CHLORIDE
UN Number: 2225 - CAS Number: 98-09-9 Also known as: BENZENESULFONIC CHLORIDE, BENZENESULPHOCHLORIDE, BENZENESULPHONECHLORIDE, CHLORURE DE BENZENESULFONYLE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2225 CAS number 98-09-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1400 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 176.62 Density of gas (kg/m3) 7.85 (E) Boiling Point (°C) 251, decomp. Melting Point (°C) 15 Vapour Pressure (Pa) 130 (66�C) [Pa] at a temperature of 20°C Flash Point (°C) 128
### Behaviour at sea
### Additional data
Colour colourless to brown Odour irritating, pungent Standard behavior classification S/SD
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Combustibles Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Specific Health Concern (D3) Ss - Skin Sensitization Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 1.5 TEEL-2 (mg/m3) 200 TEEL-3 (mg/m3) 200
### Ecotoxicity
# BENZYL ACETATE
CAS Number: 140-11-4 Also known as: ACETATE DE BENZYLE, ACETIC ACID, BENZYL ESTER, ACETIC ACID, PHENYLMETHYL ESTER, alpha-ACETOXYTOLUENE, BENZYL ETHANOATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 140-11-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1100 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 150.2 Density of gas (kg/m3) 6.71 Boiling Point (°C) 212 Melting Point (°C) -52 Vapour Pressure (Pa) 130 [Pa] at a temperature of 20°C Ignition Temperature (°C) 460 Flash Point (°C) 102 Lower explosivity limit (LEL) (volume %) 0.9 Upper explosivity limit (UEL) (volume %) 8.4
### Behaviour at sea
### Additional data
Colour colourless Odour characteristic, pear-like
### Transportation data
Cargo group 34 State liquid Family name esters
### Reactivity data
Water No Acid(s) Yes Base(s) No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TLV-TWA 10
### Ecotoxicity
# BENZYL ALCOHOL
UN Number: 1993 - CAS Number: 100-51-6 Also known as: ALCOOL BENZYLIQUE, Tert-Butyl Ethyl Ether, 1,1-Dimethylethyl Ethyl Ether, 2-Ethoxy-2-Methylpropane, Ethyl 1,1-Dimethylethyl Ether, Ethyl Tert-Butyl Oxide, Methyl-2-Ethoxypropane, 2-Methyl-2-Ethoxypropane, Ethyl T-Butyl Ether, Ethyl Tert-Butyl Ether
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1993 CAS number 100-51-6 Formula C 6 H 1 4 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1050 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 108.13 Density of gas (kg/m3) 4.773 Solubility (g/L) 12400 [g/L] at a temperature of 20°C and salinity of 0‰ 13000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 205 Melting Point (°C) -15 Critical molar volume (m³/mol) 0.000395 Critical temperature (°C) 509.4 Critical pressure (Pa) 2934000 Vapour Pressure (Pa) 13 [Pa] at a temperature of 20°C 20664.97 [Pa] at a temperature of 25°C Ignition Temperature (°C) 435 Flash Point (°C) 101 Lower explosivity limit (LEL) (volume %) 1.3 Upper explosivity limit (UEL) (volume %) 1.3 Combus enthalpy (J/Kg) 36300000 Combustion efficiency (%) 96 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.08 Rad fraction (%) 23 Henry's constant (mol/(m³·Pa)) 165.6
### Behaviour at sea
Persistence (days) 1.6 Log kow 1.68 Log koc 2.29 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) Not biodegradable Bioconcentration factor (BCF) 11.1
### Additional data
Colour coulourless Odour mild pleasant odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification SD
### Transportation data
Transport mode Bulk,Packaged State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
Hazard statements Physical H225 Highly flammable liquid and vapour. Health H336 May cause drowsiness or dizziness. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P243 Take precautionary measures against static discharge. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P271 Use only outdoors or in a well-ventilated area. Storage P403 + P233 Store in a well-ventilated place. Keep container tightly closed. TEEL-1 (mg/m3) 60 TEEL-2 (mg/m3) 150 TEEL-3 (mg/m3) 150
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 1100 Lowest median lethal concentration (LC50) on crustacean (mg/l) 37 Lowest median lethal concentration (LC50) on fishes (mg/l) 41.5 Highest no observed effect concentration (NOEC) on algae (mg/l) 7.5 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 51 Highest no observed effect concentration (NOEC) on fishes (mg/l) 63.9 Assessment factor (AF) 1000 on the Short term 10000 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 37 [µg/l] on the Short term 3.7 [µg/l] on the Long term
# BENZYL ALCOHOL
UN Number: 1738 - CAS Number: 100-44-7 Also known as: CHLORMETHYLBENZENE, CHLOROPHENYLMETHANE, alpha- CHLOROTOLUENE, CHLORURE DE BENZYLE, Chloromethyl Benzene, Alpha- Chlorotoluene, Benzyl Chloride, α-Chlorotoluene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1738 CAS number 100-44-7 Formula C 7 H 7 Cl
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1100 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 126.6 Density of gas (kg/m3) 5.16 Solubility (g/L) 1200 [g/L] at a temperature of 20°C and salinity of 0‰ 525 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 179.6 Melting Point (°C) -39 Critical temperature (°C) 411 Surface tension (mN/m) 37.46 [mN/m] at a temperature of 20°C 36.76 [mN/m] at a temperature of 26.3°C Vapour Pressure (Pa) 120 [Pa] at a temperature of 20°C 133.3 [Pa] at a temperature of 22°C 164 [Pa] at a temperature of 25°C Ignition Temperature (°C) 585 Flash Point (°C) 60 Flash Point (Pensky-Martens closed cup) (°C) 67 Flash Point (Cleveland open cup) (°C) 74 Lower explosivity limit (LEL) (volume %) 1.1 Upper explosivity limit (UEL) (volume %) 7.1 Vapor enthalpy (J/Kg) 395785 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 29292802 Specific heat capacity (J/(Kg·K)) 1440 Henry's constant (mol/(m³·Pa)) 41.54
### Behaviour at sea
Persistence (days) 3.1 Log kow 0.36 Log koc 2.65
### Additional data
Colour colourless to yellow Odour sharp, irritating odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Pressure (Pa) under pressure IMO class 6.1
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 10 Hazard statements Health H302 Harmful if swallowed. H315 Causes skin irritation. H317 May cause an allergic skin reaction. H318 Causes serious eye damage. H331 Toxic if inhaled. H335 May cause respiratory irritation. H350 May cause cancer. H373 May cause damage to organs through prolonged or repeated exposure, exposure cause the hazard: ERPG-2 (ppm) 10 ERPG-3 (ppm) 50
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 19.3 Lowest median lethal concentration (LC50) on crustacean (mg/l) 3.9 Lowest median lethal concentration (LC50) on fishes (mg/l) 6 Highest no observed effect concentration (NOEC) on algae (mg/l) 10 Assessment factor (AF) 100 on the Short term 100 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 3.9 [µg/l] on the Short term 1 [µg/l] on the Long term
# BENZYL CHLOROFORMATE
UN Number: 1739 Also known as: BENZYL CHLOROCARBONATE, CHLOROFORMATE DE BENZYLE, CHLOROFORMIC ACID, BENZYL ESTER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1739
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1220 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 170.6 Boiling Point (°C) 152
### Behaviour at sea
Persistence (days) 2.7
### Additional data
Colour colourless Odour sharp, irritating odour Standard behavior classification DE, D, SD
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) under pressure
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 0.125 ppm TEEL-2 (mg/m3) 0.97 ppm TEEL-3 (mg/m3) 2.9 ppm
### Ecotoxicity
# BENZYL normal-BUTYL PHTHALATE
UN Number: 3082 - CAS Number: 85-68-7 Also known as: BBP, BENZYL N-BUTYL PHTHALATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082 CAS number 85-68-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1120 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 313 Boiling Point (°C) 370 Vapour Pressure (Pa) 21 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless Odour weak odour
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 2 - Moderate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# beta-PROPIOLACTONE
CAS Number: 57-57-8 Also known as: BETAPRONE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 57-57-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1148 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 72.1 Density of gas (kg/m3) 3.225 Boiling Point (°C) 155 Melting Point (°C) -33 Vapour Pressure (Pa) 500 [Pa] at a temperature of 20°C Flash Point (°C) 74 Lower explosivity limit (LEL) (volume %) 2.9
### Behaviour at sea
### Additional data
Colour colourless Odour irritating odour
### Transportation data
State liquid Temperature (°C) <16� Pressure (Pa) under pressure
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 4 - High Skin irritation/corrosivity (D1) 3B - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TLV-TWA 0.5 TEEL-1 (mg/m3) 0.509 ppm TEEL-2 (mg/m3) 5.09 ppm TEEL-3 (mg/m3) 15 ppm
### Ecotoxicity
# BISPHENOL A
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1200 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 228.28 Density of gas (kg/m3) 1.548 Boiling Point (°C) 250 Melting Point (°C) 153 Vapour Pressure (Pa) 520 [Pa] at a temperature of 20°C Ignition Temperature (°C) 600 Flash Point (°C) 207
### Behaviour at sea
### Additional data
Colour white to light brown Odour weak medicine odour Standard behavior classification D, SD, S
### Transportation data
State solid
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 15 TEEL-2 (mg/m3) 100 TEEL-3 (mg/m3) 500
### Ecotoxicity
# BLACK POWDER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Solid
### Behaviour at sea
### Additional data
### Transportation data
State solid IMO class 1.1 D
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# BROMOCHLOROMETHANE
UN Number: 1887 - CAS Number: 74-97-5
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1887 CAS number 74-97-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1930 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 129.39 Density of gas (kg/m3) 5.93 Boiling Point (°C) 68 Melting Point (°C) -88 Vapour Pressure (Pa) 15330 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless to pale yellow Odour odourless Standard behavior classification SD
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid IMO class 6.1
### Reactivity data
Metal(s) and alloys Yes (Al, Mg, Zn)
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
TEEL-1 (mg/m3) 600 ppm TEEL-2 (mg/m3) 1000 ppm TEEL-3 (mg/m3) 2000 ppm
### Ecotoxicity
# BUTADIENES inhibited
UN Number: 1010
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1010
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 2.451 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 54.09 Density of gas (kg/m3) 2.451 Boiling Point (°C) -4.2 Melting Point (°C) -109 Vapour Pressure (Pa) 506500 [Pa] at a temperature of 20°C Ignition Temperature (°C) 415 Flash Point (°C) -85 Upper explosivity limit (UEL) (volume %) 11.5
### Behaviour at sea
### Additional data
Colour colourless Odour gasoline odour
### Transportation data
Transport mode Gas,Packaged Ship type 2G,2PG Cargo group 30 State gas Temperature (°C) ambient Pressure (Pa) under pressure Family name olefins IMO class 2(2.1)
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Static electricity Yes Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 20000 TLV-TWA 1000 ERPG-1 (ppm) 10 ERPG-2 (ppm) 200 ERPG-3 (ppm) 5000
### Ecotoxicity
# BUTANE
UN Number: 1011 - CAS Number: 106-97-8 Also known as: Methylethylmethane, Butane
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1011 CAS number 106-97-8 Formula C 4 H 1 0
### Physical chemical data
Physical State (20°C) Gas Physical State (25°C) Gas Density (kg/m3) 2.709 [Kg/m³] at a temperature of 20°C 573 [Kg/m³] at a temperature of 25°C Molar mass (g/mol) 58.12 Density of gas (kg/m3) 2.709 Solubility (g/L) 61 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) -1 Melting Point (°C) -135 Critical temperature (°C) 425.13 Critical pressure (Pa) 3796000 Surface tension (mN/m) 14.7 [mN/m] at a temperature of 0°C Interfacial tension (mN/m) 65 [mN/m] at a temperature of 22°C and salinity of 0‰ Vapour Pressure (Pa) 202600 [Pa] at a temperature of 20°C 243680 [Pa] at a temperature of 25°C Vapour pressure at 70% of critical temperature (Pa) 239070 Ignition Temperature (°C) 365 Flash Point (°C) -60 Flash Point (Pensky-Martens closed cup) (°C) -60 Lower explosivity limit (LEL) (volume %) 1.9 Upper explosivity limit (UEL) (volume %) 8.5 Vapor enthalpy (J/Kg) 385211 [J/Kg] at a temperature of -0.5°C Combus enthalpy (J/Kg) 45385000 Henry's constant (mol/(m³·Pa)) 96258.75
### Behaviour at sea
Log kow 2.89 Log koc 1.6 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 40
### Additional data
Colour colourless Odour gasoline odour MARPOL pollution category Category Description Other Substances Substances which have been evaluated and found to fall outside Category X, Y or Z because they are considered to present no harm to marine resources, human health, amenities or other legitimate uses of the sea when discharged into the sea from tank cleaning of deballasting operations. The discharge of bilge or ballast water or other residues or mixtures containing these substances are not subject to any requirements of MARPOL Annex II.
### Transportation data
Transport mode Gas,Packaged Ship type 2G,2PG Cargo group 31 State liq.compr.gas Temperature (°C) ambient Pressure (Pa) under pressure Family name paraffins IMO class 2(2.1)
### Reactivity data
Water No Static electricity Yes
### GESAMP Hazard profile
Interference with coastal amenities (E2) G - Gas
### Human toxicity threshold
Hazard statements Physical H220 Extremely flammable gas. TEEL-1 (mg/m3) 5500 ppm TEEL-2 (mg/m3) 17000 ppm TEEL-3 (mg/m3) 53000 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 69.43 Lowest median lethal concentration (LC50) on fishes (mg/l) 49.9
# BUTENE OLIGOMER
Also known as: BUTENE oligomère
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 730 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 112.22 Boiling Point (°C) 60/282 Melting Point (°C) < -50 Flash Point (°C) > 20
### Behaviour at sea
### Additional data
Colour colourless Odour gasoline odour Standard behavior classification F/FE/E
### Transportation data
Cargo group 30 State liquid Family name olefins
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# BUTYL BENZENE
UN Number: 2709 - CAS Number: 104-51-8 Also known as: BUTYLBENZENE, 1-BUTYLBENZENE, n-BUTYLBENZENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2709 CAS number 104-51-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 860 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 134.22 Boiling Point (°C) 183 Melting Point (°C) -88 Vapour Pressure (Pa) 133 (22.7�C) [Pa] at a temperature of 20°C Ignition Temperature (°C) 412 Flash Point (°C) 59 Lower explosivity limit (LEL) (volume %) 0.8 Upper explosivity limit (UEL) (volume %) 5.8
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Transport mode Bulk.Packaged Package group III Cargo group 32 State liquid Family name aromatic hydrocarbons IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 20 ppm TEEL-2 (mg/m3) 150 ppm TEEL-3 (mg/m3) 750 ppm
### Ecotoxicity
# BUTYL BENZYL PHTHALATE
UN Number: 3082 Also known as: BENZENE-1,2-DICARBOXYLIC ACID, BENZYL BUTYL ESTER, BENZYL-n-BUTYL PHTHALATE, BUTYL PHENYLMETHYL ESTER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1120 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 313 Density of gas (kg/m3) 13.945 Boiling Point (°C) 370 Melting Point (°C) 1.285714286 Vapour Pressure (Pa) < 0.1 [Pa] at a temperature of 20°C Ignition Temperature (°C) 435 Flash Point (°C) 199
### Behaviour at sea
### Additional data
Colour colourless Odour slight
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 34 State liquid Temperature (°C) ambient Family name esters
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 2 - Moderate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 0 - Not irritating Specific Health Concern (D3) R - Reprotoxicity Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 15 TEEL-2 (mg/m3) 500 TEEL-3 (mg/m3) 500
### Ecotoxicity
# BUTYL BUTYRATE
UN Number: 3272 - CAS Number: 109-21-7 Also known as: BUTANOIC ACID, BUTYL ESTER, BUTYLBUTANOATE, BUTYRATE DE BUTYLE, BUTYRIC ACID, BUTYL ESTER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3272 CAS number 109-21-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 872 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 144.21 Density of gas (kg/m3) 6.41 Boiling Point (°C) 166.6 Melting Point (°C) -91.5 Flash Point (°C) 53.3
### Behaviour at sea
### Additional data
Colour colourless Odour apple odour Standard behavior classification F/FE/E
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 34 State liquid Temperature (°C) ambient Family name esters IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 5 ppm TEEL-2 (mg/m3) 35 ppm TEEL-3 (mg/m3) 150 ppm
### Ecotoxicity
# BUTYL STEARATE
Also known as: BUTYLOCTADECANOATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 861 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 340 Boiling Point (°C) 220/225 Melting Point (°C) 17/22 Flash Point (°C) 160
### Behaviour at sea
### Additional data
Colour colourless Odour faint fatty odour
### Transportation data
State liquid
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# BUTYL, DECYL, CETYL-EICOSYL METHACRYLATE
Also known as: BUTYL, DECYL, CETYL, EICOSYL 2-METHYL-2-PROPENOATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Molar mass (g/mol) 142.2 Boiling Point (°C) 163 Melting Point (°C) -50 Vapour Pressure (Pa) 300 [Pa] at a temperature of 20°C Ignition Temperature (°C) 290 Flash Point (°C) 50
### Behaviour at sea
### Additional data
Colour colourless Odour mild
### Transportation data
Cargo group 14 State liquid Temperature (°C) ambient Family name acrylates
### Reactivity data
Water No Acid(s) Yes Base(s) Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 7.5 TEEL-2 (mg/m3) 50 TEEL-3 (mg/m3) 500
### Ecotoxicity
# BUTYLAMINE (normal, secondary, tertiary)
UN Number: 1125 - CAS Number: 109-73-9 Also known as: 1-AMINOBUTANE, 1-BUTANAMINE, N-BUTYLAMINE 1-AMINOBUTANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1125 CAS number 109-73-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 741 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 73.14 Density of gas (kg/m3) 3.225 Boiling Point (°C) 77 Melting Point (°C) -50 Vapour Pressure (Pa) 9100 [Pa] at a temperature of 20°C Ignition Temperature (°C) 312 Flash Point (°C) -3 Lower explosivity limit (LEL) (volume %) 1.7 Upper explosivity limit (UEL) (volume %) 9.8
### Behaviour at sea
### Additional data
Colour colourless Odour ammonia, fish odour
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aliphatic amines IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys Yes Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 3000 TEEL-1 (mg/m3) 7.5 ppm TEEL-2 (mg/m3) 50 ppm TEEL-3 (mg/m3) 300 ppm
### Ecotoxicity
# BUTYLENE
UN Number: 1012 Also known as: BUTENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1012
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 2.451 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 56.1 Density of gas (kg/m3) 2.451 Boiling Point (°C) -7 Melting Point (°C) -185 Vapour Pressure (Pa) 253250 [Pa] at a temperature of 20°C Ignition Temperature (°C) 440 Flash Point (°C) -12 Lower explosivity limit (LEL) (volume %) 1.6 Upper explosivity limit (UEL) (volume %) 9.3
### Behaviour at sea
### Additional data
Colour colourless Odour fragrant, gasoline odour
### Transportation data
Transport mode Gas,Packaged Ship type 2G,2PG Cargo group 30 State liq.compr.gas Temperature (°C) ambient Pressure (Pa) under pressure Family name olefins IMO class 2(2.1)
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# BUTYLENE GLYCOL
CAS Number: 110-63-4 Also known as: BUTANEDIOL, BUTYLENEGLYCOL, 1,3 BUTYLENEGLYCOL, DIHYDROXYBUTANE, 1,4-Butanediol, Butane-1,4-Diol, 1,4-Butylene Glycol, Tetramethylene Glycol, 1,4-Dihydroxybutane, Butylene Glycol
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 110-63-4 Formula C 4 H 1 0 O 2
### Physical chemical data
Physical State (20°C) Liquid/Solid Physical State (25°C) Liquid Density (kg/m3) 1010 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 87.74 [cSt] at a temperature of 20°C 70.3 [cSt] at a temperature of 25°C Molar mass (g/mol) 89.6 Density of gas (kg/m3) 40 Solubility (g/L) 100000 [g/L] at a temperature of 20°C and salinity of 0‰ 100000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 207.5 Melting Point (°C) < 23 Critical molar volume (m³/mol) 0.000305 Critical temperature (°C) 692.4 Critical pressure (Pa) 5180000 Surface tension (mN/m) 44.6 [mN/m] at a temperature of 20°C Vapour Pressure (Pa) 100 [Pa] at a temperature of 20°C 1.9 [Pa] at a temperature of 25°C Ignition Temperature (°C) 377 Flash Point (°C) 121 Flash Point (Pensky-Martens closed cup) (°C) 132 Flash Point (Cleveland open cup) (°C) 121 Lower explosivity limit (LEL) (volume %) 1.9 Vapor enthalpy (J/Kg) 585000 [J/Kg] at a temperature of 235°C 826222 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 27607328 Specific heat capacity (J/(Kg·K)) 2521 Henry's constant (mol/(m³·Pa)) 0.00013
### Behaviour at sea
Log kow 0.5 Log koc 0 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable
### Additional data
Colour colourless Odour odourless MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment.
### Transportation data
Cargo group 20 Temperature (°C) ambient Family name alcohols, glycols
### Reactivity data
Water No Abilities Miscible in water. Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
Hazard statements Health H302 Harmful if swallowed. H336 May cause drowsiness or dizziness. Precautionary statements Prevention P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P264 Wash ... thoroughly after handling. P270 Do no eat, drink or smoke when using this product. Response P301 + P312 IF SWALLOWED: Call a POISON CENTER or doctor/physician if you feel unwell. P330 Rinse mouth. Disposal P501 Dispose of contents/container to ... TEEL-1 (mg/m3) 3.5 TEEL-2 (mg/m3) 25 TEEL-3 (mg/m3) 250
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) > 1000 Lowest median lethal concentration (LC50) on crustacean (mg/l) > 85 Lowest median lethal concentration (LC50) on fishes (mg/l) > 100 Highest no observed effect concentration (NOEC) on algae (mg/l) > 1000 Highest no observed effect concentration (NOEC) on crustacean (mg/l) > 85 Assessment factor (AF) 10000 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 80 [µg/l] on the Short term
# BUTYRALDEHYDE
UN Number: 1129 - CAS Number: 123-72-8 Also known as: BUTAL, BUTALDEHYDE, BUTANAL, BUTYL ALDEHYDE, BUTYRAL, 2-Butanone, 3-Butanone, Butanone, Ethyl Methyl Ketone, Mek, Methyl Acetone, Methyl-2-Propanone, Methylethyl Ketone, Methylethylketone, Butan-2-One, Methyl Ethyl Ketone
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1129 CAS number 123-72-8 Formula C 4 H 8 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 803 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.51 [cSt] at a temperature of 20°C 0.5 [cSt] at a temperature of 25°C Molar mass (g/mol) 72.11 Density of gas (kg/m3) 3.225 Solubility (g/L) 263000 [g/L] at a temperature of 20°C and salinity of 0‰ 136000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 75 Melting Point (°C) -97 Critical molar volume (m³/mol) 0.000267 Critical temperature (°C) 536.7 Critical pressure (Pa) 4207000 Surface tension (mN/m) 24.6 [mN/m] at a temperature of 20°C 23.97 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 12300 [Pa] at a temperature of 20°C 12079 [Pa] at a temperature of 25°C Ignition Temperature (°C) 230 Flash Point (°C) -6 Flash Point (Pensky-Martens closed cup) (°C) -2 Flash Point (Cleveland open cup) (°C) 1 Lower explosivity limit (LEL) (volume %) 2.47 Upper explosivity limit (UEL) (volume %) 10.6 Vapor enthalpy (J/Kg) 434059 [J/Kg] at a temperature of 79.6°C 482457 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 32700000 Specific heat capacity (J/(Kg·K)) 2200.8 Combustion efficiency (%) 96 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.07 Rad fraction (%) 28 Henry's constant (mol/(m³·Pa)) 5.83
### Behaviour at sea
Log kow 0.29 Log koc 0.55 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 10 Bioconcentration factor (BCF) 0.98
### Additional data
Colour colourless Odour pungent odour MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment. Standard behavior classification DE
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 19 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name aldehydes IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 300 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H319 Causes serious eye irritation. H336 May cause drowsiness or dizziness. Precautionary statements General P102 Keep out of reach of children. Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P233 Keep container tightly closed. P240 Ground/bond container and receiving equipment. P241 Use explosion-proof electrical/ventilating/lighting/.../equipment. P242 Use only non- sparking tools. P243 Take precautionary measures against static discharge. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P264 Wash ... thoroughly after handling. P271 Use only outdoors or in a well-ventilated area. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P312 Call a POISON CENTER or doctor/physician if you feel unwell. P337 + P313 If eye irritation persists: Get medical advice/attention. P370 + P378 In case of fire: Use ... for extinction. Storage P403 + P233 Store in a well-ventilated place. Keep container tightly closed. P405 Store locked up. Disposal P501 Dispose of contents/container to ... TEEL-1 (mg/m3) 0.06 ppm TEEL-2 (mg/m3) 0.4 ppm TEEL-3 (mg/m3) 12.5 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 1382 Lowest median lethal concentration (LC50) on fishes (mg/l) 1656 Highest no observed effect concentration (NOEC) on fishes (mg/l) 1170 Assessment factor (AF) 1 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 55.8 [µg/l] on the Short term
# BUTYROLACTONE
Also known as: BUTYRIC ACID LACTONE, gamma-BUTYROLACTONE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1050/1130 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 86.1 Boiling Point (°C) 204/206 Melting Point (°C) -44 Vapour Pressure (Pa) 150 [Pa] at a temperature of 20°C Ignition Temperature (°C) 455 Flash Point (°C) 98 Lower explosivity limit (LEL) (volume %) 0.3 Upper explosivity limit (UEL) (volume %) 16
### Behaviour at sea
### Additional data
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Specific Health Concern (D3) C - Carcinogenicity Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-2 (mg/m3) 40 TEEL-3 (mg/m3) 500
### Ecotoxicity
# CACODYLIC ACID
UN Number: 1572 Also known as: ACIDE CACODYLIQUE, AGENT BLUE (T), ANSAR (T), ARSAN (T), ARSINE OXIDE, DIMETHYLHYDROXY-, CHEXMATE (T), DIMETHYLARSINIC ACIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1572
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1100 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 138 Boiling Point (°C) 200
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour colourless, dyed blue Odour odourless Standard behavior classification D,SD, S
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 1.5
### Ecotoxicity
# CADMIUM CHLORIDE
UN Number: 2570 Also known as: CADDY, CHLORURE DE CADMIUM
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2570
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 3327 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 228.35 Boiling Point (°C) 960 Melting Point (°C) 568
### Behaviour at sea
### Additional data
Colour white Odour odourless Marine pollutant P Standard behavior classification SD
### Transportation data
Transport mode Bulk,Packaged State cryst. solid IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.007 TEEL-1 (mg/m3) 0.0489 TEEL-2 (mg/m3) 0.5 TEEL-3 (mg/m3) 14.7
### Ecotoxicity
# CAESIUM
UN Number: 1407 Also known as: CESIUM
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1407
### Physical chemical data
Physical State (20°C) Solid Molar mass (g/mol) 132.91
### Behaviour at sea
### Additional data
### Transportation data
State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 4.3
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 20 TEEL-2 (mg/m3) 150 TEEL-3 (mg/m3) 500
### Ecotoxicity
CALCIUM ALKYL PHENOL SULPHIDE polyolefin phosphorosulphide mixture (LOA) =====
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid/Solid Density (kg/m3) 945 [Kg/m³] at a temperature of 20°C Vapour Pressure (Pa) 400 [Pa] at a temperature of 20°C Flash Point (°C) 177
### Behaviour at sea
### Additional data
Standard behavior classification FED
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible
### Human toxicity threshold
### Ecotoxicity
# CALCIUM ARSENATE
UN Number: 1573 Also known as: ARSENIATE DE CALCIUM, CUCUMBER DUST (T)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1573
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 3620 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 398 Melting Point (°C) 1455
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour white Odour odourless Standard behavior classification D, SD, S
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.0006 TEEL-1 (mg/m3) 1.5 TEEL-2 (mg/m3) 10 TEEL-3 (mg/m3) 13.3
### Ecotoxicity
# CALCIUM CARBIDE
UN Number: 1402 Also known as: ACETHYLENOGEN, CALCIUM ACETYLIDE, CARBURE DE CALCIUM
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1402
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2220 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 64.1 Melting Point (°C) 2300
### Behaviour at sea
### Additional data
Colour grey to blue-black Odour garlic odour Standard behavior classification D,SD
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 4.3
### Reactivity data
Water Yes Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 30 TEEL-2 (mg/m3) 50 TEEL-3 (mg/m3) 250
### Ecotoxicity
# CALCIUM CARBONATE slurry
CAS Number: 471-34-1 Also known as: CARBONATE DE CALCIUM boue, CARBONIC ACID CALCIUM SALT, CHALK
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 471-34-1
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2900 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 100.1 Boiling Point (°C) 825
### Behaviour at sea
### Additional data
Colour white, gray Odour odourless
### Transportation data
State solid
### Reactivity data
Water No Acid(s) Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 0 - Is not a floater; and does not pose any known health hazards
### Human toxicity threshold
TLV-TWA 2.4 TEEL-1 (mg/m3) 45 TEEL-2 (mg/m3) 500 TEEL-3 (mg/m3) 500
### Ecotoxicity
# CALCIUM CHLORIDE
Also known as: CALCIUM DICHLORIDE, CALPUS (T), CALTAC (T), CHLORUREDECALCIUM, DOWFLAKE (T)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2100 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 110.99 Boiling Point (°C) 1600 Melting Point (°C) 772
### Behaviour at sea
### Additional data
Colour white to off-white Odour odourless Standard behavior classification SD
### Transportation data
State solid, solut. Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# CALCIUM CHLORITE
UN Number: 1453 Also known as: CHLORITE DE CALCIUM
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1453
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2700 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 243 Melting Point (°C) 100
### Behaviour at sea
### Additional data
Standard behavior classification SD
### Transportation data
Package group II State solid IMO class 5.1
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles Yes Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# CALCIUM HYDRIDE
UN Number: 1404
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1404
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1900 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 41.1 Density of gas (kg/m3) 1900 Melting Point (°C) 675
### Behaviour at sea
### Additional data
Standard behavior classification D,SD
### Transportation data
State solid IMO class 4.3
### Reactivity data
Water Yes Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-2 (mg/m3) 35 TEEL-3 (mg/m3) 150
### Ecotoxicity
# CALCIUM HYDROXIDE
CAS Number: 1305-62-0
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 1305-62-0
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2240 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 74.09
### Behaviour at sea
### Additional data
Colour white Odour odourless Standard behavior classification D, SD, S
### Transportation data
State solid, solut.
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TLV-TWA 1.5 TEEL-1 (mg/m3) 15 TEEL-2 (mg/m3) 500 TEEL-3 (mg/m3) 500
### Ecotoxicity
# CALCIUM HYPOCHLORITE dry or mixtures(>39% avail. chlorine)
UN Number: 1748 - CAS Number: 8061-52-7 Also known as: BLEACHING POWDER, CAL HYPO, CHLORINATED LIME, CHLOROX (T), Lignosulfonic Acid, Calcium Salt, Calcium 3-(2-Hydroxy-3-Methoxyp henyl)-2-[2-Methoxy-4-(3-Sulfonatopropyl)Phenoxy]Propane-1-Sulfonate, Calcium Lignosulphonate Solutions, Solutions De Lignosulfonate De Calcium
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1748 CAS number 8061-52-7 Formula C 2 0 H 2 4 CaO 1 0 S 2
### Physical chemical data
Physical State (20°C) Solid Physical State (25°C) Liquid Mixed Yes Density (kg/m3) 2300 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 174.98 Solubility (g/L) 10000000 [g/L] at a temperature of 20°C and salinity of 0‰ Melting Point (°C) 100
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour white Odour bleaching liquid odour MARPOL pollution category Category Description Other Substances Substances which have been evaluated and found to fall outside Category X, Y or Z because they are considered to present no harm to marine resources, human health, amenities or other legitimate uses of the sea when discharged into the sea from tank cleaning of deballasting operations. The discharge of bilge or ballast water or other residues or mixtures containing these substances are not subject to any requirements of MARPOL Annex II. Standard behavior classification D, SD
### Transportation data
Transport mode Bulk,Packaged Package group II State solid IMO class 5.1
### Reactivity data
Water No Abilities Solution. Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 5 - Very highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
Hazard statements Environmental H413 May cause long lasting harmful effects to aquatic life. TEEL-1 (mg/m3) 10 TEEL-2 (mg/m3) 75 TEEL-3 (mg/m3) 350
### Ecotoxicity
# CALCIUM LIGNOSULPHATE solutions
CAS Number: 8061-52-7
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 8061-52-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1260/1280 [Kg/m³] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour brown Odour slight Standard behavior classification D/DE
### Transportation data
State liquid
### Reactivity data
Water No
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 5 - Very highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# CALCIUM NITRATE (40-50% aqueous solution)
UN Number: 1454 - CAS Number: 10124-37-5 Also known as: CALCIUM (II) NITRATE, Calcium Dinitrate, Lime Nitrate, Calcium Nitrate Solutions (50% Or Less), Solution De Nitrate De Calcium (50% Ou Moins)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1454 CAS number 10124-37-5 Formula Ca(NO 3 ) 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Mixed Yes Density (kg/m3) 2500 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 164.1 Solubility (g/L) 10000000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 115 Melting Point (°C) 560
### Behaviour at sea
### Additional data
Colour colourless to slightly yellow Odour odourless MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment. Standard behavior classification D/DE
### Transportation data
Package group III State liquid IMO class 5.1
### Reactivity data
Water No Abilities Solution. Acid(s) Yes Reducing agents Yes Combustibles Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
Hazard statements Health H302 Harmful if swallowed. H318 Causes serious eye damage. Precautionary statements Prevention P264 Wash ... thoroughly after handling. P270 Do no eat, drink or smoke when using this product. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P310 Immediately call a POISON CENTER or doctor/physician. P330 Rinse mouth. TEEL-1 (mg/m3) 3.5 TEEL-2 (mg/m3) 25 TEEL-3 (mg/m3) 125
### Ecotoxicity
# CALCIUM PERMANGANATE
UN Number: 1456
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1456
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2400 [Kg/m³] at a temperature of 20°C
### Behaviour at sea
### Additional data
Standard behavior classification SD
### Transportation data
Package group II State solid IMO class 5.1
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# CAMPHOR OIL
UN Number: 1130 Also known as: CAMPHOR LINIMENT (T), HUILE DE CAMPHRE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1130
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 923 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 200
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour colourless, brown, blue Odour penetrating, camphor odour Standard behavior classification D, FD, F
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 18 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name ketones IMO class 7-Mar
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 30 TLV-TWA 0.3
### Ecotoxicity
# CAPROLACTAM liquid
CAS Number: 105-60-2 Also known as: AMINOCAPROIC LACTAM, 6-AMINOHEXANOIC ACID LACTAM, CAPROLACTAME liquide
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 105-60-2
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1020 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 113 Density of gas (kg/m3) 5.031 Boiling Point (°C) 268 Melting Point (°C) 69 Vapour Pressure (Pa) 373 [Pa] at a temperature of 20°C Ignition Temperature (°C) 375 Flash Point (°C) 110 Lower explosivity limit (LEL) (volume %) 1.84
### Behaviour at sea
### Additional data
Colour colourless Odour mild odour Standard behavior classification FD
### Transportation data
Cargo group 22 State liquid Temperature (°C) 75� - 24� Pressure (Pa) under pressure Family name caprolactam solution
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-3 (mg/m3) 20
### Ecotoxicity
# CARBARYL
UN Number: 2757 Also known as: ARYLAM, CARBATOX, CARPOLIN AND OTHERS
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2757
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1200 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 201 Melting Point (°C) 142 Vapour Pressure (Pa) negligible [Pa] at a temperature of 20°C
### Behaviour at sea
Persistence (days) 3.1
### Additional data
Colour white to grey Odour weak odour
### Transportation data
Transport mode Bulk,Packaged Package group III State solid IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 70 TLV-TWA 0.6 TEEL-2 (mg/m3) 15 TEEL-3 (mg/m3) 100
### Ecotoxicity
# CARBOLIC OIL (mixture)
UN Number: 2821 Also known as: CARBOLIC ACID
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2821
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1040 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 94.11 Boiling Point (°C) 181.8 Melting Point (°C) 41 Vapour Pressure (Pa) 82.7 [Pa] at a temperature of 20°C Ignition Temperature (°C) 715 Flash Point (°C) 79.4 Lower explosivity limit (LEL) (volume %) 1.7 Upper explosivity limit (UEL) (volume %) 8.6
### Behaviour at sea
### Additional data
Colour darkens with light Odour sweet tar
### Transportation data
Transport mode Bulk,Packaged Package group II/III Cargo group 21 State liquid Temperature (°C) ambient Family name phenols, cresols IMO class 6.1
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 3 - ≥100 and <500 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 250 ERPG-1 (ppm) 10 ERPG-2 (ppm) 50 ERPG-3 (ppm) 200
### Ecotoxicity
# CARBON DISULPHIDE
UN Number: 1131 - CAS Number: 75-15-0 Also known as: CARBON BISULFIDE, CARBON BISULPHIDE, DISULPHURE DE CARBONE, Carbonbisulfide, Carbon Disulphide, Disulfure De Carbone
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1131 CAS number 75-15-0 Formula CS 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1260 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.2874 [cSt] at a temperature of 20°C 0.279 [cSt] at a temperature of 25°C Molar mass (g/mol) 76.14 Density of gas (kg/m3) 3.354 Solubility (g/L) 2000 [g/L] at a temperature of 20°C and salinity of 0‰ 2160 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 46 Melting Point (°C) -110 Critical molar volume (m³/mol) 0.000173 Critical temperature (°C) 552 Critical pressure (Pa) 7900000 Surface tension (mN/m) 32.25 [mN/m] at a temperature of 20°C 31.58 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 40520 [Pa] at a temperature of 20°C 57328 [Pa] at a temperature of 30°C Ignition Temperature (°C) 100 Flash Point (°C) -30 Flash Point (Pensky-Martens closed cup) (°C) -30 Lower explosivity limit (LEL) (volume %) 1.3 Upper explosivity limit (UEL) (volume %) 44 Vapor enthalpy (J/Kg) 352109 [J/Kg] at a temperature of 46°C 337667 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 17756763 Specific heat capacity (J/(Kg·K)) 1003 Henry's constant (mol/(m³·Pa)) 1459.1
### Behaviour at sea
Persistence (days) 3.1 Log kow 1.84 Log koc 1.34 Biodegradation in estuary environment (Half-life) (days) 400
### Additional data
Colour colourless to yellow Odour rotten egg to sweet odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Cargo group 38 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name carbon disulfide IMO class 3.1
### Reactivity data
Base(s) Yes Static electricity Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 4 - High Skin irritation/corrosivity (D1) 3A - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 500 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H319 Causes serious eye irritation. H332 Harmful if inhaled. H361 Suspected of damaging fertility or the unborn child. H372 Causes damage to organs through prolonged or repeated exposure, exposure cause the hazard: Precautionary statements Prevention P201 Obtain special instructions before use. P202 Do not handle until all safety precautions have been read and understood. P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P233 Keep container tightly closed. P240 Ground/bond container and receiving equipment. P241 Use explosion-proof electrical/ventilating/lighting/.../equipment. P243 Take precautionary measures against static discharge. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P264 Wash ... thoroughly after handling. P270 Do no eat, drink or smoke when using this product. P271 Use only outdoors or in a well-ventilated area. P280 Wear protective gloves/protective clothing/eye protection/face protection. P281 Use personal protective equipment as required. Response P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P308 + P313 IF exposed or concerned: Get medical advice/attention. P312 Call a POISON CENTER or doctor/physician if you feel unwell. P314 Get medical advice/attention if you feel unwell. P337 + P313 If eye irritation persists: Get medical advice/attention. ERPG-2 (ppm) 50 ERPG-3 (ppm) 500
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 2.1 Lowest median lethal concentration (LC50) on fishes (mg/l) 2.99 Highest no observed effect concentration (NOEC) on fishes (mg/l) 135 Assessment factor (AF) 1000 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 1 [µg/l] on the Short term
# CARBON TETRACHLORIDE
UN Number: 1846 Also known as: CARBON TET
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1846
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1590 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 153.83 Density of gas (kg/m3) 7.095 Boiling Point (°C) 76 Melting Point (°C) -23 Vapour Pressure (Pa) 11997 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless Odour sweet odour
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 36 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name halogenated hydrocarb IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
Biodegradation (A2) NR - Not readily biodegradable
### Human toxicity threshold
IDHL 300 ERPG-1 (ppm) 20 ERPG-2 (ppm) 100 ERPG-3 (ppm) 750
### Ecotoxicity
# CELLULOID (scrap)
UN Number: 2002
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2002
### Physical chemical data
Physical State (20°C) Solid
### Behaviour at sea
### Additional data
### Transportation data
Package group III State solid IMO class 4.2
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# CETYL EICOSYL METHACRYLATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 860 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 370 Melting Point (°C) < 0/20 Vapour Pressure (Pa) very low [Pa] at a temperature of 20°C Flash Point (°C) 149
### Behaviour at sea
### Additional data
Colour clear to brownish Odour mild sweet
### Transportation data
Cargo group 14 State liquid
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# CHLORINE
UN Number: 1017 Also known as: BERTHOLITE, CHLORE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1017
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 3.225 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 70.91 Density of gas (kg/m3) 3.225 Boiling Point (°C) -34 Melting Point (°C) -101 Vapour Pressure (Pa) 680000 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour greenish yellow Odour irritat., choking, bleaking
### Transportation data
Transport mode Gas,Packaged Ship type 1G State liq.compr.gas Temperature (°C) ambient Pressure (Pa) under pressure IMO class 2(2.3)
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 30 TLV-TWA 0.5 ERPG-3 (ppm) 20 10 min 30 min 60 min 4 hrs 8 hrs AEGL-1 (ppm) 0.5 0.5 0.5 0.5 0.5 AEGL-2 (ppm) 2.8 2.8 0.7 AEGL-3 (ppm) 50 28 20 10 7.1
### Ecotoxicity
# CHLOROACETIC ACID solid
UN Number: 1751 - CAS Number: 79-11-8 Also known as: ACIDE CHLOROACETIQUE solide, CHLOROACETIC ACID, CHLOROETHANOIC ACID, Monochloroacetic Acid, Chloroacetic Acid Solutions, Solutions D'Acide Chloroacetique
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1751 CAS number 79-11-8 Formula C 2 H 3 ClO 2
### Physical chemical data
Physical State (20°C) Solid Physical State (25°C) Liquid Density (kg/m3) 1580 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 94.5 Density of gas (kg/m3) 4.26 Solubility (g/L) 10000000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 188 Melting Point (°C) 57 Vapour Pressure (Pa) 130 [Pa] at a temperature of 20°C Ignition Temperature (°C) 470 Flash Point (°C) 126
### Behaviour at sea
### Additional data
Colour white to brown Odour strong vinegar-like MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group II State solid Temperature (°C) ambient IMO class 6.1
### Reactivity data
Water No Abilities Solution. Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 4 - High Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
Hazard statements Physical H290 May be corrosive to metals. Health H301 Toxic if swallowed. H311 Toxic in contact with skin. H314 Causes severe skin burns and eye damage. H331 Toxic if inhaled. H335 May cause respiratory irritation. Environmental H410 Very toxic to aquatic life with long lasting effects. Precautionary statements Prevention P234 Keep only in original container. P260 Do not breathe dust/fume/gas/mist/vapours/spray. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P330 + P331 IF SWALLOWED: rinse mouth. Do NOT induce vomiting. P302 + P352 IF ON SKIN: Wash with plenty of soap and water. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P309 + P311 IF exposed or if you feel unwell: Call a POISON CENTER or doctor/physician. P390 Absorb spillage to prevent material damage. Storage P406 Store in corrosive resistant/... container with a resistant inner liner. Disposal P501 Dispose of contents/container to ... TEEL-1 (mg/m3) 1.5 ppm TEEL-2 (mg/m3) 6.6 ppm TEEL-3 (mg/m3) 20 ppm
### Ecotoxicity
# CHLOROBENZENE
UN Number: 1134 - CAS Number: 108-90-7 Also known as: BENZENE CHLORIDE, CHLOROBENZOL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1134 CAS number 108-90-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1110 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 112.56 Density of gas (kg/m3) 5.005 Boiling Point (°C) 132 Melting Point (°C) -45 Vapour Pressure (Pa) 1200 [Pa] at a temperature of 20°C Ignition Temperature (°C) 660 Flash Point (°C) 28 Lower explosivity limit (LEL) (volume %) 1.3 Upper explosivity limit (UEL) (volume %) 7.1
### Behaviour at sea
### Additional data
Colour colourless Odour sweet, almond odour
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 36 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name halogenated hydrocarb IMO class 3.3
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 2400 TLV-TWA 75 TEEL-1 (mg/m3) 10 ppm TEEL-2 (mg/m3) 150 ppm TEEL-3 (mg/m3) 400 ppm
### Ecotoxicity
# CHLOROFORM
UN Number: 1888 - CAS Number: 67-66-3 Also known as: CHLOROFORME, Formyl Trichloride, Methane Trichloride, Methenyl Trichloride, Methyl Trichloride, Trichloroform, Trichloromethane, Chloroform
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1888 CAS number 67-66-3 Formula CHCl 3
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1490 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.38 [cSt] at a temperature of 20°C 0.36 [cSt] at a temperature of 25°C Molar mass (g/mol) 119.39 Density of gas (kg/m3) 5.289 Solubility (g/L) 8220 [g/L] at a temperature of 20°C and salinity of 0‰ 7950 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 61 Melting Point (°C) -63 Critical molar volume (m³/mol) 0.000239 Critical temperature (°C) 536.4 Critical pressure (Pa) 5470000 Surface tension (mN/m) 27.14 [mN/m] at a temperature of 20°C 26.67 [mN/m] at a temperature of 25°C Interfacial tension (mN/m) 32.8 [mN/m] at a temperature of 20°C and salinity of 0‰ Vapour Pressure (Pa) 20260 [Pa] at a temperature of 20°C 26000 [Pa] at a temperature of 25°C Vapor enthalpy (J/Kg) 244.93 [J/Kg] at a temperature of 61.3°C 279364 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 3180000 Specific heat capacity (J/(Kg·K)) 956.6 Combustion efficiency (%) 50 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.02 Rad fraction (%) 40 Henry's constant (mol/(m³·Pa)) 371
### Behaviour at sea
Log kow 1.97 Log koc 1.5 Aqueous photolysis (Half-life) 22 Biodegradation in estuary environment (Half-life) (days) 450 Biodegradation in marine environment (Half-life) (days) Not biodegradable Bioconcentration factor (BCF) 12.7
### Additional data
Colour colourless Odour sweet odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 36 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name halogenated hydrocarb IMO class 6.1
### Reactivity data
Notable risks Reacts violently with strong bases, strong oxidants and some metals such as aluminium, magnesium and zinc.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 1000 Hazard statements Health H302 Harmful if swallowed. H315 Causes skin irritation. H319 Causes serious eye irritation. H331 Toxic if inhaled. H351 Suspected of causing cancer. H361 Suspected of damaging fertility or the unborn child. H372 Causes damage to organs through prolonged or repeated exposure, exposure cause the hazard: Precautionary statements Prevention P202 Do not handle until all safety precautions have been read and understood. P260 Do not breathe dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P308 + P313 IF exposed or concerned: Get medical advice/attention. Storage P403 + P233 Store in a well-ventilated place. Keep container tightly closed. Disposal P501 Dispose of contents/container to ... ERPG-2 (ppm) 50 ERPG-3 (ppm) 5000
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 13.3 Lowest median lethal concentration (LC50) on crustacean (mg/l) 29 Lowest median lethal concentration (LC50) on fishes (mg/l) 18 Highest no observed effect concentration (NOEC) on algae (mg/l) 3.61 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 6.3 Highest no observed effect concentration (NOEC) on fishes (mg/l) 1.463 Assessment factor (AF) 50 on the Short term 10 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 266 [µg/l] on the Short term 146 [µg/l] on the Long term
# CHLOROHYDRINS
CAS Number: 96-24-2 Also known as: CHLOROHYDRINES, CHLOROPROPANE DIOLS, CHLOROPROPYLENE GLYCOLS, CRUDE EPICHLOROHYDRIN
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 96-24-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1180 [Kg/m³] at a temperature of 20°C Vapour Pressure (Pa) 786 [Pa] at a temperature of 20°C Ignition Temperature (°C) 428 Flash Point (°C) 33.3 Lower explosivity limit (LEL) (volume %) 3.8 Upper explosivity limit (UEL) (volume %) 21
### Behaviour at sea
### Additional data
Colour colourless to pale yellow Odour pungent, garlic-like Standard behavior classification SD/D
### Transportation data
Cargo group 17 State liquid Temperature (°C) ambient Family name epichlorohydrin
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 3A - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Specific Health Concern (D3) C - Carcinogenicity Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 75 TLV-TWA 0.5 ERPG-2 (ppm) 20 ERPG-3 (ppm) 100
### Ecotoxicity
# CHLOROSULFONIC ACID (with or without SO3)
UN Number: 1754 Also known as: ACIDE CHLOROSULFONIQUE (avec ou sans SO3), CHLOROSULFURIC ACID
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1754
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1750 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 116.53 Density of gas (kg/m3) 5.16 Boiling Point (°C) 155 Melting Point (°C) -80 Vapour Pressure (Pa) 130 [Pa] at a temperature of 20°C
### Behaviour at sea
Persistence (days) 0.8
### Additional data
Colour colourless to light yellow Odour sharp, choking odour Standard behavior classification D, SD
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) under pressure
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles Yes Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
ERPG-2 (ppm) 10 ERPG-3 (ppm) 30
### Ecotoxicity
# CHOLINE CHLORIDE solutions
CAS Number: 67-48-1 Also known as: BIOCOLINA, CHLORURE DE CHOLINE en solution, CHOLINE CHLOROHYDRATE, CHOLINE HYDROCHLORID, CHOLINIUM CHLORIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 67-48-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1100 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 139.65 (solid) Boiling Point (°C) 100 Melting Point (°C) 305 Vapour Pressure (Pa) 2400 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour white Odour odourless
### Transportation data
### Reactivity data
Water No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 0 - Is not a floater; and does not pose any known health hazards
### Human toxicity threshold
### Ecotoxicity
# CHROMIUM TRIOXIDE anhydrous
UN Number: 1463
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1463
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2700 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 99.99 Melting Point (°C) 197
### Behaviour at sea
### Additional data
Colour dark red Odour odourless
### Transportation data
Package group II State solid IMO class 5.1
### Reactivity data
Metal(s) and alloys No Oxidizing agents No Reducing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.012 TEEL-1 (mg/m3) 0.00962 TEEL-2 (mg/m3) 0.06 TEEL-3 (mg/m3) 28.8
### Ecotoxicity
# CITRIC ACID
Also known as: ACIDE CITRIQUE, ACILETTEN (T), CITRETTEN (T), CITRO (T)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1700 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 192.1 Melting Point (°C) 153 Flash Point (°C) 100 Lower explosivity limit (LEL) (volume %) 0.28 Upper explosivity limit (UEL) (volume %) 2.29
### Behaviour at sea
### Additional data
Colour white Odour odourless Standard behavior classification SD
### Transportation data
State solid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 35 TEEL-2 (mg/m3) 250 TEEL-3 (mg/m3) 500
### Ecotoxicity
# CLAY
Also known as: ALUMINIUM SILICATEHYDROXIDE, ARGILE, BALL CLAY, BENTONITE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Solid
### Behaviour at sea
### Additional data
### Transportation data
State solid
### Reactivity data
Water No
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 0 - Is not a floater; and does not pose any known health hazards
### Human toxicity threshold
### Ecotoxicity
# COAL TAR
UN Number: 3082 - CAS Number: 8007-45-2 Also known as: CARBO-CORT, CRUDE COAL TAR
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082 CAS number 8007-45-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1160/1220 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 105/355 Flash Point (°C) 125
### Behaviour at sea
### Additional data
Colour black Odour odourless
### Transportation data
Package group III State liquid
### Reactivity data
Water No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# COAL TAR NAPHTA SOLVENT
UN Number: 2553 - CAS Number: 8030-30-6
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2553 CAS number 8030-30-6
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 870 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 107.3 Density of gas (kg/m3) 4.79 Boiling Point (°C) 125/200 Melting Point (°C) < 15 Vapour Pressure (Pa) 400 [Pa] at a temperature of 20°C Ignition Temperature (°C) 277 Flash Point (°C) 15 Lower explosivity limit (LEL) (volume %) 0.8 Upper explosivity limit (UEL) (volume %) 6.1
### Behaviour at sea
### Additional data
Colour colourless to pale yellow Odour gasoline-like Standard behavior classification FE
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 33 State liquid Family name miscell. hydroc. mixt IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 10000
### Ecotoxicity
# COAL TAR PITCH
UN Number: 1136 - CAS Number: 65996-93-2 Also known as: BRAI DE GOUDRON DE HOUILLE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1136 CAS number 65996-93-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) > 1100 [Kg/m³] at a temperature of 20°C Density of gas (kg/m3) > 1.29 Boiling Point (°C) > 250 Melting Point (°C) 38/50 Vapour Pressure (Pa) <10 [Pa] at a temperature of 20°C Ignition Temperature (°C) >500 Flash Point (°C) >200
### Behaviour at sea
### Additional data
Colour black Odour tar-like
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 33 Temperature (°C) ambient Family name miscell. hydroc. mixt
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 3 - ≥100 and <500 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 2 - Moderate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# COD LIVER OIL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid
### Behaviour at sea
### Additional data
### Transportation data
Cargo group 34 State liquid Family name esters
### Reactivity data
Water No Acid(s) Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# COPPER ACETOARSENITE
UN Number: 1585 Also known as: ACETOARSENITE DE CUIVRE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1585
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1100 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 1014 Density of gas (kg/m3) 1100
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour green Odour odourless Standard behavior classification D, SD, S
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.06 (As) TEEL-1 (mg/m3) 3.38 TEEL-2 (mg/m3) 22 TEEL-3 (mg/m3) 22
### Ecotoxicity
# COPPER ARSENITE
UN Number: 1586 Also known as: ARSENITE DE CUIVRE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1586
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1100 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 277.4 Vapour Pressure (Pa) 130 [Pa] at a temperature of 20°C
### Behaviour at sea
Persistence (days) 1.9
### Additional data
Colour green Odour odourless Standard behavior classification D, SD, S
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.06 (As)
### Ecotoxicity
# COPPER CHLORIDE
UN Number: 2802 Also known as: CHLORURE DE CUIVRE, CUPRIC CHLORIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2802
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 3300 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 170.48 Boiling Point (°C) 993 Melting Point (°C) 498
### Behaviour at sea
### Additional data
Colour blue-green Odour odourless Standard behavior classification SD
### Transportation data
Package group III State solid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.4 (Cu) TEEL-1 (mg/m3) 0.317 TEEL-2 (mg/m3) 0.529
### Ecotoxicity
# COPPER CYANIDE
UN Number: 1587 Also known as: CUPRIC CYANIDE, CUPROUS CYANIDE, CYANURE DE CUIVRE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1587
### Physical chemical data
Physical State (20°C) Solid Molar mass (g/mol) 89.56
### Behaviour at sea
### Additional data
Colour white Marine pollutant P
### Transportation data
Package group II State solid Temperature (°C) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 45 TLV-TWA 4.5 TEEL-2 (mg/m3) 4.23 TEEL-3 (mg/m3) 7.05
### Ecotoxicity
# CREOSOTE (coal tar)
UN Number: 3082 - CAS Number: 8001-58-9 Also known as: COAL TAR OIL, CREOSOTE OIL, DEAD OIL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082 CAS number 8001-58-9
### Physical chemical data
Physical State (20°C) Liquid/Solid Density (kg/m3) 1070 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 93.38 Density of gas (kg/m3) 4.17 Boiling Point (°C) 182/400 Melting Point (°C) -0.146341463 Vapour Pressure (Pa) 300 [Pa] at a temperature of 20°C Ignition Temperature (°C) 336 Flash Point (°C) > 68
### Behaviour at sea
### Additional data
Colour yellow to black Odour tarry odour
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 21 Temperature (°C) ambient Family name phenols, cresols
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 2 - Moderate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 0.6 TEEL-2 (mg/m3) 80 TEEL-3 (mg/m3) 80
### Ecotoxicity
# CREOSOTE (wood tar)
UN Number: 3082 - CAS Number: 8021-39-4 Also known as: BEECHWOOD CREOSOTE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082 CAS number 8021-39-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1050 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) > 80 Density of gas (kg/m3) 3.57 Boiling Point (°C) 195/400 Melting Point (°C) < 15 Vapour Pressure (Pa) 100 [Pa] at a temperature of 20°C Ignition Temperature (°C) 335 Flash Point (°C) 68
### Behaviour at sea
### Additional data
Colour yellow to black Odour tarry odour
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 21 State liquid Temperature (°C) ambient Family name phenols, cresols
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes
### GESAMP Hazard profile
Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 5 - Very highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# CRESOLS (ortho, meta, para)
UN Number: 2076 - CAS Number: 1319-77-3
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2076 CAS number 1319-77-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1070 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 108.13 Density of gas (kg/m3) 4.799 Boiling Point (°C) 177 Melting Point (°C) 24 Vapour Pressure (Pa) 67 [Pa] at a temperature of 20°C Ignition Temperature (°C) 600 Flash Point (°C) 63 Lower explosivity limit (LEL) (volume %) 1.1
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour colourless to yellow Odour sweet, tar odour Standard behavior classification SD
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 21 State liquid, solid Family name phenols, cresols IMO class 6.1
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 4 - High Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 250 TEEL-1 (mg/m3) 15 ppm TEEL-2 (mg/m3) 24.9 ppm TEEL-3 (mg/m3) 250 ppm
### Ecotoxicity
# CRESYLIC ACID dephenolized
UN Number: 2022 Also known as: ACIDE CRESYLIQUE déphénolisé, DEPHENOLISED CRESOLS
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2022
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1040 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 250 Melting Point (°C) -12 Vapour Pressure (Pa) 133 (37.8�C) [Pa] at a temperature of 20°C Flash Point (°C) 86
### Behaviour at sea
### Additional data
Colour dark brown Odour phenolic odour Standard behavior classification SD
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid IMO class 6.1
### Reactivity data
Water No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# CROTONALDEHYDE inhibited or stabilized
UN Number: 1143 - CAS Number: 4170-30-3 Also known as: 2-BUTENAL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1143 CAS number 4170-30-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 852 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 70.09 Density of gas (kg/m3) 3.096 Boiling Point (°C) 102 Melting Point (°C) -74 Vapour Pressure (Pa) 4000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 230 Flash Point (°C) 13 Lower explosivity limit (LEL) (volume %) 2.1 Upper explosivity limit (UEL) (volume %) 15.5
### Behaviour at sea
### Additional data
Colour yellow Odour tar odour
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 19 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name aldehydes IMO class 6.1
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 4 - High Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 4 - High Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 400 ERPG-1 (ppm) 0.2 ERPG-3 (ppm) 15 10 min 30 min 60 min 4 hrs 8 hrs AEGL-1 (ppm) 0.19 0.19 0.19 0.19 0.19 AEGL-2 (ppm) 27 8.9 4.4 1.1 0.56 AEGL-3 (ppm) 44 27 14 2.6 1.5
### Ecotoxicity
# CUPRIETHYLENEDIAMINE solution
UN Number: 1761
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1761
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1100 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 100
### Behaviour at sea
### Additional data
Colour blue, dark purple Odour fish odour
### Transportation data
Package group II State liquid Temperature (°C) ambient Pressure (Pa) under pressure
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# CUT BACKS (asphalt or bitumen)
UN Number: 1999
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1999
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1100 [Kg/m³] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour black Odour tar odour
### Transportation data
Package group II Cargo group 33 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name miscell. hydroc. mixt IMO class 3.2/3.3
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# CYANOGEN BROMIDE
UN Number: 1889 Also known as: BROMINE CYANIDE, BROMOCYAN (T), BROMOCYANIDE, BROMOCYANOGEN, BROMURE DE CYANOGENE, CAMPILIT (T), CYANOBROMIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1889
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2000 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 105.93 Density of gas (kg/m3) 4.644 Boiling Point (°C) 62 Melting Point (°C) 52 Vapour Pressure (Pa) 13300 [Pa] at a temperature of 20°C
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour colourless Odour penetrating odour Standard behavior classification D, SD, S
### Transportation data
State solid IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 10 (as CN) TLV-TWA 1.1 (CN) TEEL-1 (mg/m3) 44 TEEL-2 (mg/m3) 44 TEEL-3 (mg/m3) 44
### Ecotoxicity
# CYANOGEN CHLORIDE inhibited
UN Number: 1589 Also known as: CHLORCYAN (T), CHLORINE CYANIDE, CHLOROCYANIDE, CHLOROCYANOGEN, CHLORURE DE CYANOGENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1589
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 2.58 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 61.48 Density of gas (kg/m3) 2.58 Boiling Point (°C) 13 Melting Point (°C) -6 Vapour Pressure (Pa) 176000 [Pa] at a temperature of 20°C Flash Point (°C) 51
### Behaviour at sea
### Additional data
Colour colourless Odour sharp, pungent odour
### Transportation data
State liq.compr.gas IMO class 2(2.3)
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 45 (as CN) TLV-TWA 0.3 (CN) ERPG-2 (ppm) 0.4
### Ecotoxicity
# CYCLOHEPTANE
UN Number: 2241 - CAS Number: 291-64-5
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2241 CAS number 291-64-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 811 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 98.19 Density of gas (kg/m3) 4.37 Boiling Point (°C) 118.5 Melting Point (°C) -12 Vapour Pressure (Pa) 2000 [Pa] at a temperature of 20°C Lower explosivity limit (LEL) (volume %) 1.1 Upper explosivity limit (UEL) (volume %) 6.7
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification FE
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 31 State liquid Temperature (°C) ambient Family name paraffins IMO class 3.2
### Reactivity data
Water No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# CYCLOHEXANE
UN Number: 1145 - CAS Number: 110-82-7 Also known as: Hexamethylene, Hexanaphthene, Hexahydrobenene, Cyclohexane
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1145 CAS number 110-82-7 Formula C 6 H 1 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 779 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 1.27 [cSt] at a temperature of 20°C 1.1552 [cSt] at a temperature of 25°C Molar mass (g/mol) 84.16 Density of gas (kg/m3) 3.741 Solubility (g/L) 55 [g/L] at a temperature of 20°C and salinity of 0‰ 45 [g/L] at a temperature of 15°C and salinity of 0‰ Boiling Point (°C) 80.9 Melting Point (°C) 6.59 Critical molar volume (m³/mol) 0.000308 Critical temperature (°C) 553.8 Critical pressure (Pa) 4080000 Surface tension (mN/m) 24.68 [mN/m] at a temperature of 20°C 24.16 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 10397 [Pa] at a temperature of 20°C 15999 [Pa] at a temperature of 30°C Ignition Temperature (°C) 260 Flash Point (°C) -18 Flash Point (Pensky-Martens closed cup) (°C) -18 Lower explosivity limit (LEL) (volume %) 1.3 Upper explosivity limit (UEL) (volume %) 8.4 Vapor enthalpy (J/Kg) 356195 [J/Kg] at a temperature of 80.73°C 390810 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 46573747 Specific heat capacity (J/(Kg·K)) 1841 Henry's constant (mol/(m³·Pa)) 15198.7
### Behaviour at sea
Log kow 3.4 Log koc 2.68 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) Not biodegradable Bioconcentration factor (BCF) 239
### Additional data
Colour colourless Odour gasoline odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 31 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name paraffins IMO class 3.1
### Reactivity data
Water No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 3 - ≥100 and <500 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 10000 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H304 May be fatal if swallowed and enters airways. H315 Causes skin irritation. H336 May cause drowsiness or dizziness. Environmental H400 Very toxic to aquatic life. H410 Very toxic to aquatic life with long lasting effects. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P243 Take precautionary measures against static discharge. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P331 Do NOT induce vomiting. P332 + P313 If skin irritation occurs: Get medical advice/attention. P391 Collect spillage. TLV-TWA 300 TEEL-1 (mg/m3) 300 ppm TEEL-2 (mg/m3) 500 ppm TEEL-3 (mg/m3) 1300 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 2.4 Lowest median lethal concentration (LC50) on fishes (mg/l) 8.3 Highest no observed effect concentration (NOEC) on algae (mg/l) 0.9 Highest no observed effect concentration (NOEC) on fishes (mg/l) 32 Assessment factor (AF) 100 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 9 [µg/l] on the Short term
# CYCLOHEXANOL
CAS Number: 108-93-0
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 108-93-0
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 947 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 100.16 Density of gas (kg/m3) 1.67 Boiling Point (°C) 161 Melting Point (°C) 23 Vapour Pressure (Pa) 130 [Pa] at a temperature of 20°C Ignition Temperature (°C) 300 Flash Point (°C) 68 Lower explosivity limit (LEL) (volume %) 2.4 Upper explosivity limit (UEL) (volume %) 12
### Behaviour at sea
### Additional data
Colour colourless to light yellow Odour alcohol odour
### Transportation data
Cargo group 20 State liquid, solid Family name alcohols, glycols
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 3500 TLV-TWA 50 TEEL-1 (mg/m3) 50 ppm TEEL-2 (mg/m3) 50 ppm TEEL-3 (mg/m3) 400 ppm
### Ecotoxicity
# CYCLOHEXANONE
UN Number: 1915 - CAS Number: 108-94-1 Also known as: Anone, Cyclohexyl Ketone, Hexanon, Ketohexamethylene, Nadone, Pimelic Ketone, Pimelin Ketone, Sextone, Cyclohexanone
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1915 CAS number 108-94-1 Formula C 6 H 1 0 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 950 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 2.32 [cSt] at a temperature of 25°C Molar mass (g/mol) 98.15 Density of gas (kg/m3) 4.386 Solubility (g/L) 23000 [g/L] at a temperature of 20°C and salinity of 0‰ 25000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 156 Melting Point (°C) -31.2 Critical temperature (°C) 665 Critical pressure (Pa) 4600000 Surface tension (mN/m) 34 [mN/m] at a temperature of 20°C 35.05 [mN/m] at a temperature of 25°C Interfacial tension (mN/m) 90 [mN/m] at a temperature of 20°C and salinity of 0‰ Vapour Pressure (Pa) 470 [Pa] at a temperature of 20°C 690 [Pa] at a temperature of 25°C Ignition Temperature (°C) 420 Flash Point (°C) 43 Flash Point (Pensky-Martens closed cup) (°C) 43.9 Flash Point (Cleveland open cup) (°C) 53.9 Lower explosivity limit (LEL) (volume %) 1.1 Upper explosivity limit (UEL) (volume %) 9.4 Vapor enthalpy (J/Kg) 459093 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 33600000 Specific heat capacity (J/(Kg·K)) 1856.3 Combustion efficiency (%) 96 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.05 Rad fraction (%) 23 Henry's constant (mol/(m³·Pa)) 0.91
### Behaviour at sea
Log kow 0.81 Log koc 1.79 Aqueous photolysis (Half-life) 4.3 Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 10 Bioconcentration factor (BCF) 2.23
### Additional data
Colour colourless to light yellow Odour sweet, peppermint odour MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment. Standard behavior classification FED
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 18 State liquid Family name ketones IMO class 3.3
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes Combustibles Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 5000 Hazard statements Physical H226 Flammable liquid and vapour. Health H332 Harmful if inhaled. Precautionary statements Prevention P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. TLV-TWA 25 TEEL-1 (mg/m3) 50 ppm TEEL-2 (mg/m3) 50 ppm TEEL-3 (mg/m3) 700 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 26 Lowest median lethal concentration (LC50) on crustacean (mg/l) 800 Lowest median lethal concentration (LC50) on fishes (mg/l) 527 Highest no observed effect concentration (NOEC) on algae (mg/l) 26 Assessment factor (AF) 100 on the Short term 1000 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 260 [µg/l] on the Short term 26 [µg/l] on the Long term
# CYCLOHEXYL ACETATE
UN Number: 2243 - CAS Number: 622-45-7 Also known as: ACETATE DE CYCLOHEXYLE, ACETIC ACID, CYCLOHEXYL ESTER, CYCLOHEXANYL ACETATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2243 CAS number 622-45-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 966 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 142.22 Density of gas (kg/m3) 6.32 Boiling Point (°C) 177 Melting Point (°C) -65 Vapour Pressure (Pa) 500 [Pa] at a temperature of 20°C Ignition Temperature (°C) 335 Flash Point (°C) 57.8
### Behaviour at sea
### Additional data
Colour colourless Odour fruity odour Standard behavior classification F/FE
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 34 State liquid Temperature (°C) ambient Family name esters IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# CYCLOHEXYLAMINE
UN Number: 2357 - CAS Number: 108-91-8 Also known as: AMINOCYCLOHEXANE, AMINOHEXAHYDROBENZENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2357 CAS number 108-91-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 865 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 99.18 Density of gas (kg/m3) 4.386 Boiling Point (°C) 134 Melting Point (°C) -18 Vapour Pressure (Pa) 1500 [Pa] at a temperature of 20°C Ignition Temperature (°C) 290 Flash Point (°C) 32 Lower explosivity limit (LEL) (volume %) 1.5 Upper explosivity limit (UEL) (volume %) 9.4
### Behaviour at sea
### Additional data
Colour colourless Odour strong fish odour
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Family name aliphatic amines
### Reactivity data
Acid(s) Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TLV-TWA 10 10 min 30 min 60 min 4 hrs 8 hrs AEGL-1 (ppm) 1.8 1.8 1.8 1.8 1.8 AEGL-2 (ppm) 11 11 8.6 5.4 2.7 AEGL-3 (ppm) 38 38 30 19 9.5
### Ecotoxicity
# CYCLOPENTANE
UN Number: 1146 - CAS Number: 287-92-3
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1146 CAS number 287-92-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 740 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 70.1 Density of gas (kg/m3) 3.1 Boiling Point (°C) 49 Melting Point (°C) -94 Vapour Pressure (Pa) 33500 [Pa] at a temperature of 20°C Ignition Temperature (°C) 380 Flash Point (°C) -38 Lower explosivity limit (LEL) (volume %) 1.1 Upper explosivity limit (UEL) (volume %) 8.7
### Behaviour at sea
### Additional data
Colour colourless Odour mild sweet
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 31 State liquid Temperature (°C) ambient Family name paraffins IMO class 3.1
### Reactivity data
Water No Acid(s) No Base(s) No Static electricity Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TLV-TWA 600 TEEL-1 (mg/m3) 1800 ppm TEEL-2 (mg/m3) 3840 ppm TEEL-3 (mg/m3) 15000 ppm
### Ecotoxicity
# CYCLOPENTENE
UN Number: 2246 - CAS Number: 142-29-0
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2246 CAS number 142-29-0
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 800 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 68.12 Density of gas (kg/m3) 3.1 Boiling Point (°C) 44 Melting Point (°C) -93 Vapour Pressure (Pa) 40000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 395 Flash Point (°C) -30 Lower explosivity limit (LEL) (volume %) 1.5
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 30 State liquid Temperature (°C) refrigerate Family name olefins IMO class 3.1
### Reactivity data
Water No Acid(s) Yes Static electricity Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 0 - Not irritating Specific Health Concern (D3) A - Aspiration Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# CYMENES (ortho, meta, para)
UN Number: 2046
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2046
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 857 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 134.2 Density of gas (kg/m3) 6.063 Boiling Point (°C) 177 Melting Point (°C) -68 Vapour Pressure (Pa) 688840 [Pa] at a temperature of 20°C Ignition Temperature (°C) 435 Flash Point (°C) 47 Lower explosivity limit (LEL) (volume %) 0.7 Upper explosivity limit (UEL) (volume %) 5.6
### Behaviour at sea
### Additional data
Colour colourless Odour mild pleasant odour Marine pollutant P
### Transportation data
Package group III Cargo group 32 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aromatic hydrocarbons IMO class 3.3
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# CYPERMETHRIN
UN Number: 2588
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2588
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1250 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 416.3 Boiling Point (°C) 220 Melting Point (°C) 60/80 Vapour Pressure (Pa) <10000 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Marine pollutant P
### Transportation data
Package group I/II/III State solid IMO class 6.1
### Reactivity data
Water No Base(s) Yes Metal(s) and alloys No
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# DDT
UN Number: 2761 Also known as: AGRITAN, ANOFEX, ARKOTINE, AZOTOX, BOVIDERMOL, CHLOROPHENOTHAN, CHLOROPHENOTHANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2761
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1560 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 354.5
### Behaviour at sea
Persistence (days) 2.7
### Additional data
Colour colourless Odour odourless Marine pollutant P Standard behavior classification D, SD, S
### Transportation data
Package group III State solid IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.06 TEEL-3 (mg/m3) 500
### Ecotoxicity
# DECAHYDRONAPHTHALENE
UN Number: 1147 - CAS Number: 91-17-8 Also known as: BICYCLO (4,4,0) DECANE, DEC (T), DECALIN (T), DEKALIN (T)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1147 CAS number 91-17-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 890 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 138.2 Density of gas (kg/m3) 6.192 Boiling Point (°C) 195 Melting Point (°C) -31 Vapour Pressure (Pa) 130 [Pa] at a temperature of 20°C Ignition Temperature (°C) 250 Flash Point (°C) 56 Lower explosivity limit (LEL) (volume %) 0.7 Upper explosivity limit (UEL) (volume %) 5.4
### Behaviour at sea
### Additional data
Colour colourless Odour turpentine odour
### Transportation data
Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient IMO class 3.3
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
TLV-TWA 25 TEEL-1 (mg/m3) 1.5 ppm TEEL-2 (mg/m3) 10 ppm TEEL-3 (mg/m3) 75 ppm
### Ecotoxicity
# DECALDEHYDE
UN Number: 3082 - CAS Number: 143-08-8 Also known as: CAPRALDEHYDE, CAPRIC ALDEHYDE, 1-DECANAL, n-DECANAL, 1-DECYL ALDEHYDE, 1, Nonanol, N-Nonyl Alcohol, Nonanol
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082 CAS number 143-08-8 Formula C 9 H 2 0 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 830 [Kg/m³] at a temperature of 20°C 838.3 [Kg/m³] at a temperature of 5°C 834.8 [Kg/m³] at a temperature of 10°C 829.1 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 14.142 [cSt] at a temperature of 20°C 11.014 [cSt] at a temperature of 25°C 18.192 [cSt] at a temperature of 5°C 22.484 [cSt] at a temperature of 10°C 14.944 [cSt] at a temperature of 20°C Molar mass (g/mol) 145.3 Density of gas (kg/m3) 6.94 Solubility (g/L) 0.14 [g/L] at a temperature of 25°C and salinity of 0‰ 130 [g/L] at a temperature of 20°C and salinity of 0‰ 120 [g/L] at a temperature of 20°C and salinity of 5‰ 94 [g/L] at a temperature of 20°C and salinity of 30‰ Boiling Point (°C) 209 Melting Point (°C) -5 Critical molar volume (m³/mol) 0.000572 Critical temperature (°C) 670.7 Critical pressure (Pa) 2528000 Surface tension (mN/m) 27.89 [mN/m] at a temperature of 25°C 28.91 [mN/m] at a temperature of 5.7°C 28.02 [mN/m] at a temperature of 11.2°C 27.8 [mN/m] at a temperature of 18.8°C Vapour Pressure (Pa) 29 [Pa] at a temperature of 20°C Vapor enthalpy (J/Kg) 532810 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 41198164 Specific heat capacity (J/(Kg·K)) 2470 Henry's constant (mol/(m³·Pa)) 3.14
### Behaviour at sea
Log kow 4.26 Log koc 2.46 Biodegradation in estuary environment (Half- life) (days) Not hydrolysable Bioconcentration factor (BCF) 160
### Additional data
Colour colourless to light yellow Odour pleasant odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Cargo group 19 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aldehydes
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 7.5 ppm TEEL-2 (mg/m3) 50 ppm TEEL-3 (mg/m3) 250 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 25 Lowest median lethal concentration (LC50) on fishes (mg/l) 5.7 Assessment factor (AF) 50 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 8 [µg/l] on the Short term
# DECANE
UN Number: 2247 - CAS Number: 124-18-5 Also known as: n-ALKANES (C10+), n-DECANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2247 CAS number 124-18-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 730 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 142.29 Density of gas (kg/m3) 6.32 Boiling Point (°C) 174 Melting Point (°C) -30 Vapour Pressure (Pa) 52 [Pa] at a temperature of 20°C Ignition Temperature (°C) 210 Flash Point (°C) 46 Lower explosivity limit (LEL) (volume %) 0.82 Upper explosivity limit (UEL) (volume %) 5.4
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification F/FD
### Transportation data
Package group III Cargo group 31 State liquid Temperature (°C) ambient Family name paraffins IMO class 3.3
### Reactivity data
Water No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
TEEL-1 (mg/m3) 0.2 ppm TEEL-2 (mg/m3) 1.25 ppm TEEL-3 (mg/m3) 5000 ppm
### Ecotoxicity
# DECANOIC ACID
CAS Number: 334-48-5 Also known as: ACIDE DECANOIQUE, n-CAPRIC ACID, CAPRINIC ACID, n-DECANOIC ACID, DECOIC ACID, n-DECYLIC ACID
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 334-48-5
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 893 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 172.27 Density of gas (kg/m3) 7.66 Boiling Point (°C) 268/270 Melting Point (°C) 31/32 Flash Point (°C) > 110
### Behaviour at sea
### Additional data
Colour white Odour rancid, unpleasant
### Transportation data
State solid Temperature (°C) ambient Family name organic acids
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# DECYL ACRYLATE
UN Number: 3082 - CAS Number: 2156-96-9 Also known as: ACRYLATE DE DECYLE, ACRYLIC ACID, DECYL ESTER, n-DECYL ACRYLATE, DECYL ACRYLATE, inhibited, DECYL PROP-2-ENOATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082 CAS number 2156-96-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 878 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 212.37 Density of gas (kg/m3) 9.42 (E) Boiling Point (°C) 263 Melting Point (°C) < 0 Flash Point (°C) 227
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification F/FE/E
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 14 State liquid Temperature (°C) ambient Family name acrylates
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes (Cu, Zn) Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 5 - Very highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# DECYLOXYTETRAHYDROTHIOPHENE DIOXIDE
Also known as: DIOXYDE DE DECYLOXYTETRAHYDROTHIOPHENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1030 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 276 Boiling Point (°C) > 150 Melting Point (°C) < 10 Vapour Pressure (Pa) < 10 [Pa] at a temperature of 20°C Flash Point (°C) 130
### Behaviour at sea
### Additional data
Colour yellow Odour odourless
### Transportation data
State liquid
### Reactivity data
Water No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# DEXTROSE solutions
CAS Number: 50-99-7 Also known as: COM SUGAR SOLUTION
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 50-99-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1200 (E) [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 180.2 Boiling Point (°C) > 100 Melting Point (°C) 146
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Cargo group 43 State liquid Temperature (°C) 54.4/62.7 Family name miscell. water solut.
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 0 - Is not a floater; and does not pose any known health hazards
### Human toxicity threshold
TEEL-1 (mg/m3) 1.25 TEEL-2 (mg/m3) 7.5 TEEL-3 (mg/m3) 500
### Ecotoxicity
# DI-(2-ETHYLHEXYL)ADIPATE
CAS Number: 103-23-1 Also known as: ADIPATE DE DI-(2-ETHYLHEXYL), ADIPIC ACID, BIS(2-ETHYLHEXYL)ESTER, BIS(2-ETHYLHEXYL)ADIPATE, Adipic Acid, Bis(2-Ethylhexyl) Ester, Bis(2-Ethylhexyl) Hexanedioate, Di(2-Ethylhexyl)Adipate, Di-2-Ethylhexyl Adipate, Dioctyl Adipate, Hexanedioic Acid, Bis(2-Ethylhexyl) Ester, Hexanedioic Acid, Dioctyl Ester, Deha, Adipic Acid, Di-2-Ethylhexyl Ester, Bis(Ethyl-2-Hexyl) Adipate, Doa, Bis(2-Ethylhexyl) Adipate, Adipate De Di-2-Ethylhexyle
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 103-23-1 Formula C 2 2 H 4 2 O 4
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 923 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 14.2 [cSt] at a temperature of 20°C Molar mass (g/mol) 370.58 Density of gas (kg/m3) 16.51 Solubility (g/L) 1 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 417 Melting Point (°C) -67.8 Surface tension (mN/m) 30.2 [mN/m] at a temperature of 20°C Flash Point (°C) 204 Flash Point (Pensky-Martens closed cup) (°C) 196 Combus enthalpy (J/Kg) 33600000 Combustion efficiency (%) 96 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.02 Rad fraction (%) 23 Henry's constant (mol/(m³·Pa)) 0.04
### Behaviour at sea
Log kow 8.1 Log koc 5.78 Biodegradation in estuary environment (Half- life) (days) 1 Biodegradation in marine environment (Half-life) (days) 10 Bioconcentration factor (BCF) 27
### Additional data
Colour clear to straw coloured Odour odourless MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification F/FE/E
### Transportation data
Cargo group 34 State liquid Temperature (°C) ambient Family name esters
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 2 - Moderate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) > 1.4 Lowest median lethal concentration (LC50) on crustacean (mg/l) > 0.23 Lowest median lethal concentration (LC50) on fishes (mg/l) > 0.78 Highest no observed effect concentration (NOEC) on algae (mg/l) > 0.78 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.035 Assessment factor (AF) 100 on the Short term 100 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 2.3 [µg/l] on the Short term 0.35 [µg/l] on the Long term
# DI-(2-ETHYLHEXYL)PHOSPHORIC ACID
UN Number: 1902 - CAS Number: 298-07-7 Also known as: ACIDE DI-(2-ETHYLHEXYL)PHOSPHORIQUE, BIS(2-ETHYLHEXYL)HYDROGEN PHOSPHATE, BIS(2-ETHYLHEXYL)ORTHOPHOSPHATE, DEHPA, DI-(2-ETHYLHEXYL)PHOSPHATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1902 CAS number 298-07-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 977 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 322.4 Boiling Point (°C) decomp. Melting Point (°C) < -60 Vapour Pressure (Pa) < 100 [Pa] at a temperature of 20°C Flash Point (°C) 196
### Behaviour at sea
### Additional data
Colour light yellow Odour odourless
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) ambient
### Reactivity data
Water No Metal(s) and alloys Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 0.06 TEEL-2 (mg/m3) 0.4
### Ecotoxicity
# DI-(normal)-BUTYL AMINE
UN Number: 2248 Also known as: N-BUTYL-1-BUTANAMINE, DI-n-BUTYL AMINE, N-DIBUTYLAMINE, DNBA (T)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2248
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 759 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 129.25 Boiling Point (°C) 159 Vapour Pressure (Pa) 300 [Pa] at a temperature of 20°C Lower explosivity limit (LEL) (volume %) 1.1
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour colourless Odour weak ammonia, fish odour Standard behavior classification D, FED, FE
### Transportation data
Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 0.75 ppm TEEL-2 (mg/m3) 5 ppm TEEL-3 (mg/m3) 50 ppm
### Ecotoxicity
# DI-(normal)-BUTYL PHTHALATE
UN Number: 3082 Also known as: o-BENZENE DICARBOXYLIC ACID DIBUTYL ESTER, BENZENE-o-DICARBOXYLIC ACID DI-N-BUTYL ESTER, BUTYL PHTHALATE, CELLUFLEX DPB, DBP (T), DIBUTYL 1,2-BENZENE DICARBOXYLATE, DI-N-BUTYL PHTHALATE, DIBUTYL PHTHALATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1049 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 278.35 Boiling Point (°C) 335 Melting Point (°C) -35 Vapour Pressure (Pa) 446556 [Pa] at a temperature of 20°C Flash Point (°C) 180 Lower explosivity limit (LEL) (volume %) 0.5 Upper explosivity limit (UEL) (volume %) 2.5
### Behaviour at sea
Persistence (days) 1.9
### Additional data
Colour colourless Odour odourless
### Transportation data
Cargo group 34 State liquid Family name esters
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 800 TLV-TWA 0.4
### Ecotoxicity
# DI-n-BUTYL ETHER
UN Number: 1149 - CAS Number: 111-92-2 Also known as: BUTYL ETHER, n-BUTYL ETHER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1149 CAS number 111-92-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 800 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 130.2 Density of gas (kg/m3) 5.805 Boiling Point (°C) 142 Melting Point (°C) -95 Vapour Pressure (Pa) 600 [Pa] at a temperature of 20°C Ignition Temperature (°C) 175 Flash Point (°C) 22 Lower explosivity limit (LEL) (volume %) 0.9 Upper explosivity limit (UEL) (volume %) 8.5
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification FE
### Transportation data
Package group III Cargo group 41 State liquid Family name ethers IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Static electricity Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 3 ppm TEEL-2 (mg/m3) 20 ppm TEEL-3 (mg/m3) 400 ppm
### Ecotoxicity
# DI-n-HEXYL ADIPATE
CAS Number: 110-33-8 Also known as: ADIPATE DE DI-n-HEXYLE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 110-33-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 939 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 155.07 Boiling Point (°C) > 200 Melting Point (°C) -11 Vapour Pressure (Pa) 500 [Pa] at a temperature of 20°C Flash Point (°C) 163
### Behaviour at sea
### Additional data
Colour colourless Odour mild, ester-like Standard behavior classification FE/F
### Transportation data
Cargo group 34 State liquid Temperature (°C) ambient Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 5 - Very highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
### Ecotoxicity
# DI-tertiary-BUTYL PEROXIDE
UN Number: 2102
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2102
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 800 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 146.2 Density of gas (kg/m3) 6.579 Boiling Point (°C) 80 Melting Point (°C) -30 Vapour Pressure (Pa) 2800 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Standard behavior classification FE
### Transportation data
Package group II State liquid IMO class 5.2
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# DIACETONE ALCOHOL
UN Number: 1148 Also known as: DIACETONE, DIACETONE ALCOOL, DIKETONE ALCOHOL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1148
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 938 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 116.16 Density of gas (kg/m3) 1.806 Boiling Point (°C) 169.4 Melting Point (°C) -47 Vapour Pressure (Pa) 140 [Pa] at a temperature of 20°C Ignition Temperature (°C) 640 Flash Point (°C) 58 Lower explosivity limit (LEL) (volume %) 1.8 Upper explosivity limit (UEL) (volume %) 6.9
### Behaviour at sea
### Additional data
Colour colourless to light yellow Odour mild pleasant odour
### Transportation data
Package group III Cargo group 20 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alcohols, glycols IMO class 3.2/3.3
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 2100 TLV-TWA 50 TEEL-1 (mg/m3) 50 ppm TEEL-2 (mg/m3) 50 ppm TEEL-3 (mg/m3) 1800 ppm
### Ecotoxicity
# DIBROMODIFLUOROMETHANE
UN Number: 1941
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1941
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 2270 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 209.8 Density of gas (kg/m3) 8.7 Boiling Point (°C) 22.8 Melting Point (°C) -101.1 Vapour Pressure (Pa) 83000 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
### Transportation data
Package group III State liquid IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# DIBROMOMETHANE
UN Number: 2664 - CAS Number: 74-95-3
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2664 CAS number 74-95-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 2497 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 173.83 Density of gas (kg/m3) 7.80 (E) Boiling Point (°C) 99 Melting Point (°C) -52 Vapour Pressure (Pa) 4650 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless to pale yellow Odour sweet, pleasant Standard behavior classification SD
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 36 State liquid Family name halogenated hydrocarbons IMO class 6.1
### Reactivity data
Water No Metal(s) and alloys Yes (Al, Mn, Zn)
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 30 ppm TEEL-2 (mg/m3) 200 ppm TEEL-3 (mg/m3) 1250 ppm
### Ecotoxicity
# DIBUTYL HYDROGEN PHOSPHONATE
Also known as: DIBUTYL HYDROGENPHOSPHITE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 980 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 194.21 Boiling Point (°C) 121 Melting Point (°C) < 0 Vapour Pressure (Pa) < 5000 [Pa] at a temperature of 20°C Flash Point (°C) 120
### Behaviour at sea
### Additional data
Colour colourless Odour mild
### Transportation data
State liquid
### Reactivity data
Water Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# DICHLOROBENZENE (ortho-)
UN Number: 1591
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1591
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1306 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 147.01 Density of gas (kg/m3) 6.54 Boiling Point (°C) 180 Melting Point (°C) -18 Vapour Pressure (Pa) 23328 [Pa] at a temperature of 20°C Ignition Temperature (°C) 640 Flash Point (°C) 66 Lower explosivity limit (LEL) (volume %) 2.2 Upper explosivity limit (UEL) (volume %) 9.2
### Behaviour at sea
### Additional data
Colour colourless Odour pleasant odour
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 36 State liquid Family name halogenated hydrocarb IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 1000 TLV-TWA 75 TEEL-1 (mg/m3) 50 ppm TEEL-2 (mg/m3) 50 ppm TEEL-3 (mg/m3) 200 ppm
### Ecotoxicity
# DICHLOROETHYLETHER
UN Number: 1916
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1916
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1220 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 143 Density of gas (kg/m3) 1.548 Boiling Point (°C) 178 Melting Point (°C) -52 Vapour Pressure (Pa) 1100 [Pa] at a temperature of 20°C Ignition Temperature (°C) 370 Flash Point (°C) 55
### Behaviour at sea
### Additional data
Colour colourless Odour sweet, pleasant odour
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 41 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name ethers IMO class 6.1
### Reactivity data
Acid(s) Yes
### GESAMP Hazard profile
Biodegradation (A2) NR - Not readily biodegradable
### Human toxicity threshold
IDHL 250 TEEL-1 (mg/m3) 10 ppm TEEL-2 (mg/m3) 25.7 ppm TEEL-3 (mg/m3) 100 ppm
### Ecotoxicity
# DICHLOROMETHANE
UN Number: 1593 - CAS Number: 75-09-2 Also known as: AEROTHANE MM (T), DCM, Dichloromethane, Methylene Dichloride, Methane Dichloride, Methylene Bichloride, Methylene Chloride
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1593 CAS number 75-09-2 Formula CH 2 Cl 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1322 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.32 [cSt] at a temperature of 20°C 0.31132 [cSt] at a temperature of 25°C Molar mass (g/mol) 84.93 Density of gas (kg/m3) 3.741 Solubility (g/L) 20000 [g/L] at a temperature of 20°C and salinity of 0‰ 16700 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 40 Melting Point (°C) -97 Critical temperature (°C) 510 Critical pressure (Pa) 6100000 Surface tension (mN/m) 28.33 [mN/m] at a temperature of 20°C 27.2 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 47000 [Pa] at a temperature of 20°C 58200 [Pa] at a temperature of 25°C Ignition Temperature (°C) 665 Lower explosivity limit (LEL) (volume %) 12 Upper explosivity limit (UEL) (volume %) 19 Vapor enthalpy (J/Kg) 330390 [J/Kg] at a temperature of 40°C 339338 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 6050000 Specific heat capacity (J/(Kg·K)) 1191.6 Combustion efficiency (%) 33 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.03 Rad fraction (%) 40 Henry's constant (mol/(m³·Pa)) 206
### Behaviour at sea
Log kow 1.3 Log koc 1.4 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) Not biodegradable Bioconcentration factor (BCF) 40
### Additional data
Colour colourless Odour sweet, pleasant odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification SD
### Transportation data
Package group III Cargo group 36 State liquid Family name halogenated hydrocarb IMO class 6.1
### Reactivity data
Notable risks On combustion, forms toxic and corrosive fumes Reacts with alkalis.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Specific Health Concern (D3) C - Carcinogenicity Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 5000 Hazard statements Health H351 Suspected of causing cancer. Precautionary statements Prevention P201 Obtain special instructions before use. P202 Do not handle until all safety precautions have been read and understood. P281 Use personal protective equipment as required. Response P308 + P313 IF exposed or concerned: Get medical advice/attention. Storage P405 Store locked up. Disposal P501 Dispose of contents/container to ... TLV-TWA 500 ERPG-1 (ppm) 300 ERPG-2 (ppm) 750 ERPG-3 (ppm) 4000
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 500 Lowest median lethal concentration (LC50) on crustacean (mg/l) 108.5 Lowest median lethal concentration (LC50) on fishes (mg/l) 97 Highest no observed effect concentration (NOEC) on algae (mg/l) 550 Highest no observed effect concentration (NOEC) on fishes (mg/l) 82.5 Assessment factor (AF) 50 on the Short term 50 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 1940 [µg/l] on the Short term 1650 [µg/l] on the Long term
# DICHLOROPROPENES
UN Number: 2047 - CAS Number: 8003-19-8
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2047 CAS number 8003-19-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1200 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 110.98 Density of gas (kg/m3) 4.64 Boiling Point (°C) 77 Melting Point (°C) -60 Vapour Pressure (Pa) 5598 [Pa] at a temperature of 20°C Flash Point (°C) 29 Lower explosivity limit (LEL) (volume %) 5.3 Upper explosivity limit (UEL) (volume %) 14.5
### Behaviour at sea
### Additional data
Colour colourless Odour sweet odour
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 15 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name substituted allyls IMO class 3.3
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# DICYCLOPENTADIENE
UN Number: 2048 - CAS Number: 77-73-6 Also known as: Dicyclopentadiene, Cyclopentadiene Dimer, Bicyclopentadiene, 1,3-Cyclopentadiene Dimer
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2048 CAS number 77-73-6 Formula C 1 0 H 1 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Solid Density (kg/m3) 978 [Kg/m³] at a temperature of 20°C 930.2 [Kg/m³] at a temperature of 35°C Kinematic viscosity (cSt) 0.79 [cSt] at a temperature of 21°C Molar mass (g/mol) 132.31 Density of gas (kg/m3) 5.934 Solubility (g/L) 20 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 170 Melting Point (°C) 32 Critical temperature (°C) 659.95 Critical pressure (Pa) 3060000 Vapour Pressure (Pa) 1300 [Pa] at a temperature of 20°C 1300 [Pa] at a temperature of 37.7°C Flash Point (°C) 104 Flash Point (Cleveland open cup) (°C) 32 Lower explosivity limit (LEL) (volume %) 0.8 Upper explosivity limit (UEL) (volume %) 6.3 Combus enthalpy (J/Kg) 43700000 Specific heat capacity (J/(Kg·K)) 1700 Henry's constant (mol/(m³·Pa)) 1084.2
### Behaviour at sea
Log kow 2.78 Log koc 3.18 Aqueous photolysis (Half-life) 32 Biodegradation in marine environment (Half-life) (days) Not biodegradable Bioconcentration factor (BCF) 100
### Additional data
Colour colourless Odour camphor odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification FE
### Transportation data
Package group III Cargo group 30 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name olefins IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
Hazard statements Physical H225 Highly flammable liquid and vapour. Health H302 Harmful if swallowed. H315 Causes skin irritation. H319 Causes serious eye irritation. H330 Fatal if inhaled. H335 May cause respiratory irritation. Environmental H411 Toxic to aquatic life with long lasting effects. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P243 Take precautionary measures against static discharge. P260 Do not breathe dust/fume/gas/mist/vapours/spray. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P330 Rinse mouth. P391 Collect spillage. ERPG-1 (ppm) 0.01 ERPG-3 (ppm) 75
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 27 Lowest median lethal concentration (LC50) on crustacean (mg/l) 8.0 Lowest median lethal concentration (LC50) on fishes (mg/l) 4.3 Highest no observed effect concentration (NOEC) on algae (mg/l) 18 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 3.2 Assessment factor (AF) 100 on the Short term 100 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 43 [µg/l] on the Short term 32 [µg/l] on the Long term
# DIETHANOLAMINE
CAS Number: 111-42-2 Also known as: BIS-2-HYDROXY ETHYLAMINE, DEA (T), DIETHYLALAMINE, DIETHYLAMINE, 2,2-DIHYDROXY, DIETHYLOLAMINE, 2,2-DIHYDROXYDIETHYL AMINE, DI (2-HYDROXY ETHYL) AMINE, DIOLAMINE, DIOLAMINE (T)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 111-42-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1095 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 105.14 Density of gas (kg/m3) 4.709 Boiling Point (°C) 268 Melting Point (°C) 28 Vapour Pressure (Pa) 1.3 [Pa] at a temperature of 20°C Ignition Temperature (°C) 660 Flash Point (°C) 138 Lower explosivity limit (LEL) (volume %) 1.6 Upper explosivity limit (UEL) (volume %) 10.8
### Behaviour at sea
### Additional data
Colour colourless, white Odour weak ammonia, dead fish
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alkanolamines
### Reactivity data
Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Specific Health Concern (D3) T - Specific Target Organ Toxicity following single or repeated exposure Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 150 TEEL-2 (mg/m3) 300 TEEL-3 (mg/m3) 300
### Ecotoxicity
# DIETHYL CARBONATE
UN Number: 2366 Also known as: CARBONATE D'ETHYLE, CARBONIC ACID, DIETHYL ESTER, DIATOL (T)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2366
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 975 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 118.13 Density of gas (kg/m3) 5.289 Boiling Point (°C) 127 Melting Point (°C) -43 Vapour Pressure (Pa) 1330 [Pa] at a temperature of 20°C Ignition Temperature (°C) 445 Flash Point (°C) 25 Lower explosivity limit (LEL) (volume %) 1.4 Upper explosivity limit (UEL) (volume %) 11
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour colourless Odour pleasant odour Standard behavior classification FE
### Transportation data
Package group III State liquid IMO class 3.3
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 7.5 ppm TEEL-2 (mg/m3) 60 ppm TEEL-3 (mg/m3) 300 ppm
### Ecotoxicity
# DIETHYL ETHER
UN Number: 1155 - CAS Number: 60-29-7 Also known as: DIETHYL OXIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1155 CAS number 60-29-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 714 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 74.12 Density of gas (kg/m3) 3.35 Boiling Point (°C) 34.8 Melting Point (°C) -116 Vapour Pressure (Pa) 59000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 170 Flash Point (°C) -45 Lower explosivity limit (LEL) (volume %) 1.85 Upper explosivity limit (UEL) (volume %) 36.5
### Behaviour at sea
### Additional data
Colour colourless Odour sweet odour Standard behavior classification ED
### Transportation data
Transport mode Bulk,Packaged State liquid Temperature (°C) ambient Pressure (Pa) under pressure IMO class 3.1
### Reactivity data
Static electricity Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 19000 TLV-TWA 400 TEEL-1 (mg/m3) 500 ppm TEEL-2 (mg/m3) 500 ppm TEEL-3 (mg/m3) 1900 ppm
### Ecotoxicity
# DIETHYL PHTHALATE
CAS Number: 84-66-2 Also known as: ANOZOL (T), 1,2-BENZENE DICARBOXYLIC ACID, DIETHYL- ESTER, DEP (T)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 84-66-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1120 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 222 Density of gas (kg/m3) 9.88 Boiling Point (°C) 298 Melting Point (°C) -44 Ignition Temperature (°C) 457 Flash Point (°C) 117 Lower explosivity limit (LEL) (volume %) 0.75
### Behaviour at sea
### Additional data
Colour white Odour mild chemical odour
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 3 - ≥100 and <500 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
TLV-TWA 0.5 TEEL-1 (mg/m3) 15 TEEL-2 (mg/m3) 100 TEEL-3 (mg/m3) 500
### Ecotoxicity
# DIETHYL SULPHATE
UN Number: 1594 - CAS Number: 64-67-5 Also known as: DIETHYL SULPHATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1594 CAS number 64-67-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1200 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 154.2 Density of gas (kg/m3) 6.84 Boiling Point (°C) 208 Melting Point (°C) -25 Vapour Pressure (Pa) 130 (47�C) [Pa] at a temperature of 20°C Ignition Temperature (°C) 436 Flash Point (°C) 104 Lower explosivity limit (LEL) (volume %) 4.1
### Behaviour at sea
### Additional data
Colour colourless Odour etheral, peppermint-like Standard behavior classification SD
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 34 State liquid Temperature (°C) ambient Family name esters IMO class 6.1
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Oxidizing agents Yes Combustibles Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 0.2 ppm TEEL-2 (mg/m3) 1.5 ppm TEEL-3 (mg/m3) 25 ppm
### Ecotoxicity
# DIETHYLAMINE
UN Number: 1154 - CAS Number: 109-89-7
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1154 CAS number 109-89-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 708 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 73.14 Density of gas (kg/m3) 3.264 Boiling Point (°C) 55 Melting Point (°C) -50 Vapour Pressure (Pa) 53320 [Pa] at a temperature of 20°C Ignition Temperature (°C) 310 Flash Point (°C) -20 Lower explosivity limit (LEL) (volume %) 1.8 Upper explosivity limit (UEL) (volume %) 10.1
### Behaviour at sea
### Additional data
Colour colourless Odour ammonia, fish odour Standard behavior classification DE
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Family name aliphatic amines IMO class 3.1
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 3C - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 2000 TLV-TWA 10 TEEL-1 (mg/m3) 15 ppm TEEL-2 (mg/m3) 75 ppm TEEL-3 (mg/m3) 200 ppm
### Ecotoxicity
# DIETHYLBENZENE
UN Number: 2049 - CAS Number: 25340-17-4 Also known as: DIETHYLBENZENES
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2049 CAS number 25340-17-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 860 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 134.21 Density of gas (kg/m3) 5.96 Boiling Point (°C) 180 Melting Point (°C) -57 Vapour Pressure (Pa) 133 [Pa] at a temperature of 20°C Ignition Temperature (°C) 423 Flash Point (°C) 56 Upper explosivity limit (UEL) (volume %) 12.8
### Behaviour at sea
### Additional data
Colour colourless Odour sweet, gasoline odour
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 32 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aromatic hydrocarbons IMO class 3.3
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
ERPG-1 (ppm) 10 ERPG-2 (ppm) 100 ERPG-3 (ppm) 500
### Ecotoxicity
# DIETHYLENE GLYCOL
CAS Number: 111-46-6 Also known as: CELLOSOHE (T), DEG (T), DICOL (T), DIGLYCOL, DIHYDROXYDIETHYL ETHER, 2,2'-Oxybisethanol, 2,2'-Oxydiethanol, Bis(2-Hydroxyethyl) Ether, Ethanol, 2,2'-Oxybis-, 2-Hydroxyethyl Ether, Diethylene Glycol
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 111-46-6 Formula C 4 H 1 0 O 3
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1118 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 32.2 [cSt] at a temperature of 20°C 32.2 [cSt] at a temperature of 25°C Molar mass (g/mol) 106.12 Density of gas (kg/m3) 4.72 Solubility (g/L) 1120000 [g/L] at a temperature of 20°C and salinity of 0‰ 1120000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 245 Melting Point (°C) -6 Critical temperature (°C) 750 Critical pressure (Pa) 4700000 Surface tension (mN/m) 45.21 [mN/m] at a temperature of 20°C 44.77 [mN/m] at a temperature of 25°C Ignition Temperature (°C) 225 Flash Point (°C) 124 Flash Point (Pensky-Martens closed cup) (°C) 124 Lower explosivity limit (LEL) (volume %) 1.6 Upper explosivity limit (UEL) (volume %) 10.8 Vapor enthalpy (J/Kg) 492745 [J/Kg] at a temperature of 246°C Combus enthalpy (J/Kg) 20300000 Specific heat capacity (J/(Kg·K)) 2306.4 Combustion efficiency (%) 98 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.02 Rad fraction (%) 22 Henry's constant (mol/(m³·Pa)) 0
### Behaviour at sea
Log kow -1.47 Log koc 0.55 Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 1
### Additional data
Colour colourless Odour odourless MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment.
### Transportation data
Cargo group 40 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name glycol ethers
### Reactivity data
Abilities Miscible in water. Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
Hazard statements Health H302 Harmful if swallowed. H373 May cause damage to organs through prolonged or repeated exposure, exposure cause the hazard: TLV-TWA 100 TEEL-1 (mg/m3) 40 ppm TEEL-2 (mg/m3) 200 ppm TEEL-3 (mg/m3) 200ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) > 1000 Lowest median lethal concentration (LC50) on crustacean (mg/l) 48900 Lowest median lethal concentration (LC50) on fishes (mg/l) 77900 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 8590 Highest no observed effect concentration (NOEC) on fishes (mg/l) 15380 Assessment factor (AF) 1000 on the Short term 10000 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 1000 [µg/l] on the Short term 100 [µg/l] on the Long term
# DIETHYLENE GLYCOL DI-n-BUTYL ETHER
CAS Number: 112-73-2 Also known as: BIS(2-BUTOXYETHYL)ETHER, BUTYLDIGLYME, 2,2'-DIBUTOXYETHYL ETHER, DIBUTYL CARBITOL, DIETHYLENE GLYCOL DIBUTYL ETHER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 112-73-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 885 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 218.34 Density of gas (kg/m3) > 1.29 Boiling Point (°C) 256 Melting Point (°C) -60 Flash Point (°C) 48
### Behaviour at sea
### Additional data
Colour colourless Odour characteristic Standard behavior classification F/FD/D
### Transportation data
Cargo group 40 State liquid Temperature (°C) ambient Family name glycol ethers
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
### Ecotoxicity
# DIETHYLENE GLYCOL DIETHYL ETHER
CAS Number: 112-36-7 Also known as: DETHYL CARBITOL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 112-36-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 900 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 162.2 Density of gas (kg/m3) 7.22 Boiling Point (°C) 188 Melting Point (°C) -44 Vapour Pressure (Pa) 70 [Pa] at a temperature of 20°C Ignition Temperature (°C) 205 Flash Point (°C) 82
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Cargo group 40 State liquid Family name glycol ethers
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 250 TEEL-2 (mg/m3) 500 TEEL-3 (mg/m3) 500
### Ecotoxicity
# DIETHYLENE GLYCOL MONOBUTYL ETHER ACETATE
Also known as: ACETATE DE L'ETHER MONOBUTYLIQUE DU DIETHYLENE GLYCOL, 2-(2-BUTOXYETHOXY) ETHYL ACETATE, BUTYL CARBITOL ACETATE, DIGLYCOL MONOBUTYL ETHER ACETATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 985 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 204.3 Boiling Point (°C) 246 Melting Point (°C) -32 Vapour Pressure (Pa) 13 [Pa] at a temperature of 20°C Ignition Temperature (°C) 290 Flash Point (°C) 105 Lower explosivity limit (LEL) (volume %) 0.6 Upper explosivity limit (UEL) (volume %) 10.7
### Behaviour at sea
Persistence (days) 0.8
### Additional data
Colour colourless Odour mild odour Standard behavior classification D, FD, F
### Transportation data
Cargo group 34 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name esters
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# DIETHYLENE GLYCOL MONOMETHYL ETHER
Also known as: DIGLYCOL MONOMETHYL ETHER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 9900 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 134.2 Density of gas (kg/m3) 5.934 Boiling Point (°C) 194 Melting Point (°C) -65 Vapour Pressure (Pa) 13 [Pa] at a temperature of 20°C Ignition Temperature (°C) 215 Flash Point (°C) 91 Lower explosivity limit (LEL) (volume %) 1.6 Upper explosivity limit (UEL) (volume %) 16.1
### Behaviour at sea
### Additional data
Colour colourless Odour pleasant odour
### Transportation data
Cargo group 40 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name glycol ethers
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 0.35 ppm TEEL-2 (mg/m3) 0.35 ppm TEEL-3 (mg/m3) 0.35 ppm
### Ecotoxicity
# DIETHYLENE GLYCOL PHTHALATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1150 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 254.23 Boiling Point (°C) > 240 Melting Point (°C) < -20 Vapour Pressure (Pa) < 4000 [Pa] at a temperature of 20°C Flash Point (°C) 93.3
### Behaviour at sea
### Additional data
Colour pale yellow Odour odourless Standard behavior classification S/SD
### Transportation data
Cargo group 34 State liquid Temperature (°C) ambient Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# DIETHYLENETRIAMINE
UN Number: 2079 - CAS Number: 111-40-0 Also known as: BIS(2-AMINOETHYL)AMINE, 2,2-DIAMINODIETHYLAMINE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2079 CAS number 111-40-0
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 954 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 103.17 Density of gas (kg/m3) 4.515 Boiling Point (°C) 207 Melting Point (°C) -39 Vapour Pressure (Pa) 50 [Pa] at a temperature of 20°C Ignition Temperature (°C) 395 Flash Point (°C) 102 Upper explosivity limit (UEL) (volume %) 10
### Behaviour at sea
### Additional data
Colour colourless to yellow Odour ammonia odour
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aliphatic amines
### Reactivity data
Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 1 ppm TEEL-2 (mg/m3) 1.25 ppm TEEL-3 (mg/m3) 100 ppm
### Ecotoxicity
# DIETHYLETHANOLAMINE
UN Number: 2686 Also known as: DIETHYLAMINOETHANOL, N-DIETHYLAMINOETHANOL, 2-DIETHYLAMINOETHANOL, beta-DIETHYLAMINOETHYLALCOHOL, DIETHYL(2-HYDROXYETHYL)AMINE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2686
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 900 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 117.2 Density of gas (kg/m3) 5.16 Boiling Point (°C) 161 Melting Point (°C) -70 Vapour Pressure (Pa) 190 [Pa] at a temperature of 20°C Ignition Temperature (°C) 320 Flash Point (°C) 60 Lower explosivity limit (LEL) (volume %) 6.7 Upper explosivity limit (UEL) (volume %) 11.7
### Behaviour at sea
### Additional data
Colour colourless Odour characteristic
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Family name alkanolamines
### Reactivity data
Acid(s) Yes Metal(s) and alloys Yes (light metals, Cu) Oxidizing agents Yes Combustibles Yes
### GESAMP Hazard profile
Biodegradation (A2) NR - Not readily biodegradable
### Human toxicity threshold
TLV-TWA 10 TEEL-1 (mg/m3) 10 ppm TEEL-2 (mg/m3) 20 ppm TEEL-3 (mg/m3) 100 ppm
### Ecotoxicity
# DIHEPTYL PHTHALATE
CAS Number: 3648-21-3
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 3648-21-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 988 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 362.51 Boiling Point (°C) 360 Melting Point (°C) -46 Flash Point (°C) 224
### Behaviour at sea
### Additional data
Colour white Odour odourless Standard behavior classification F/FE/E
### Transportation data
Cargo group 34 State liquid Temperature (°C) ambient Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# DIHEXYL PHTHALATE
CAS Number: 84-75-3 Also known as: 1,2-BENZENEDICARBOXYLIC ACID, DIHEXYL ESTER, DI-n-HEXYL PHTHALATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 84-75-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 995 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 334.5 Boiling Point (°C) > 210 (666 Pa) Melting Point (°C) -58 Flash Point (°C) 176
### Behaviour at sea
### Additional data
### Transportation data
Cargo group 34 State liquid Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 2 - Moderate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# DIISOBUTYL KETONE
UN Number: 1157 - CAS Number: 108-83-8 Also known as: DIBK (T), DIISOBUTYLCETONE, S-DIISOPROPYLACETONE, sym- DI ISOPROPYL ACETONE, 2,6-DIMETHYL-4-HEPTANONE, 2,6-DIMETHYL- HEPTAN-4-ONE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1157 CAS number 108-83-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 806 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 142.23 Density of gas (kg/m3) 2.451 Boiling Point (°C) 163 Melting Point (°C) -42 Vapour Pressure (Pa) 227 [Pa] at a temperature of 20°C Ignition Temperature (°C) 396 Flash Point (°C) 49 Lower explosivity limit (LEL) (volume %) 0.81 Upper explosivity limit (UEL) (volume %) 7.1
### Behaviour at sea
### Additional data
Colour colourless Odour mild sweet odour Standard behavior classification D, FD, F
### Transportation data
Package group III Cargo group 18 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name ketones IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 2000 TLV-TWA 25 TEEL-1 (mg/m3) 50 ppm TEEL-2 (mg/m3) 50 ppm TEEL-3 (mg/m3) 500 ppm
### Ecotoxicity
# DIISOBUTYL PHTHALATE
CAS Number: 84-69-5 Also known as: 1,2-BENZENE DICARBOXYLIC ACID, DI(-2-METHYLPROPYL)ESTER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 84-69-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1047 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 278.35 Density of gas (kg/m3) 12.37 Boiling Point (°C) 298 Melting Point (°C) -64 Vapour Pressure (Pa) 10 [Pa] at a temperature of 20°C Ignition Temperature (°C) 432 Flash Point (°C) 196 Lower explosivity limit (LEL) (volume %) 0.4
### Behaviour at sea
### Additional data
Colour colourless Odour slight ester
### Transportation data
Cargo group 34 State liquid Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 0 - Not irritating Specific Health Concern (D3) R - Reprotoxicity Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# DIISOBUTYLAMINE
UN Number: 2361 - CAS Number: 110-96-3 Also known as: N,N,-BIS(2-METHYLPROPYL)AMINE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2361 CAS number 110-96-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 745 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 129.25 Density of gas (kg/m3) 5.75 Boiling Point (°C) 139.5 Melting Point (°C) -70 Vapour Pressure (Pa) < 1475 [Pa] at a temperature of 20°C Ignition Temperature (°C) 290 Flash Point (°C) 29
### Behaviour at sea
### Additional data
Colour colourless Odour ammonia-like Standard behavior classification FED
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) ambient Family name aliphatic amines IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys Yes (Al, Cu, Zn) Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 0.6 ppm TEEL-2 (mg/m3) 4 ppm TEEL-3 (mg/m3) 20 ppm
### Ecotoxicity
# DIISOBUTYLENE
UN Number: 2050 - CAS Number: 11071-47-9
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2050 CAS number 11071-47-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 700 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 112.22 Density of gas (kg/m3) 5.16 Boiling Point (°C) 102 Melting Point (°C) -100 Vapour Pressure (Pa) 4826 [Pa] at a temperature of 20°C Ignition Temperature (°C) 305 Flash Point (°C) -5 Lower explosivity limit (LEL) (volume %) 0.9 (E)
### Behaviour at sea
### Additional data
Colour colourless Odour gasoline-like
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 30 State liquid Temperature (°C) ambient Family name olefins IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys Yes Static electricity Yes Oxidizing agents Yes Combustibles Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# DIISODECYL PHTHALATE
CAS Number: 26761-40-0 Also known as: 1,2-BENZENE DICARBOXYLIC ACID DILSODECYLESTER, BIS (ISO-DECYL) PHTHALATE, BIS (8-METHYL NONYL) ESTER, DI ALKYL (C7-C13) PHTHALATE, DISODECYL ESTER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 26761-40-0
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 967 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 446.7 Melting Point (°C) -50 Ignition Temperature (°C) 402 Flash Point (°C) 229 Lower explosivity limit (LEL) (volume %) 0.3 Upper explosivity limit (UEL) (volume %) 264
### Behaviour at sea
### Additional data
Colour colourless Odour weak odour
### Transportation data
Cargo group 34 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name esters
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# DIISONONYL ADIPATE
CAS Number: 33703-08-1 Also known as: ADIPATE DE DIISONONYLE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 33703-08-1
### Physical chemical data
Physical State (20°C) Liquid Molar mass (g/mol) 398.63
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Cargo group 34 State liquid Temperature (°C) ambient Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# Diisononyl Phthalate
CAS Number: 28553-12-0 Also known as: 1,2-Benzenedicarboxylic Acid, 1,2-Diisononyl Ester, Diisononyl Phthalate, Phtalate De Diisononyle
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 28553-12-0 Formula C 2 6 H 4 2 O 4
### Physical chemical data
Physical State (25°C) Liquid Kinematic viscosity (cSt) 82.47 [cSt] at a temperature of 20°C Molar mass (g/mol) 418.609 Solubility (g/L) 0.2 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 432 Melting Point (°C) -42 Flash Point (Pensky-Martens closed cup) (°C) 221 Henry's constant (mol/(m³·Pa)) 0.15
### Behaviour at sea
Log kow 9.37 Log koc 5.52 Biodegradation in estuary environment (Half- life) (days) 1242 Bioconcentration factor (BCF) 230
### Additional data
MARPOL pollution category Category Description Other Substances Substances which have been evaluated and found to fall outside Category X, Y or Z because they are considered to present no harm to marine resources, human health, amenities or other legitimate uses of the sea when discharged into the sea from tank cleaning of deballasting operations. The discharge of bilge or ballast water or other residues or mixtures containing these substances are not subject to any requirements of MARPOL Annex II.
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
Lowest median lethal concentration (LC50) on fishes (mg/l) 0.42 Highest no observed effect concentration (NOEC) on algae (mg/l) 1.8 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.004 Highest no observed effect concentration (NOEC) on fishes (mg/l) 75
# DIISOOCTYL ACID PHOSPHATE
UN Number: 1902
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1902
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 977 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 322.4
### Behaviour at sea
### Additional data
Colour light yellow Odour odourless
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 25 TEEL-2 (mg/m3) 150 TEEL-3 (mg/m3) 500
### Ecotoxicity
# DIISOPROPANOLAMINE
CAS Number: 110-97-4 Also known as: DIPA, DIPROPYL-2,2-DIHYDROXYAMINE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 110-97-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 990 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 133.19 Density of gas (kg/m3) 5.92 Boiling Point (°C) 248 Melting Point (°C) 42 Ignition Temperature (°C) 374 Flash Point (°C) 127 Lower explosivity limit (LEL) (volume %) 1.1 Upper explosivity limit (UEL) (volume %) 5.4
### Behaviour at sea
### Additional data
Colour colourless,white to yellow Odour ammonia, dead fish odour
### Transportation data
State liquid, solid Temperature (°C) ambient Pressure (Pa) ambient Family name alkanolamines
### Reactivity data
Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# DIISOPROPYL ETHER
UN Number: 1159 - CAS Number: 108-20-3 Also known as: DIISOPROPYL OXIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1159 CAS number 108-20-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 724 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 102.2 Density of gas (kg/m3) 7.095 Boiling Point (°C) 68 Melting Point (°C) -86 Vapour Pressure (Pa) 18000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 435 Flash Point (°C) -28 Upper explosivity limit (UEL) (volume %) 21
### Behaviour at sea
### Additional data
Colour colourless Odour sweet odour
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 41 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name ethers IMO class 3.1
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Static electricity Yes Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 10000 TLV-TWA 500 TEEL-1 (mg/m3) 310 ppm TEEL-2 (mg/m3) 310 ppm TEEL-3 (mg/m3) 1400 ppm
### Ecotoxicity
# DIISOPROPYLAMINE
UN Number: 1158 - CAS Number: 108-18-9 Also known as: DIPA
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1158 CAS number 108-18-9
### Physical chemical data
Density (kg/m3) 717 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 101.19 Density of gas (kg/m3) 4.5 Boiling Point (°C) 84 Melting Point (°C) -61 Vapour Pressure (Pa) 9331 [Pa] at a temperature of 20°C Ignition Temperature (°C) 275 Flash Point (°C) -15 Lower explosivity limit (LEL) (volume %) 0.8 Upper explosivity limit (UEL) (volume %) 7.1
### Behaviour at sea
### Additional data
Colour colourless Odour fish odour
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aliphatic amines IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Static electricity Yes Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 1000 TEEL-1 (mg/m3) 6 ppm TEEL-2 (mg/m3) 40 ppm TEEL-3 (mg/m3) 200 ppm
### Ecotoxicity
# DIMETHYL ACETAMIDE
CAS Number: 127-19-5 Also known as: ACETIC ACID, DIMETHYLAMIDE, DIMETHYLACETAMIDE, N,N-DIMETHYLACETAMIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 127-19-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 900 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 87.14 Density of gas (kg/m3) 3.87 Boiling Point (°C) 164 Melting Point (°C) -20 Vapour Pressure (Pa) 170 [Pa] at a temperature of 20°C Ignition Temperature (°C) 490 Flash Point (°C) 66 Upper explosivity limit (UEL) (volume %) 11.5
### Behaviour at sea
### Additional data
Colour colourless Odour weak fishy
### Transportation data
Cargo group 10 State liquid Temperature (°C) ambient Family name amides
### Reactivity data
Water Yes Acid(s) Yes Oxidizing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 300 TLV-TWA 10 TEEL-1 (mg/m3) 75 ppm TEEL-2 (mg/m3) 300 ppm TEEL-3 (mg/m3) 300 ppm
### Ecotoxicity
# DIMETHYL ADIPATE
CAS Number: 627-93-0 Also known as: ADIPATE DE DIMETHYLE, ADIPIC ACID, DIMETHYL ESTER, DIMETHYLHEXANEDIOATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 627-93-0
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1063 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 174.2 Density of gas (kg/m3) 7.74 Boiling Point (°C) 109/110 Vapour Pressure (Pa) 10 [Pa] at a temperature of 20°C Ignition Temperature (°C) 360 Flash Point (°C) 107 Lower explosivity limit (LEL) (volume %) 0.81 Upper explosivity limit (UEL) (volume %) 8.1
### Behaviour at sea
### Additional data
Colour colourless Odour sweet
### Transportation data
Cargo group 34 Temperature (°C) ambient Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# DIMETHYL GLUTARATE
CAS Number: 26717-67-9
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 26717-67-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1087 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 160.17 Density of gas (kg/m3) 7.12 Boiling Point (°C) 93/95 Flash Point (°C) 103
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Cargo group 34 Temperature (°C) ambient Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 2 - Irritating Specific Health Concern (D3) A - Aspiration Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# DIMETHYL HYDROGEN PHOSPHITE
CAS Number: 868-89-9 Also known as: DIMETHYL PHOSPHITE, DIMETHYLPHOSPHONATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 868-89-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1200 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 110.05 Density of gas (kg/m3) 4.89 Boiling Point (°C) 170/171 Melting Point (°C) <-60 Vapour Pressure (Pa) 135 [Pa] at a temperature of 20°C Ignition Temperature (°C) 237 Flash Point (°C) 70 Lower explosivity limit (LEL) (volume %) 5.8 Upper explosivity limit (UEL) (volume %) 38.1
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Cargo group 34 Temperature (°C) ambient Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
### Ecotoxicity
# DIMETHYL PHTHALATE
CAS Number: 131-11-3
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 131-11-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1190 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 194.2 Density of gas (kg/m3) 8.63 Boiling Point (°C) 284 Melting Point (°C) 5.5 Vapour Pressure (Pa) 800 [Pa] at a temperature of 20°C Ignition Temperature (°C) 491 Flash Point (°C) 146 Lower explosivity limit (LEL) (volume %) 0.9
### Behaviour at sea
### Additional data
Colour colourless to pale yellow Odour odourless Standard behavior classification SD
### Transportation data
Cargo group 34 Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
IDHL 248 TEEL-1 (mg/m3) 15 TEEL-2 (mg/m3) 75 TEEL-3 (mg/m3) 500
### Ecotoxicity
# DIMETHYL SUCCINATE
CAS Number: 106-65-0
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 106-65-0
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1117 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 146.14 Density of gas (kg/m3) 6.5 Boiling Point (°C) 200 Melting Point (°C) 18/19 Vapour Pressure (Pa) 41 [Pa] at a temperature of 20°C Ignition Temperature (°C) 365 Flash Point (°C) 85 Upper explosivity limit (UEL) (volume %) 8.5
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification S/SD/D
### Transportation data
Cargo group 34 Temperature (°C) ambient Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 10 ppm TEEL-2 (mg/m3) 75 ppm TEEL-3 (mg/m3) 350 ppm
### Ecotoxicity
# DIMETHYLAMINE 40% solution in water
UN Number: 1160 - CAS Number: 124-40-3
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1160 CAS number 124-40-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 900 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 45.1 (pure) Density of gas (kg/m3) 2.06 Boiling Point (°C) 54 Melting Point (°C) -37 Vapour Pressure (Pa) 28700 [Pa] at a temperature of 20°C Ignition Temperature (°C) 390 Flash Point (°C) -18 Lower explosivity limit (LEL) (volume %) 2.6 Upper explosivity limit (UEL) (volume %) 12.3
### Behaviour at sea
### Additional data
Colour colourless Odour dead fish Standard behavior classification DE
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Family name aliphatic amines IMO class 3.1
### Reactivity data
Water No Acid(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 500 ERPG-1 (ppm) 0.6 ERPG-2 (ppm) 100 ERPG-3 (ppm) 350
### Ecotoxicity
# DIMETHYLAMINE anhydrous
UN Number: 1032 - CAS Number: 124-40-3 Also known as: DMA, N-Methylmethanamine, Dimethylamine Solutions (40%), Solutions De Dimethylamine (40%)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1032 CAS number 124-40-3 Formula C 2 H 7 N
### Physical chemical data
Physical State (20°C) Gas Physical State (25°C) Liquid Density (kg/m3) 2.064 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 1.8994 [cSt] at a temperature of 20°C Molar mass (g/mol) 45.08 Density of gas (kg/m3) 2.064 Solubility (g/L) 10000000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 51.5 Melting Point (°C) -92 Vapour Pressure (Pa) 28708 [Pa] at a temperature of 20°C Ignition Temperature (°C) 400 Flash Point (°C) -18 Lower explosivity limit (LEL) (volume %) 2.8 Upper explosivity limit (UEL) (volume %) 14.4
### Behaviour at sea
Log kow -0.38
### Additional data
Colour colourless Odour ammonia, dead fish odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification GD
### Transportation data
Transport mode Gas,Packaged Ship type 2G,2PG State liq.compr.gas Temperature (°C) ambient Pressure (Pa) under pressure Family name aliphatic amines IMO class 2(2.1)
### Reactivity data
Water No Abilities Solution. Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 2000 Hazard statements Physical H224 Extremely flammable liquid and vapour. Health H302 Harmful if swallowed. H314 Causes severe skin burns and eye damage. H332 Harmful if inhaled. H335 May cause respiratory irritation. Environmental H412 Harmful to aquatic life with long lasting effects. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. Storage P410 + P403 Protect from sunlight. Store in a well-ventilated place. TLV-TWA 10 ERPG-1 (ppm) 0.6 ERPG-2 (ppm) 100 ERPG-3 (ppm) 350
### Ecotoxicity
# DIMETHYLCYCLOHEXYLAMINE
UN Number: 2264 Also known as: CYCLOHEXYLAMINE, N,N-DIMETHYL, n-DIMETHYLCYCLOHEXANAMINE, N,N-DIMETHYLCYCLOHEXYLAMINE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2264
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 849 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 127.23 Density of gas (kg/m3) 5.68 Boiling Point (°C) 162 Melting Point (°C) -60 Vapour Pressure (Pa) 400 [Pa] at a temperature of 20°C Ignition Temperature (°C) 215 Flash Point (°C) 42 Lower explosivity limit (LEL) (volume %) 3.6 Upper explosivity limit (UEL) (volume %) 19
### Behaviour at sea
### Additional data
Colour colourless Odour musky ammonia
### Transportation data
Transport mode Bulk,Packaged Package group II Temperature (°C) ambient Family name aliphatic amines
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Biodegradation (A2) NR - Not readily biodegradable
### Human toxicity threshold
### Ecotoxicity
# DIMETHYLETHANOLAMINE
UN Number: 2051 - CAS Number: 108-01-0 Also known as: DEANOL, 2-(DIMETHYLAMINO)ETHANOL, beta- DIMETHYLAMINOETHYLALCOHOL, N,N-DIMETHYL-N-(2-HYDROXYETHYL)AMINE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2051 CAS number 108-01-0
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 887 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 89.14 Density of gas (kg/m3) 4.13 Boiling Point (°C) 134.6 Melting Point (°C) -58.6 Vapour Pressure (Pa) < 700 [Pa] at a temperature of 20°C Ignition Temperature (°C) 295 Flash Point (°C) 41 Lower explosivity limit (LEL) (volume %) 1.6 Upper explosivity limit (UEL) (volume %) 11.9
### Behaviour at sea
### Additional data
Colour colourless Odour amine
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Family name alkanolamines
### Reactivity data
Water No Acid(s) Yes Metal(s) and alloys Yes (Cu, Zn) Oxidizing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 35 ppm TEEL-2 (mg/m3) 150 ppm TEEL-3 (mg/m3) 150 ppm
### Ecotoxicity
# DIMETHYLPOLYSILOXANE
Also known as: DIMETHICONE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 980 [Kg/m³] at a temperature of 20°C Melting Point (°C) -50 Flash Point (°C) >110
### Behaviour at sea
### Additional data
### Transportation data
State liquid
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 25 TEEL-2 (mg/m3) 150 TEEL-3 (mg/m3) 500
### Ecotoxicity
# DIMETHYLZINC
UN Number: 1370
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1370
### Physical chemical data
Physical State (20°C) Liquid Boiling Point (°C) -227
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) under pressure IMO class 4.2
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# DINITROPHENOLS dry or wetted (with <15 wt% water)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1683 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 184.1 Density of gas (kg/m3) 8.2
### Behaviour at sea
Persistence (days) 3.1
### Additional data
Colour yellow Odour sweet, musty odour
### Transportation data
State solid Temperature (°C) ambient IMO class 1.1 D
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles Yes Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 0.65 TLV-TWA 0.03
### Ecotoxicity
# DINITROSOBENZENE
UN Number: 406
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 406
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1580 [Kg/m³] at a temperature of 20°C
### Behaviour at sea
### Additional data
Standard behavior classification D, SD, S
### Transportation data
State solid IMO class 1.3 C
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# DINITROTOLUENE solid
UN Number: 2038 - CAS Number: 25321-14-6 Also known as: DINITROPHENYL METHANE, DINITROTOLUOL, DNT
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2038 CAS number 25321-14-6
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1379 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 182.1 Density of gas (kg/m3) 8.09 Boiling Point (°C) 250 Melting Point (°C) 70 Ignition Temperature (°C) 400 Flash Point (°C) 212
### Behaviour at sea
### Additional data
Colour yellow to red Odour weak odour
### Transportation data
Transport mode Bulk,Packaged Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 2 - Moderate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 26 TLV-TWA 0.2 TEEL-1 (mg/m3) 0.6 TEEL-2 (mg/m3) 12.5 TEEL-3 (mg/m3) 50
### Ecotoxicity
# DINITROTOLUENES molten
UN Number: 2038 - CAS Number: 25321-14-6 Also known as: DNT
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2038 CAS number 25321-14-6
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1259/1379 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 182.13 Density of gas (kg/m3) 8.1 Boiling Point (°C) decomp. Melting Point (°C) 60/70 Flash Point (°C) 207
### Behaviour at sea
### Additional data
Colour yellow to red Odour slight
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 42 State liquid Family name nitrocompounds IMO class 6.1
### Reactivity data
Water No Acid(s) No Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Reducing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 2 - Moderate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 0.6 TEEL-2 (mg/m3) 30 TEEL-3 (mg/m3) 50
### Ecotoxicity
# DINONYL PHTHALATE
CAS Number: 84-76-4 Also known as: DINONYL 1,2-BENZENEDICARBOXYLATE, DI-n-NONYL PHTHALATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 84-76-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 970 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 418.68 Density of gas (kg/m3) 18.62 Boiling Point (°C) 413 Flash Point (°C) 216
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification F/FE/E
### Transportation data
Cargo group 34 Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# DINOSEB
UN Number: 2779 Also known as: DINOSEB, DNBP
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2779
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1260 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 240.22 Melting Point (°C) 30/42 Flash Point (°C) 177
### Behaviour at sea
### Additional data
Colour orange to brown
### Transportation data
Package group I/II/III Cargo group 42 State solid Family name nitro compounds IMO class 6.1
### Reactivity data
Base(s) Yes Metal(s) and alloys Yes (mild steel)
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 2.5 TEEL-2 (mg/m3) 4.5 TEEL-3 (mg/m3) 10
### Ecotoxicity
# DIOCTYL ADIPATE
Also known as: ADIPATE DE DIOCTYLE, ADIPIC ACID BIS (2-ETHYL HEXYL ESTER), ADIPOL 2EH, BEHA, BIS (2-ETHYL HEXYL ADIPATE), DI-(2-ETHYL- HEXYL ADIPATE), DIOCTYL ADIPATE, DOA
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 928 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 371 Boiling Point (°C) 417 Melting Point (°C) -67.8 Vapour Pressure (Pa) 347 [Pa] at a temperature of 20°C Ignition Temperature (°C) 340 Flash Point (°C) 196 Lower explosivity limit (LEL) (volume %) 0.3 Upper explosivity limit (UEL) (volume %) 2.8
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification D, FED, FE
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 150 TEEL-2 (mg/m3) 500 TEEL-3 (mg/m3) 500
### Ecotoxicity
# DIOCTYL PHTHALATE
CAS Number: 117-84-0 Also known as: o-BENZENE DICARBOXYLIC ACID DIOCTYL ESTER, 1,2-BENZENE DICARBOXYLIC ACID DIOCTYL ESTER, CELLUFLEX DOP, DEHP, DIETHYL HEXYL PHTHALATE, DI-(2-ETHYL-HEXYL) PHTHALATE, DINOPOL NOP, DIOCTYL-o-BENZENE DICARBOXYLATE, DNOP, DOP, Bis(2-Ethylhexyl) Phthalate, Bis(2-Ethylhexyl)Phthalate, Diethylhexyl Phthalate, Bis(2-Ethylhexyl) 1,2-Benzenedicarboxylate, Di(2-Ethylhexyl)Phthalate, Di(2-Ethylhexyl) Orthophthalate, Dioctyl Phthalate, 1,2-Benzenedicarboxylic Acid, Bis(2-Ethylhexyl) Ester, Phthalic Acid, Bis(2-Ethylhexyl) Ester, Di-Sec-Octyl Phthalate
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 117-84-0 Formula C 2 4 H 3 8 O 4
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 980 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 82.4 [cSt] at a temperature of 20°C 59 [cSt] at a temperature of 25°C Molar mass (g/mol) 390.6 Solubility (g/L) 0 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 386 Melting Point (°C) 412 Critical temperature (°C) 835 Critical pressure (Pa) 1070000 Ignition Temperature (°C) 390 Flash Point (°C) 199 Flash Point (Pensky-Martens closed cup) (°C) 200 Flash Point (Cleveland open cup) (°C) 218 Lower explosivity limit (LEL) (volume %) 0.17 Combus enthalpy (J/Kg) 28200000 Specific heat capacity (J/(Kg·K)) 1804 Combustion efficiency (%) 70 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.03 Rad fraction (%) 30 Henry's constant (mol/(m³·Pa)) 4.43
### Behaviour at sea
Log kow 7.5 Log koc 6 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) Not biodegradable Bioconcentration factor (BCF) 2500
### Additional data
Colour colourless Odour weak odour MARPOL pollution category Category Description X Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a major hazard to either marine resources or human health and, therefore, justify the prohibition of the discharge into the marine environment.
### Transportation data
Cargo group 34 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name esters
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
Hazard statements Health H360 May damage fertility or the unborn child. Precautionary statements Prevention P201 Obtain special instructions before use. P281 Use personal protective equipment as required. Response P308 + P313 IF exposed or concerned: Get medical advice/attention. TLV-TWA 0.3 TEEL-1 (mg/m3) 10 TEEL-2 (mg/m3) 75 TEEL-3 (mg/m3) 500
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 0.511 Lowest median lethal concentration (LC50) on fishes (mg/l) 0.69 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 1 Highest no observed effect concentration (NOEC) on fishes (mg/l) 5
# DIOXANE
UN Number: 1165 - CAS Number: 123-91-1 Also known as: DIOXANNE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1165 CAS number 123-91-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1036 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 88.11 Density of gas (kg/m3) 3.87 Boiling Point (°C) 101 Melting Point (°C) 10 Vapour Pressure (Pa) 4100 [Pa] at a temperature of 20°C Ignition Temperature (°C) 375 Flash Point (°C) 12 Upper explosivity limit (UEL) (volume %) 22.5
### Behaviour at sea
### Additional data
Colour colourless Odour weak alcohol odour
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 41 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name ethers IMO class 3.2
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 2000 TLV-TWA 25 TEEL-1 (mg/m3) 17 ppm TEEL-2 (mg/m3) 320 ppm TEEL-3 (mg/m3) 760 ppm
### Ecotoxicity
# DIPENTENE
UN Number: 2052 - CAS Number: 138-86-3 Also known as: CAJEPUTENE, CINENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2052 CAS number 138-86-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 842 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 136.2 Density of gas (kg/m3) 6.321 Boiling Point (°C) 178 Melting Point (°C) -156 Vapour Pressure (Pa) 133 [Pa] at a temperature of 20°C Ignition Temperature (°C) 237 Flash Point (°C) 45 Lower explosivity limit (LEL) (volume %) 0.7 Upper explosivity limit (UEL) (volume %) 6.1
### Behaviour at sea
Persistence (days) 0.8
### Additional data
Colour colourless to light yellow Odour pleasant, lemon odour Standard behavior classification D, FD, F
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) ambient Pressure (Pa) ambient IMO class 3.3
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Specific Health Concern (D3) Ss - Skin Sensitization Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# DIPHENYL
UN Number: 3077 - CAS Number: 92-52-4 Also known as: BIBENZENE, BIPHENYL, 1,1'-BIPHENYL, DIPHENYLE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3077 CAS number 92-52-4
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 992 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 154.21 Density of gas (kg/m3) 6.85 Boiling Point (°C) 255 Melting Point (°C) 69/72 Ignition Temperature (°C) 540 Flash Point (°C) 113 Lower explosivity limit (LEL) (volume %) 0.6 Upper explosivity limit (UEL) (volume %) 5.8
### Behaviour at sea
### Additional data
Colour colourless to pale yellow Odour characteristic, aromatic
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 32 State solid Temperature (°C) ambient Family name aromatic hydrocarbons
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
IDHL 15.6 TLV-TWA 0.2
### Ecotoxicity
# DIPHENYL ETHER
UN Number: 3082 - CAS Number: 101-84-8 Also known as: BIPHENYL OXIDE, DIPHENYL ETHER, DIPHENYL OXIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082 CAS number 101-84-8
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1070 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 170.2 Density of gas (kg/m3) 7.482 Boiling Point (°C) 257 Melting Point (°C) 27 Ignition Temperature (°C) 610 Flash Point (°C) 115 Lower explosivity limit (LEL) (volume %) 0.8 Upper explosivity limit (UEL) (volume %) 1.5
### Behaviour at sea
### Additional data
Colour colourless Odour mild pleasant odour
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
TEEL-1 (mg/m3) 2 ppm TEEL-2 (mg/m3) 20 ppm TEEL-3 (mg/m3) 100 ppm
### Ecotoxicity
# DIPHENYLMETHANE-4,4'-DIISOCYANATE
UN Number: 2489 - CAS Number: 101-68-8 Also known as: DIISOCYANATE DE DIPHENYLMETHANE-4,4
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2489 CAS number 101-68-8
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1200 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 250.3 Boiling Point (°C) 392 Melting Point (°C) 37 Ignition Temperature (°C) 240 Flash Point (°C) 196
### Behaviour at sea
Persistence (days) 2.7
### Additional data
Colour white to light yellow Standard behavior classification D, SD
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 12 State solid Temperature (°C) -18� to 5� Pressure (Pa) under pressure Family name isocyanates
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 4 - High Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 10 TLV-TWA 0.02 ERPG-1 (ppm) 0.2 mg ERPG-2 (ppm) 2 mg ERPG-3 (ppm) 25 mg
### Ecotoxicity
# DIPROPYLAMINE
UN Number: 2383 - CAS Number: 142-84-7
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2383 CAS number 142-84-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 738 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 101.19 Density of gas (kg/m3) 4.386 Boiling Point (°C) 109 Melting Point (°C) -100 Vapour Pressure (Pa) 4212 [Pa] at a temperature of 20°C Ignition Temperature (°C) 316 Lower explosivity limit (LEL) (volume %) 1.8 Upper explosivity limit (UEL) (volume %) 9.3
### Behaviour at sea
### Additional data
Colour colourless Odour strong ammonia odour
### Transportation data
Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aliphatic amines IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 50 TEEL-2 (mg/m3) 350 TEEL-3 (mg/m3) 500
### Ecotoxicity
# DIPROPYLENE GLYCOL
CAS Number: 110-98-5 Also known as: 2,2'-DIHYDROXYDIPROPYL ETHER, 2,2-DIHYDROXY ISOPROPYL ETHER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 110-98-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1023 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 134.17 Density of gas (kg/m3) 2.103 Boiling Point (°C) 232 Melting Point (°C) -30 Ignition Temperature (°C) 37 Flash Point (°C) 446 Lower explosivity limit (LEL) (volume %) 2.2 Upper explosivity limit (UEL) (volume %) 12.6
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Cargo group 40 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name glycol ethers
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
### Ecotoxicity
# DITRIDECYL PHTHALATE
CAS Number: 119-06-2
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 119-06-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 951 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 530.8 Density of gas (kg/m3) 23.61 Boiling Point (°C) > 315.6 Melting Point (°C) < -37 Flash Point (°C) 254
### Behaviour at sea
### Additional data
Colour colourless Odour nearly odourless
### Transportation data
Cargo group 34 State liquid Temperature (°C) ambient Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# DODECYL ALCOHOL
CAS Number: 112-53-8 Also known as: DODECANOL, DODECANOL, 1-Dodecanol, Lauryl Alcohol, Dodecyl Alcohol, Alcool Dodecylique
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 112-53-8 Formula C 1 2 H 2 6 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 831 [Kg/m³] at a temperature of 20°C 830.9 [Kg/m³] at a temperature of 24°C Kinematic viscosity (cSt) 22.63 [cSt] at a temperature of 20°C Molar mass (g/mol) 186.33 Solubility (g/L) 1.9 [g/L] at a temperature of 20°C and salinity of 0‰ 4 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 259 Melting Point (°C) 24 Critical temperature (°C) 719.4 Critical pressure (Pa) 1994000 Surface tension (mN/m) 29.4 [mN/m] at a temperature of 24°C Ignition Temperature (°C) 275 Flash Point (°C) 127 Flash Point (Pensky-Martens closed cup) (°C) 127 Lower explosivity limit (LEL) (volume %) 0.6 Upper explosivity limit (UEL) (volume %) 5.1 Vapor enthalpy (J/Kg) 487297 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 39381108 Specific heat capacity (J/(Kg·K)) 2351 Henry's constant (mol/(m³·Pa)) 2.25
### Behaviour at sea
Log kow 5.3 Log koc 2.63 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 48
### Additional data
Colour colourless Odour sweet MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification F/FE/E
### Transportation data
Cargo group 20 Temperature (°C) ambient Family name alcohols, glycols
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
Hazard statements Health H319 Causes serious eye irritation. Environmental H400 Very toxic to aquatic life. H411 Toxic to aquatic life with long lasting effects. Precautionary statements Prevention P264 Wash ... thoroughly after handling. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P337 + P313 If eye irritation persists: Get medical advice/attention. P391 Collect spillage. Disposal P501 Dispose of contents/container to ... TEEL-2 (mg/m3) 7.5 TEEL-3 (mg/m3) 500
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 0.97 Lowest median lethal concentration (LC50) on crustacean (mg/l) 320 Lowest median lethal concentration (LC50) on fishes (mg/l) 894 Highest no observed effect concentration (NOEC) on algae (mg/l) 0.085 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 1 Assessment factor (AF) 50 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 0 [µg/l] on the Short term
# DODECYL METHACRYLATE
Also known as: METHACRYLATE DE DODECYLE, DODECYL-2-METHYL-2-PROPENOATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 868 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 254.42 Density of gas (kg/m3) 11.35 Melting Point (°C) -22.2 Flash Point (°C) > 110
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification F/FE/E
### Transportation data
Cargo group 14 State liquid Temperature (°C) ambient Family name acrylates
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Reducing agents Yes
### GESAMP Hazard profile
Biodegradation (A2) NR - Not readily biodegradable
### Human toxicity threshold
TEEL-1 (mg/m3) 15 ppm TEEL-2 (mg/m3) 100 ppm TEEL-3 (mg/m3) 500 ppm
### Ecotoxicity
# DODECYL XYLENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Density (kg/m3) 880 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 274.49 Boiling Point (°C) 299 Vapour Pressure (Pa) 666 (21�C) [Pa] at a temperature of 20°C Ignition Temperature (°C) high Flash Point (°C) 140
### Behaviour at sea
### Additional data
Standard behavior classification FE
### Transportation data
Cargo group 32 Family name aromatic hydrocarbons
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# Dodecylbenzene
CAS Number: 123-01-3 Also known as: 1-Phenyldodecane, Laurylbenzene, Dodecylbenzene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 123-01-3 Formula C 1 8 H 3 0
### Physical chemical data
Physical State (25°C) Liquid Molar mass (g/mol) 246.431 Solubility (g/L) 0.041 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 328 Melting Point (°C) 3 Flash Point (Pensky-Martens closed cup) (°C) 141 Vapor enthalpy (J/Kg) 351417 [J/Kg] at a temperature of 25°C Henry's constant (mol/(m³·Pa)) 91.1
### Behaviour at sea
Log kow 5.7 Log koc 5.26 Bioconcentration factor (BCF) 35
### Additional data
MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment.
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 0.009 Lowest median lethal concentration (LC50) on fishes (mg/l) 796
# DODECYLPHENOL
UN Number: 3145 - CAS Number: 27193-86-8 Also known as: p-DODECYLPHENOL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3145 CAS number 27193-86-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 940 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 262.44 Boiling Point (°C) 154/168 Vapour Pressure (Pa) 0.005 (25�C) [Pa] at a temperature of 20°C Flash Point (°C) 163
### Behaviour at sea
### Additional data
Colour straw coloured Odour phenolic Marine pollutant P
### Transportation data
Transport mode Bulk,Packaged Package group I/II/III Cargo group 21 Temperature (°C) ambient Family name phenols, cresols
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 25 TEEL-2 (mg/m3) 150 TEEL-3 (mg/m3) 500
### Ecotoxicity
# DOWTHERM
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1060 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 166 Density of gas (kg/m3) 6.837 Boiling Point (°C) 257 Melting Point (°C) 12 Vapour Pressure (Pa) 650 [Pa] at a temperature of 20°C Flash Point (°C) 401 Lower explosivity limit (LEL) (volume %) 0.8 Upper explosivity limit (UEL) (volume %) 3.3
### Behaviour at sea
### Additional data
Colour light to dark brown Odour fragrant odour Standard behavior classification D, SD, S
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# ENDRIN
UN Number: 2761
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2761
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1650 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 380.82 Melting Point (°C) 177 Lower explosivity limit (LEL) (volume %) 1.1
### Behaviour at sea
Persistence (days) 3.1
### Additional data
Colour colourless to tan Odour odourless Marine pollutant P
### Transportation data
Transport mode Bulk,Packaged State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 125 TLV-TWA 0.006 TEEL-1 (mg/m3) 0.3
### Ecotoxicity
# EPICHLOROHYDRIN
UN Number: 2023 - CAS Number: 106-89-8 Also known as: 1-CHLORO-2,3-EPOXYPROPANE, 3-CHLORO-1,2-EPOXYPROPANE, 2-(CHLOROMETHYL)-OXIRANE, CHLOROMETHYLOXIRANE, CHLOROPROPYLENE OXIDE, 1,2-Epoxy-3-Chloropropane, 2-(Chloromethyl)Oxirane, 3-Chloro-1,2-Propylene Oxide, Alpha-Epichlorohydrin, Ech, Epichlorohydrine, Epichlorohydrin, Epichlorhydrine, α-Epichlorohydrin
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2023 CAS number 106-89-8 Formula C 3 H 5 ClO
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1180 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.87 [cSt] at a temperature of 20°C 0.91 [cSt] at a temperature of 25°C Molar mass (g/mol) 92.53 Density of gas (kg/m3) 4.244 Solubility (g/L) 64000 [g/L] at a temperature of 20°C and salinity of 0‰ 65900 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 115.4 Melting Point (°C) -48 Critical molar volume (m³/mol) 0.000168 Surface tension (mN/m) 37 [mN/m] at a temperature of 20°C 36.36 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 1730 [Pa] at a temperature of 20°C 2200 [Pa] at a temperature of 25°C Ignition Temperature (°C) 416 Flash Point (°C) 34 Flash Point (Pensky-Martens closed cup) (°C) 31 Flash Point (Cleveland open cup) (°C) 37.8 Lower explosivity limit (LEL) (volume %) 3.8 Upper explosivity limit (UEL) (volume %) 21 Vapor enthalpy (J/Kg) 410000 [J/Kg] at a temperature of 115°C Combus enthalpy (J/Kg) 17700000 Specific heat capacity (J/(Kg·K)) 1422 Combustion efficiency (%) 55 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.04 Rad fraction (%) 35 Henry's constant (mol/(m³·Pa)) 2.8
### Behaviour at sea
Log kow 0.26 Log koc 1.85 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) Not biodegradable Bioconcentration factor (BCF) 0.66
### Additional data
Colour colourless Odour sweet, garlic odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Package group II Cargo group 17 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name epichlorohydrin IMO class 6.1
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Oxidizing agents Yes Notable risks Violent reactions. On combustion, forms toxic and corrosive fumes.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 3A - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 250 Hazard statements Physical H226 Flammable liquid and vapour. Health H301 Toxic if swallowed. H311 Toxic in contact with skin. H314 Causes severe skin burns and eye damage. H317 May cause an allergic skin reaction. H331 Toxic if inhaled. H350 May cause cancer. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P330 + P331 IF SWALLOWED: rinse mouth. Do NOT induce vomiting. P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P308 + P313 IF exposed or concerned: Get medical advice/attention. Storage P403 + P233 Store in a well-ventilated place. Keep container tightly closed. Disposal P501 Dispose of contents/container to ... ERPG-2 (ppm) 20 ERPG-3 (ppm) 100
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 24.2 Lowest median lethal concentration (LC50) on crustacean (mg/l) 8.87 Lowest median lethal concentration (LC50) on fishes (mg/l) 0.65 Highest no observed effect concentration (NOEC) on algae (mg/l) 10.7 Assessment factor (AF) 1000 on the Short term 5000 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 0.65 [µg/l] on the Short term 0.13 [µg/l] on the Long term
# ETHANE (compressed gas)
UN Number: 1035
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1035
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 1.342 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 30.07 Density of gas (kg/m3) 1.342 Boiling Point (°C) -8.4 Melting Point (°C) -183 Vapour Pressure (Pa) 3850000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 515 Lower explosivity limit (LEL) (volume %) 2.9 Upper explosivity limit (UEL) (volume %) 13
### Behaviour at sea
### Additional data
Colour colourless Odour mild gasoline odour
### Transportation data
Transport mode Gas,Packaged Cargo group 31 State liq.compr.gas Temperature (°C) -89� Pressure (Pa) under pressure Family name paraffins IMO class 2(2.1)
### Reactivity data
Water No Static electricity Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 3000 ppm TEEL-2 (mg/m3) 5000 ppm TEEL-3 (mg/m3) 25000 ppm
### Ecotoxicity
# ETHANE (refrigerated liquid)
UN Number: 1961
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1961
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 1.342 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 30.07 Density of gas (kg/m3) 1.342 Boiling Point (°C) -8.4 Melting Point (°C) -183 Vapour Pressure (Pa) 3850000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 515 Lower explosivity limit (LEL) (volume %) 2.9 Upper explosivity limit (UEL) (volume %) 13.1
### Behaviour at sea
### Additional data
Colour colourless Odour mild gasoline odour
### Transportation data
Transport mode Gas,Packaged Ship type 2G Cargo group 31 State liquefied gas Temperature (°C) -89� Pressure (Pa) under pressure Family name paraffins IMO class 2(2.1)
### Reactivity data
Water No
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 3001 ppm TEEL-2 (mg/m3) 5001 ppm TEEL-3 (mg/m3) 25001 ppm
### Ecotoxicity
# ETHANOL
UN Number: 1170 - CAS Number: 64-17-5 Also known as: ABSOLUTE ALCOHOL, AETHANOL, ALCOHOL, ALGRAIN, ANHYDOL, COLOGNE SPIRIT, Anhydrous Ethanol, Ethanol Denatured, Ethyl Alcohol, Ethyl Hydrate, Ethyl Hydroxide, Fermentation Alcohol, Grain Alcohol, 1-Hydroxyethane, Methyl Carbinol, Ethyl Alcohol Anhydrous, Absolute Ethanol, Alcohol, Anhydrous, Denaturated Ethanol, Ethanol
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1170 CAS number 64-17-5 Formula C 2 H 6 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 790 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 1.51 [cSt] at a temperature of 20°C 1.36 [cSt] at a temperature of 25°C Molar mass (g/mol) 46.07 Density of gas (kg/m3) 2.064 Solubility (g/L) 790000 [g/L] at a temperature of 20°C and salinity of 0‰ 790000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 78.5 Melting Point (°C) -81 Critical molar volume (m³/mol) 0.000168 Critical temperature (°C) 514 Critical pressure (Pa) 6137000 Surface tension (mN/m) 22.4 [mN/m] at a temperature of 20°C 21.97 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 5875 [Pa] at a temperature of 20°C 7906 [Pa] at a temperature of 25°C Ignition Temperature (°C) 425 Flash Point (°C) 19 Flash Point (Pensky-Martens closed cup) (°C) 13 Lower explosivity limit (LEL) (volume %) 3.3 Upper explosivity limit (UEL) (volume %) 19 Vapor enthalpy (J/Kg) 794009 [J/Kg] at a temperature of 78.3°C 918602 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 26800000 Specific heat capacity (J/(Kg·K)) 2437.6 Combustion efficiency (%) 99 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.03 Rad fraction (%) 40 Henry's constant (mol/(m³·Pa)) 0.5
### Behaviour at sea
Log kow -0.32 Log koc 1.27 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 10 Bioconcentration factor (BCF) 3.16
### Additional data
Colour colourless Odour alcohol odour MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment.
### Transportation data
Package group II/III Cargo group 20 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alcohols, glycols IMO class 3.2/3.3
### Reactivity data
Abilities Miscible in water. Acid(s) Yes Base(s) Yes Static electricity Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 3300 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H319 Causes serious eye irritation. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P233 Keep container tightly closed. P240 Ground/bond container and receiving equipment. P241 Use explosion- proof electrical/ventilating/lighting/.../equipment. P242 Use only non-sparking tools. P243 Take precautionary measures against static discharge. P264 Wash ... thoroughly after handling. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P337 + P313 If eye irritation persists: Get medical advice/attention. P370 + P378 In case of fire: Use ... for extinction. Storage P403 + P233 Store in a well-ventilated place. Keep container tightly closed. Disposal P501 Dispose of contents/container to ... TLV-TWA 1000 TEEL-1 (mg/m3) 3000 ppm TEEL-2 (mg/m3) 3300 ppm TEEL-3 (mg/m3) 3300 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 1000 Lowest median lethal concentration (LC50) on crustacean (mg/l) 695 Lowest median lethal concentration (LC50) on fishes (mg/l) 11200 Highest no observed effect concentration (NOEC) on algae (mg/l) 280 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 9.6 Assessment factor (AF) 500 on the Short term 500 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 1390 [µg/l] on the Short term 19.2 [µg/l] on the Long term
# ETHANOLAMINE pure or solutions
UN Number: 2491 - CAS Number: 141-43-5 Also known as: 2-AMINOETHANOL, beta-AMINO ETHYL ALCOHOL, COLAMINE, 2-Aminoethol, β-Aminoethyl Alcohol, Ethyloamine, β-Hydroxyethylamine, Monoethanolamine, Mea, Ethanolamine, Beta-Aminoethyl Alcohol, Beta- Hydroxyethylamine
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2491 CAS number 141-43-5 Formula C 2 H 7 NO
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1016 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 18.61 [cSt] at a temperature of 25°C Molar mass (g/mol) 61.08 Density of gas (kg/m3) 2.709 Solubility (g/L) 100000 [g/L] at a temperature of 20°C and salinity of 0‰ 100000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 170 Melting Point (°C) 10 Critical temperature (°C) 671 Critical pressure (Pa) 8000000 Surface tension (mN/m) 48.32 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 64 [Pa] at a temperature of 20°C Ignition Temperature (°C) 410 Flash Point (°C) 85 Flash Point (Pensky-Martens closed cup) (°C) 86 Lower explosivity limit (LEL) (volume %) 5.5 Upper explosivity limit (UEL) (volume %) 17 Vapor enthalpy (J/Kg) 815775 [J/Kg] at a temperature of 171°C Combus enthalpy (J/Kg) 24900000 Specific heat capacity (J/(Kg·K)) 3201 Henry's constant (mol/(m³·Pa)) 0.003
### Behaviour at sea
Log kow -1.31 Log koc 0.07 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 3.2
### Additional data
Colour colourless Odour weak ammonia odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Package group III State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alkanolamines
### Reactivity data
Water No Abilities Miscible in water. Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 1000 Hazard statements Health H302 Harmful if swallowed. H312 Harmful in contact with skin. H314 Causes severe skin burns and eye damage. H332 Harmful if inhaled. H335 May cause respiratory irritation. Environmental H412 Harmful to aquatic life with long lasting effects. Precautionary statements Prevention P273 Avoid release to the environment. Disposal P501 Dispose of contents/container to ... TEEL-1 (mg/m3) 6 ppm TEEL-2 (mg/m3) 30 ppm TEEL-3 (mg/m3) 30 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 140 Lowest median lethal concentration (LC50) on fishes (mg/l) 150 Highest no observed effect concentration (NOEC) on algae (mg/l) 1 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.85 Highest no observed effect concentration (NOEC) on fishes (mg/l) 1.24 Assessment factor (AF) 100 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 9 [µg/l] on the Short term
# ETHOPROPHOS
UN Number: 3018
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3018
### Physical chemical data
Physical State (20°C) Liquid Molar mass (g/mol) 254.31 Boiling Point (°C) 90 Melting Point (°C) -13 Vapour Pressure (Pa) 0.046 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour pale yellow
### Transportation data
Package group I/II/III IMO class 6.1
### Reactivity data
Water No
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 0.75 TEEL-3 (mg/m3) 15
### Ecotoxicity
# ETHYL ACETATE
UN Number: 1173 - CAS Number: 141-78-6 Also known as: ACETATE D'ETHYLE, ACETIC ESTER, ACETIC ETHER, ACETIDIN, ACETOXYETHANE, AETHYL ACETAT, Acetic Acid, Ethyl Ester, Ethyl Acetic Ester, Ethyl Ethanoate, Ethyl Acetate, Acetate D’Ethyle
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1173 CAS number 141-78-6 Formula C 4 H 8 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 902 [Kg/m³] at a temperature of 20°C 918.1 [Kg/m³] at a temperature of 5°C 911.9 [Kg/m³] at a temperature of 10°C 902 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.49 [cSt] at a temperature of 25°C 1.7754 [cSt] at a temperature of 5°C 1.7875 [cSt] at a temperature of 10°C 1.7627 [cSt] at a temperature of 20°C Molar mass (g/mol) 88.11 Density of gas (kg/m3) 3.87 Solubility (g/L) 86000 [g/L] at a temperature of 20°C and salinity of 0‰ 54390 [g/L] at a temperature of 20°C and salinity of 0‰ 38860 [g/L] at a temperature of 20°C and salinity of 5‰ 36810 [g/L] at a temperature of 20°C and salinity of 30‰ Boiling Point (°C) 77 Melting Point (°C) -83 Critical molar volume (m³/mol) 0.000286 Critical temperature (°C) 523.3 Critical pressure (Pa) 3870000 Surface tension (mN/m) 24 [mN/m] at a temperature of 20°C 23.39 [mN/m] at a temperature of 25°C 25.08 [mN/m] at a temperature of 5.6°C 24.39 [mN/m] at a temperature of 10.4°C 23.82 [mN/m] at a temperature of 18.6°C Interfacial tension (mN/m) 6.79 [mN/m] at a temperature of 20°C and salinity of 0‰ Vapour Pressure (Pa) 9826 [Pa] at a temperature of 20°C 12600 [Pa] at a temperature of 25°C Ignition Temperature (°C) 460 Flash Point (°C) -4 Flash Point (Pensky-Martens closed cup) (°C) -4.4 Flash Point (Cleveland open cup) (°C) 12.8 Lower explosivity limit (LEL) (volume %) 2.2 Upper explosivity limit (UEL) (volume %) 11.5 Vapor enthalpy (J/Kg) 362500 [J/Kg] at a temperature of 77°C 404040 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 23400000 Specific heat capacity (J/(Kg·K)) 1937.4 Combustion efficiency (%) 98 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.06 Rad fraction (%) 23 Henry's constant (mol/(m³·Pa)) 11.9
### Behaviour at sea
Log kow 0.73 Log koc 0.78 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 50 Bioconcentration factor (BCF) 3.2
### Additional data
Colour colorless Odour pleasant, fruit odour MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment.
### Transportation data
Package group II Cargo group 34 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name esters IMO class 3.2
### Reactivity data
Acid(s) Yes Static electricity Yes Oxidizing agents Yes Notable risks Reacts with oxidizers.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 10000 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H319 Causes serious eye irritation. H336 May cause drowsiness or dizziness. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P233 Keep container tightly closed. P240 Ground/bond container and receiving equipment. P241 Use explosion-proof electrical/ventilating/lighting/.../equipment. P242 Use only non- sparking tools. P243 Take precautionary measures against static discharge. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P264 Wash ... thoroughly after handling. P271 Use only outdoors or in a well-ventilated area. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P312 Call a POISON CENTER or doctor/physician if you feel unwell. P337 + P313 If eye irritation persists: Get medical advice/attention. P370 + P378 In case of fire: Use ... for extinction. Storage P403 + P233 Store in a well-ventilated place. Keep container tightly closed. P405 Store locked up. TLV-TWA 400 TEEL-1 (mg/m3) 400 ppm TEEL-2 (mg/m3) 400 ppm TEEL-3 (mg/m3) 2000 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 5600 Lowest median lethal concentration (LC50) on crustacean (mg/l) 130 Lowest median lethal concentration (LC50) on fishes (mg/l) 455 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 2.4 Assessment factor (AF) 1000 on the Short term 1000 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 130 [µg/l] on the Short term 2.4 [µg/l] on the Long term
# ETHYL ACETOACETATE
CAS Number: 141-97-9 Also known as: ACETOACETATE D'ETHYLE, ACETOACETIC ESTER, DIACETIC ESTER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 141-97-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1028 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 130.1 Density of gas (kg/m3) 5.779 Boiling Point (°C) 184 Melting Point (°C) -44 Vapour Pressure (Pa) 0.1 [Pa] at a temperature of 20°C Ignition Temperature (°C) 295 Flash Point (°C) 65 Lower explosivity limit (LEL) (volume %) 1.4 Upper explosivity limit (UEL) (volume %) 9.5
### Behaviour at sea
### Additional data
Colour colourless Odour pleasant, fruit odour
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
TEEL-1 (mg/m3) 50 TEEL-2 (mg/m3) 350 TEEL-3 (mg/m3) 500
### Ecotoxicity
# ETHYL ACRYLATE inhibited
UN Number: 1917 - CAS Number: 140-88-5 Also known as: ACRYLATE D'ETHYLE, ACRYLIC ACID ETHYL ESTER, Ethoxycarbonylethylene, Ethyl Acrylic Ester, Ethyl Propenoate, Ethyl 2-Propenoate, 2-Propenoic Acid, Ethyl Ester, Ethyl Acrylate, Acrylate D’Ethyle
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1917 CAS number 140-88-5 Formula C 5 H 8 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 923 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.75 [cSt] at a temperature of 20°C 0.6 [cSt] at a temperature of 25°C Molar mass (g/mol) 100.12 Density of gas (kg/m3) 3.87 Solubility (g/L) 17500 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 99 Melting Point (°C) -75 Vapour Pressure (Pa) 11447 [Pa] at a temperature of 20°C 5150 [Pa] at a temperature of 25°C Ignition Temperature (°C) 350 Flash Point (Pensky-Martens closed cup) (°C) 8 Flash Point (Cleveland open cup) (°C) 6.7 Lower explosivity limit (LEL) (volume %) 1.8 Upper explosivity limit (UEL) (volume %) 9.5 Vapor enthalpy (J/Kg) 646549 [J/Kg] at a temperature of 99.5°C Combus enthalpy (J/Kg) 25700000 Combustion efficiency (%) 96 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.09 Rad fraction (%) 23 Henry's constant (mol/(m³·Pa)) 39.82
### Behaviour at sea
Log kow 1.25 Log koc 1.62 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) Not biodegradable Bioconcentration factor (BCF) 2.1
### Additional data
Colour colourless Odour fruit odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification ED
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 14 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name acrylates IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No Notable risks Polymerization.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 2000 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H302 Harmful if swallowed. H312 Harmful in contact with skin. H315 Causes skin irritation. H317 May cause an allergic skin reaction. H319 Causes serious eye irritation. H331 Toxic if inhaled. H335 May cause respiratory irritation. Environmental H412 Harmful to aquatic life with long lasting effects. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P240 Ground/bond container and receiving equipment. P260 Do not breathe dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. Storage P403 + P233 Store in a well-ventilated place. Keep container tightly closed. Disposal P501 Dispose of contents/container to ... ERPG-1 (ppm) 0.01 ERPG-2 (ppm) 30 ERPG-3 (ppm) 300
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 5.5 Lowest median lethal concentration (LC50) on crustacean (mg/l) 7.9 Lowest median lethal concentration (LC50) on fishes (mg/l) 4.6 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.19 Highest no observed effect concentration (NOEC) on fishes (mg/l) 0.78 Assessment factor (AF) 100 on the Short term 1000 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 46 [µg/l] on the Short term 0.19 [µg/l] on the Long term
# ETHYL ALUMINIUM CHLORIDE
UN Number: 3052 Also known as: CHLORURE DE DIETHYL-ALUMINIUM
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3052
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1200 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 129.6 Boiling Point (°C) 194 Melting Point (°C) -32 Vapour Pressure (Pa) 650 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Standard behavior classification D, SD, S
### Transportation data
State liquid IMO class 4.2
### Reactivity data
Water Yes Acid(s) Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# ETHYL AMYL KETONE
UN Number: 2271 - CAS Number: 106-68-3 Also known as: AMYL ETHYL KETONE, EAK
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2271 CAS number 106-68-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 822 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 128.22 Density of gas (kg/m3) 5.68 Boiling Point (°C) 160 Melting Point (°C) -56.7 Vapour Pressure (Pa) 270 [Pa] at a temperature of 20°C Flash Point (°C) 46
### Behaviour at sea
### Additional data
Colour colourless Odour mild fruity Standard behavior classification FD
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 18 Temperature (°C) ambient Family name ketones IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TLV-TWA 25 TEEL-1 (mg/m3) 25 ppm TEEL-2 (mg/m3) 25 ppm TEEL-3 (mg/m3) 100 ppm
### Ecotoxicity
# ETHYL BUTYRATE
UN Number: 1180 - CAS Number: 105-54-4 Also known as: BUTYRATE D'ETHYLE, BUTYRIC ACID ETHYL ESTER, BUTYRIC ETHER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1180 CAS number 105-54-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 879 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 116.16 Density of gas (kg/m3) 5.16 Boiling Point (°C) 121 Melting Point (°C) -93 Vapour Pressure (Pa) 1868 [Pa] at a temperature of 20°C Ignition Temperature (°C) 463 Flash Point (°C) 24
### Behaviour at sea
### Additional data
Colour colourless Odour fruity Standard behavior classification FED
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 34 State liquid Temperature (°C) ambient Family name esters IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Combustibles Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# ETHYL CHLORIDE
UN Number: 1037 Also known as: CHLOROETHANE, CHLORURE D'ETHYLE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1037
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 2.838 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 64.52 Density of gas (kg/m3) 2.838 Boiling Point (°C) 12.4 Melting Point (°C) -142 Vapour Pressure (Pa) 131690 [Pa] at a temperature of 20°C Ignition Temperature (°C) 510 Flash Point (°C) -50 Lower explosivity limit (LEL) (volume %) 3.6 Upper explosivity limit (UEL) (volume %) 14.8
### Behaviour at sea
### Additional data
Colour colourless Odour pleasant odour
### Transportation data
Transport mode Gas,Packaged Ship type 2G,2PG Cargo group 36 State liq.compr.gas Temperature (°C) ambient Pressure (Pa) under pressure Family name halogenated hydrocarb IMO class 2(2.1)
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 20000 TLV-TWA 1000 TEEL-1 (mg/m3) 1500 ppm TEEL-2 (mg/m3) 3800 ppm TEEL-3 (mg/m3) 3800 ppm
### Ecotoxicity
# ETHYL CYCLOHEXANE
CAS Number: 1678-91-7 Also known as: CYCLOHEXYLETHANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 1678-91-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 788 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 112.22 Density of gas (kg/m3) 4.99 Boiling Point (°C) 132 Melting Point (°C) -111.3 Vapour Pressure (Pa) < 1427 [Pa] at a temperature of 20°C Ignition Temperature (°C) 238 Flash Point (°C) 18 Lower explosivity limit (LEL) (volume %) 0.9 Upper explosivity limit (UEL) (volume %) 6.6
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification FE/FED
### Transportation data
Cargo group 31 State liquid Family name paraffins
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# ETHYL HEXALDEHYDE
UN Number: 1191
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1191
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 857 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 128.22 Boiling Point (°C) 164 Melting Point (°C) < -76 Ignition Temperature (°C) 197 Flash Point (°C) 53
### Behaviour at sea
### Additional data
Colour colourless Odour mild odour
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 19 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aldehydes IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# ETHYL LACTATE
UN Number: 1192 Also known as: ACTYOL (T), ACYTOL (T)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1192
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1030 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 118.1 Boiling Point (°C) 154 Flash Point (°C) 42 Lower explosivity limit (LEL) (volume %) 1.5 Upper explosivity limit (UEL) (volume %) 11.4
### Behaviour at sea
### Additional data
Colour colourless Odour mild odour
### Transportation data
Package group III State liquid Temperature (°C) ambient Pressure (Pa) ambient IMO class 3.3
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# ETHYL METHACRYLATE inhibited
UN Number: 2277 - CAS Number: 97-63-2
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2277 CAS number 97-63-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 915 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 114 Density of gas (kg/m3) 5.083 Boiling Point (°C) 117 Melting Point (°C) -75 Vapour Pressure (Pa) 1995 [Pa] at a temperature of 20°C Ignition Temperature (°C) 450 Flash Point (°C) 20 Lower explosivity limit (LEL) (volume %) 1.8
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour colourless Odour sharp, unpleasant odour Standard behavior classification FE
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 14 State liquid Temperature (°C) < 38� Pressure (Pa) ambient Family name acrylates IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 150 ppm TEEL-2 (mg/m3) 750 ppm TEEL-3 (mg/m3) 750 ppm
### Ecotoxicity
# ETHYL PROPIONATE
UN Number: 1195 - CAS Number: 105-37-3
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1195 CAS number 105-37-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 890 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 102.1 Density of gas (kg/m3) 4.515 Boiling Point (°C) 99 Melting Point (°C) -74 Vapour Pressure (Pa) < 5300 [Pa] at a temperature of 20°C Ignition Temperature (°C) 440 Flash Point (°C) 12 Lower explosivity limit (LEL) (volume %) 1.9 Upper explosivity limit (UEL) (volume %) 11
### Behaviour at sea
### Additional data
Colour colourless Odour pineapple-like
### Transportation data
Package group II Cargo group 34 State liquid Temperature (°C) ambient Family name esters IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 25 ppm TEEL-2 (mg/m3) 150 ppm TEEL-3 (mg/m3) 750 ppm
### Ecotoxicity
# ETHYL TOLUENE
CAS Number: 95-63-6 Also known as: Pseudocumene, Trimethyl-1,2,4 Benzene, Trimethylbenzene, 1,2,4-Trimethylbenzene, 1,2,4-Trimethyl Benzene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 95-63-6 Formula C 9 H 1 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 881 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.843 [cSt] at a temperature of 20°C Molar mass (g/mol) 120.19 Density of gas (kg/m3) 5.35 Solubility (g/L) 60 [g/L] at a temperature of 20°C and salinity of 0‰ 42 [g/L] at a temperature of 25°C and salinity of 0‰ 40 [g/L] at a temperature of 25°C and salinity of 34.5‰ Boiling Point (°C) 165.2 Melting Point (°C) -80.8 Critical temperature (°C) 649.1 Critical pressure (Pa) 3232000 Surface tension (mN/m) 29.2 [mN/m] at a temperature of 25°C Ignition Temperature (°C) 440 Flash Point (°C) 39 Flash Point (Pensky-Martens closed cup) (°C) 44 Lower explosivity limit (LEL) (volume %) 0.9 Upper explosivity limit (UEL) (volume %) 6.4 Vapor enthalpy (J/Kg) 398785 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 41000000 Specific heat capacity (J/(Kg·K)) 1789 Combustion efficiency (%) 70 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.06 Rad fraction (%) 30 Henry's constant (mol/(m³·Pa)) 624.162
### Behaviour at sea
Log kow 3.78 Log koc 3.33 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 10 Bioconcentration factor (BCF) 152
### Additional data
Colour colourless Odour pleasant MARPOL pollution category Category Description X Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a major hazard to either marine resources or human health and, therefore, justify the prohibition of the discharge into the marine environment.
### Transportation data
Cargo group 32 State liquid Temperature (°C) ambient Family name aromatic hydrocarbons
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
Hazard statements Physical H226 Flammable liquid and vapour. Health H315 Causes skin irritation. H319 Causes serious eye irritation. H332 Harmful if inhaled. H335 May cause respiratory irritation. Environmental H411 Toxic to aquatic life with long lasting effects. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P243 Take precautionary measures against static discharge. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P302 + P352 IF ON SKIN: Wash with plenty of soap and water. TEEL-1 (mg/m3) 500 TEEL-2 (mg/m3) 500 TEEL-3 (mg/m3) 500
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 4.35 Lowest median lethal concentration (LC50) on fishes (mg/l) 7.72 Assessment factor (AF) 1 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 120 [µg/l] on the Short term
# ETHYL-3-ETHOXYPROPIONATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 950 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 146.21 Density of gas (kg/m3) 6.45 Boiling Point (°C) 170 Melting Point (°C) -100 Vapour Pressure (Pa) 90 [Pa] at a temperature of 20°C Ignition Temperature (°C) 377 Flash Point (°C) 58 Lower explosivity limit (LEL) (volume %) 1.05
### Behaviour at sea
### Additional data
Colour water-white Odour esteric Standard behavior classification FD
### Transportation data
Cargo group 34 State liquid Temperature (°C) ambient Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Biodegradation (A2) NR - Not readily biodegradable
### Human toxicity threshold
### Ecotoxicity
# ETHYLAMINE
UN Number: 1036 - CAS Number: 75-04-7 Also known as: AMINOETHANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1036 CAS number 75-04-7
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 2.064 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 45.1 Density of gas (kg/m3) 2.064 Boiling Point (°C) 16.7 Melting Point (°C) -81 Vapour Pressure (Pa) 120000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 335 Flash Point (°C) -49 Lower explosivity limit (LEL) (volume %) 3.5 Upper explosivity limit (UEL) (volume %) 14
### Behaviour at sea
### Additional data
Colour colourless Odour strong ammonia odour Standard behavior classification GD
### Transportation data
Transport mode Bulk,Gas,Packaged State liq.compr.gas Temperature (°C) ambient Pressure (Pa) under pressure Family name aliphatic amines IMO class 2(2.1)
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) GD - Gas/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 4000 TLV-TWA 10 TEEL-1 (mg/m3) 7.5 ppm TEEL-2 (mg/m3) 49 ppm TEEL-3 (mg/m3) 270 ppm
### Ecotoxicity
# ETHYLAMINE solutions (less than 72%)
UN Number: 2270 Also known as: AMINOETHANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2270
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 687 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 45.1 Density of gas (kg/m3) 1.935 Boiling Point (°C) 16.5 Melting Point (°C) -81 Vapour Pressure (Pa) 154000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 384 Flash Point (°C) -18 Lower explosivity limit (LEL) (volume %) 3.5 Upper explosivity limit (UEL) (volume %) 14
### Behaviour at sea
### Additional data
Colour colourless Odour strong ammonia-like Standard behavior classification DE
### Transportation data
Transport mode Bulk,Packaged (sol.) Ship type 2 (sol.) Package group II (sol.) Cargo group 7 (sol.) State liquid Temperature (°C) ambient Family name aliphatic amines IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 600 TEEL-1 (mg/m3) 7.5 ppm TEEL-2 (mg/m3) 49 ppm TEEL-3 (mg/m3) 270 ppm
### Ecotoxicity
# ETHYLBENZENE
UN Number: 1175 - CAS Number: 100-41-4 Also known as: Ethyl Benzene, Ethylbenzol, Eb, Phenylethane, Ethylbenzene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1175 CAS number 100-41-4 Formula C 8 H 1 0
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 867 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.77 [cSt] at a temperature of 20°C 0.73151 [cSt] at a temperature of 25°C Molar mass (g/mol) 106.17 Density of gas (kg/m3) 3.773 Solubility (g/L) 152 [g/L] at a temperature of 20°C and salinity of 0‰ 160 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 136.4 Melting Point (°C) -95 Critical molar volume (m³/mol) 0.000374 Critical temperature (°C) 617.5 Critical pressure (Pa) 3609000 Surface tension (mN/m) 29.2 [mN/m] at a temperature of 20°C 28.75 [mN/m] at a temperature of 25°C Interfacial tension (mN/m) 35.48 [mN/m] at a temperature of 20°C and salinity of 0‰ Vapour Pressure (Pa) 930 [Pa] at a temperature of 20°C 1270 [Pa] at a temperature of 25°C Ignition Temperature (°C) 430 Flash Point (°C) 15 Flash Point (Pensky-Martens closed cup) (°C) 21 Flash Point (Cleveland open cup) (°C) 26.7 Lower explosivity limit (LEL) (volume %) 0.8 Upper explosivity limit (UEL) (volume %) 6.7 Vapor enthalpy (J/Kg) 335029 [J/Kg] at a temperature of 136.2°C 397853 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 40900000 Specific heat capacity (J/(Kg·K)) 1725.5 Combustion efficiency (%) 70 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.07 Rad fraction (%) 60 Henry's constant (mol/(m³·Pa)) 798
### Behaviour at sea
Persistence (days) 0.8 Log kow 3.13 Log koc 2.38 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 50 Bioconcentration factor (BCF) 91
### Additional data
Colour colourless Odour sweet, gasoline odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification FE
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 32 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aromatic hydrocarbons IMO class 3.2
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Specific Health Concern (D3) T - Specific Target Organ Toxicity following single or repeated exposure Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 2000 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H304 May be fatal if swallowed and enters airways. H332 Harmful if inhaled. H373 May cause damage to organs through prolonged or repeated exposure, exposure cause the hazard: Environmental H412 Harmful to aquatic life with long lasting effects. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P240 Ground/bond container and receiving equipment. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P331 Do NOT induce vomiting. Disposal P501 Dispose of contents/container to ... TLV-TWA 100
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 3.6 Lowest median lethal concentration (LC50) on crustacean (mg/l) 1.8 Lowest median lethal concentration (LC50) on fishes (mg/l) 4.2 Highest no observed effect concentration (NOEC) on algae (mg/l) 1 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 1 Assessment factor (AF) 100 on the Short term 100 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 18 [µg/l] on the Short term 10 [µg/l] on the Long term
# ETHYLENE (compressed gas)
UN Number: 1962
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1962
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 1.125 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 28.05 Density of gas (kg/m3) 1.125 Boiling Point (°C) -103.5 Melting Point (°C) -169 Vapour Pressure (Pa) 415330041 [Pa] at a temperature of 20°C Ignition Temperature (°C) 425 Flash Point (°C) -16 Lower explosivity limit (LEL) (volume %) 2.7 Upper explosivity limit (UEL) (volume %) 34
### Behaviour at sea
### Additional data
Colour colourless Odour sweet odour
### Transportation data
Transport mode Gas,Packaged Cargo group 30 State liq.compr.gas Temperature (°C) -104� Pressure (Pa) under pressure Family name olefins IMO class 2(2.1)
### Reactivity data
Acid(s) Yes Static electricity Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 600 ppm TEEL-2 (mg/m3) 7500 ppm TEEL-3 (mg/m3) 7500 ppm
### Ecotoxicity
# ETHYLENE (refrigerated liquid)
UN Number: 1038
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1038
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 1.125 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 28.05 Density of gas (kg/m3) 1.125 Boiling Point (°C) -103.5 Melting Point (°C) -169 Vapour Pressure (Pa) 415330041 [Pa] at a temperature of 20°C Ignition Temperature (°C) 425 Flash Point (°C) -16 Lower explosivity limit (LEL) (volume %) 2.7 Upper explosivity limit (UEL) (volume %) 34
### Behaviour at sea
### Additional data
Colour colourless Odour sweet odour
### Transportation data
Transport mode Gas,Packaged Ship type 2G Cargo group 30 State liquefied gas Temperature (°C) -104� Pressure (Pa) under pressure Family name olefins IMO class 2(2.1)
### Reactivity data
Acid(s) Yes Static electricity Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 600 ppm TEEL-2 (mg/m3) 7500 ppm TEEL-3 (mg/m3) 7500 ppm
### Ecotoxicity
# ETHYLENE CARBONATE
CAS Number: 96-49-1 Also known as: CARBONATE D'ETHYLENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 96-49-1
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1300 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 88 Density of gas (kg/m3) 3.87 Boiling Point (°C) 244 Melting Point (°C) 36 Flash Point (°C) 143
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
### Reactivity data
Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# ETHYLENE CHLOROHYDRIN
UN Number: 1135 - CAS Number: 107-07-3 Also known as: 2-CHLOROETHANOL, 2-CHLOROETHYL ALCOHOL, beta- CHLOROETHYL ALCOHOL, CHLOROHYDRINE ETHYLENIQUE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1135 CAS number 107-07-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1197 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 80.51 Density of gas (kg/m3) 3.612 Boiling Point (°C) 128.9 Melting Point (°C) -70 Vapour Pressure (Pa) 730 [Pa] at a temperature of 20°C Ignition Temperature (°C) 425 Flash Point (°C) 55 Lower explosivity limit (LEL) (volume %) 4.9 Upper explosivity limit (UEL) (volume %) 15.9
### Behaviour at sea
### Additional data
Colour colourless Odour weak sweet, pleasant odour
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 20 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alcohols, glycols IMO class 6.1
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 4 - High Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 10 TEEL-1 (mg/m3) 0.54 ppm TEEL-2 (mg/m3) 0.66 ppm TEEL-3 (mg/m3) 0.5 ppm
### Ecotoxicity
# ETHYLENE CYANOHYDRIN
CAS Number: 109-78-4 Also known as: 2-CYANOETHANOL, 2-CYANOETHYL ALCOHOL, CYANOHYDRINE ETHYLENIQUE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 109-78-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1047 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 71.08 Density of gas (kg/m3) 3.225 Boiling Point (°C) 229.9 Melting Point (°C) -46 Vapour Pressure (Pa) 10 [Pa] at a temperature of 20°C Ignition Temperature (°C) 494 Flash Point (°C) 21 Lower explosivity limit (LEL) (volume %) 2.3 Upper explosivity limit (UEL) (volume %) 12.1
### Behaviour at sea
### Additional data
Colour colourless, yellow-brown Odour weak odour to odourless
### Transportation data
Cargo group 20 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alcohols, glycols
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# ETHYLENE DIAMINE TETRA-ACETIC ACID
CAS Number: #Error Also known as: ACIDE ETHYLENE DIAMINE TETRA-ACETIQUE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number #Error
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 860 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 292.2 Melting Point (°C) 240
### Behaviour at sea
### Additional data
Colour white Odour odourless
### Transportation data
State solid Temperature (°C) ambient
### Reactivity data
Water No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# ETHYLENE DIBROMIDE
UN Number: 1605 - CAS Number: 106-93-4 Also known as: BOWFUME (T), BROMOFUME (T), DBE, sym-DIBROMETHANE, 1,2-DIBROMOETHANE, DIBROMURE D'ETHYLENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1605 CAS number 106-93-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 2180 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 187.86 Density of gas (kg/m3) 8.359 Boiling Point (°C) 131 Melting Point (°C) 10 Vapour Pressure (Pa) 1133 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless Odour sweet odour Standard behavior classification SD
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 36 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name halogenated hydrocarb IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 400 TLV-TWA 20 TEEL-1 (mg/m3) 17 ppm TEEL-2 (mg/m3) 24 ppm TEEL-3 (mg/m3) 46 ppm
### Ecotoxicity
# ETHYLENE GLYCOL
CAS Number: 107-21-1 Also known as: 1,2-DIHYDROXY ETHANE, DIHYDROXYETHANE, DOWTHERM SRI (T), 1,2-Dihydroxyethane, 1,2-Ethanediol, Ethylene Alcohol, Ethylene Dihydrate, Glycol, Glycol Alcohol, Monoethylene Glycol, 2-Hydroxyethanol, Eg, Ethylene Glycol
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 107-21-1 Formula C 2 H 6 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1115 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 18.9 [cSt] at a temperature of 20°C 15.05 [cSt] at a temperature of 25°C Molar mass (g/mol) 62.07 Density of gas (kg/m3) 2.761 Solubility (g/L) 1110000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 197.8 Melting Point (°C) -16 Critical temperature (°C) 720 Critical pressure (Pa) 8000000 Surface tension (mN/m) 48.4 [mN/m] at a temperature of 20°C 47.99 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 2266 [Pa] at a temperature of 20°C 10 [Pa] at a temperature of 25°C Ignition Temperature (°C) 410 Flash Point (°C) 111 Flash Point (Pensky-Martens closed cup) (°C) 111 Flash Point (Cleveland open cup) (°C) 115 Lower explosivity limit (LEL) (volume %) 3.2 Upper explosivity limit (UEL) (volume %) 15.3 Vapor enthalpy (J/Kg) 813598 [J/Kg] at a temperature of 198°C 1029482 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 17000000 Specific heat capacity (J/(Kg·K)) 2394.1 Combustion efficiency (%) 98 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.02 Rad fraction (%) 22 Henry's constant (mol/(m³·Pa)) 0
### Behaviour at sea
Log kow -1.93 Log koc 0.6 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 50 Bioconcentration factor (BCF) 10
### Additional data
Colour colourless Odour odourless MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Cargo group 20 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alcohols, glycols
### Reactivity data
Abilities Miscible in water. Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes Notable risks Reacts with oxidizers.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
Hazard statements Health H302 Harmful if swallowed. H373 May cause damage to organs through prolonged or repeated exposure, exposure cause the hazard: TLV-TWA 100 TEEL-1 (mg/m3) 10 ppm TEEL-2 (mg/m3) 40 ppm TEEL-3 (mg/m3) 60 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 10000 Lowest median lethal concentration (LC50) on crustacean (mg/l) 20000 Lowest median lethal concentration (LC50) on fishes (mg/l) 56484 Highest no observed effect concentration (NOEC) on algae (mg/l) 5740 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 3000 Assessment factor (AF) 1000 on the Short term 1000 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 10000 [µg/l] on the Short term 3000 [µg/l] on the Long term
# ETHYLENE GLYCOL ACETATE
Also known as: ACETATE D'ETHYLENEGLYCOL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1100 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 104.1 Density of gas (kg/m3) 4.63 Boiling Point (°C) 182 Melting Point (°C) -42 Vapour Pressure (Pa) 400 [Pa] at a temperature of 20°C Ignition Temperature (°C) 460 Flash Point (°C) 102 Lower explosivity limit (LEL) (volume %) 7.8 Upper explosivity limit (UEL) (volume %) 27.7
### Behaviour at sea
### Additional data
Colour colourless Odour weak fruity
### Transportation data
Cargo group 34 State liquid Temperature (°C) ambient Family name esters
### Reactivity data
Water Yes Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# ETHYLENE GLYCOL DIACETATE
CAS Number: 111-55-7 Also known as: DIACETATE D'ETHYLENEGLYCOL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 111-55-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1104 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 146.1 Boiling Point (°C) 190.9 Melting Point (°C) -41.5 Ignition Temperature (°C) 482 Flash Point (°C) 98 Lower explosivity limit (LEL) (volume %) 1.6 Upper explosivity limit (UEL) (volume %) 8.4
### Behaviour at sea
### Additional data
Colour colourless Odour weak fruity Standard behavior classification D/DE
### Transportation data
State liquid Temperature (°C) ambient Family name esters
### Reactivity data
Water No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
### Ecotoxicity
# Ethylene Glycol Methyl Butyl Ether
CAS Number: 13343-98-1 Also known as: 2,5-Dioxanonane, Butyl 2-Methoxyethyl Ether, 1-(2-Methoxyethoxy)Butane, 1-Butoxy-2-Methoxy-Ethane, Ethylene Glycol Methyl Butyl Ether, Ether Methylbutylique De L'Ethylene Glycol
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 13343-98-1 Formula C 7 H 1 6 O 2
### Physical chemical data
Physical State (25°C) Liquid Molar mass (g/mol) 132.20284 Boiling Point (°C) 147 Henry's constant (mol/(m³·Pa)) 3.03
### Behaviour at sea
Log kow 1.27 Log koc 0.442 Bioconcentration factor (BCF) 1.883
### Additional data
MARPOL pollution category Category Description Other Substances Substances which have been evaluated and found to fall outside Category X, Y or Z because they are considered to present no harm to marine resources, human health, amenities or other legitimate uses of the sea when discharged into the sea from tank cleaning of deballasting operations. The discharge of bilge or ballast water or other residues or mixtures containing these substances are not subject to any requirements of MARPOL Annex II.
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Interference with coastal amenities (E2) D - Dissolver
### Human toxicity threshold
### Ecotoxicity
# ETHYLENE GLYCOL METHYL ETHER ACETATE
UN Number: 1189 - CAS Number: 110-49-6 Also known as: ACETATE DE L'ETHER METHYLIQUE DE L'ETHYLENEGLYCOL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1189 CAS number 110-49-6
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1006 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 118.13 Density of gas (kg/m3) 5.29 Boiling Point (°C) 145 Melting Point (°C) -65 Vapour Pressure (Pa) 269 [Pa] at a temperature of 20°C Ignition Temperature (°C) 393 Flash Point (°C) 44 Lower explosivity limit (LEL) (volume %) 1.5 (93�C) Upper explosivity limit (UEL) (volume %) 12.3 (93�C
### Behaviour at sea
### Additional data
Colour colourless Odour mild, ether-like
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) ambient Family name esters IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Specific Health Concern (D3) R - Reprotoxicity Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 200 TEEL-1 (mg/m3) 0.3 ppm TEEL-2 (mg/m3) 20 ppm TEEL-3 (mg/m3) 200 ppm
### Ecotoxicity
# ETHYLENE GLYCOL MONOBUTYL ETHER ACETATE
CAS Number: 112-07-2 Also known as: ACETATE DE L'ETHER MONOBUTYLIQUE DE L' ETHYLENE GLYCOL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 112-07-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 942 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 160.21 Boiling Point (°C) 192.4 Melting Point (°C) -63 Vapour Pressure (Pa) 400 [Pa] at a temperature of 20°C Ignition Temperature (°C) 340 Flash Point (°C) 71 Lower explosivity limit (LEL) (volume %) 0.9 Upper explosivity limit (UEL) (volume %) 8.5
### Behaviour at sea
Persistence (days) 0.8
### Additional data
Colour colourless Odour weak fruit odour Standard behavior classification E, FE, F
### Transportation data
Cargo group 34 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name esters
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
TEEL-1 (mg/m3) 60 ppm TEEL-2 (mg/m3) 100 ppm TEEL-3 (mg/m3) 150 ppm
### Ecotoxicity
# ETHYLENE GLYCOL MONOETHYL ETHER
UN Number: 1171 - CAS Number: 110-80-5 Also known as: CELLOSOLVE, CELLOSOLVE SOLVENT, DOWANOL EE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1171 CAS number 110-80-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 931 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 90.12 Density of gas (kg/m3) 3.87 Boiling Point (°C) 135.1 Melting Point (°C) -69.4 Vapour Pressure (Pa) 503 [Pa] at a temperature of 20°C Ignition Temperature (°C) 235 Flash Point (°C) 40 Lower explosivity limit (LEL) (volume %) 1.7 Upper explosivity limit (UEL) (volume %) 15.7
### Behaviour at sea
### Additional data
Colour colourless Odour sweet ether-like
### Transportation data
Package group III Cargo group 40 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name glycol ethers IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Metal(s) and alloys Yes (Cu) Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 500 TEEL-1 (mg/m3) 15 ppm TEEL-2 (mg/m3) 500 ppm TEEL-3 (mg/m3) 500 ppm
### Ecotoxicity
# ETHYLENE GLYCOL MONOETHYL ETHER ACETATE
UN Number: 1172 Also known as: ACETATE DE CELLOSOLVE, ACETATE DE L'ETHER MONOETHYLIQUE DE L'ETHYLENE GLYCOL, ACETIC ACID-2-ETHOXY ETHYL ESTER, CELLOSOLVE ACETATE, CSAC
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1172
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 974 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 132.16 Density of gas (kg/m3) 6.06 Boiling Point (°C) 156 Melting Point (°C) -61.7 Vapour Pressure (Pa) 159 [Pa] at a temperature of 20°C Ignition Temperature (°C) 382 Flash Point (°C) 49 Lower explosivity limit (LEL) (volume %) 1.2 Upper explosivity limit (UEL) (volume %) 12.7
### Behaviour at sea
### Additional data
Colour colourless Odour mild ester-like
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 34 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name esters IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 500 TEEL-1 (mg/m3) 75 ppm TEEL-2 (mg/m3) 500 ppm TEEL-3 (mg/m3) 500 ppm
### Ecotoxicity
# ETHYLENE GLYCOL MONOMETHYL ETHER
UN Number: 1188 - CAS Number: 109-86-4 Also known as: DOWANOL EM, 2-Methoxyethanol, Methyl Cellosolve, Methyl Oxitol, Methylglycol, Ethylene Glycol Monomethyl Ether, Ether Monomethylique De L'Ethylene Glycol
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1188 CAS number 109-86-4 Formula C 3 H 8 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 966 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 76.1 Density of gas (kg/m3) 5.289 Solubility (g/L) 1000000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 124.7 Melting Point (°C) -85 Critical molar volume (m³/mol) 0.000263 Critical temperature (°C) 597.6 Critical pressure (Pa) 5285000 Surface tension (mN/m) 30.84 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 505 [Pa] at a temperature of 20°C Ignition Temperature (°C) 285 Flash Point (°C) 37 Flash Point (Pensky-Martens closed cup) (°C) 42 Lower explosivity limit (LEL) (volume %) 2.5 Upper explosivity limit (UEL) (volume %) 19.8 Vapor enthalpy (J/Kg) 493331 [J/Kg] at a temperature of 124.1°C 593600 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 21980699 Specific heat capacity (J/(Kg·K)) 2249 Henry's constant (mol/(m³·Pa)) 0.033
### Behaviour at sea
Log kow -0.77 Log koc 0 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 3
### Additional data
Colour colourless Odour odourless MARPOL pollution category Category Description Other Substances Substances which have been evaluated and found to fall outside Category X, Y or Z because they are considered to present no harm to marine resources, human health, amenities or other legitimate uses of the sea when discharged into the sea from tank cleaning of deballasting operations. The discharge of bilge or ballast water or other residues or mixtures containing these substances are not subject to any requirements of MARPOL Annex II.
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 40 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name glycol ethers IMO class 3.3
### Reactivity data
Abilities Miscible in water. Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Interference with coastal amenities (E2) G - Gas
### Human toxicity threshold
IDHL 2000 Hazard statements Physical H226 Flammable liquid and vapour. Health H302 Harmful if swallowed. H312 Harmful in contact with skin. H332 Harmful if inhaled. H360 May damage fertility or the unborn child. Precautionary statements Prevention P201 Obtain special instructions before use. P202 Do not handle until all safety precautions have been read and understood. P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P233 Keep container tightly closed. P240 Ground/bond container and receiving equipment. P241 Use explosion-proof electrical/ventilating/lighting/.../equipment. P242 Use only non- sparking tools. P243 Take precautionary measures against static discharge. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P264 Wash ... thoroughly after handling. P270 Do no eat, drink or smoke when using this product. P271 Use only outdoors or in a well- ventilated area. P280 Wear protective gloves/protective clothing/eye protection/face protection. P281 Use personal protective equipment as required. Response P301 + P312 IF SWALLOWED: Call a POISON CENTER or doctor/physician if you feel unwell. P302 + P352 IF ON SKIN: Wash with plenty of soap and water. P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P308 + P313 IF exposed or concerned: Get medical advice/attention. P312 Call a POISON CENTER or doctor/physician if you feel unwell. P322 Specific measures (see ... on this label). P330 Rinse mouth. P363 Wash contaminated clothing before reuse. P370 + P378 In case of fire: Use ... for extinction. Storage P403 + P235 Store in a well-ventilated place. Keep cool. P405 Store locked up. Disposal P501 Dispose of contents/container to ... TLV-TWA 25 TEEL-1 (mg/m3) 0.35 ppm TEEL-2 (mg/m3) 2.5 ppm TEEL-3 (mg/m3) 200 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 1000 Lowest median lethal concentration (LC50) on fishes (mg/l) > 10000 Assessment factor (AF) 500 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 1000 [µg/l] on the Short term
# ETHYLENE GLYCOL PHENYL ETHER
CAS Number: 122-99-6 Also known as: AROSOL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 122-99-6
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1100 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 138.2 Density of gas (kg/m3) 6.19 Boiling Point (°C) 242 Melting Point (°C) 14 Vapour Pressure (Pa) 5200 [Pa] at a temperature of 20°C Ignition Temperature (°C) 500 Flash Point (°C) 121
### Behaviour at sea
### Additional data
Colour colourless Odour characteristic, pleasant
### Transportation data
Cargo group 40 Temperature (°C) ambient Family name glycol ethers
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 20 ppm TEEL-2 (mg/m3) 20 ppm TEEL-3 (mg/m3) 100 ppm
### Ecotoxicity
# ETHYLENE OXIDE (< 0.2% nitrogen)
UN Number: 1040 - CAS Number: 75-21-8 Also known as: ANPROLENE (T), DIHYDROOXIRANE, DIMETHYLENE OXIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1040 CAS number 75-21-8
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 1.935 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 44.05 Density of gas (kg/m3) 1.935 Boiling Point (°C) 10.8 Melting Point (°C) -112 Vapour Pressure (Pa) 150000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 440 Flash Point (°C) -18 Upper explosivity limit (UEL) (volume %) 100
### Behaviour at sea
### Additional data
Colour colourless Odour sweet odour Standard behavior classification GD
### Transportation data
Transport mode Gas,Packaged Ship type 1G State liq.compr.gas Temperature (°C) ambient Pressure (Pa) under pressure IMO class 2(2.3)
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Metal(s) and alloys No Static electricity Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) GD - Gas/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 800 ERPG-2 (ppm) 50 ERPG-3 (ppm) 500
### Ecotoxicity
# ETHYLENEDIAMINE
UN Number: 1604 - CAS Number: 107-15-3 Also known as: 1,2-DIAMINOETHANE, DIMETHYLENEDIAMINE, Ethane-1,2-Diamine, 1,2-Ethanediamine, Ethylenediamine
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1604 CAS number 107-15-3 Formula C 2 H 8 N 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 909 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.017151 [cSt] at a temperature of 25°C Molar mass (g/mol) 60.1 Density of gas (kg/m3) 2.709 Solubility (g/L) 110000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 117 Melting Point (°C) 11.14 Critical temperature (°C) 613.1 Critical pressure (Pa) 6710000 Vapour Pressure (Pa) 1200 [Pa] at a temperature of 20°C Ignition Temperature (°C) 385 Flash Point (°C) 34 Flash Point (Pensky- Martens closed cup) (°C) 34 Lower explosivity limit (LEL) (volume %) 5.8 Upper explosivity limit (UEL) (volume %) 11.1 Vapor enthalpy (J/Kg) 631968 [J/Kg] at a temperature of 117°C 748444 [J/Kg] at a temperature of 25°C Specific heat capacity (J/(Kg·K)) 2872 Henry's constant (mol/(m³·Pa)) 0.00018
### Behaviour at sea
Log kow -1.3 Log koc 1.17 Bioconcentration factor (BCF) 1
### Additional data
Colour colourless Odour mild ammonia odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name aliphatic amines
### Reactivity data
Water Yes Abilities Miscible in water. Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 2000 Hazard statements Physical H226 Flammable liquid and vapour. Health H302 Harmful if swallowed. H311 Toxic in contact with skin. H314 Causes severe skin burns and eye damage. H317 May cause an allergic skin reaction. H332 Harmful if inhaled. H334 May cause allergy or asthma symptoms or breathing difficulties if inhaled. Environmental H412 Harmful to aquatic life with long lasting effects. Precautionary statements General P101 If medical advice is needed, have product container or label at hand. P102 Keep out of reach of children. Prevention P260 Do not breathe dust/fume/gas/mist/vapours/spray. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P308 + P313 IF exposed or concerned: Get medical advice/attention. Storage P405 Store locked up. Disposal P501 Dispose of contents/container to ... TLV-TWA 10 10 min 30 min 60 min 4 hrs 8 hrs AEGL-2 (ppm) 12 12 9.7 6.1 4.8 AEGL-3 (ppm) 25 25 20 13 10
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 61 Lowest median lethal concentration (LC50) on crustacean (mg/l) 3 Lowest median lethal concentration (LC50) on fishes (mg/l) 115.7 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.16 Highest no observed effect concentration (NOEC) on fishes (mg/l) > 10 Assessment factor (AF) 100 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 2 [µg/l] on the Short term
# ETHYLIDENE NORBORNENE
CAS Number: 16219-75-3
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 16219-75-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 896 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 120.2 Density of gas (kg/m3) 5.418 Boiling Point (°C) 147.8 Melting Point (°C) -80 Vapour Pressure (Pa) 540 [Pa] at a temperature of 20°C Flash Point (°C) 33 Lower explosivity limit (LEL) (volume %) 0.9 Upper explosivity limit (UEL) (volume %) 6.4
### Behaviour at sea
### Additional data
Colour white Odour turpentine odour Standard behavior classification FE
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 3 - ≥100 and <500 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
ERPG-1 (ppm) 0.2 ERPG-2 (ppm) 100 ERPG-3 (ppm) 500
### Ecotoxicity
# Fatty Acid Methyl Esters
Also known as: Fame, Fatty Acid Methyl Esters, Ester Methylique D'Acide Gras
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
Formula CH 3 (CH 2 )nCOOCH 3
### Physical chemical data
Physical State (25°C) Liquid Mixed Yes Kinematic viscosity (cSt) 4.5 [cSt] at a temperature of 20°C Solubility (g/L) 0 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 302 Melting Point (°C) -12
### Behaviour at sea
### Additional data
MARPOL pollution category Category Description Other Substances Substances which have been evaluated and found to fall outside Category X, Y or Z because they are considered to present no harm to marine resources, human health, amenities or other legitimate uses of the sea when discharged into the sea from tank cleaning of deballasting operations. The discharge of bilge or ballast water or other residues or mixtures containing these substances are not subject to any requirements of MARPOL Annex II.
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
Predicted No Effect Concentration (PNEC) (µg/l) 0.2504 [µg/l] on the Short term
# FERRIC CHLORIDE anhydrous
UN Number: 1773 - CAS Number: 7705-08-0 Also known as: CHLORURE FERRIQUE anhydre
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1773 CAS number 7705-08-0
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2900 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 162.22 Boiling Point (°C) 315 Melting Point (°C) 306
### Behaviour at sea
Persistence (days) 0.8
### Additional data
Colour greenish black Odour odourless Standard behavior classification SD
### Transportation data
Package group III State solid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 5 - ≥ 4000 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TLV-TWA 0.4 (Fe) TEEL-1 (mg/m3) 3.5 TEEL-2 (mg/m3) 25 TEEL-3 (mg/m3) 125
### Ecotoxicity
# FERRIC CHLORIDE solutions (39%)
UN Number: 2582 - CAS Number: 7705-08-0 Also known as: CHLORURE DE FER (III), CHLORURE FERRIQUE en solution (39%)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2582 CAS number 7705-08-0
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1410 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 110 Melting Point (°C) -2 Vapour Pressure (Pa) 1466 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour orange/brown Odour pungent
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 43 State liquid Temperature (°C) ambient Family name miscell. water solut.
### Reactivity data
Water No Acid(s) Yes Metal(s) and alloys Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 5 - ≥ 4000 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 3.5 TEEL-2 (mg/m3) 25 TEEL-3 (mg/m3) 125
### Ecotoxicity
# FERRIC NITRATE
UN Number: 1466
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1466
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1700 [Kg/m³] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour green,colourless to violet Odour odourless Standard behavior classification SD
### Transportation data
Package group III State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 5.1
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 5 - ≥ 4000 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TLV-TWA 0.4 (Fe) TEEL-1 (mg/m3) 13 TEEL-2 (mg/m3) 21.7 TEEL-3 (mg/m3) 100
### Ecotoxicity
# FIRE EXTINGUISHERS (containing compressed or liquified gas)
UN Number: 1044
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1044
### Physical chemical data
Physical State (20°C) Gas
### Behaviour at sea
### Additional data
Standard behavior classification GD, G
### Transportation data
State liq.compr.gas IMO class 2(2.2)
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# FLUOROSILICIC ACID
UN Number: 1778 - CAS Number: 16961-83-4 Also known as: ACIDE FLUOROSILICIQUE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1778 CAS number 16961-83-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1290 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 144.09 Density of gas (kg/m3) 6.44 Boiling Point (°C) 109 Melting Point (°C) 1.727272727 Vapour Pressure (Pa) 2000 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless Odour sharp, unpleasant
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Family name non oxid. min. acids
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 4 - High Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 9.48 TEEL-2 (mg/m3) 15.8 TEEL-3 (mg/m3) 50
### Ecotoxicity
# FORMALDEHYDE flammable solutions
UN Number: 1198 - CAS Number: 50-00-0 Also known as: Formaldehyde Solutions (45% Or Less), Solutions De Formaldhyde (45% Ou Moins)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1198 CAS number 50-00-0 Formula CH 2 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1100 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 18 Density of gas (kg/m3) 1.33 Solubility (g/L) 10000000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) -20 Melting Point (°C) -15 Vapour Pressure (Pa) 133 [Pa] at a temperature of 20°C Ignition Temperature (°C) 430 Flash Point (°C) 68 Upper explosivity limit (UEL) (volume %) 73
### Behaviour at sea
### Additional data
Colour colourless Odour irritating odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 19 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name aldehydes IMO class 3.3
### Reactivity data
Abilities Solution. Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 30 Hazard statements Health H301 Toxic if swallowed. H311 Toxic in contact with skin. H314 Causes severe skin burns and eye damage. H317 May cause an allergic skin reaction. H331 Toxic if inhaled. H351 Suspected of causing cancer. Precautionary statements Prevention P201 Obtain special instructions before use. P260 Do not breathe dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P312 Call a POISON CENTER or doctor/physician if you feel unwell. P361 Remove/Take off immediately all contaminated clothing. P370 + P378 In case of fire: Use ... for extinction. Storage P403 + P233 Store in a well- ventilated place. Keep container tightly closed. ERPG-2 (ppm) 10 ERPG-3 (ppm) 25
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 14.7 Lowest median lethal concentration (LC50) on crustacean (mg/l) 14.7 Lowest median lethal concentration (LC50) on fishes (mg/l) 6.7 Predicted No Effect Concentration (PNEC) (µg/l) 5.8 [µg/l] on the Short term
# FORMAMIDE
CAS Number: 75-12-7 Also known as: CARBAMALDEHYDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 75-12-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1100 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 45.04 Density of gas (kg/m3) 2.06 Boiling Point (°C) 210.5 Melting Point (°C) 2.6 Vapour Pressure (Pa) 130 [Pa] at a temperature of 20°C Ignition Temperature (°C) > 500 Flash Point (°C) 154
### Behaviour at sea
### Additional data
Colour colourless to pale yellow Odour ammonia-like
### Transportation data
Cargo group 10 State liquid Temperature (°C) ambient Family name amides
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Reducing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Specific Health Concern (D3) R - Reprotoxicity Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 20 ppm TEEL-2 (mg/m3) 125 ppm TEEL-3 (mg/m3) 1250 ppm
### Ecotoxicity
# FORMIC ACID
UN Number: 1779 - CAS Number: 64-18-6 Also known as: ACIDE FORMIQUE, Methanoic Acid, Formilic Acid, Aminic Acid, Formic Acid
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1779 CAS number 64-18-6 Formula CH 2 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1220 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 1.3172 [cSt] at a temperature of 25°C Molar mass (g/mol) 46.03 Density of gas (kg/m3) 2.051 Solubility (g/L) 1000000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 101 Melting Point (°C) 8.3 Critical temperature (°C) 588 Surface tension (mN/m) 34.38 [mN/m] at a temperature of 25°C Interfacial tension (mN/m) 1.32 [mN/m] at a temperature of 25°C and salinity of 0‰ Vapour Pressure (Pa) 4399 [Pa] at a temperature of 20°C Ignition Temperature (°C) 600 Flash Point (°C) 69 Flash Point (Pensky-Martens closed cup) (°C) 69 Flash Point (Cleveland open cup) (°C) 50 Lower explosivity limit (LEL) (volume %) 18 Upper explosivity limit (UEL) (volume %) 57 Vapor enthalpy (J/Kg) 492982 [J/Kg] at a temperature of 101°C 436710 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 5531656 Specific heat capacity (J/(Kg·K)) 2151 Henry's constant (mol/(m³·Pa)) 0.017
### Behaviour at sea
Log kow -0.22 Log koc 0 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 3.2
### Additional data
Colour colourless Odour penetrating odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name organic acids
### Reactivity data
Abilities Miscible in water. Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 3C - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 30 Hazard statements Physical H226 Flammable liquid and vapour. Health H302 Harmful if swallowed. H314 Causes severe skin burns and eye damage. H331 Toxic if inhaled. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. TEEL-1 (mg/m3) 0.92 ppm TEEL-2 (mg/m3) 0.92 ppm TEEL-3 (mg/m3) 30 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 34 Lowest median lethal concentration (LC50) on fishes (mg/l) 46 Assessment factor (AF) 500 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 200 [µg/l] on the Short term
# FUEL AVIATION TURBINE ENGINE
UN Number: 1863 Also known as: CARBUREACTEUR
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1863
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 810 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 176 Vapour Pressure (Pa) 400 [Pa] at a temperature of 20°C Ignition Temperature (°C) 220 Flash Point (°C) 30 Lower explosivity limit (LEL) (volume %) 1.3
### Behaviour at sea
### Additional data
Colour colourless Odour gasoline odour Standard behavior classification E, FE, F
### Transportation data
Transport mode Bulk,Packaged Package group I/II/III Cargo group 33 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name miscell. hydroc. mixt IMO class 3.1/3.2/3.
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 200
### Ecotoxicity
# FURATHIOCARB
UN Number: 2982 Also known as: APRON
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2982
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1160 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 382.48 Boiling Point (°C) 160 (1.33 Pa) Vapour Pressure (Pa) 8.4*10-5 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour yellow Marine pollutant P
### Transportation data
Package group I/II/III IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# FURFURAL
UN Number: 1199 - CAS Number: 98-01-1 Also known as: ANT OIL (ARTIFICIAL), BRAN OIL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1199 CAS number 98-01-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1159 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 96.08 Density of gas (kg/m3) 4.269 Boiling Point (°C) 161.9 Melting Point (°C) -34 Vapour Pressure (Pa) 140 [Pa] at a temperature of 20°C Ignition Temperature (°C) 315 Flash Point (°C) 56 Lower explosivity limit (LEL) (volume %) 2.1 Upper explosivity limit (UEL) (volume %) 19.3
### Behaviour at sea
### Additional data
Colour colorless to reddish-brown Odour almond odour
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 19 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name aldehydes IMO class 6.1
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Specific Health Concern (D3) C - Carcinogenicity Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 250 ERPG-2 (ppm) 10 ERPG-3 (ppm) 100
### Ecotoxicity
# FURFURYL ALCOHOL
UN Number: 2874 - CAS Number: 98-00-0
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2874 CAS number 98-00-0
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1130 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 98.1 Density of gas (kg/m3) 4.23 Boiling Point (°C) 170 Melting Point (°C) -34 Vapour Pressure (Pa) 50 [Pa] at a temperature of 20°C Ignition Temperature (°C) 315 Flash Point (°C) 52 Lower explosivity limit (LEL) (volume %) 1.8 Upper explosivity limit (UEL) (volume %) 16.3
### Behaviour at sea
### Additional data
Colour colourless to light yellow Odour mild irritating odour
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 20 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alcohols, glycols IMO class 6.1
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 250 TLV-TWA 10 TEEL-1 (mg/m3) 15 ppm TEEL-2 (mg/m3) 15 ppm TEEL-3 (mg/m3) 75 ppm
### Ecotoxicity
# GAS OIL
UN Number: 1202
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1202
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 848 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 190 Melting Point (°C) -23 Vapour Pressure (Pa) 400 [Pa] at a temperature of 20°C Ignition Temperature (°C) 250 Flash Point (°C) 62 Upper explosivity limit (UEL) (volume %) 13.5
### Behaviour at sea
### Additional data
Colour colourless Odour gasoline odour Standard behavior classification E, FE, F
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 33 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name miscell. hydroc. mixt IMO class 3.3
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# GASOLINE
UN Number: 1203
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1203
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 732 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 14 /71 Vapour Pressure (Pa) 400 [Pa] at a temperature of 20°C Ignition Temperature (°C) 250 Flash Point (°C) -18 Lower explosivity limit (LEL) (volume %) 1.1 Upper explosivity limit (UEL) (volume %) 8.7
### Behaviour at sea
### Additional data
Colour colourless to brown,purple Odour gasoline odour Standard behavior classification E, FE, F
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 33 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name miscell. hydroc. mixt IMO class 3.1
### Reactivity data
Acid(s) Yes Static electricity Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 500 ppm TEEL-2 (mg/m3) 500 ppm TEEL-3 (mg/m3) 1500 ppm
### Ecotoxicity
# GLUCOSE
Also known as: DEXTROSE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Solid Molar mass (g/mol) 180.16 Melting Point (°C) 146
### Behaviour at sea
### Additional data
Colour white
### Transportation data
State solid
### Reactivity data
Reducing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# GLUTARALDEHYDE solution
Also known as: ALDEHYDE GLUTARIQUE en solution
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1093 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 100.1 Density of gas (kg/m3) 4.515 Boiling Point (°C) 187 Melting Point (°C) -14 Vapour Pressure (Pa) 2300 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour light yellow Odour rotten apple odour
### Transportation data
Cargo group 19 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aldehydes
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.2 ERPG-1 (ppm) 0.2
### Ecotoxicity
# GLYCERINE
CAS Number: 56-81-5
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 56-81-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1261 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 92.1 Density of gas (kg/m3) 4.089 Boiling Point (°C) 290 Melting Point (°C) 18 Vapour Pressure (Pa) 10100 [Pa] at a temperature of 20°C Ignition Temperature (°C) 400 Flash Point (°C) 160
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification DE, D
### Transportation data
Cargo group 20 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alcohols, glycols
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
TLV-TWA 2.5 TEEL-1 (mg/m3) 125 TEEL-2 (mg/m3) 500 TEEL-3 (mg/m3) 500
### Ecotoxicity
# GLYCEROL MONOOLEATE
CAS Number: 25496-72-4
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 25496-72-4
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 950 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 356 Boiling Point (°C) > 100 Melting Point (°C) 25/34 Flash Point (°C) 224
### Behaviour at sea
### Additional data
Colour yellow Odour sweet
### Transportation data
State solid Temperature (°C) < 34 �C Family name alcohols, glycols
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# GLYOXAL solutions (40% or less)
CAS Number: 107-22-2 Also known as: BIFORMYL, DIFORMYL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 107-22-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1290 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 58 Boiling Point (°C) 104 Melting Point (°C) -15 Vapour Pressure (Pa) 2400 [Pa] at a temperature of 20°C Ignition Temperature (°C) 285 Flash Point (°C) >100
### Behaviour at sea
### Additional data
Colour light yellow Odour weak sour
### Transportation data
Cargo group 19 State liquid Temperature (°C) -0.244897959 Family name aldehydes
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Combustibles Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 35 TEEL-2 (mg/m3) 75 TEEL-3 (mg/m3) 75
### Ecotoxicity
# HELIUM (compressed gas)
UN Number: 1046
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1046
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 1.25 [Kg/m³] at a temperature of 20°C Density of gas (kg/m3) 1.25 Boiling Point (°C) -268.75 Melting Point (°C) -272.2 Vapour Pressure (Pa) 25000000 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
### Transportation data
State liq.compr.gas IMO class 2(2.2)
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 65000 ppm TEEL-2 (mg/m3) 230000 ppm TEEL-3 (mg/m3) 400000 ppm
### Ecotoxicity
# HELIUM (refrigerated liquid)
UN Number: 1963
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1963
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 1.25 [Kg/m³] at a temperature of 20°C Density of gas (kg/m3) 1.25 Boiling Point (°C) -268.75 Melting Point (°C) -272.2 Vapour Pressure (Pa) 25000000 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
### Transportation data
State liquefied gas IMO class 2(2.2)
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 65000 ppm TEEL-2 (mg/m3) 230000 ppm TEEL-3 (mg/m3) 400000 ppm
### Ecotoxicity
# HEPTACHLOR solid
UN Number: 2761 Also known as: AGROARES, 2-CHLOROCHLORIDENE, DRINOX
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2761
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1660 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 373.5 Boiling Point (°C) 160 Melting Point (°C) 95
### Behaviour at sea
### Additional data
Colour white to light tan Odour camphor odour Marine pollutant P Standard behavior classification D, SD, S
### Transportation data
Transport mode Bulk,Packaged State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 45 TLV-TWA 0.03 TEEL-1 (mg/m3) 0.5 TEEL-2 (mg/m3) 0.5 TEEL-3 (mg/m3) 35
### Ecotoxicity
# HEPTANE
UN Number: 1206 - CAS Number: 142-82-5 Also known as: DIPROPYLMETHANE, Heptane, Heptyl Hydride, N-Heptane
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1206 CAS number 142-82-5 Formula C 7 H 1 6
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 683.8 [Kg/m³] at a temperature of 20°C 697.1 [Kg/m³] at a temperature of 5°C 693.8 [Kg/m³] at a temperature of 10°C 685.3 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.6 [cSt] at a temperature of 20°C 0.57 [cSt] at a temperature of 25°C 2.037 [cSt] at a temperature of 5°C 1.989 [cSt] at a temperature of 10°C 1.9408 [cSt] at a temperature of 20°C Molar mass (g/mol) 100.21 Density of gas (kg/m3) 4.463 Solubility (g/L) 3 [g/L] at a temperature of 25°C and salinity of 0‰ 3.2 [g/L] at a temperature of 20°C and salinity of 0‰ 2.8 [g/L] at a temperature of 20°C and salinity of 5‰ 0.48 [g/L] at a temperature of 20°C and salinity of 30‰ Boiling Point (°C) 98 Melting Point (°C) -91 Surface tension (mN/m) 19.3 [mN/m] at a temperature of 20°C 19.65 [mN/m] at a temperature of 25°C 21.6 [mN/m] at a temperature of 6°C 21.08 [mN/m] at a temperature of 10.1°C 20.32 [mN/m] at a temperature of 18.1°C Interfacial tension (mN/m) 51 [mN/m] at a temperature of 20°C and salinity of 0‰ Vapour Pressure (Pa) 4799 [Pa] at a temperature of 20°C 6133 [Pa] at a temperature of 25°C Ignition Temperature (°C) 220 Flash Point (°C) -4 Flash Point (Pensky- Martens closed cup) (°C) -4 Lower explosivity limit (LEL) (volume %) 1.2 Upper explosivity limit (UEL) (volume %) 6.7 Vapor enthalpy (J/Kg) 317065 [J/Kg] at a temperature of 98°C 364960 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 44600000 Specific heat capacity (J/(Kg·K)) 2242.4 Combustion efficiency (%) 97 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.11 Rad fraction (%) 33 Henry's constant (mol/(m³·Pa)) 202650
### Behaviour at sea
Log kow 4.66 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 10 Bioconcentration factor (BCF) 1480
### Additional data
Colour colourless Odour gasoline odour MARPOL pollution category Category Description X Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a major hazard to either marine resources or human health and, therefore, justify the prohibition of the discharge into the marine environment.
### Transportation data
Package group II Cargo group 31 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name paraffins IMO class 3.2
### Reactivity data
Water No Static electricity Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Specific Health Concern (D3) A - Aspiration Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 5000 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H304 May be fatal if swallowed and enters airways. H315 Causes skin irritation. H336 May cause drowsiness or dizziness. Environmental H410 Very toxic to aquatic life with long lasting effects. Precautionary statements General P102 Keep out of reach of children. Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P331 Do NOT induce vomiting. Disposal P501 Dispose of contents/container to ... TLV-TWA 400 TEEL-1 (mg/m3) 440 ppm TEEL-2 (mg/m3) 440 ppm TEEL-3 (mg/m3) 750 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 0.1 Lowest median lethal concentration (LC50) on fishes (mg/l) 4 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.17 Highest no observed effect concentration (NOEC) on fishes (mg/l) 1.284
# HEPTANOL
Also known as: ALCOHOL C7
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 822 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 116.2 Density of gas (kg/m3) 5.16 Boiling Point (°C) 176 Melting Point (°C) -30 Vapour Pressure (Pa) 100 [Pa] at a temperature of 20°C Flash Point (°C) 65
### Behaviour at sea
### Additional data
Colour colourless Odour weak alcohol odour
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 10 TEEL-2 (mg/m3) 500 TEEL-3 (mg/m3) 500
### Ecotoxicity
# HEPTYL ACETATE
Also known as: ACETATE D'HEPTYLE, ACETIC ACID, HEPTYL ESTER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 875 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 158.27 Density of gas (kg/m3) 7.1 Boiling Point (°C) 192.5 Melting Point (°C) -50.2 Flash Point (°C) 68
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification F/FE/E
### Transportation data
Cargo group 34 State liquid Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# HEXACHLOROCYCLOPENTADIENE
UN Number: 2646
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2646
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1720 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 272.7 Density of gas (kg/m3) 12.15 Boiling Point (°C) 239 Melting Point (°C) 10 Vapour Pressure (Pa) 1241 (104�C) [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour greenish yellow Odour harch unpleasant
### Transportation data
State liquid Temperature (°C) ambient IMO class 6.1
### Reactivity data
Water Yes Metal(s) and alloys Yes (Fe & others)
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.01 TEEL-1 (mg/m3) 0.0179 ppm TEEL-2 (mg/m3) 0.0179 ppm TEEL-3 (mg/m3) 0.0179 ppm
### Ecotoxicity
# Hexamethylenediamine
UN Number: 2280 - CAS Number: 124-09-4 Also known as: 1,6-Hexanediamine, 1,6-Diaminohexane, Hexane-1,6-Diamine, Hmda, Hexamethylenediamine
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2280 CAS number 124-09-4 Formula C 6 H 1 6 N 2
### Physical chemical data
Physical State (25°C) Solid Molar mass (g/mol) 116.204 Solubility (g/L) 10000000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 204.6 Melting Point (°C) 39.13 Flash Point (Cleveland open cup) (°C) 71 Lower explosivity limit (LEL) (volume %) 0.7 Upper explosivity limit (UEL) (volume %) 6.3 Combus enthalpy (J/Kg) 28400000 Henry's constant (mol/(m³·Pa)) 7e-05
### Behaviour at sea
Log kow 0.35 Log koc 2.21 Biodegradation in marine environment (Half- life) (days) Not biodegradable Bioconcentration factor (BCF) 1
### Additional data
MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
### Reactivity data
Abilities Soluble in water.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
Hazard statements Health H302 Harmful if swallowed. H312 Harmful in contact with skin. H314 Causes severe skin burns and eye damage. H335 May cause respiratory irritation. Precautionary statements Prevention P260 Do not breathe dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P330 + P331 IF SWALLOWED: rinse mouth. Do NOT induce vomiting. P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P310 Immediately call a POISON CENTER or doctor/physician.
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 14.8 Lowest median lethal concentration (LC50) on crustacean (mg/l) 23.4 Lowest median lethal concentration (LC50) on fishes (mg/l) 73.5 Highest no observed effect concentration (NOEC) on algae (mg/l) 3.2 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 4.16 Assessment factor (AF) 100 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 40 [µg/l] on the Short term
# HEXAMETHYLENEDIAMINE solution
UN Number: 1783 Also known as: 1,6-DIAMINO HEXANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1783
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 933 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 116.21 Density of gas (kg/m3) 5.16 Boiling Point (°C) 205 Melting Point (°C) 41 Vapour Pressure (Pa) 400 [Pa] at a temperature of 20°C Ignition Temperature (°C) 305 Flash Point (°C) 80 Lower explosivity limit (LEL) (volume %) 0.7 Upper explosivity limit (UEL) (volume %) 6.3
### Behaviour at sea
### Additional data
Colour colourless Odour weak ammonia odour
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid, solid Temperature (°C) ambient Pressure (Pa) under pressure Family name aliphatic amines
### Reactivity data
Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# HEXAMETHYLENEIMINE
UN Number: 2493 - CAS Number: 111-49-9 Also known as: AZACYCLOHEPTANE, CYCLO HEXAMETHYLENEAMINE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2493 CAS number 111-49-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 880 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 99 Boiling Point (°C) 132 Vapour Pressure (Pa) 665 [Pa] at a temperature of 20°C Lower explosivity limit (LEL) (volume %) 1.6 Upper explosivity limit (UEL) (volume %) 2.3
### Behaviour at sea
### Additional data
Colour colourless to light yellow Odour ammonia odour
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aliphatic amines IMO class 3.2
### Reactivity data
Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 40 TEEL-2 (mg/m3) 300 TEEL-3 (mg/m3) 500
### Ecotoxicity
# Hexamethylenetetramine Solutions
UN Number: 1328 - CAS Number: 100-97-0 Also known as: Hexamethylenetetramine Solutions, Solutions D'Hexamethylene Tetramine
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1328 CAS number 100-97-0 Formula C 6 H 1 2 N 4
### Physical chemical data
Physical State (25°C) Liquid Molar mass (g/mol) 140.186 Solubility (g/L) 10000000 [g/L] at a temperature of 20°C and salinity of 0‰
### Behaviour at sea
Log kow -2.13
### Additional data
MARPOL pollution category Category Description Other Substances Substances which have been evaluated and found to fall outside Category X, Y or Z because they are considered to present no harm to marine resources, human health, amenities or other legitimate uses of the sea when discharged into the sea from tank cleaning of deballasting operations. The discharge of bilge or ballast water or other residues or mixtures containing these substances are not subject to any requirements of MARPOL Annex II.
### Transportation data
### Reactivity data
Abilities Solution.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
Hazard statements Physical H228 Flammable solid. Health H317 May cause an allergic skin reaction. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P241 Use explosion-proof electrical/ventilating/lighting/.../equipment. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P302 + P352 IF ON SKIN: Wash with plenty of soap and water.
### Ecotoxicity
# HEXYL ACETATE
UN Number: 1233 - CAS Number: 142-92-7 Also known as: ACETATE D'HEXYLE, ACETIC ACID, HEXYL ESTER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1233 CAS number 142-92-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 876 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 144.21 Density of gas (kg/m3) 6.41 Boiling Point (°C) 168/170 Melting Point (°C) -80 Vapour Pressure (Pa) 400 [Pa] at a temperature of 20°C Flash Point (°C) 37 Lower explosivity limit (LEL) (volume %) 0.9 Upper explosivity limit (UEL) (volume %) 5.7
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification F/FE/E
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 34 State liquid Family name esters IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# HEXYLENE GLYCOL
CAS Number: 107-41-5
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 107-41-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 900 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 118.2 Density of gas (kg/m3) 5.16 Boiling Point (°C) 196 Melting Point (°C) -100 Vapour Pressure (Pa) 6.5 [Pa] at a temperature of 20°C Ignition Temperature (°C) 306 Flash Point (°C) 96 Lower explosivity limit (LEL) (volume %) 1.2 Upper explosivity limit (UEL) (volume %) 8.1
### Behaviour at sea
### Additional data
Colour colourless Odour mild sweet
### Transportation data
Cargo group 20 State liquid Temperature (°C) ambient Family name alcohols, glycols
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Reducing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TLV-TWA 25 TEEL-1 (mg/m3) 10 ppm TEEL-2 (mg/m3) 25 ppm TEEL-3 (mg/m3) 350 ppm
### Ecotoxicity
# HYDRAZINE aqueous solut. (up to 64 wt% hydrazine)
UN Number: 2030 Also known as: DIAMIDE, DIAMINE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2030
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1010 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 32.05 Density of gas (kg/m3) 1.35 Boiling Point (°C) 113.7 Vapour Pressure (Pa) 1386 [Pa] at a temperature of 20°C Ignition Temperature (°C) 270 Flash Point (°C) 5-38 Lower explosivity limit (LEL) (volume %) 4.7 Upper explosivity limit (UEL) (volume %) 100
### Behaviour at sea
### Additional data
Colour colourless Odour mild sweet odour
### Transportation data
Package group II State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name aliphatic amines
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 80 TLV-TWA 0.1 TEEL-1 (mg/m3) 0.0075 TEEL-2 (mg/m3) 0.0625 TEEL-3 (mg/m3) 50
### Ecotoxicity
# HYDROCHLORIC ACID solution
UN Number: 1789 - CAS Number: 7647-01-0 Also known as: ACIDE CHLORHYDRIQUE en solution, CHLOROHYDRIC ACID, Hydrochloric Acid Solutions (20%), Solutions D'Acide Chlorhydrique (20%)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1789 CAS number 7647-01-0 Formula HCl
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1190 [Kg/m³] at a temperature of 20°C 1098 [Kg/m³] at a temperature of 25°C Kinematic viscosity (cSt) 1.2386 [cSt] at a temperature of 20°C Molar mass (g/mol) 36.5 Density of gas (kg/m3) 1.677 Solubility (g/L) 10000000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 50 Melting Point (°C) -114 Vapour Pressure (Pa) 28000 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless Odour sharp, irritating odour MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment. Standard behavior classification DE
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name non oxid. min. acids
### Reactivity data
Water No Abilities Solution. Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 100 Hazard statements Health H314 Causes severe skin burns and eye damage. H331 Toxic if inhaled. Precautionary statements General P101 If medical advice is needed, have product container or label at hand. Prevention P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P314 Get medical advice/attention if you feel unwell. Storage P403 + P233 Store in a well-ventilated place. Keep container tightly closed. P405 Store locked up. ERPG-2 (ppm) 20 ERPG-3 (ppm) 150 10 min 30 min 60 min 4 hrs 8 hrs AEGL-1 (ppm) 1.8 1.8 1.8 1.8 1.8 AEGL-2 (ppm) 100 43 22 11 11 AEGL-3 (ppm) 620 210 100 26 26
### Ecotoxicity
# HYDROGEN BROMIDE
UN Number: 1048 Also known as: ACIDE BROMIDRIQUE ANHYDRE, BROMURE D'HYDROGENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1048
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 2140 (-67�C) [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 80.92 Density of gas (kg/m3) 3.5 Boiling Point (°C) -66.8 Melting Point (°C) -87 Vapour Pressure (Pa) 2445000 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless Odour irritating Standard behavior classification DE
### Transportation data
State gas Temperature (°C) ambient or lower IMO class 2(2.3)
### Reactivity data
Water Yes Metal(s) and alloys Yes
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 30 TEEL-1 (mg/m3) 1 ppm TEEL-2 (mg/m3) 22 ppm TEEL-3 (mg/m3) 120 ppm
### Ecotoxicity
# HYDROGEN PEROXIDE solutions (8 to 60%)
UN Number: 2014 - CAS Number: 7722-84-1 Also known as: EAU OXYGENEE, Hydroperoxide, Hydrogen Peroxide, Peroxyde D'Hydrogene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2014 CAS number 7722-84-1 Formula H 2 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1000/1200 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 34.01 (pure) Density of gas (kg/m3) 1.29/1.55 Solubility (g/L) 10000000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 100/114 Melting Point (°C) -50 Critical temperature (°C) 728 Critical pressure (Pa) 22000000 Surface tension (mN/m) 80.4 [mN/m] at a temperature of 20°C Vapour Pressure (Pa) 40/100 [Pa] at a temperature of 20°C 262.6 [Pa] at a temperature of 25°C Vapor enthalpy (J/Kg) 1517000 [J/Kg] at a temperature of 25°C Specific heat capacity (J/(Kg·K)) 2619 Henry's constant (mol/(m³·Pa)) 0.0007
### Behaviour at sea
Log kow -1.57 Log koc 1.12
### Additional data
Colour colourless Odour slighty sharp MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group I/II State liquid Temperature (°C) ambient IMO class 5.1
### Reactivity data
Water No Abilities Miscible in water. Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Reducing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 75 Hazard statements Physical H271 May cause fire or explosion, strong oxidiser. Health H302 Harmful if swallowed. H314 Causes severe skin burns and eye damage. H332 Harmful if inhaled. H335 May cause respiratory irritation. Environmental H412 Harmful to aquatic life with long lasting effects. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P370 + P378 In case of fire: Use ... for extinction. ERPG-1 (ppm) 10 ERPG-2 (ppm) 50 ERPG-3 (ppm) 100
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 2.4 Lowest median lethal concentration (LC50) on fishes (mg/l) 0.1 Highest no observed effect concentration (NOEC) on algae (mg/l) 0.1 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.61 Highest no observed effect concentration (NOEC) on fishes (mg/l) 5 Assessment factor (AF) 50 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 10 [µg/l] on the Short term
# HYDROGEN PEROXIDE stabilized
UN Number: 2015
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2015
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1290 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 34.01 Density of gas (kg/m3) 1.548 Boiling Point (°C) 125 Melting Point (°C) -30 Vapour Pressure (Pa) 100 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless Odour weak sharp odour
### Transportation data
Transport mode Bulk,Packaged State liquid Temperature (°C) ambient Pressure (Pa) under pressure IMO class 5.1
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 75 ERPG-1 (ppm) 10 ERPG-2 (ppm) 50 ERPG-3 (ppm) 100
### Ecotoxicity
# HYDROGEN SULPHIDE
UN Number: 1053
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1053
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 1.548 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 34.08 Density of gas (kg/m3) 1.548 Boiling Point (°C) -60.4 Melting Point (°C) -86 Vapour Pressure (Pa) 1924700 [Pa] at a temperature of 20°C Ignition Temperature (°C) 260 Lower explosivity limit (LEL) (volume %) 4.3 Upper explosivity limit (UEL) (volume %) 45
### Behaviour at sea
### Additional data
Colour colourless Odour rotten egg odour Standard behavior classification GD, G
### Transportation data
State liq.compr.gas Temperature (°C) ambient Pressure (Pa) under pressure IMO class 2(2.3)
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 300 TLV-TWA 10 ERPG-1 (ppm) 0.1 ERPG-2 (ppm) 30 ERPG-3 (ppm) 100
### Ecotoxicity
# IRON (III) OXIDE spent
UN Number: 1376
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1376
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 5240 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 159.69 Melting Point (°C) 1565
### Behaviour at sea
### Additional data
Colour red to reddish-brown Odour odourless
### Transportation data
Package group III State solid IMO class 4.2
### Reactivity data
Water No Metal(s) and alloys No Oxidizing agents No
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 15 TEEL-2 (mg/m3) 40 TEEL-3 (mg/m3) 250
### Ecotoxicity
# ISOAMYL ACETATE
UN Number: 1104 Also known as: ACETATE D'ISOAMYLE, ACETIC ACID, ISOPENTYL ESTER, AMYLACETIC ESTER, BANANA OIL (T)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1104
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 876 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 130.19 Density of gas (kg/m3) 5.805 Boiling Point (°C) 146 Melting Point (°C) -78 Vapour Pressure (Pa) 650 [Pa] at a temperature of 20°C Ignition Temperature (°C) 380 Flash Point (°C) 25 Lower explosivity limit (LEL) (volume %) 1.1 Upper explosivity limit (UEL) (volume %) 7.5
### Behaviour at sea
Persistence (days) 0.8
### Additional data
Colour colourless to yellow Odour banana odour Standard behavior classification FE
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 34 State liquid Temperature (°C) ambient Family name esters IMO class 3.3
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 3000 TLV-TWA 100 TEEL-1 (mg/m3) 100 ppm TEEL-2 (mg/m3) 200 ppm TEEL-3 (mg/m3) 1000 ppm
### Ecotoxicity
# ISOAMYL ALCOHOL
UN Number: 1105 - CAS Number: 123-51-3 Also known as: ALCOOL ISOAMYLIQUE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1105 CAS number 123-51-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 810 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 88.15 Density of gas (kg/m3) 3.87 Boiling Point (°C) 132 Melting Point (°C) -117 Vapour Pressure (Pa) 300 [Pa] at a temperature of 20°C Ignition Temperature (°C) 340 Flash Point (°C) 43 Lower explosivity limit (LEL) (volume %) 1.2
### Behaviour at sea
### Additional data
Colour colourless Odour mild choking, alcohol odour Standard behavior classification FED
### Transportation data
Package group III State liquid Temperature (°C) ambient Pressure (Pa) ambient IMO class 3.3
### Reactivity data
Static electricity Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 10000 TLV-TWA 100 TEEL-1 (mg/m3) 125 ppm TEEL-2 (mg/m3) 125 ppm TEEL-3 (mg/m3) 500 ppm
### Ecotoxicity
# ISOBUTANE
UN Number: 1969
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1969
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 2.709 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 58.12 Density of gas (kg/m3) 2.709 Boiling Point (°C) -11.6 Melting Point (°C) -160 Vapour Pressure (Pa) 202600 [Pa] at a temperature of 20°C Ignition Temperature (°C) 460 Flash Point (°C) -20 Lower explosivity limit (LEL) (volume %) 1.8 Upper explosivity limit (UEL) (volume %) 8.4
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
State liq.compr.gas Temperature (°C) ambient Pressure (Pa) under pressure IMO class 2(2.1)
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 3000 ppm TEEL-2 (mg/m3) 5000 ppm TEEL-3 (mg/m3) 15000 ppm
### Ecotoxicity
# ISOBUTANOL
UN Number: 1212 - CAS Number: 78-83-1 Also known as: Alcool Isobutylique, Isobutanol, Isopropyl Carbinol, 1-Hydroxymethylpropane, 2-Methyl-1-Propanol, Isobutyl Alcohol
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1212 CAS number 78-83-1 Formula C 4 H 1 0 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 802 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 5 [cSt] at a temperature of 20°C 4.1532 [cSt] at a temperature of 25°C Molar mass (g/mol) 74.12 Density of gas (kg/m3) 3.354 Solubility (g/L) 98000 [g/L] at a temperature of 20°C and salinity of 0‰ 85000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 108.1 Melting Point (°C) -108 Critical molar volume (m³/mol) 0.000274 Critical temperature (°C) 547.8 Critical pressure (Pa) 4295000 Vapour Pressure (Pa) 1200 [Pa] at a temperature of 20°C 1330 [Pa] at a temperature of 25°C Ignition Temperature (°C) 430 Flash Point (°C) 27 Flash Point (Pensky-Martens closed cup) (°C) 28 Flash Point (Cleveland open cup) (°C) 32.2 Lower explosivity limit (LEL) (volume %) 1.6 Upper explosivity limit (UEL) (volume %) 10.9 Vapor enthalpy (J/Kg) 524220 [J/Kg] at a temperature of 108°C 685645 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 35900000 Specific heat capacity (J/(Kg·K)) 226.88 Combustion efficiency (%) 98 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.05 Rad fraction (%) 22 Henry's constant (mol/(m³·Pa)) 0.99
### Behaviour at sea
Log kow 0.76 Log koc 1.75 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 10 Bioconcentration factor (BCF) 1.97
### Additional data
Colour colourless Odour mild choking, alcohol odour MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment.
### Transportation data
Package group III State liquid Temperature (°C) ambient Pressure (Pa) ambient IMO class 3.3
### Reactivity data
Static electricity Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 8000 Hazard statements Physical H226 Flammable liquid and vapour. Health H315 Causes skin irritation. H318 Causes serious eye damage. H335 May cause respiratory irritation. H336 May cause drowsiness or dizziness. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P233 Keep container tightly closed. P240 Ground/bond container and receiving equipment. P241 Use explosion-proof electrical/ventilating/lighting/.../equipment. P242 Use only non- sparking tools. P243 Take precautionary measures against static discharge. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P370 + P378 In case of fire: Use ... for extinction. Storage P403 + P235 Store in a well-ventilated place. Keep cool. Disposal P501 Dispose of contents/container to ... TLV-TWA 50 TEEL-1 (mg/m3) 1250 ppm TEEL-2 (mg/m3) 1600 ppm TEEL-3 (mg/m3) 1600 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 225 Lowest median lethal concentration (LC50) on crustacean (mg/l) 1100 Lowest median lethal concentration (LC50) on fishes (mg/l) 1430 Highest no observed effect concentration (NOEC) on algae (mg/l) 53 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 20 Assessment factor (AF) 1000 on the Short term 10000 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 225 [µg/l] on the Short term 22.5 [µg/l] on the Long term
# ISOBUTYL ACETATE
UN Number: 1213 Also known as: ACETATE D'ISOBUTYLE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1213
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 871 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 116.16 Density of gas (kg/m3) 2.761 Boiling Point (°C) 117.5 Melting Point (°C) -99 Vapour Pressure (Pa) 13333 [Pa] at a temperature of 20°C Ignition Temperature (°C) 420 Flash Point (°C) 18 Upper explosivity limit (UEL) (volume %) 15
### Behaviour at sea
### Additional data
Colour colourless Odour pleasant, fruit odour
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient IMO class 3.2
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Static electricity Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 7500 TLV-TWA 150 TEEL-1 (mg/m3) 150 ppm TEEL-2 (mg/m3) 250 ppm TEEL-3 (mg/m3) 1300 ppm
### Ecotoxicity
# ISOBUTYLENE
UN Number: 1055
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1055
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 2.451 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 56.1 Density of gas (kg/m3) 2.451 Boiling Point (°C) -6.7 Melting Point (°C) -140 Vapour Pressure (Pa) 19995 [Pa] at a temperature of 20°C Ignition Temperature (°C) 465 Flash Point (°C) -76.1 Lower explosivity limit (LEL) (volume %) 1.8 Upper explosivity limit (UEL) (volume %) 9.6
### Behaviour at sea
### Additional data
Colour colourless Odour sweet, gasoline odour
### Transportation data
State liq.compr.gas Temperature (°C) ambient Pressure (Pa) under pressure IMO class 2(2.1)
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 750 ppm TEEL-2 (mg/m3) 1250 ppm TEEL-3 (mg/m3) 100000 ppm
### Ecotoxicity
# ISODECALDEHYDE
UN Number: 3082 Also known as: ALDEHYDE ISODECALIQUE, 2,6-DIMETHYL OCTANAL, 2,6-DIMETHYL OCTANOIC ALDEHYDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 840 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 156.28 Density of gas (kg/m3) 5.65 Vapour Pressure (Pa) 29 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless Odour fruit odour
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# ISODECANOL
CAS Number: 25339-17-7
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 25339-17-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 841 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 158.29 Boiling Point (°C) 220 Vapour Pressure (Pa) 400 [Pa] at a temperature of 20°C Ignition Temperature (°C) 266 Flash Point (°C) 104 Lower explosivity limit (LEL) (volume %) 0.8 Upper explosivity limit (UEL) (volume %) 4.5
### Behaviour at sea
Persistence (days) 0.8
### Additional data
Colour colourless Odour mild alcohol odour Standard behavior classification E, FE, F
### Transportation data
Cargo group 20 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alcohols, glycols
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# ISODECANOL inhibited
Also known as: ACRYLATE D'ISODECYLE stabilisé, ACRYLIC ACID, ISODECYL ESTER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 885 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 212.4 Density of gas (kg/m3) 9.42
### Behaviour at sea
Persistence (days) 0.8
### Additional data
Colour colourless Odour weak odour Standard behavior classification D, FD, F
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# ISOPENTANE
UN Number: 1265
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1265
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 620 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 72.15 Density of gas (kg/m3) 3.225 Boiling Point (°C) 28.1 Melting Point (°C) -160 Vapour Pressure (Pa) 99000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 420 Flash Point (°C) -20 Lower explosivity limit (LEL) (volume %) 1.4 Upper explosivity limit (UEL) (volume %) 7.6
### Behaviour at sea
### Additional data
Colour colourless Odour gasoline odour
### Transportation data
Transport mode Bulk,Packaged Package group I/II Cargo group 31 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name paraffins IMO class 3.1
### Reactivity data
Water No
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 610 ppm TEEL-2 (mg/m3) 610 ppm TEEL-3 (mg/m3) 20000 ppm
### Ecotoxicity
# ISOPHORONE
CAS Number: 78-79-5
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 78-79-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 921 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 138.2 Density of gas (kg/m3) 6.153 Boiling Point (°C) 215 Melting Point (°C) -8 Vapour Pressure (Pa) 40 [Pa] at a temperature of 20°C Ignition Temperature (°C) 460 Flash Point (°C) 96 Lower explosivity limit (LEL) (volume %) 0.84 Upper explosivity limit (UEL) (volume %) 3.8
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour colourless Odour camphor odour Standard behavior classification FD
### Transportation data
Cargo group 18 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name ketones
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 800 TEEL-1 (mg/m3) 0.71 ppm TEEL-2 (mg/m3) 0.71 ppm TEEL-3 (mg/m3) 200 ppm
### Ecotoxicity
# ISOPHORONE DIAMINE
UN Number: 2289 - CAS Number: 2855-13-2 Also known as: 3-AMINOMETHYL-3,5,5-TRIMETHYLCYCLOHEXYLAMINE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2289 CAS number 2855-13-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 924 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 170.3 Boiling Point (°C) 247 Melting Point (°C) 10 Vapour Pressure (Pa) 20.7 [Pa] at a temperature of 20°C Flash Point (°C) 110 Lower explosivity limit (LEL) (volume %) 1.2
### Behaviour at sea
### Additional data
Colour colourless Odour faint amine
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) ambient Family name aliphatic amines
### Reactivity data
Water No Acid(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Specific Health Concern (D3) Ss - Skin Sensitization Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# ISOPHORONE DIISOCYANATE
UN Number: 2290 - CAS Number: 4098-71-9 Also known as: DIISOCYANATE D'ISOPHORONE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2290 CAS number 4098-71-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1060 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 222.32 Density of gas (kg/m3) 9.93 Boiling Point (°C) decomp at 310 Melting Point (°C) -60 Vapour Pressure (Pa) 40 [Pa] at a temperature of 20°C Ignition Temperature (°C) 430 Flash Point (°C) 163 Lower explosivity limit (LEL) (volume %) 0.7 Upper explosivity limit (UEL) (volume %) 4.5
### Behaviour at sea
### Additional data
Colour colourless or yellowish Odour odourless
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 12 Family name isocyanates IMO class 6.1
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes (Al, Cu) Oxidizing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TLV-TWA 0.005 TEEL-1 (mg/m3) 0.02 ppm TEEL-2 (mg/m3) 0.135 ppm TEEL-3 (mg/m3) 6 ppm
### Ecotoxicity
# ISOPRENE inhibited
UN Number: 1218
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1218
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 681 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 68.12 Density of gas (kg/m3) 3.032 Boiling Point (°C) 34.3 Melting Point (°C) -146 Vapour Pressure (Pa) 53320 [Pa] at a temperature of 20°C Ignition Temperature (°C) 220 Flash Point (°C) -20
### Behaviour at sea
### Additional data
Colour colourless Odour mild odour
### Transportation data
Transport mode Bulk,Gas,Packaged Ship type 2G,2PG Cargo group 30 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name olefins IMO class 3.1
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Static electricity Yes Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
ERPG-2 (ppm) 1000 ERPG-3 (ppm) 4000
### Ecotoxicity
# ISOPROPANOL
UN Number: 1219 - CAS Number: 67-63-0 Also known as: DIMETHYL CARBINOL, Dimethylcarbinol, 2-Hydroxypropane, Ipa, Isopropanol, Isopropyl Alcohol, Propan-2-Ol, Sec-Propyl Alcohol, 2-Propyl Alcohol, Propanol, Propyl Alcohol, 2-Propanol
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1219 CAS number 67-63-0 Formula C 3 H 8 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 785 [Kg/m³] at a temperature of 20°C 787.5 [Kg/m³] at a temperature of 5°C 794.6 [Kg/m³] at a temperature of 10°C 794.6 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 3.05 [cSt] at a temperature of 20°C 2.59 [cSt] at a temperature of 25°C 5.6381 [cSt] at a temperature of 5°C 4.5683 [cSt] at a temperature of 10°C 4.4173 [cSt] at a temperature of 20°C Molar mass (g/mol) 60.1 Density of gas (kg/m3) 2.67 Solubility (g/L) 790000 [g/L] at a temperature of 20°C and salinity of 0‰ 790000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 82.5 Melting Point (°C) -88 Critical molar volume (m³/mol) 0.000222 Critical temperature (°C) 508.3 Critical pressure (Pa) 4764000 Surface tension (mN/m) 21.32 [mN/m] at a temperature of 20°C 20.93 [mN/m] at a temperature of 25°C 21.44 [mN/m] at a temperature of 6.9°C 21.0 [mN/m] at a temperature of 12.5°C 20.79 [mN/m] at a temperature of 20.2°C Vapour Pressure (Pa) 27593 [Pa] at a temperature of 20°C 6060 [Pa] at a temperature of 25°C Ignition Temperature (°C) 395 Flash Point (°C) 12 Flash Point (Pensky- Martens closed cup) (°C) 12 Flash Point (Cleveland open cup) (°C) 14 Lower explosivity limit (LEL) (volume %) 2.3 Upper explosivity limit (UEL) (volume %) 12.7 Vapor enthalpy (J/Kg) 663172 [J/Kg] at a temperature of 82.3°C 755367 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 30500000 Specific heat capacity (J/(Kg·K)) 2604.4 Combustion efficiency (%) 98 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.05 Rad fraction (%) 22 Henry's constant (mol/(m³·Pa)) 1.06
### Behaviour at sea
Log kow 0.05 Log koc 1.5 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 10 Bioconcentration factor (BCF) 1
### Additional data
Colour colourless Odour unpleasant alcohol odour MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment. Standard behavior classification DE
### Transportation data
Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient IMO class 3.2
### Reactivity data
Abilities Miscible in water. Static electricity Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 20000 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H319 Causes serious eye irritation. H336 May cause drowsiness or dizziness. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P233 Keep container tightly closed. P240 Ground/bond container and receiving equipment. P241 Use explosion-proof electrical/ventilating/lighting/.../equipment. P242 Use only non- sparking tools. P243 Take precautionary measures against static discharge. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P264 Wash ... thoroughly after handling. P271 Use only outdoors or in a well-ventilated area. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P312 Call a POISON CENTER or doctor/physician if you feel unwell. P337 + P313 If eye irritation persists: Get medical advice/attention. P370 + P378 In case of fire: Use ... for extinction. Storage P403 + P233 Store in a well-ventilated place. Keep container tightly closed. P403 + P235 Store in a well-ventilated place. Keep cool. P405 Store locked up. Disposal P501 Dispose of contents/container to ... TLV-TWA 400 TEEL-1 (mg/m3) 400 ppm TEEL-2 (mg/m3) 400 ppm TEEL-3 (mg/m3) 2000 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 1800 Lowest median lethal concentration (LC50) on crustacean (mg/l) 1400 Lowest median lethal concentration (LC50) on fishes (mg/l) 9640 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 30 Assessment factor (AF) 1000 on the Short term 1000 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 1400 [µg/l] on the Short term 30 [µg/l] on the Long term
# ISOPROPANOLAMINE
CAS Number: 78-96-6 Also known as: 1-AMINOPROPANOL-2
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 78-96-6
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 970 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 75.1 Density of gas (kg/m3) 3.35 Boiling Point (°C) 159 Vapour Pressure (Pa) 190 [Pa] at a temperature of 20°C Ignition Temperature (°C) 335 Flash Point (°C) 71 Lower explosivity limit (LEL) (volume %) 2.2 Upper explosivity limit (UEL) (volume %) 12
### Behaviour at sea
### Additional data
Colour colourless Odour characteristic
### Transportation data
Family name alkanolamines
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# ISOPROPYL ACETATE
UN Number: 1220 - CAS Number: 108-21-4 Also known as: ACETATE D'ISOPROPYLE, ACETIC ACID, ISOPROPYL ESTER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1220 CAS number 108-21-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 874 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 102.13 Density of gas (kg/m3) 3.52 Boiling Point (°C) 88.7 Melting Point (°C) -73 Vapour Pressure (Pa) 6483 [Pa] at a temperature of 20°C Ignition Temperature (°C) 460 Lower explosivity limit (LEL) (volume %) 1.8
### Behaviour at sea
### Additional data
Colour colourless Odour pleasant, fruit odour Standard behavior classification D, ED, E
### Transportation data
Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient IMO class 3.2
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 16000 TLV-TWA 250 TEEL-1 (mg/m3) 200 ppm TEEL-2 (mg/m3) 200 ppm TEEL-3 (mg/m3) 1800 ppm
### Ecotoxicity
# ISOPROPYL CYCLOHEXANE
CAS Number: 696-29-7
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 696-29-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 802 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 126.24 Density of gas (kg/m3) 5.61 Boiling Point (°C) 154.5 Melting Point (°C) -89.4 Ignition Temperature (°C) 283 Flash Point (°C) 36
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Cargo group 31 State liquid Temperature (°C) ambient Family name paraffins
### Reactivity data
Water No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# ISOPROPYLAMINE
UN Number: 1221 - CAS Number: 75-31-0 Also known as: 2-AMINOPROPANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1221 CAS number 75-31-0
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 691 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 59.11 Density of gas (kg/m3) 2.63 Boiling Point (°C) 32.4 Melting Point (°C) -95 Vapour Pressure (Pa) 66580 [Pa] at a temperature of 20°C Ignition Temperature (°C) 402 Flash Point (°C) -26 Lower explosivity limit (LEL) (volume %) 2.3 Upper explosivity limit (UEL) (volume %) 12
### Behaviour at sea
### Additional data
Colour colourless Odour strong ammonia Standard behavior classification DE
### Transportation data
Transport mode Bulk,Packaged State liquid Temperature (°C) ambient Family name aliphatic amines IMO class 3.1
### Reactivity data
Water No Acid(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 750 TEEL-1 (mg/m3) 10 ppm TEEL-2 (mg/m3) 150 ppm TEEL-3 (mg/m3) 750 ppm
### Ecotoxicity
# ISOPROPYLAMINE
UN Number: 1221 Also known as: 2-AMINOPROPANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1221
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 691 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 59.11 Density of gas (kg/m3) 2.58 Boiling Point (°C) 32.6 Melting Point (°C) -95 Vapour Pressure (Pa) 61300 [Pa] at a temperature of 20°C Ignition Temperature (°C) 402 Flash Point (°C) -37 Lower explosivity limit (LEL) (volume %) 2.3 Upper explosivity limit (UEL) (volume %) 12
### Behaviour at sea
### Additional data
Colour colourless Odour strong ammonia odour Standard behavior classification DE
### Transportation data
Transport mode Bulk,Gas,Packaged Ship type 2G,2PG State liquid Temperature (°C) ambient Pressure (Pa) ambient IMO class 3.1
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 4000 TEEL-1 (mg/m3) 10 ppm TEEL-2 (mg/m3) 150 ppm TEEL-3 (mg/m3) 750 ppm
### Ecotoxicity
# ISOPROPYLBENZENE
UN Number: 1918 - CAS Number: 98-82-8 Also known as: CUMENE, CUMOL, 2-Phenylpropane, Isopropylbenzene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1918 CAS number 98-82-8 Formula C 9 H 1 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 866 [Kg/m³] at a temperature of 20°C 864 [Kg/m³] at a temperature of 25°C Kinematic viscosity (cSt) 0.853 [cSt] at a temperature of 25°C Molar mass (g/mol) 120.19 Density of gas (kg/m3) 5.354 Solubility (g/L) 50 [g/L] at a temperature of 20°C and salinity of 0‰ 61.3 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 152 Melting Point (°C) -96 Critical temperature (°C) 631 Critical pressure (Pa) 3209000 Surface tension (mN/m) 27.69 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 5333 [Pa] at a temperature of 20°C 600 [Pa] at a temperature of 25°C Ignition Temperature (°C) 420 Flash Point (°C) 31 Flash Point (Pensky-Martens closed cup) (°C) 39 Lower explosivity limit (LEL) (volume %) 0.9 Upper explosivity limit (UEL) (volume %) 6.5 Vapor enthalpy (J/Kg) 375485 [J/Kg] at a temperature of 25°C Specific heat capacity (J/(Kg·K)) 1753 Henry's constant (mol/(m³·Pa)) 1165
### Behaviour at sea
Log kow 3.66 Log koc 2.84 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) Not biodegradable Bioconcentration factor (BCF) 35.5
### Additional data
Colour colourless Odour gasoline odour MARPOL pollution category Category Description Other Substances Substances which have been evaluated and found to fall outside Category X, Y or Z because they are considered to present no harm to marine resources, human health, amenities or other legitimate uses of the sea when discharged into the sea from tank cleaning of deballasting operations. The discharge of bilge or ballast water or other residues or mixtures containing these substances are not subject to any requirements of MARPOL Annex II.
### Transportation data
Package group III Cargo group 32 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aromatic hydrocarbons IMO class 3.3
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 8000 Hazard statements Physical H226 Flammable liquid and vapour. Health H304 May be fatal if swallowed and enters airways. H335 May cause respiratory irritation. Environmental H411 Toxic to aquatic life with long lasting effects. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P333 If skin irritation or rash occurs: TLV-TWA 50 TEEL-1 (mg/m3) 50 ppm TEEL-2 (mg/m3) 300 ppm TEEL-3 (mg/m3) 730 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 7.4 Lowest median lethal concentration (LC50) on fishes (mg/l) 2.7 Highest no observed effect concentration (NOEC) on algae (mg/l) 0.73 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.00068 Highest no observed effect concentration (NOEC) on fishes (mg/l) 0.0019 Predicted No Effect Concentration (PNEC) (µg/l) 22 [µg/l] on the Long term
# KEROSENE
UN Number: 1223
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1223
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 800 [Kg/m³] at a temperature of 20°C Density of gas (kg/m3) 5.81 Boiling Point (°C) 200 Melting Point (°C) -20 Vapour Pressure (Pa) 271 [Pa] at a temperature of 20°C Ignition Temperature (°C) 220 Flash Point (°C) 30 Lower explosivity limit (LEL) (volume %) 0.7
### Behaviour at sea
### Additional data
Colour colourless Odour gasoline odour
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 33 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name miscell. hydroc. mixt IMO class 3.3
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 200 TEEL-1 (mg/m3) 290 TEEL-2 (mg/m3) 1100 TEEL-3 (mg/m3) 1100
### Ecotoxicity
# LACTIC ACID
CAS Number: 50-21-5 Also known as: ACIDE LACTIQUE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 50-21-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1200 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 90
### Behaviour at sea
### Additional data
Colour colourless to yellow Odour weak unpleasant odour
### Transportation data
State syrupy liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 40 TEEL-2 (mg/m3) 300 TEEL-3 (mg/m3) 500
### Ecotoxicity
# LATEX liquid synthetic
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1057 [Kg/m³] at a temperature of 20°C
### Behaviour at sea
Persistence (days) 1.9
### Additional data
Colour white Odour characteristic odour
### Transportation data
Cargo group 43 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name miscell. water solut.
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# Lauric Acid
CAS Number: 143-07-7 Also known as: Dodecanoic Acid, Dodecylic Acid, Vulvic Acid, Laurostearic Acid, Lauric Acid, Acide Laurique
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 143-07-7 Formula C 1 2 H 2 4 O 2
### Physical chemical data
Physical State (25°C) Solid Kinematic viscosity (cSt) 8.41 [cSt] at a temperature of 50°C Molar mass (g/mol) 200.318 Solubility (g/L) 4.81 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 225 Melting Point (°C) 43.8 Critical temperature (°C) 743 Critical pressure (Pa) 1930000 Surface tension (mN/m) 26.6 [mN/m] at a temperature of 70°C Combus enthalpy (J/Kg) 37009655 Henry's constant (mol/(m³·Pa)) 0.94
### Behaviour at sea
Log kow 4.2 Log koc 2.5 Biodegradation in estuary environment (Half- life) (days) Not hydrolysable Bioconcentration factor (BCF) 255
### Additional data
MARPOL pollution category Category Description X Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a major hazard to either marine resources or human health and, therefore, justify the prohibition of the discharge into the marine environment.
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
Hazard statements Health H318 Causes serious eye damage. Precautionary statements Prevention P280 Wear protective gloves/protective clothing/eye protection/face protection.
### Ecotoxicity
Lowest median lethal concentration (LC50) on fishes (mg/l) 35 Highest no observed effect concentration (NOEC) on algae (mg/l) 4.4 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 1.5 Highest no observed effect concentration (NOEC) on fishes (mg/l) 6.4
# LEAD ACETATE
UN Number: 1616 Also known as: ACETATE DE PLOMB, DIBASIC LEAD ACETATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1616
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2600 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 379.3 Density of gas (kg/m3) 2600 Boiling Point (°C) 200 Melting Point (°C) 75
### Behaviour at sea
### Additional data
Colour white Odour odourless Standard behavior classification SD
### Transportation data
Package group III State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.02 (Pb) TEEL-1 (mg/m3) 0.235 TEEL-2 (mg/m3) 75 TEEL-3 (mg/m3) 157
### Ecotoxicity
# LEAD ARSENATE
UN Number: 1617 Also known as: ARSENIATES DE PLOMB
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1617
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 7800 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 347.12 Density of gas (kg/m3) 7800 Melting Point (°C) 280
### Behaviour at sea
### Additional data
Colour white Odour odourless Standard behavior classification D, SD, S
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.01 (Pb) TEEL-1 (mg/m3) 0.012 TEEL-2 (mg/m3) 0.012 TEEL-3 (mg/m3) 30
### Ecotoxicity
# LEAD NITRATE
UN Number: 1469
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1469
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 4500 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 331.2 Melting Point (°C) 470
### Behaviour at sea
### Additional data
Colour white Odour odourless Standard behavior classification SD
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 5.1
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.02 (Pb) TEEL-1 (mg/m3) 0.6 TEEL-3 (mg/m3) 160
### Ecotoxicity
# LINDANE
UN Number: 2761 Also known as: AFICIDE, gamma-BENZENE HEXACHLORIDE, BENZENE HEXACHLORIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2761
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1900 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 290.85 Boiling Point (°C) 323 Melting Point (°C) 112.5/113.5 Vapour Pressure (Pa) 1.2 [Pa] at a temperature of 20°C Flash Point (°C) 999
### Behaviour at sea
### Additional data
Marine pollutant P
### Transportation data
Package group I/II/III State solid IMO class 6.1
### Reactivity data
Base(s) Yes Metal(s) and alloys Yes (Al)
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 80 TEEL-1 (mg/m3) 1.5 TEEL-2 (mg/m3) 50 TEEL-3 (mg/m3) 50
### Ecotoxicity
# MAGNESIUM HYDROXIDE slurry
CAS Number: 1309-42-8
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 1309-42-8
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2400 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 58.3 Melting Point (°C) 350
### Behaviour at sea
### Additional data
Colour white Odour odourless
### Transportation data
### Reactivity data
Water No Acid(s) Yes Combustibles Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
### Ecotoxicity
# MAGNESIUM PHOSPHIDE
UN Number: 2011
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2011
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2060 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 134.86 Boiling Point (°C) 1000, decomp. Melting Point (°C) >750
### Behaviour at sea
### Additional data
### Transportation data
State solid IMO class 4.3
### Reactivity data
Water Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 0.6 ppm TEEL-2 (mg/m3) 1 ppm TEEL-3 (mg/m3) 1.8 ppm
### Ecotoxicity
# MALATHION
UN Number: 3082
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1234 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 330.36 Flash Point (°C) 163
### Behaviour at sea
### Additional data
Colour yellow to dark brown Odour skunk odour
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) < 49�
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 350 TLV-TWA 0.7 TEEL-1 (mg/m3) 15 TEEL-2 (mg/m3) 15 TEEL-3 (mg/m3) 250
### Ecotoxicity
# MALEIC ANHYDRIDE molten
UN Number: 2215 - CAS Number: 108-31-6 Also known as: ANHYDRIDE MALEIQUE fondu, cis-BUTENEDIOIC ANHYDRIDE, Butenedioic Anhydride, 2,5-Furandione, Toxilic Anhydride, Maleic Anhydride
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2215 CAS number 108-31-6 Formula C 4 H 2 O 3
### Physical chemical data
Physical State (20°C) Solid Physical State (25°C) Solid Density (kg/m3) 134 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 98.06 Density of gas (kg/m3) 4.36 Solubility (g/L) 4912 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 200 Melting Point (°C) 53 Critical temperature (°C) 721 Critical pressure (Pa) 7280000 Ignition Temperature (°C) 475 Flash Point (°C) 103 Flash Point (Pensky-Martens closed cup) (°C) 102 Flash Point (Cleveland open cup) (°C) 110 Lower explosivity limit (LEL) (volume %) 1.4 Upper explosivity limit (UEL) (volume %) 7.1 Henry's constant (mol/(m³·Pa)) 0.398
### Behaviour at sea
Persistence (days) 1.6 Log kow 1.62 Log koc 0 Biodegradation in estuary environment (Half-life) (days) 0.00208 Bioconcentration factor (BCF) 5
### Additional data
Colour colourless Odour choking odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification D, FD, F
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys No Static electricity Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
Hazard statements Health H302 Harmful if swallowed. H314 Causes severe skin burns and eye damage. H317 May cause an allergic skin reaction. H334 May cause allergy or asthma symptoms or breathing difficulties if inhaled. Precautionary statements Prevention P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. P284 Wear respiratory protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P342 + P311 If experiencing respiratory symptoms: Call a POISON CENTER or doctor/physician. TLV- TWA 0.25 ERPG-1 (ppm) 0.2 ERPG-3 (ppm) 20
### Ecotoxicity
Lowest median lethal concentration (LC50) on fishes (mg/l) 230 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 17.5 Highest no observed effect concentration (NOEC) on fishes (mg/l) 150 Assessment factor (AF) 1000 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 10 [µg/l] on the Short term
# Marine Diesel Oil
CAS Number: 68476-34-6 Also known as: Mdo, Marine Diesel Oil, Diesel Marine Leger
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 68476-34-6
### Physical chemical data
Physical State (25°C) Liquid Mixed Yes Solubility (g/L) 0 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 150 Lower explosivity limit (LEL) (volume %) 0.7 Upper explosivity limit (UEL) (volume %) 5
### Behaviour at sea
### Additional data
MARPOL pollution category Category Description Other Substances Substances which have been evaluated and found to fall outside Category X, Y or Z because they are considered to present no harm to marine resources, human health, amenities or other legitimate uses of the sea when discharged into the sea from tank cleaning of deballasting operations. The discharge of bilge or ballast water or other residues or mixtures containing these substances are not subject to any requirements of MARPOL Annex II.
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Interference with coastal amenities (E2) G - Gas
### Human toxicity threshold
### Ecotoxicity
# MERCURIC AMMONIUM CHLORIDE
UN Number: 1636 Also known as: CIANURRINA, CYANURE DE MERCURE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1636
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 3996 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 252.63
### Behaviour at sea
Persistence (days) 3.1
### Additional data
Colour white Odour odourless Marine pollutant P
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.006 (Pb) TEEL-1 (mg/m3) 1.5 TEEL-2 (mg/m3) 12.6 TEEL-3 (mg/m3) 12.6
### Ecotoxicity
# MERCURIC AMMONIUM CHLORIDE
UN Number: 1630 Also known as: AMINO MERCURIC CHLORIDE, AMMONIATED MERCURIC CHLORIDE, AMMONIATED MERCURY, CHLORURE DE MERCURE AMMONIACAL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1630
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 5700 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 252.1
### Behaviour at sea
Persistence (days) 2.7
### Additional data
Colour white Odour odourless Marine pollutant P Standard behavior classification D, SD, S
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.012 (Pb)
### Ecotoxicity
# MERCURIC CHLORIDE
UN Number: 1624 Also known as: CHLORURE MERCURIQUE, CORROSIVE SUBLIMATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1624
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 5400 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 271.5 Boiling Point (°C) 302 Melting Point (°C) 276 Vapour Pressure (Pa) 0.1 [Pa] at a temperature of 20°C
### Behaviour at sea
Persistence (days) 3.1
### Additional data
Colour white Odour odourless Marine pollutant P
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.005 (Pb) TEEL-2 (mg/m3) 13.5 TEEL-3 (mg/m3) 13.5
### Ecotoxicity
# MERCURIC NITRATE
UN Number: 1625
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1625
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 4390 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 342.6 Melting Point (°C) 79
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour white Odour sharp odour Marine pollutant P Standard behavior classification SD
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.006 (Pb) TEEL-1 (mg/m3) 0.0405 TEEL-2 (mg/m3) 0.162 TEEL-3 (mg/m3) 16.2
### Ecotoxicity
# MERCUROUS CHLORIDE solid
UN Number: 3077 Also known as: CHLORURE DE MERCURE (I) solide
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3077
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 7150 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 236.1
### Behaviour at sea
### Additional data
Colour white Odour odourless Marine pollutant P Standard behavior classification D, SD, S
### Transportation data
State solid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.006 (Pb) TEEL-1 (mg/m3) 0.0883 TEEL-2 (mg/m3) 1.18 TEEL-3 (mg/m3) 11.8
### Ecotoxicity
# MERCUROUS NITRATE
UN Number: 1627
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1627
### Physical chemical data
Physical State (20°C) Solid Molar mass (g/mol) 280.6
### Behaviour at sea
### Additional data
Colour white Odour weak odour Marine pollutant P Standard behavior classification D, SD, FD
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.006 (Pb) TEEL-1 (mg/m3) 0.0327 TEEL-2 (mg/m3) 0.131 TEEL-3 (mg/m3) 13.1
### Ecotoxicity
# MERCURY ACETATE
UN Number: 1629 Also known as: ACETATE DE MERCURE, DIACETOXYMERCURY
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1629
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 3270 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 318.7 Melting Point (°C) 178
### Behaviour at sea
Persistence (days) 2.7
### Additional data
Colour white Odour mild vinegar odour Marine pollutant P Standard behavior classification SD
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.005 (Pb) TEEL-1 (mg/m3) 0.159 TEEL-2 (mg/m3) 0.159 TEEL-3 (mg/m3) 15.9
### Ecotoxicity
# MERCURY IODIDE
UN Number: 1638
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1638
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 6300 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 454.9 Boiling Point (°C) 354 Vapour Pressure (Pa) 20881 [Pa] at a temperature of 20°C
### Behaviour at sea
Persistence (days) 1.9
### Additional data
Colour red Odour odourless
### Transportation data
Transport mode Bulk,Packaged State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.005 (Pb) TEEL-1 (mg/m3) 0.17 TEEL-2 (mg/m3) 0.227 TEEL-3 (mg/m3) 22.7
### Ecotoxicity
# MERCURY OXIDE
UN Number: 1641
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1641
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 11100 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 216.61 Melting Point (°C) 500
### Behaviour at sea
Persistence (days) 3.1
### Additional data
Colour red, orange, yellow Odour odourless Marine pollutant P
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.005 (Pb) TEEL-1 (mg/m3) 0.026 TEEL-2 (mg/m3) 0.104 TEEL-3 (mg/m3) 10.4
### Ecotoxicity
# MESITYL OXIDE
UN Number: 1229 - CAS Number: 141-79-7
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1229 CAS number 141-79-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 853 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 98.2 Density of gas (kg/m3) 4.386 Boiling Point (°C) 130 Melting Point (°C) -59 Vapour Pressure (Pa) 1000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 340 Flash Point (°C) 31 Lower explosivity limit (LEL) (volume %) 1.3 Upper explosivity limit (UEL) (volume %) 8.8
### Behaviour at sea
### Additional data
Colour colourless to light yellow Odour strong peppermint, honey Standard behavior classification FED
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 18 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name ketones IMO class 3.3
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 5000 TLV-TWA 15 TEEL-1 (mg/m3) 25 ppm TEEL-2 (mg/m3) 25ppm TEEL-3 (mg/m3) 1400 ppm
### Ecotoxicity
# METALAXYL
Also known as: APRON
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1210 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 279.34 Melting Point (°C) 71.8/72.3 Vapour Pressure (Pa) 2.9*10-4 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
### Transportation data
State solid
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# METHACRYLIC ACID inhibited
UN Number: 2531 - CAS Number: 79-41-4 Also known as: ACIDE METHACRYLIQUE stabilisé, 2-Methacrylic Acid, 2-Methyl-2-Propenoic Acid, Methacrylic Acid, Acide Methacrylique
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2531 CAS number 79-41-4 Formula C 4 H 6 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Solid Density (kg/m3) 1010 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 1.28 [cSt] at a temperature of 20°C Molar mass (g/mol) 86.1 Density of gas (kg/m3) 3.87 Solubility (g/L) 89000 [g/L] at a temperature of 20°C and salinity of 0‰ 89000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 161 Melting Point (°C) 15 Surface tension (mN/m) 65.9 [mN/m] at a temperature of 20°C Vapour Pressure (Pa) 90 [Pa] at a temperature of 20°C 133 [Pa] at a temperature of 25°C Ignition Temperature (°C) 400 Flash Point (°C) 77 Flash Point (Cleveland open cup) (°C) 77 Lower explosivity limit (LEL) (volume %) 2.4 Upper explosivity limit (UEL) (volume %) 8.8 Specific heat capacity (J/(Kg·K)) 1871 Henry's constant (mol/(m³·Pa)) 0.039
### Behaviour at sea
Log kow 0.93 Log koc 0.35 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 3.1
### Additional data
Colour colourless Odour sharp, acrid, repulsive MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group III Temperature (°C) ambient Family name organic acids
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
Hazard statements Health H302 Harmful if swallowed. H311 Toxic in contact with skin. H314 Causes severe skin burns and eye damage. H332 Harmful if inhaled. H335 May cause respiratory irritation. Precautionary statements Prevention P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. Storage P405 Store locked up. Disposal P501 Dispose of contents/container to ... TLV-TWA 20 TEEL-1 (mg/m3) 6.7 ppm TEEL-2 (mg/m3) 61 ppm TEEL-3 (mg/m3) 220 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 45 Lowest median lethal concentration (LC50) on crustacean (mg/l) 140 Lowest median lethal concentration (LC50) on fishes (mg/l) 85 Highest no observed effect concentration (NOEC) on algae (mg/l) 8.2 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 53 Highest no observed effect concentration (NOEC) on fishes (mg/l) 10 Assessment factor (AF) 50 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 164 [µg/l] on the Short term
# METHACRYLONITRILE inhibited
UN Number: 3079 - CAS Number: 126-98-7 Also known as: 2-CYANOPROPENE-1
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3079 CAS number 126-98-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 800 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 67.09 Density of gas (kg/m3) 2.98 Boiling Point (°C) 90/92 Melting Point (°C) -35.8 Vapour Pressure (Pa) 8536 [Pa] at a temperature of 20°C Flash Point (°C) 12 Upper explosivity limit (UEL) (volume %) 6.8
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification ED
### Transportation data
Transport mode Bulk,Packaged Cargo group 15 State liquid Temperature (°C) ambient Family name substitued allyls IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 4 - High Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 1 ppm TEEL-2 (mg/m3) 13 ppm TEEL-3 (mg/m3) 25 ppm
### Ecotoxicity
# METHAMIDOPHOS
UN Number: 2783
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2783
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1310 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 141.13 Melting Point (°C) 46.1 Vapour Pressure (Pa) 0.002 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless
### Transportation data
Package group I/II/III State solid IMO class 6.1
### Reactivity data
Water No Base(s) Yes Metal(s) and alloys Yes (mild steel and Cu)
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 10 TEEL-2 (mg/m3) 60 TEEL-3 (mg/m3) 60
### Ecotoxicity
# Methane
CAS Number: 72-82-8 Also known as: Methyl Hydride, Marsh Gas, Methane
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 72-82-8 Formula CH 4
### Physical chemical data
Physical State (25°C) Gas Molar mass (g/mol) 16.043 Solubility (g/L) 22 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) -161 Melting Point (°C) -183 Critical temperature (°C) 190.56 Critical pressure (Pa) 4599000 Surface tension (mN/m) 14 [mN/m] at a temperature of -161°C Interfacial tension (mN/m) 50 [mN/m] at a temperature of -161°C and salinity of 0‰ Vapour pressure at 70% of critical temperature (Pa) 447990 Flash Point (Pensky-Martens closed cup) (°C) -188 Lower explosivity limit (LEL) (volume %) 5.3 Upper explosivity limit (UEL) (volume %) 14 Henry's constant (mol/(m³·Pa)) 68901
### Behaviour at sea
Log kow 1.09 Log koc 0.6 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 2
### Additional data
MARPOL pollution category Category Description Other Substances Substances which have been evaluated and found to fall outside Category X, Y or Z because they are considered to present no harm to marine resources, human health, amenities or other legitimate uses of the sea when discharged into the sea from tank cleaning of deballasting operations. The discharge of bilge or ballast water or other residues or mixtures containing these substances are not subject to any requirements of MARPOL Annex II.
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Interference with coastal amenities (E2) G - Gas
### Human toxicity threshold
Hazard statements Physical H220 Extremely flammable gas.
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 46.6 Lowest median lethal concentration (LC50) on fishes (mg/l) 24.11
# METHANE (compressed gas)
UN Number: 1971
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1971
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 0.774 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 16.04 Density of gas (kg/m3) 0.774 Boiling Point (°C) -261.3 Melting Point (°C) -182 Vapour Pressure (Pa) 25000000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 595 Upper explosivity limit (UEL) (volume %) 15
### Behaviour at sea
### Additional data
Colour colourless Odour weak odour
### Transportation data
Transport mode Gas,Packaged Cargo group 31 State liq.compr.gas Temperature (°C) < -162� Pressure (Pa) under pressure Family name paraffins IMO class 2(2.1)
### Reactivity data
Water No Static electricity Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 3000 ppm TEEL-2 (mg/m3) 5000 ppm TEEL-3 (mg/m3) 200000 ppm
### Ecotoxicity
# METHANE (refrigerated liquid)
UN Number: 1972
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1972
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 0.774 [Kg/m³] at a temperature of 20°C Density of gas (kg/m3) 0.774 Boiling Point (°C) -161 Melting Point (°C) -183 Vapour Pressure (Pa) 25000000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 537 Upper explosivity limit (UEL) (volume %) 15
### Behaviour at sea
### Additional data
Colour colourless Odour weak odour
### Transportation data
Transport mode Gas,Packaged Ship type 2G Cargo group 31 State liquefied gas Temperature (°C) < -162� Pressure (Pa) under pressure Family name paraffins IMO class 2(2.1)
### Reactivity data
Water No Static electricity Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 3000 ppm TEEL-2 (mg/m3) 5000 ppm TEEL-3 (mg/m3) 200000 ppm
### Ecotoxicity
# METHANOL
UN Number: 1230 - CAS Number: 67-56-1 Also known as: COLONIAL SPIRIT, COLUMBIAN SPIRIT, Methylalcohol, Carbinol, Methanol
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1230 CAS number 67-56-1 Formula CH 4 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 792 [Kg/m³] at a temperature of 20°C 805.5 [Kg/m³] at a temperature of 5°C 801.3 [Kg/m³] at a temperature of 10°C 793.2 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.776 [cSt] at a temperature of 20°C 0.68739 [cSt] at a temperature of 25°C 2.4209 [cSt] at a temperature of 5°C 2.2339 [cSt] at a temperature of 10°C 2.0171 [cSt] at a temperature of 20°C Molar mass (g/mol) 32.04 Density of gas (kg/m3) 1.419 Solubility (g/L) 10000000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 64.7 Melting Point (°C) -98 Critical molar volume (m³/mol) 0.000117 Critical temperature (°C) 512.5 Critical pressure (Pa) 8084000 Surface tension (mN/m) 22.5 [mN/m] at a temperature of 20°C 20.14 [mN/m] at a temperature of 25°C 23.88 [mN/m] at a temperature of 4.1°C 23.06 [mN/m] at a temperature of 10.1°C 22.67 [mN/m] at a temperature of 18.1°C Vapour Pressure (Pa) 12865 [Pa] at a temperature of 20°C Ignition Temperature (°C) 455 Flash Point (°C) 11 Flash Point (Pensky-Martens closed cup) (°C) 12 Flash Point (Cleveland open cup) (°C) 15.6 Lower explosivity limit (LEL) (volume %) 5.5 Upper explosivity limit (UEL) (volume %) 36.5 Vapor enthalpy (J/Kg) 1098870 [J/Kg] at a temperature of 64.6°C 1168154 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 22660882 Specific heat capacity (J/(Kg·K)) 2531 Henry's constant (mol/(m³·Pa)) 0.46
### Behaviour at sea
Log kow -0.77 Log koc 0 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 10
### Additional data
Colour colourless Odour alcohol odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification DE
### Transportation data
Package group II Cargo group 20 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alcohols, glycols IMO class 3.2
### Reactivity data
Abilities Miscible in water. Acid(s) Yes Base(s) Yes Static electricity Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Specific Health Concern (D3) T - Specific Target Organ Toxicity following single or repeated exposure Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 25000 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H301 Toxic if swallowed. H311 Toxic in contact with skin. H331 Toxic if inhaled. H370 Causes damage to organs. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P233 Keep container tightly closed. P240 Ground/bond container and receiving equipment. P241 Use explosion-proof electrical/ventilating/lighting/.../equipment. P242 Use only non- sparking tools. P243 Take precautionary measures against static discharge. P260 Do not breathe dust/fume/gas/mist/vapours/spray. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P270 Do no eat, drink or smoke when using this product. P271 Use only outdoors or in a well-ventilated area. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P302 + P352 IF ON SKIN: Wash with plenty of soap and water. P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P312 Call a POISON CENTER or doctor/physician if you feel unwell. P361 Remove/Take off immediately all contaminated clothing. P370 + P378 In case of fire: Use ... for extinction. Storage P403 + P235 Store in a well-ventilated place. Keep cool. Disposal P501 Dispose of contents/container to ... TLV-TWA 200 ERPG-1 (ppm) 200 ERPG-2 (ppm) 1000 ERPG-3 (ppm) 5000
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 1700 Lowest median lethal concentration (LC50) on fishes (mg/l) 11.5 Highest no observed effect concentration (NOEC) on algae (mg/l) 530 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 6.7 Highest no observed effect concentration (NOEC) on fishes (mg/l) 0.04 Assessment factor (AF) 100 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 2080 [µg/l] on the Short term
# METHYL ACETATE
UN Number: 1231 - CAS Number: 79-20-9 Also known as: ACETATE DE METHYLE, ACETIC ACID, METHYL ESTER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1231 CAS number 79-20-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 927 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 74.1 Density of gas (kg/m3) 3.61 Boiling Point (°C) 57 Melting Point (°C) -98 Vapour Pressure (Pa) 22752 [Pa] at a temperature of 20°C Ignition Temperature (°C) 502 Flash Point (°C) -6 Lower explosivity limit (LEL) (volume %) 3.1 Upper explosivity limit (UEL) (volume %) 16
### Behaviour at sea
### Additional data
Colour colourless Odour mild sweet Standard behavior classification DE
### Transportation data
Package group II Cargo group 34 State liquid Temperature (°C) ambient Family name esters IMO class 3.2
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Oxidizing agents Yes Combustibles Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 3100 TLV-TWA 200 TEEL-1 (mg/m3) 250 ppm TEEL-2 (mg/m3) 500 ppm TEEL-3 (mg/m3) 3100 ppm
### Ecotoxicity
# METHYL ACETOACETATE
CAS Number: 105-45-3 Also known as: ACETOACETATE DE METHYLE, ACETOACETIC ACID, METHYL ESTER, BUTANOIC ACID, 3-OXO-METHYL ESTER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 105-45-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1076 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 116.12 Density of gas (kg/m3) 5.16 Boiling Point (°C) 169/170 Melting Point (°C) -80 Vapour Pressure (Pa) 228 [Pa] at a temperature of 20°C Ignition Temperature (°C) 280 Flash Point (°C) 70 Lower explosivity limit (LEL) (volume %) 3.1 Upper explosivity limit (UEL) (volume %) 16
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Cargo group 34 State liquid Temperature (°C) ambient Family name esters
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# METHYL ACETYLENE/PROPADIENE MIXTURES stabilized
UN Number: 1060
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1060
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 1.94 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 40.1 Density of gas (kg/m3) 1.94 Boiling Point (°C) -38 Vapour Pressure (Pa) 747460 [Pa] at a temperature of 20°C Lower explosivity limit (LEL) (volume %) 3.4 Upper explosivity limit (UEL) (volume %) 10.8
### Behaviour at sea
### Additional data
Colour colourless Odour garlic odour
### Transportation data
Transport mode Gas,Packaged Ship type 2G,2PG Cargo group 30 State liq.compr.gas Temperature (°C) < 52� Pressure (Pa) under pressure Family name olefins IMO class 2(2.1)
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 15000 TLV-TWA 1000 TEEL-1 (mg/m3) 1250 ppm TEEL-2 (mg/m3) 1250 ppm TEEL-3 (mg/m3) 3400 ppm
### Ecotoxicity
# METHYL ACRYLATE inhibited
UN Number: 1919 - CAS Number: 96-33-3 Also known as: ACRYLATE DE METHYLE, ACRYLIC ACID, METHYL ESTER, CURITHANE 103 (T), Acrylic Acid Methyl Ester, Methyl Prop-2-Enoate, Methyl Acrylate
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1919 CAS number 96-33-3 Formula C 4 H 6 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 956 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.5055 [cSt] at a temperature of 20°C Molar mass (g/mol) 86.09 Density of gas (kg/m3) 3.831 Solubility (g/L) 52000 [g/L] at a temperature of 20°C and salinity of 0‰ 49400 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 80.8 Melting Point (°C) -75 Critical molar volume (m³/mol) 0.000265 Critical temperature (°C) 536 Critical pressure (Pa) 4357000 Surface tension (mN/m) 24.2 [mN/m] at a temperature of 20°C Interfacial tension (mN/m) 30 [mN/m] at a temperature of 20°C and salinity of 0‰ Vapour Pressure (Pa) 933 [Pa] at a temperature of 20°C 14665 [Pa] at a temperature of 25°C Ignition Temperature (°C) 390 Flash Point (°C) -3 Flash Point (Pensky-Martens closed cup) (°C) -2.8 Flash Point (Cleveland open cup) (°C) -3 Lower explosivity limit (LEL) (volume %) 2.8 Upper explosivity limit (UEL) (volume %) 25 Vapor enthalpy (J/Kg) 384481 [J/Kg] at a temperature of 80.7°C Combus enthalpy (J/Kg) 5841329 Specific heat capacity (J/(Kg·K)) 1845 Henry's constant (mol/(m³·Pa)) 20.26
### Behaviour at sea
Persistence (days) 1.6 Log kow 0.8 Log koc 0.77 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) 3100 Bioconcentration factor (BCF) 3
### Additional data
Colour colourless Odour sharp, sweet odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification FED
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 14 State liquid Temperature (°C) < 5�, ambient Pressure (Pa) ambient Family name acrylates IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 1000 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H302 Harmful if swallowed. H312 Harmful in contact with skin. H315 Causes skin irritation. H317 May cause an allergic skin reaction. H319 Causes serious eye irritation. H331 Toxic if inhaled. H335 May cause respiratory irritation. Environmental H412 Harmful to aquatic life with long lasting effects. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P311 Call a POISON CENTER or doctor/physician. TLV-TWA 10 TEEL-1 (mg/m3) 2 ppm TEEL-2 (mg/m3) 7.5 ppm TEEL-3 (mg/m3) 150 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on fishes (mg/l) 1.1 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.19 Assessment factor (AF) 500 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 0 [µg/l] on the Short term
# METHYL AMYL ACETATE
UN Number: 1233
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1233
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 860 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 144.22 Density of gas (kg/m3) 6.45 Boiling Point (°C) 146 Vapour Pressure (Pa) 507 [Pa] at a temperature of 20°C Flash Point (°C) 42 Lower explosivity limit (LEL) (volume %) 0.9 Upper explosivity limit (UEL) (volume %) 5.7
### Behaviour at sea
### Additional data
Colour colourless Odour pleasant, fruit odour
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 34 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name esters IMO class 3.3
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# METHYL AMYL ALCOHOL
UN Number: 2053 - CAS Number: 108-11-2 Also known as: ALCOOL METHYLAMYLIQUE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2053 CAS number 108-11-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 810 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 102.18 Density of gas (kg/m3) 4.515 Boiling Point (°C) 132 Melting Point (°C) < -90 Vapour Pressure (Pa) 400 [Pa] at a temperature of 20°C Ignition Temperature (°C) 312 Flash Point (°C) 41 Upper explosivity limit (UEL) (volume %) 5.5
### Behaviour at sea
### Additional data
Colour colourless Odour mild, alcohol-like Standard behavior classification FED
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 20 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alcohols, glycols IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Reducing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 400 TLV-TWA 25
### Ecotoxicity
# METHYL AMYL KETONE
UN Number: 1110 - CAS Number: 110-43-0 Also known as: AMYLMETHYLCETONE, n-AMYLMETHYLCETONE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1110 CAS number 110-43-0
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 820 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 114.19 Density of gas (kg/m3) > 1.29 Boiling Point (°C) 149 Melting Point (°C) -35 Vapour Pressure (Pa) 345 [Pa] at a temperature of 20°C Ignition Temperature (°C) 393 Flash Point (°C) 39 Lower explosivity limit (LEL) (volume %) 1.1 Upper explosivity limit (UEL) (volume %) 7.9
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification FED
### Transportation data
Package group III Cargo group 18 State liquid Temperature (°C) ambient Family name ketones IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Reducing agents Yes Combustibles Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 800 TLV-TWA 50 TEEL-1 (mg/m3) 100 ppm TEEL-2 (mg/m3) 125 ppm TEEL-3 (mg/m3) 800 ppm
### Ecotoxicity
# METHYL BROMIDE
UN Number: 1062 Also known as: BROMOMETHANE, BROMURE DE METHYLE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1062
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 4.257 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 94.95 Density of gas (kg/m3) 4.257 Boiling Point (°C) 3.8 Melting Point (°C) -94 Vapour Pressure (Pa) 187000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 538 Flash Point (°C) 194 Lower explosivity limit (LEL) (volume %) 10 Upper explosivity limit (UEL) (volume %) 15
### Behaviour at sea
### Additional data
Colour colourless Odour odourless to sweet odour
### Transportation data
Transport mode Bulk,Gas,Packaged Ship type 1G Cargo group 36 State liquefied gas Temperature (°C) ambient Pressure (Pa) under pressure Family name halogenated hydrocarb IMO class 2(2.3)
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 2000 ERPG-2 (ppm) 50 ERPG-3 (ppm) 200
### Ecotoxicity
# METHYL BUTENOL
CAS Number: 556-82-1 Also known as: 1-BUTEN-3-OL, 3-METHYL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 556-82-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 824 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 824 Density of gas (kg/m3) 3.83 Boiling Point (°C) 98/99 Vapour Pressure (Pa) 6800 (250�C) [Pa] at a temperature of 20°C Flash Point (°C) 13
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification E/ED
### Transportation data
Cargo group 20 Temperature (°C) ambient Family name alcohols, glycols
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# METHYL BUTYNOL
CAS Number: 115-19-5
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 115-19-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 867 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 84.12 Boiling Point (°C) 104/105 Melting Point (°C) 2.6 Flash Point (°C) 25
### Behaviour at sea
### Additional data
Colour colourless to straw yellow Odour odourless
### Transportation data
Cargo group 20 State liquid Temperature (°C) ambient Family name alcohols, glycols
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# METHYL BUTYRATE
UN Number: 1237 - CAS Number: 623-42-7 Also known as: BUTANOIC ACID, METHYL ESTER, BUTYRATE DE METHYLE, BUTYRIC ACID, METHYL ESTER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1237 CAS number 623-42-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 898 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 102.13 Density of gas (kg/m3) 4.55 Boiling Point (°C) 102.3 Melting Point (°C) -84.8 Vapour Pressure (Pa) 2455 [Pa] at a temperature of 20°C Flash Point (°C) 14 Lower explosivity limit (LEL) (volume %) 0.9 Upper explosivity limit (UEL) (volume %) 3.5
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification FED
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 34 State liquid Family name esters IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# METHYL CHLORIDE
UN Number: 1063 Also known as: CHLOROMETHANE, CHLORURE DE METHYLE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1063
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 2.412 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 50.49 Density of gas (kg/m3) 2.412 Boiling Point (°C) -24 Melting Point (°C) -98 Vapour Pressure (Pa) 506540 [Pa] at a temperature of 20°C Ignition Temperature (°C) 625 Flash Point (°C) -24 Lower explosivity limit (LEL) (volume %) 8.1 Upper explosivity limit (UEL) (volume %) 17.2
### Behaviour at sea
### Additional data
Colour colourless Odour odourless to sweet odour
### Transportation data
Transport mode Gas,Packaged Ship type 2G,2PG Cargo group 36 State liquefied gas Temperature (°C) ambient Pressure (Pa) under pressure Family name halogenated hydrocarb IMO class 2(2.1)
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 10000 TLV-TWA 50 ERPG-2 (ppm) 400 ERPG-3 (ppm) 1000
### Ecotoxicity
# METHYL CYCLOHEXANE
UN Number: 2296 - CAS Number: 108-87-2 Also known as: CYCLOHEXYLMETHANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2296 CAS number 108-87-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 800 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 98.2 Density of gas (kg/m3) 4.39 Boiling Point (°C) 100 Melting Point (°C) -126 Vapour Pressure (Pa) 4800 [Pa] at a temperature of 20°C Ignition Temperature (°C) 258 Flash Point (°C) -4 Lower explosivity limit (LEL) (volume %) 1.1 Upper explosivity limit (UEL) (volume %) 6.7
### Behaviour at sea
### Additional data
Colour colourless Odour faint benzene-like
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 31 State liquid Temperature (°C) ambient Family name paraffins IMO class 3.2
### Reactivity data
Water No Static electricity Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 3 - ≥100 and <500 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Specific Health Concern (D3) A - Aspiration Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 1200 TLV-TWA 400 TEEL-1 (mg/m3) 1200 ppm TEEL-2 (mg/m3) 1200 ppm TEEL-3 (mg/m3) 1200 ppm
### Ecotoxicity
# METHYL DIETHANOLAMINE
CAS Number: 105-59-9
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 105-59-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1038 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 119.16 Boiling Point (°C) 247 Melting Point (°C) -21 Vapour Pressure (Pa) 30 [Pa] at a temperature of 20°C Ignition Temperature (°C) 265 Flash Point (°C) 126 Lower explosivity limit (LEL) (volume %) 0.9 Upper explosivity limit (UEL) (volume %) 8.4
### Behaviour at sea
### Additional data
Colour colourless
### Transportation data
State liquid Temperature (°C) ambient Family name alkanolamines
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# METHYL ETHYL KETONE
UN Number: 1193 Also known as: 2-BUTANONE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1193
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 810 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 72.11 Density of gas (kg/m3) 3.225 Boiling Point (°C) 80 Melting Point (°C) -86 Vapour Pressure (Pa) 10500 [Pa] at a temperature of 20°C Ignition Temperature (°C) 505 Flash Point (°C) -1 Lower explosivity limit (LEL) (volume %) 1.8 Upper explosivity limit (UEL) (volume %) 11.5
### Behaviour at sea
### Additional data
Colour colourless Odour sweet Standard behavior classification DE
### Transportation data
Package group II Cargo group 18 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name ketones IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Static electricity Yes Oxidizing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 3000 TLV-TWA 200 TEEL-1 (mg/m3) 200 ppm TEEL-2 (mg/m3) 2700 ppm TEEL-3 (mg/m3) 4000 ppm
### Ecotoxicity
# METHYL FORMATE
UN Number: 1243 - CAS Number: 107-31-3
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1243 CAS number 107-31-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 977 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 60.1 Density of gas (kg/m3) 2.709 Boiling Point (°C) 32 Melting Point (°C) -100 Vapour Pressure (Pa) 64000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 450 Flash Point (°C) -20 Upper explosivity limit (UEL) (volume %) 22.7
### Behaviour at sea
### Additional data
Colour colourless Odour pleasant odour Standard behavior classification DE
### Transportation data
Transport mode Bulk,Packaged State liquid Temperature (°C) < 29� Pressure (Pa) under pressure IMO class 3.1
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 5000 TLV-TWA 100 TEEL-1 (mg/m3) 150 ppm TEEL-2 (mg/m3) 750 ppm TEEL-3 (mg/m3) 4500 ppm
### Ecotoxicity
# METHYL HEPTYL KETONE
CAS Number: 821-55-6
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 821-55-6
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 832 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 142.24 Density of gas (kg/m3) 6.32 Boiling Point (°C) 192 Melting Point (°C) -21 Vapour Pressure (Pa) < 130 [Pa] at a temperature of 20°C Flash Point (°C) 64
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Cargo group 18 State liquid Temperature (°C) ambient Family name ketones
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver
### Human toxicity threshold
TEEL-1 (mg/m3) 3 ppm TEEL-2 (mg/m3) 20 ppm TEEL-3 (mg/m3) 75 ppm
### Ecotoxicity
# METHYL ISOBUTYL KETONE
UN Number: 1245 - CAS Number: 108-10-1 Also known as: Hexanone, Hexone, Isobutyl Methyl Ketone, Isopropylacetone, 4-Methyl-2-Oxopentane, 2-Methyl-4-Pentanone, 4-Methyl-2-Pentanone, 2-Methylpropyl Methyl Ketone, Mibk, Methyl Isobutyl Cetone, Mic, Methyl Isobutyl Ketone
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1245 CAS number 108-10-1 Formula C 6 H 1 2 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 302 [Kg/m³] at a temperature of 20°C 814.5 [Kg/m³] at a temperature of 5°C 810.2 [Kg/m³] at a temperature of 10°C 803.1 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.76 [cSt] at a temperature of 20°C 0.68424 [cSt] at a temperature of 25°C 2.3327 [cSt] at a temperature of 5°C 2.8511 [cSt] at a temperature of 10°C 2.2164 [cSt] at a temperature of 20°C Molar mass (g/mol) 100.16 Density of gas (kg/m3) 4.463 Solubility (g/L) 18000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 116.4 Melting Point (°C) -80 Critical temperature (°C) 574.6 Critical pressure (Pa) 3270000 Surface tension (mN/m) 23.6 [mN/m] at a temperature of 20°C 24.47 [mN/m] at a temperature of 5.1°C 23.73 [mN/m] at a temperature of 11.8°C 23.61 [mN/m] at a temperature of 18.2°C Vapour Pressure (Pa) 799 [Pa] at a temperature of 20°C 2640 [Pa] at a temperature of 25°C Ignition Temperature (°C) 460 Flash Point (°C) 14 Flash Point (Pensky-Martens closed cup) (°C) 13 Flash Point (Cleveland open cup) (°C) 23 Lower explosivity limit (LEL) (volume %) 1.4 Upper explosivity limit (UEL) (volume %) 7.5 Vapor enthalpy (J/Kg) 342299 [J/Kg] at a temperature of 116.2°C 403037 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 34700000 Specific heat capacity (J/(Kg·K)) 2116.9 Combustion efficiency (%) 96 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.06 Rad fraction (%) 23 Henry's constant (mol/(m³·Pa)) 14
### Behaviour at sea
Persistence (days) 0.8 Log kow 1.38 Log koc 2.1 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 50 Bioconcentration factor (BCF) 6
### Additional data
Colour colourless Odour mild pleasant odour MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment. Standard behavior classification FED
### Transportation data
Package group II Cargo group 18 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name ketones IMO class 3.2
### Reactivity data
Acid(s) Yes Base(s) Yes Static electricity Yes Oxidizing agents Yes Notable risks Reacts with oxidizers.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 500 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H319 Causes serious eye irritation. H332 Harmful if inhaled. H335 May cause respiratory irritation. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. Response P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. TLV-TWA 100
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 2000 Lowest median lethal concentration (LC50) on crustacean (mg/l) 1230 Lowest median lethal concentration (LC50) on fishes (mg/l) 505 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 7.8 Highest no observed effect concentration (NOEC) on fishes (mg/l) 57 Assessment factor (AF) 500 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 15.6 [µg/l] on the Long term
# METHYL METHACRYLATE MONOMER inihibited
UN Number: 1247 - CAS Number: 80-62-6 Also known as: DIAKON (T), Methyl Alpha-Methyl Acrylate, Methyl 2-Methyl-2-Propenoate, Methyl 2-Methyl Propenoate, 2-Methyl 2-Propenoic Acid, Methyl Ester, 2-Methyl Propenoic Acid, Methyl Ester, Methylpropylene-2-Carboxylate, Mma, Methyl Ester, Methyl Methacrylate, Methacrylate De Methyle, Methyl α-Methyl Acrylate
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1247 CAS number 80-62-6 Formula C 5 H 8 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 945 [Kg/m³] at a temperature of 20°C 957.4 [Kg/m³] at a temperature of 5°C 953.4 [Kg/m³] at a temperature of 10°C 943.8 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.65 [cSt] at a temperature of 20°C 0.56 [cSt] at a temperature of 25°C 2.1811 [cSt] at a temperature of 5°C 2.1292 [cSt] at a temperature of 10°C 1.9284 [cSt] at a temperature of 20°C Molar mass (g/mol) 100.12 Density of gas (kg/m3) 4.451 Solubility (g/L) 16000 [g/L] at a temperature of 20°C and salinity of 0‰ 13640 [g/L] at a temperature of 20°C and salinity of 0‰ 13000 [g/L] at a temperature of 20°C and salinity of 5‰ 10370 [g/L] at a temperature of 20°C and salinity of 30‰ Boiling Point (°C) 101 Melting Point (°C) -48 Surface tension (mN/m) 28 [mN/m] at a temperature of 20°C 27.77 [mN/m] at a temperature of 5.1°C 27.1 [mN/m] at a temperature of 10.9°C 25.99 [mN/m] at a temperature of 19.8°C Interfacial tension (mN/m) 14.3 [mN/m] at a temperature of 20°C and salinity of 0‰ Vapour Pressure (Pa) 5332 [Pa] at a temperature of 20°C 5100 [Pa] at a temperature of 25°C Ignition Temperature (°C) 430 Flash Point (°C) 10 Flash Point (Pensky-Martens closed cup) (°C) 2 Flash Point (Cleveland open cup) (°C) 10 Lower explosivity limit (LEL) (volume %) 2.1 Upper explosivity limit (UEL) (volume %) 12.5 Vapor enthalpy (J/Kg) 359568 [J/Kg] at a temperature of 101°C Combus enthalpy (J/Kg) 25400000 Specific heat capacity (J/(Kg·K)) 1910 Combustion efficiency (%) 96 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.06 Rad fraction (%) 23 Henry's constant (mol/(m³·Pa)) 26.3
### Behaviour at sea
Log kow 1.38 Log koc 2.11 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 6.2
### Additional data
Colour colourless Odour sharp, pleasant odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification ED
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 14 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name acrylates IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 4000 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H315 Causes skin irritation. H317 May cause an allergic skin reaction. H335 May cause respiratory irritation. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P302 + P352 IF ON SKIN: Wash with plenty of soap and water. Disposal P501 Dispose of contents/container to ... TLV-TWA 100 TEEL-1 (mg/m3) 17 ppm TEEL-2 (mg/m3) 120 ppm TEEL-3 (mg/m3) 570 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) > 110 Lowest median lethal concentration (LC50) on crustacean (mg/l) 69 Lowest median lethal concentration (LC50) on fishes (mg/l) > 79 Highest no observed effect concentration (NOEC) on algae (mg/l) 49 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 37 Highest no observed effect concentration (NOEC) on fishes (mg/l) 40 Assessment factor (AF) 1000 on the Short term 500 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 69 [µg/l] on the Short term 74 [µg/l] on the Long term
# METHYL PARATHION liquid
UN Number: 3018
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3018
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1360 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 263.2 Boiling Point (°C) 120 Melting Point (°C) 35 Vapour Pressure (Pa) 0.001 [Pa] at a temperature of 20°C Flash Point (°C) 45
### Behaviour at sea
### Additional data
Colour white, brown Odour rotten egg, garlic odour Standard behavior classification D, SD
### Transportation data
State liquid, solid Temperature (°C) < 10� Pressure (Pa) under pressure IMO class 6.1
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.018 TEEL-1 (mg/m3) 0.34 TEEL-2 (mg/m3) 0.34 TEEL-3 (mg/m3) 15
### Ecotoxicity
# METHYL PROPYL KETONE
UN Number: 1249
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1249
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 810 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 86.1 Density of gas (kg/m3) 3.87 Boiling Point (°C) 102 Melting Point (°C) -78 Vapour Pressure (Pa) 1600 [Pa] at a temperature of 20°C Ignition Temperature (°C) 452 Lower explosivity limit (LEL) (volume %) 1.6 Upper explosivity limit (UEL) (volume %) 8.2
### Behaviour at sea
### Additional data
Colour water-white Odour pleasant Standard behavior classification FED
### Transportation data
Package group II Cargo group 18 State liquid Temperature (°C) ambient Family name ketones IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Static electricity Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 1500 TEEL-1 (mg/m3) 150 ppm TEEL-2 (mg/m3) 150 ppm TEEL-3 (mg/m3) 1500 ppm
### Ecotoxicity
# METHYL SALICYLATE
UN Number: 3082 - CAS Number: 119-36-8 Also known as: o-ASINIC ACID, BENZOIC ACID, 2-METHOXY, BETULA OR GAULTHERIA OIL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082 CAS number 119-36-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1174 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 152.15 Density of gas (kg/m3) 6.77 Boiling Point (°C) 222 Melting Point (°C) -8.6 Vapour Pressure (Pa) 6000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 453 Flash Point (°C) 96
### Behaviour at sea
### Additional data
Colour colourless, yellowish or reddi Odour odourless
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 34 State liquid Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Specific Health Concern (D3) R - Reprotoxicity Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# METHYL tertiary-BUTYL ETHER
UN Number: 2398 - CAS Number: 1634-04-4 Also known as: Tert-Butyl Methyl Ether, 2-Methoxy-2-Methyl Propane, Methyl T-Butyl Ether, Methyl-Tert-Butyl Ether, Methyl Tertiary Butyl Ether, Methyl 1,1-Dimethylethyl Ether, 2-Methyl-2-Methoxypropane, Mtbe, Methyl Butyl Ether, Methyl Tert-Butyl Ether, Methyl-Tertio- Butyl-Ether
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2398 CAS number 1634-04-4 Formula C 5 H 1 2 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 740.5 [Kg/m³] at a temperature of 20°C 757.4 [Kg/m³] at a temperature of 5°C 752.7 [Kg/m³] at a temperature of 10°C 753.1 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.47 [cSt] at a temperature of 20°C 1.756 [cSt] at a temperature of 5°C 1.7537 [cSt] at a temperature of 10°C 1.5137 [cSt] at a temperature of 20°C Molar mass (g/mol) 88.15 Density of gas (kg/m3) 3.87 Solubility (g/L) 48000 [g/L] at a temperature of 20°C and salinity of 0‰ 31780 [g/L] at a temperature of 20°C and salinity of 0‰ 26870 [g/L] at a temperature of 20°C and salinity of 5‰ 20550 [g/L] at a temperature of 20°C and salinity of 30‰ Boiling Point (°C) 55.2 Melting Point (°C) -109 Critical temperature (°C) 467.1 Critical pressure (Pa) 3430000 Surface tension (mN/m) 20 [mN/m] at a temperature of 20°C 18.3 [mN/m] at a temperature of 25°C 20.04 [mN/m] at a temperature of 5°C 25.02 [mN/m] at a temperature of 10.1°C 18.06 [mN/m] at a temperature of 18.5°C Vapour Pressure (Pa) 310 [Pa] at a temperature of 20°C 33000 [Pa] at a temperature of 25°C Flash Point (°C) -26 Flash Point (Pensky-Martens closed cup) (°C) -28.2 Lower explosivity limit (LEL) (volume %) 1.26 Upper explosivity limit (UEL) (volume %) 8.4 Vapor enthalpy (J/Kg) 316960 [J/Kg] at a temperature of 55.25°C 338287 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 35300000 Specific heat capacity (J/(Kg·K)) 2127 Combustion efficiency (%) 96 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.04 Rad fraction (%) 23 Henry's constant (mol/(m³·Pa)) 43.8
### Behaviour at sea
Log kow 1.06 Log koc 1.05 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) Not biodegradable Bioconcentration factor (BCF) 1.5
### Additional data
MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment. Standard behavior classification FED
### Transportation data
Package group II Cargo group 41 State liquid IMO class 3.1
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
Hazard statements Physical H225 Highly flammable liquid and vapour. Health H315 Causes skin irritation. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P243 Take precautionary measures against static discharge. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P302 + P352 IF ON SKIN: Wash with plenty of soap and water. Storage P403 + P235 Store in a well-ventilated place. Keep cool. TLV-TWA 40 TEEL-1 (mg/m3) 50 ppm TEEL-2 (mg/m3) 570 ppm TEEL-3 (mg/m3) 5300 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 184 Lowest median lethal concentration (LC50) on crustacean (mg/l) 136 Lowest median lethal concentration (LC50) on fishes (mg/l) 574 Highest no observed effect concentration (NOEC) on algae (mg/l) 103 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 26 Highest no observed effect concentration (NOEC) on fishes (mg/l) 293.5 Assessment factor (AF) 100 on the Short term 100 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 1360 [µg/l] on the Short term 260 [µg/l] on the Long term
# METHYLAMINE anhydrous
UN Number: 1061 Also known as: AMINOMETHANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1061
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 1.393 [Kg/m³] at a temperature of 20°C Vapour Pressure (Pa) 40000 [Pa] at a temperature of 20°C Flash Point (°C) -18
### Behaviour at sea
### Additional data
Standard behavior classification GD
### Transportation data
IMO class 2(2.1)
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 100 TLV-TWA 10 ERPG-1 (ppm) 10 ERPG-2 (ppm) 100 ERPG-3 (ppm) 500
### Ecotoxicity
# METHYLAMINE solution in water (42% or less)
UN Number: 1235 - CAS Number: 74-89-5 Also known as: AMINOMETHANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1235 CAS number 74-89-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 890 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 31.1 (pure) Density of gas (kg/m3) 1.39 Boiling Point (°C) 48 Melting Point (°C) -38 Vapour Pressure (Pa) 40000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 430 Flash Point (°C) < 10 Lower explosivity limit (LEL) (volume %) 4.9 Upper explosivity limit (UEL) (volume %) 20.7
### Behaviour at sea
### Additional data
Colour colourless Odour ammonia-like Standard behavior classification DE
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Family name aliphatic amines IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Metal(s) and alloys Yes (Al, Cu, Zn) Oxidizing agents Yes Reducing agents Yes (Hg) Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 100 ERPG-1 (ppm) 10 ERPG-2 (ppm) 100 ERPG-3 (ppm) 500
### Ecotoxicity
# METHYLCYCLOPENTADIENE DIMER
CAS Number: 26472-00-4
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 26472-00-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 941 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 160.26 Density of gas (kg/m3) 1.2 Boiling Point (°C) 200 Melting Point (°C) -51 Flash Point (°C) 27 Upper explosivity limit (UEL) (volume %) 10
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification F/FE/E
### Transportation data
Cargo group 30 State liquid Temperature (°C) ambient Family name olefins
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 25 TEEL-2 (mg/m3) 200 TEEL-3 (mg/m3) 500
### Ecotoxicity
# METHYLSTYRENE
UN Number: 2303
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2303
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 910 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 118.18 Density of gas (kg/m3) 5.28 Boiling Point (°C) 163/165 Melting Point (°C) -23 Vapour Pressure (Pa) 300 [Pa] at a temperature of 20°C Ignition Temperature (°C) 420 Flash Point (°C) 40 Lower explosivity limit (LEL) (volume %) 0.7 Upper explosivity limit (UEL) (volume %) 6.6
### Behaviour at sea
### Additional data
Colour colourless Odour characteristic
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 30 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name olefins IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys Yes Static electricity Yes Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 700 TLV-TWA 50 TEEL-1 (mg/m3) 100 ppm TEEL-2 (mg/m3) 100 ppm TEEL-3 (mg/m3) 700 ppm
### Ecotoxicity
# MORPHOLINE
UN Number: 2054 - CAS Number: 110-91-8 Also known as: DIETHYLENE OXIMIDE, DIETHYLENIMIDE OXIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2054 CAS number 110-91-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1000 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 87.12 Density of gas (kg/m3) 3.87 Boiling Point (°C) 128.2 Melting Point (°C) -5 Vapour Pressure (Pa) 10666 [Pa] at a temperature of 20°C Ignition Temperature (°C) 255 Flash Point (°C) 31 Lower explosivity limit (LEL) (volume %) 1.8 Upper explosivity limit (UEL) (volume %) 10.8
### Behaviour at sea
### Additional data
Colour colourless Odour ammonia, fish odour Standard behavior classification DE
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aliphatic amines IMO class 3.3
### Reactivity data
Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 8000 TLV-TWA 20 TEEL-1 (mg/m3) 30 ppm TEEL-2 (mg/m3) 30 ppm TEEL-3 (mg/m3) 1400 ppm
### Ecotoxicity
# MOTOR FUEL ANTI-KNOCK COMPOUNDS (containing lead alkyls)
UN Number: 1649
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1649
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1500/1700 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 90/120 Melting Point (°C) 6.111111111 Vapour Pressure (Pa) 6000 [Pa] at a temperature of 20°C Ignition Temperature (°C) > 140 Flash Point (°C) 38/100 Lower explosivity limit (LEL) (volume %) 1.8
### Behaviour at sea
### Additional data
Colour red, orange or blue Odour sweet, fruity
### Transportation data
Transport mode Bulk,Packaged Cargo group 33 State liquid Temperature (°C) ambient IMO class 6.1
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 40 mg/m3 TLV-TWA 0.15 mg/m3
### Ecotoxicity
# MUSTARD GAS
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1274 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 216 Melting Point (°C) 13.5 Vapour Pressure (Pa) 9.33 [Pa] at a temperature of 20°C Flash Point (°C) 105
### Behaviour at sea
### Additional data
### Transportation data
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
10 min 30 min 60 min 4 hrs 8 hrs AEGL-1 (ppm) 0.06 0.02 0.01 0.003 0.001 AEGL-2 (ppm) 0.09 0.03 0.02 0.004 0.002 AEGL-3 (ppm) 0.59 0.41 0.32 0.08 0.04
### Ecotoxicity
# MYRCENE
CAS Number: 123-35-3
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 123-35-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 801 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 136.24 Density of gas (kg/m3) 6.03 Boiling Point (°C) 167 Vapour Pressure (Pa) 930 [Pa] at a temperature of 20°C Flash Point (°C) 39
### Behaviour at sea
### Additional data
Colour yellow tainted Odour pleasant Standard behavior classification FE
### Transportation data
Cargo group 30 Family name olefins
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# N,N'-DIMETHYLFORMAMIDE
UN Number: 2265 - CAS Number: 68-12-2 Also known as: N,N-DIMETHYLFORMAMIDE, DIMETHYL FORMAMIDE, DMF, DMFA, Dimethylformamide
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2265 CAS number 68-12-2 Formula C 3 H 7 NO
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 950 [Kg/m³] at a temperature of 20°C 944.5 [Kg/m³] at a temperature of 25°C Kinematic viscosity (cSt) 0.85 [cSt] at a temperature of 25°C Molar mass (g/mol) 73.09 Density of gas (kg/m3) 3.225 Solubility (g/L) 10000000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 153 Melting Point (°C) -61 Critical molar volume (m³/mol) 0.000262 Critical temperature (°C) 649.6 Critical pressure (Pa) 4480000 Surface tension (mN/m) 36.42 [mN/m] at a temperature of 20°C Vapour Pressure (Pa) 500 [Pa] at a temperature of 20°C 516 [Pa] at a temperature of 25°C Ignition Temperature (°C) 440 Flash Point (°C) 58 Flash Point (Pensky-Martens closed cup) (°C) 58 Flash Point (Cleveland open cup) (°C) 67 Lower explosivity limit (LEL) (volume %) 2.2 Upper explosivity limit (UEL) (volume %) 15.2 Vapor enthalpy (J/Kg) 641503 [J/Kg] at a temperature of 25°C Specific heat capacity (J/(Kg·K)) 2060 Henry's constant (mol/(m³·Pa)) 0.00747
### Behaviour at sea
Log kow -0.87 Log koc 0 Biodegradation in estuary environment (Half- life) (days) Not hydrolysable Bioconcentration factor (BCF) 0.3
### Additional data
Colour colourless Odour weak ammonia odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Package group III Cargo group 10 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name amides IMO class 3.3
### Reactivity data
Abilities Miscible in water. Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 3500 Hazard statements Physical H226 Flammable liquid and vapour. Health H312 Harmful in contact with skin. H319 Causes serious eye irritation. H332 Harmful if inhaled. H360 May damage fertility or the unborn child. Precautionary statements Prevention P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P302 + P352 IF ON SKIN: Wash with plenty of soap and water. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P308 + P313 IF exposed or concerned: Get medical advice/attention. TLV-TWA 10 ERPG-2 (ppm) 100 ERPG-3 (ppm) 200
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) > 1000 Lowest median lethal concentration (LC50) on crustacean (mg/l) > 100 Lowest median lethal concentration (LC50) on fishes (mg/l) 1430 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 1140 Assessment factor (AF) 50 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 22800 [µg/l] on the Short term
# N-AMINOETHYLPIPERAZINE
UN Number: 2815 - CAS Number: 140-31-8 Also known as: 1-(-2-AMINOETHYL)PIPERAZINE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2815 CAS number 140-31-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 985 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 129.24 Density of gas (kg/m3) 5.68 Boiling Point (°C) 222 Melting Point (°C) -19 Vapour Pressure (Pa) 150 [Pa] at a temperature of 20°C Ignition Temperature (°C) 360 Flash Point (°C) 93.3
### Behaviour at sea
### Additional data
Colour pale yellow Odour ammoniacal odour
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Family name aliphatic amines
### Reactivity data
Water No Acid(s) Yes Base(s) No Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Specific Health Concern (D3) Ss - Skin Sensitization Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 7.5 TEEL-2 (mg/m3) 50 TEEL-3 (mg/m3) 500
### Ecotoxicity
# n-AMYLENE
UN Number: 1108
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1108
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 641 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 70.13 Density of gas (kg/m3) 2.71 Boiling Point (°C) 30.1 Vapour Pressure (Pa) 66000 [Pa] at a temperature of 20°C Flash Point (°C) -18 Lower explosivity limit (LEL) (volume %) 1.4 Upper explosivity limit (UEL) (volume %) 8.7
### Behaviour at sea
### Additional data
Colour colourless Odour gasoline odour Standard behavior classification DE, ED, E
### Transportation data
Transport mode Bulk,Packaged Cargo group 30 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name olefins IMO class 3.1
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 750 ppm TEEL-2 (mg/m3) 6000 ppm TEEL-3 (mg/m3) 75000 ppm
### Ecotoxicity
# n-BUTANOL
UN Number: 1120 - CAS Number: 71-36-3 Also known as: BUTANOL, 1-BUTANOL, BUTAN-1-OL, n-BUTANOL, 2-BUTYL ALCOHOL, BUTYL ALCOHOL, n-BUTYL ALCOHOL, Normal Primary BUTYL ALCOHOL, BUTYL HYDROXIDE, CC SS 203, N-Butanol, Butyric Alcohol, 1-Hydroxybutane, Propylcarbinol, N-Butyl Alcohol
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1120 CAS number 71-36-3 Formula C 4 H 1 0 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 810 [Kg/m³] at a temperature of 20°C 821.3 [Kg/m³] at a temperature of 5°C 817.9 [Kg/m³] at a temperature of 10°C 811.6 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 3.7 [cSt] at a temperature of 20°C 3.1377 [cSt] at a temperature of 25°C 5.82 [cSt] at a temperature of 5°C 11.97 [cSt] at a temperature of 10°C 4.7807 [cSt] at a temperature of 20°C Molar mass (g/mol) 74.12 Density of gas (kg/m3) 3.29 Solubility (g/L) 77000 [g/L] at a temperature of 20°C and salinity of 0‰ 68600 [g/L] at a temperature of 25°C and salinity of 0‰ 72670 [g/L] at a temperature of 20°C and salinity of 0‰ 66730 [g/L] at a temperature of 20°C and salinity of 5‰ 54260 [g/L] at a temperature of 20°C and salinity of 30‰ Boiling Point (°C) 117.7 Melting Point (°C) -89 Critical molar volume (m³/mol) 0.000274 Critical temperature (°C) 563 Critical pressure (Pa) 4414000 Surface tension (mN/m) 24.6 [mN/m] at a temperature of 20°C 24.93 [mN/m] at a temperature of 25°C 25.71 [mN/m] at a temperature of 3.8°C 24.9 [mN/m] at a temperature of 11.1°C 24.25 [mN/m] at a temperature of 18.4°C Interfacial tension (mN/m) 50 [mN/m] at a temperature of 25°C and salinity of 0‰ Vapour Pressure (Pa) 626 [Pa] at a temperature of 20°C 893 [Pa] at a temperature of 25°C Ignition Temperature (°C) 340 Flash Point (°C) 35 Flash Point (Pensky-Martens closed cup) (°C) 28.9 Flash Point (Cleveland open cup) (°C) 36.1 Lower explosivity limit (LEL) (volume %) 1.4 Upper explosivity limit (UEL) (volume %) 11.2 Vapor enthalpy (J/Kg) 584045 [J/Kg] at a temperature of 117.6°C 706277 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 35900000 Specific heat capacity (J/(Kg·K)) 2390.7 Combustion efficiency (%) 98 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.05 Rad fraction (%) 22 Henry's constant (mol/(m³·Pa)) 0.89
### Behaviour at sea
Log kow 0.88 Log koc 1.85 Aqueous photolysis (Half-life) 4.09 Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 10 Bioconcentration factor (BCF) 2.72
### Additional data
Colour colourless Odour alcohol odour MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment.
### Transportation data
Package group III Cargo group 20 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alcohols, glycols IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Static electricity Yes Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 8000 Hazard statements Physical H226 Flammable liquid and vapour. Health H302 Harmful if swallowed. H315 Causes skin irritation. H318 Causes serious eye damage. H335 May cause respiratory irritation. H336 May cause drowsiness or dizziness. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P233 Keep container tightly closed. P240 Ground/bond container and receiving equipment. P241 Use explosion-proof electrical/ventilating/lighting/.../equipment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P370 + P378 In case of fire: Use ... for extinction. Storage P403 + P235 Store in a well-ventilated place. Keep cool. Disposal P501 Dispose of contents/container to ... TLV-TWA 50 TEEL-1 (mg/m3) 50 ppm TEEL-2 (mg/m3) 50 ppm TEEL-3 (mg/m3) 1400 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 225 Lowest median lethal concentration (LC50) on crustacean (mg/l) 1328 Lowest median lethal concentration (LC50) on fishes (mg/l) 1376 Highest no observed effect concentration (NOEC) on algae (mg/l) 129 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 20 Assessment factor (AF) 1000 on the Short term 1000 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 225 [µg/l] on the Short term 20 [µg/l] on the Long term
# n-BUTYL ACETATE
UN Number: 1123 - CAS Number: 123-86-4 Also known as: ACETATE DE BUTYLE, ACETIC ACID, n-BUTYL ESTER, BUTYL ACETATE, 1-BUTYL ACETATE, n-BUTYL ACETATE, BUTYL ETHANOATE, Acetic Acid, N-Butyl Ester, 1-Acetoxybutane, N-Butyl Acetate
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1123 CAS number 123-86-4 Formula C 6 H 1 2 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 875 [Kg/m³] at a temperature of 20°C 896 [Kg/m³] at a temperature of 5°C 891.6 [Kg/m³] at a temperature of 10°C 881 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.83 [cSt] at a temperature of 20°C 0.77 [cSt] at a temperature of 25°C 2.7009 [cSt] at a temperature of 5°C 2.5236 [cSt] at a temperature of 10°C 2.3383 [cSt] at a temperature of 20°C Molar mass (g/mol) 116.16 Density of gas (kg/m3) 5.16 Solubility (g/L) 7000 [g/L] at a temperature of 20°C and salinity of 0‰ 8500 [g/L] at a temperature of 25°C and salinity of 0‰ 7240 [g/L] at a temperature of 20°C and salinity of 0‰ 6970 [g/L] at a temperature of 20°C and salinity of 5‰ 5670 [g/L] at a temperature of 20°C and salinity of 30‰ Boiling Point (°C) 126 Melting Point (°C) -77 Surface tension (mN/m) 24.88 [mN/m] at a temperature of 25°C 25.8 [mN/m] at a temperature of 5.7°C 25.02 [mN/m] at a temperature of 10.6°C 24.83 [mN/m] at a temperature of 18.4°C Interfacial tension (mN/m) 57 [mN/m] at a temperature of 20°C and salinity of 0‰ Vapour Pressure (Pa) 1160 [Pa] at a temperature of 20°C 1990 [Pa] at a temperature of 25°C Ignition Temperature (°C) 370 Flash Point (°C) 22 Flash Point (Pensky-Martens closed cup) (°C) 22 Lower explosivity limit (LEL) (volume %) 1.4 Upper explosivity limit (UEL) (volume %) 7.6 Vapor enthalpy (J/Kg) 312328 [J/Kg] at a temperature of 126°C 377582 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 37700000 Specific heat capacity (J/(Kg·K)) 1961 Combustion efficiency (%) 98 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.1 Rad fraction (%) 23 Henry's constant (mol/(m³·Pa)) 28.8
### Behaviour at sea
Persistence (days) 0.8 Log kow 1.82 Log koc 0.35 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) 114 Biodegradation in marine environment (Half- life) (days) 10 Bioconcentration factor (BCF) 13.1
### Additional data
Colour colourless Odour pleasant, fruit odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification FED
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 34 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name esters IMO class 3.2/3.3
### Reactivity data
Acid(s) Yes Static electricity Yes Oxidizing agents Yes Notable risks Vapours may form an explosive mixture with air.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 10000 Hazard statements Physical H226 Flammable liquid and vapour. Health H336 May cause drowsiness or dizziness. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P233 Keep container tightly closed. P235 Keep cool. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P312 Call a POISON CENTER or doctor/physician if you feel unwell. TLV-TWA 200 ERPG-2 (ppm) 200 ERPG-3 (ppm) 3000
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 2 Lowest median lethal concentration (LC50) on crustacean (mg/l) 32 Lowest median lethal concentration (LC50) on fishes (mg/l) 18 Highest no observed effect concentration (NOEC) on algae (mg/l) 296 Assessment factor (AF) 1000 on the Short term 10000 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 18 [µg/l] on the Short term 1.8 [µg/l] on the Long term
# n-BUTYL ACRYLATE inhibited
UN Number: 2348 - CAS Number: 141-32-2 Also known as: ACRYLATE DE BUTYLE, ACRYLIC ACID, N-BUTYL ESTER, ACRYLIC ACID, BUTYL ESTER, 2-AGROPENOIC ACID, N-BUTYL ESTER, BUTYL ACRYLATE, BUTYL ACRYLATE MONOMER (Inhibited), n-BUTYL ANYLATE, BUTYL-2-PROPENOATE, n-BUTYL 2-PROPENOATE, Acrylic Acid, Butyl Ester, Acrylic Acid, N-Butyl Ester, Butyl 2-Propenoate, 2-Propenoic Acid, Butyl Ester, 2-Propenoic Acid, N-Butyl Ester, Acrylate De N-Butyle, N-Butyl Acrylate
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2348 CAS number 141-32-2 Formula C 7 H 1 2 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 899 [Kg/m³] at a temperature of 20°C 913.1 [Kg/m³] at a temperature of 5°C 908.5 [Kg/m³] at a temperature of 10°C 900.1 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 2.8255 [cSt] at a temperature of 5°C 2.7518 [cSt] at a temperature of 10°C 2.6219 [cSt] at a temperature of 20°C Molar mass (g/mol) 128.17 Density of gas (kg/m3) 5.702 Solubility (g/L) 2000 [g/L] at a temperature of 25°C and salinity of 0‰ 1610 [g/L] at a temperature of 20°C and salinity of 0‰ 1340 [g/L] at a temperature of 20°C and salinity of 5‰ 1440 [g/L] at a temperature of 20°C and salinity of 30‰ Boiling Point (°C) 149 Melting Point (°C) -65 Surface tension (mN/m) 20 [mN/m] at a temperature of 25°C 26.77 [mN/m] at a temperature of 6.1°C 26.56 [mN/m] at a temperature of 11.3°C 25.63 [mN/m] at a temperature of 19.1°C Interfacial tension (mN/m) 60 [mN/m] at a temperature of 25°C and salinity of 0‰ Vapour Pressure (Pa) 9100 [Pa] at a temperature of 20°C 727 [Pa] at a temperature of 25°C Flash Point (°C) 37 Flash Point (Pensky-Martens closed cup) (°C) 39 Flash Point (Cleveland open cup) (°C) 47.8 Lower explosivity limit (LEL) (volume %) 1.5 Upper explosivity limit (UEL) (volume %) 9.9 Combus enthalpy (J/Kg) 29400000 Specific heat capacity (J/(Kg·K)) 1958 Combustion efficiency (%) 96 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.05 Rad fraction (%) 23 Henry's constant (mol/(m³·Pa)) 46.59
### Behaviour at sea
Log kow 2.36 Log koc 1.54 Aqueous photolysis (Half-life) 0.0138 Biodegradation in estuary environment (Half-life) (days) 1100 Biodegradation in marine environment (Half-life) (days) 10 Bioconcentration factor (BCF) 13.1
### Additional data
Colour colourless Odour sharp, fragrant odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 14 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name acrylates IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No Notable risks Polymerize easily, inhibitor in comercial products.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
Hazard statements Health H315 Causes skin irritation. H317 May cause an allergic skin reaction. H319 Causes serious eye irritation. H332 Harmful if inhaled. H335 May cause respiratory irritation. Environmental H412 Harmful to aquatic life with long lasting effects. Precautionary statements Prevention P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. TLV-TWA 10 ERPG-1 (ppm) 0.05 ERPG-2 (ppm) 25 ERPG-3 (ppm) 250
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 2.6 Lowest median lethal concentration (LC50) on crustacean (mg/l) 8.2 Lowest median lethal concentration (LC50) on fishes (mg/l) 2.1 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.136 Assessment factor (AF) 100 on the Short term 10000 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 21 [µg/l] on the Short term 0.21 [µg/l] on the Long term
# n-BUTYL METHACRYLATE inhibited
UN Number: 2227 - CAS Number: 97-88-1
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2227 CAS number 97-88-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 897.5 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 142.2 Density of gas (kg/m3) 6.192 Boiling Point (°C) 163 Melting Point (°C) -75 Vapour Pressure (Pa) 300 [Pa] at a temperature of 20°C Ignition Temperature (°C) 294 Flash Point (°C) 46
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour colourless Odour mild odour Standard behavior classification FED
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 14 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name acrylates IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 7.5 TEEL-2 (mg/m3) 50 TEEL-3 (mg/m3) 500
### Ecotoxicity
# n-BUTYL PROPIONATE
UN Number: 1914
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1914
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 840 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 130.2 Density of gas (kg/m3) 5.805 Boiling Point (°C) 145 Melting Point (°C) -90 Vapour Pressure (Pa) 424 [Pa] at a temperature of 20°C Ignition Temperature (°C) 425 Flash Point (°C) 32 Lower explosivity limit (LEL) (volume %) 1.1 Upper explosivity limit (UEL) (volume %) 6.8
### Behaviour at sea
### Additional data
Colour colourless Odour characteristic
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 34 State liquid Temperature (°C) ambient Family name esters IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 500 TEEL-2 (mg/m3) 500 TEEL-3 (mg/m3) 500
### Ecotoxicity
# n-BUTYRIC ACID
UN Number: 2820 - CAS Number: 107-92-6 Also known as: ACIDE BUTYRIQUE, BUTANOIC ACID
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2820 CAS number 107-92-6
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 958 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 88.1 Density of gas (kg/m3) 3.6 Boiling Point (°C) 164 Vapour Pressure (Pa) 57 [Pa] at a temperature of 20°C Upper explosivity limit (UEL) (volume %) 10
### Behaviour at sea
### Additional data
Colour colourless Odour rancid, butter odour
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name organic acids
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 40 ppm TEEL-2 (mg/m3) 250 ppm TEEL-3 (mg/m3) 250 ppm
### Ecotoxicity
# n-DECYLALCOHOL
Also known as: ALCOOL DECYLIQUE, ANTAK (T), CAPRIC ALCOHOL, CAPRINIC ALCOHOL, DECANOL, DECAN-1-OL, n-DECANOL, DECATYL ALCOHOL, DECYL ALCOHOL, DECYLIC ALCOHOL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 840 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 158.29 Density of gas (kg/m3) 6.31 Boiling Point (°C) 230 Vapour Pressure (Pa) 133 [Pa] at a temperature of 20°C Ignition Temperature (°C) 285 Flash Point (°C) 82
### Behaviour at sea
### Additional data
Colour colourless to light yellow Odour weak alcohol odour
### Transportation data
Cargo group 20 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alcohols, glycols
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Interference with coastal amenities (E2) Fp - Persistent slick forming substance
### Human toxicity threshold
### Ecotoxicity
# N-ETHYL BUTYLAMINE
CAS Number: 13360-63-9 Also known as: BUTYLETHYLAMINE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 13360-63-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 740 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 101.2 Density of gas (kg/m3) 4.515 Boiling Point (°C) 108.5 Vapour Pressure (Pa) 2710 [Pa] at a temperature of 20°C Flash Point (°C) 13
### Behaviour at sea
### Additional data
Colour water-white Odour amine
### Transportation data
State liquid Temperature (°C) ambient Family name aliphatic amines
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# N-ETHYL CYCLOHEXYLAMINE
CAS Number: 5459-93-8 Also known as: CYCLOHEXYLAMINE, N-ETHYL, N-CYCLOHEXYLETHYLAMINE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 5459-93-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 853 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 127.23 Density of gas (kg/m3) 5.68 Boiling Point (°C) 165 Melting Point (°C) -45 Ignition Temperature (°C) 545 Flash Point (°C) 30
### Behaviour at sea
### Additional data
Colour colourless Odour musky ammonia Standard behavior classification FD/FED/ED
### Transportation data
State liquid Temperature (°C) ambient Family name aliphatic amines
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# n-HEPTANOIC ACID
CAS Number: 111-14-8 Also known as: ACIDE n-HEPTANOIQUE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 111-14-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 900 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 130.19 Density of gas (kg/m3) 5.8 Boiling Point (°C) 223 Melting Point (°C) -7.5 Vapour Pressure (Pa) 130 [Pa] at a temperature of 20°C Flash Point (°C) 107
### Behaviour at sea
### Additional data
Colour colourless Odour rancid Standard behavior classification FD
### Transportation data
State liquid Family name organic acids
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 15 ppm TEEL-2 (mg/m3) 100 ppm TEEL-3 (mg/m3) 600 ppm
### Ecotoxicity
# n-HEPTENE
UN Number: 2278
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2278
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 697 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 98.18 Density of gas (kg/m3) 5.173 Boiling Point (°C) 93 Melting Point (°C) 119 Vapour Pressure (Pa) 15960 [Pa] at a temperature of 20°C Ignition Temperature (°C) 260
### Behaviour at sea
### Additional data
Colour colourless Odour gasoline odour
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 30 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name PF IMO class 3.2
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# n-HEXANE
UN Number: 1208 - CAS Number: 100-54-3 Also known as: DIPROPYL, Hexane, Hexyl Hydride, Normal Hexane, N-Hexane
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1208 CAS number 100-54-3 Formula C 6 H 1 4
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 659 [Kg/m³] at a temperature of 20°C 675.3 [Kg/m³] at a temperature of 5°C 669.6 [Kg/m³] at a temperature of 10°C 661.3 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.47 [cSt] at a temperature of 20°C 0.45 [cSt] at a temperature of 25°C 1.7918 [cSt] at a temperature of 5°C 1.5532 [cSt] at a temperature of 10°C 1.6936 [cSt] at a temperature of 20°C Molar mass (g/mol) 86.17 Density of gas (kg/m3) 3.87 Solubility (g/L) 10 [g/L] at a temperature of 20°C and salinity of 0‰ 8 [g/L] at a temperature of 25°C and salinity of 35.3‰ 8.8 [g/L] at a temperature of 20°C and salinity of 0‰ 7.1 [g/L] at a temperature of 20°C and salinity of 5‰ 6.6 [g/L] at a temperature of 20°C and salinity of 30‰ Boiling Point (°C) 68.9 Melting Point (°C) -95 Surface tension (mN/m) 18.43 [mN/m] at a temperature of 20°C 17.89 [mN/m] at a temperature of 25°C 19.92 [mN/m] at a temperature of 5°C 19.09 [mN/m] at a temperature of 10°C 18.6 [mN/m] at a temperature of 17.7°C Interfacial tension (mN/m) 51.1 [mN/m] at a temperature of 20°C and salinity of 0‰ Vapour Pressure (Pa) 15996 [Pa] at a temperature of 20°C 19998 [Pa] at a temperature of 25°C Ignition Temperature (°C) 260 Flash Point (°C) -22 Flash Point (Pensky-Martens closed cup) (°C) -22 Lower explosivity limit (LEL) (volume %) 1.1 Upper explosivity limit (UEL) (volume %) 7.7 Vapor enthalpy (J/Kg) 334494 [J/Kg] at a temperature of 69°C 366295 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 44700000 Specific heat capacity (J/(Kg·K)) 2270.2 Combustion efficiency (%) 96 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.08 Rad fraction (%) 33 Henry's constant (mol/(m³·Pa)) 171239
### Behaviour at sea
Log kow 3.29 Log koc 2.9 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 585
### Additional data
Colour colourless Odour gasoline odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Package group II Cargo group 31 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name paraffins IMO class 3.1
### Reactivity data
Water No Static electricity Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 5000 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H304 May be fatal if swallowed and enters airways. H315 Causes skin irritation. H336 May cause drowsiness or dizziness. H361 Suspected of damaging fertility or the unborn child. H373 May cause damage to organs through prolonged or repeated exposure, exposure cause the hazard: Environmental H411 Toxic to aquatic life with long lasting effects. Precautionary statements General P102 Keep out of reach of children. P103 Read label before use. Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P241 Use explosion-proof electrical/ventilating/lighting/.../equipment. P243 Take precautionary measures against static discharge. P260 Do not breathe dust/fume/gas/mist/vapours/spray. P271 Use only outdoors or in a well-ventilated area. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P331 Do NOT induce vomiting. TLV- TWA 50 TEEL-1 (mg/m3) 400 ppm TEEL-2 (mg/m3) 3300 ppm TEEL-3 (mg/m3) 8600 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 50 Lowest median lethal concentration (LC50) on fishes (mg/l) 2.5
# n-HEXANOIC ACID
UN Number: 2829 - CAS Number: 142-62-1 Also known as: ACIDE n-HEXANOIQUE, BUTYLACETIC ACID, n-CAPROIC ACID, CAPRONIC ACID
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2829 CAS number 142-62-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 927 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 110.16 Density of gas (kg/m3) 5.16 Boiling Point (°C) 202/203 Melting Point (°C) -3 Flash Point (°C) 104
### Behaviour at sea
### Additional data
Colour colourless or slighty yellow Odour goat-like Standard behavior classification FD/FED
### Transportation data
Package group III State liquid Temperature (°C) ambient Family name organic acids
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 15 TEEL-2 (mg/m3) 100 TEEL-3 (mg/m3) 500
### Ecotoxicity
# n-HEXANOL
UN Number: 2282 - CAS Number: 111-27-3 Also known as: AMYL CARBINOL, CAPROYL ALCOHOL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2282 CAS number 111-27-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 850 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 102.18 Density of gas (kg/m3) 4.515 Boiling Point (°C) 157.3 Melting Point (°C) -45 Vapour Pressure (Pa) 130 [Pa] at a temperature of 20°C Ignition Temperature (°C) 290 Flash Point (°C) 63 Lower explosivity limit (LEL) (volume %) 1.2 Upper explosivity limit (UEL) (volume %) 7.7
### Behaviour at sea
### Additional data
Colour colourless Odour sweet odour
### Transportation data
Package group III Cargo group 20 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alcohols, glycols IMO class 3.3
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 2 ppm TEEL-2 (mg/m3) 15 ppm TEEL-3 (mg/m3) 75 ppm
### Ecotoxicity
# n-PENTANE
UN Number: 1265 - CAS Number: 109-66-0 Also known as: N-Pentane, Pentane
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1265 CAS number 109-66-0 Formula C 5 H 1 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 626 [Kg/m³] at a temperature of 20°C 642.9 [Kg/m³] at a temperature of 5°C 638.4 [Kg/m³] at a temperature of 10°C 627.8 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.35771 [cSt] at a temperature of 25°C 13377 [cSt] at a temperature of 5°C 1.3315 [cSt] at a temperature of 10°C 0.98758 [cSt] at a temperature of 20°C Molar mass (g/mol) 72.15 Density of gas (kg/m3) 3.211 Solubility (g/L) 38 [g/L] at a temperature of 25°C and salinity of 0‰ 28 [g/L] at a temperature of 25°C and salinity of 35‰ 37 [g/L] at a temperature of 20°C and salinity of 0‰ 38 [g/L] at a temperature of 20°C and salinity of 5‰ 27 [g/L] at a temperature of 20°C and salinity of 30‰ Boiling Point (°C) 36.3 Melting Point (°C) -130 Critical molar volume (m³/mol) 0.000311 Critical temperature (°C) 469.7 Critical pressure (Pa) 3370000 Surface tension (mN/m) 16 [mN/m] at a temperature of 20°C 15.49 [mN/m] at a temperature of 25°C 17.55 [mN/m] at a temperature of 5.1°C 16.77 [mN/m] at a temperature of 10.2°C 16.43 [mN/m] at a temperature of 16.43°C Vapour Pressure (Pa) 533320 [Pa] at a temperature of 20°C Ignition Temperature (°C) 285 Flash Point (°C) -20 Flash Point (Pensky-Martens closed cup) (°C) -49 Lower explosivity limit (LEL) (volume %) 1.4 Upper explosivity limit (UEL) (volume %) 8.5 Vapor enthalpy (J/Kg) 357455 [J/Kg] at a temperature of 30.06°C 366190 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 48635463 Specific heat capacity (J/(Kg·K)) 2317 Henry's constant (mol/(m³·Pa)) 12800
### Behaviour at sea
Log kow 3.64 Log koc 1.86 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 80
### Additional data
Colour colourless Odour gasoline odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 31 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name paraffins IMO class 3.1
### Reactivity data
Water No Static electricity Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 15000 Hazard statements Physical H224 Extremely flammable liquid and vapour. Health H304 May be fatal if swallowed and enters airways. H336 May cause drowsiness or dizziness. Environmental H411 Toxic to aquatic life with long lasting effects. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P233 Keep container tightly closed. P240 Ground/bond container and receiving equipment. P241 Use explosion-proof electrical/ventilating/lighting/.../equipment. P242 Use only non- sparking tools. P243 Take precautionary measures against static discharge. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P271 Use only outdoors or in a well-ventilated area. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P312 Call a POISON CENTER or doctor/physician if you feel unwell. P331 Do NOT induce vomiting. P370 + P378 In case of fire: Use ... for extinction. P391 Collect spillage. Storage P403 + P233 Store in a well-ventilated place. Keep container tightly closed. P403 + P235 Store in a well-ventilated place. Keep cool. P405 Store locked up. Disposal P501 Dispose of contents/container to ... TLV-TWA 600 TEEL-1 (mg/m3) 610 ppm TEEL-2 (mg/m3) 610 ppm TEEL-3 (mg/m3) 1500 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 1.19 Highest no observed effect concentration (NOEC) on algae (mg/l) 4.549 Assessment factor (AF) 100 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 27 [µg/l] on the Short term
# n-PROPANOLAMINE
CAS Number: 156-87-6 Also known as: 3-AMINO, 1-PROPANOL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 156-87-6
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 982 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 75.11 Density of gas (kg/m3) 3.35 Boiling Point (°C) 188 Melting Point (°C) 11 Flash Point (°C) 79
### Behaviour at sea
### Additional data
Colour colourless to pale yellow Odour fishy
### Transportation data
Family name alkanolamines
### Reactivity data
Water No Acid(s) Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 0.04 TEEL-2 (mg/m3) 0.3 TEEL-3 (mg/m3) 500
### Ecotoxicity
# n-PROPYL ACETATE
UN Number: 1276 - CAS Number: 109-60-4 Also known as: ACETATE DE n-PROPYLE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1276 CAS number 109-60-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 886 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 102.13 Density of gas (kg/m3) 4.541 Boiling Point (°C) 101 Melting Point (°C) -95 Vapour Pressure (Pa) 5332 [Pa] at a temperature of 20°C Ignition Temperature (°C) 430 Flash Point (°C) 10 Lower explosivity limit (LEL) (volume %) 1.7
### Behaviour at sea
### Additional data
Colour colourless Odour mild odour Standard behavior classification ED
### Transportation data
Package group II Cargo group 34 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name esters IMO class 3.2
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
IDHL 8000 TLV-TWA 200 TEEL-1 (mg/m3) 250 ppm TEEL-2 (mg/m3) 1000 ppm TEEL-3 (mg/m3) 1700 ppm
### Ecotoxicity
# n-PROPYLAMINE
UN Number: 1277 - CAS Number: 107-10-8 Also known as: 1-AMINOPROPANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1277 CAS number 107-10-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 720 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 59.11 Density of gas (kg/m3) 2.64 Boiling Point (°C) 49 Melting Point (°C) -83 Vapour Pressure (Pa) 33000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 260 Flash Point (°C) -37 Upper explosivity limit (UEL) (volume %) 10.4
### Behaviour at sea
### Additional data
Colour colourless Odour ammonia-like Standard behavior classification DE
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) cool Family name aliphatic amines IMO class 3.1
### Reactivity data
Water No Acid(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 50 ppm TEEL-2 (mg/m3) 250 ppm TEEL-3 (mg/m3) 250 ppm
### Ecotoxicity
# n-PROPYLBENZENE
UN Number: 2364 - CAS Number: 103-65-1 Also known as: BENZENE, PROPYL, Isocumene, Propylbenzene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2364 CAS number 103-65-1 Formula C 9 H 1 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 862 [Kg/m³] at a temperature of 20°C 859.3 [Kg/m³] at a temperature of 25°C Molar mass (g/mol) 120.19 Density of gas (kg/m3) 5.34 Solubility (g/L) 60 [g/L] at a temperature of 15°C and salinity of 0‰ 55 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 160 Melting Point (°C) -100 Critical molar volume (m³/mol) 0.00044 Critical temperature (°C) 638.35 Critical pressure (Pa) 3200000 Vapour Pressure (Pa) 332 [Pa] at a temperature of 20°C 455 [Pa] at a temperature of 25°C Flash Point (°C) 30 Flash Point (Pensky- Martens closed cup) (°C) 30 Lower explosivity limit (LEL) (volume %) 0.8 Upper explosivity limit (UEL) (volume %) 6 Vapor enthalpy (J/Kg) 384554 [J/Kg] at a temperature of 25°C Specific heat capacity (J/(Kg·K)) 1786 Henry's constant (mol/(m³·Pa)) 1064
### Behaviour at sea
Log kow 3.6 Log koc 2.91 Biodegradation in estuary environment (Half- life) (days) Not hydrolysable Bioconcentration factor (BCF) 138
### Additional data
Colour light yellow Odour odourless MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 32 State liquid Temperature (°C) ambient Family name aromatic hydrocarbons IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Metal(s) and alloys No Oxidizing agents Yes
### GESAMP Hazard profile
Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Interference with coastal amenities (E2) FE - Floater/Evaporator
### Human toxicity threshold
TEEL-1 (mg/m3) 75 ppm TEEL-2 (mg/m3) 600 ppm TEEL-3 (mg/m3) 3000 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on fishes (mg/l) 1.55
# n-PROPYLCHLORIDE
UN Number: 1278 - CAS Number: 540-54-5 Also known as: CHLOROPROPANE, CHLORO-1-PROPANE, 1-CHLOROPROPANE, CHLORURE DE PROPYLE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1278 CAS number 540-54-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 892 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 78.54 Density of gas (kg/m3) 3.5 Boiling Point (°C) 46/47 Melting Point (°C) -123 Ignition Temperature (°C) 520 Flash Point (°C) -18 Lower explosivity limit (LEL) (volume %) 2.6 Upper explosivity limit (UEL) (volume %) 11
### Behaviour at sea
### Additional data
Colour colourless Odour chloroform-like Standard behavior classification FD/FED/E
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 36 State liquid Temperature (°C) ambient Family name halogenated hydrocarbons IMO class 3.1
### Reactivity data
Water No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# NAPHTHA petroleum
UN Number: 1268 - CAS Number: 64742-82-1 Also known as: Naphtha (Petroleum), Hydrodesulfurized Heavy, Naphta Lourd (Petrole) Desulfure
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1268 CAS number 64742-82-1
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Boiling Point (°C) 138 Melting Point (°C) -26 Vapour Pressure (Pa) 200-600 [Pa] at a temperature of 20°C Ignition Temperature (°C) 229 Flash Point (°C) 38-60 Flash Point (Cleveland open cup) (°C) 47 Lower explosivity limit (LEL) (volume %) 0.6 Upper explosivity limit (UEL) (volume %) 6.5
### Behaviour at sea
### Additional data
Odour gasoline odour MARPOL pollution category Category Description Other Substances Substances which have been evaluated and found to fall outside Category X, Y or Z because they are considered to present no harm to marine resources, human health, amenities or other legitimate uses of the sea when discharged into the sea from tank cleaning of deballasting operations. The discharge of bilge or ballast water or other residues or mixtures containing these substances are not subject to any requirements of MARPOL Annex II.
### Transportation data
Package group II Cargo group 33 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name miscell. hydroc. mixt IMO class 3.1/3.2/3.
### Reactivity data
Acid(s) Yes Base(s) Yes Static electricity Yes Oxidizing agents Yes
### GESAMP Hazard profile
Interference with coastal amenities (E2) G - Gas
### Human toxicity threshold
IDHL 10000 Hazard statements Health H304 May be fatal if swallowed and enters airways. H340 May cause genetic defects. Exposure cause the hazard: H350 May cause cancer. Precautionary statements Prevention P201 Obtain special instructions before use. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P308 + P313 IF exposed or concerned: Get medical advice/attention. P331 Do NOT induce vomiting. TLV-TWA 100 TEEL-1 (mg/m3) 300 ppm TEEL-2 (mg/m3) 395 ppm TEEL-3 (mg/m3) 395 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on fishes (mg/l) 2.1
# NAPHTHA solvent
UN Number: 1268
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1268
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 860 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 130 Vapour Pressure (Pa) 399 [Pa] at a temperature of 20°C Lower explosivity limit (LEL) (volume %) 0.8
### Behaviour at sea
Persistence (days) 2.7
### Additional data
Colour colourless Standard behavior classification FE
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 33 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name miscell. hydroc. mixt IMO class 3.1/3.2/3.
### Reactivity data
Acid(s) Yes Base(s) Yes Static electricity Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 10000 TLV-TWA 100
### Ecotoxicity
# NAPHTHALENE molten
UN Number: 2304 - CAS Number: 91-20-3 Also known as: Naphthalin, Naphthene, Tar Camphor, White Tar, Naphthalene, Naphtalene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2304 CAS number 91-20-3 Formula C 1 0 H 8
### Physical chemical data
Physical State (20°C) Solid Physical State (25°C) Solid Density (kg/m3) 1140 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.96 [cSt] at a temperature of 20°C Molar mass (g/mol) 128.18 Density of gas (kg/m3) 5.702 Solubility (g/L) 31 [g/L] at a temperature of 25°C and salinity of 0‰ 23 [g/L] at a temperature of 25°C and salinity of 35‰ Boiling Point (°C) 218 Melting Point (°C) 80 Critical molar volume (m³/mol) 0.000407 Critical temperature (°C) 748.5 Critical pressure (Pa) 4050000 Surface tension (mN/m) 31.8 [mN/m] at a temperature of 20°C Vapour Pressure (Pa) 130 [Pa] at a temperature of 20°C 10.5 [Pa] at a temperature of 25°C Ignition Temperature (°C) 540 Flash Point (°C) 80 Flash Point (Pensky-Martens closed cup) (°C) 88 Flash Point (Cleveland open cup) (°C) 79 Lower explosivity limit (LEL) (volume %) 0.9 Upper explosivity limit (UEL) (volume %) 5.9 Vapor enthalpy (J/Kg) 337052 [J/Kg] at a temperature of 218°C Combus enthalpy (J/Kg) 38900000 Specific heat capacity (J/(Kg·K)) 1292.8 Combustion efficiency (%) 70 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.06 Rad fraction (%) 30 Henry's constant (mol/(m³·Pa)) 37.85
### Behaviour at sea
Log kow 3.7 Log koc 3.13 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) Not biodegradable Bioconcentration factor (BCF) 427
### Additional data
Colour colourless Odour mothball odour MARPOL pollution category Category Description Other Substances Substances which have been evaluated and found to fall outside Category X, Y or Z because they are considered to present no harm to marine resources, human health, amenities or other legitimate uses of the sea when discharged into the sea from tank cleaning of deballasting operations. The discharge of bilge or ballast water or other residues or mixtures containing these substances are not subject to any requirements of MARPOL Annex II.
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 32 State liquid Temperature (°C) elevated Pressure (Pa) ambient Family name aromatic hydrocarbons IMO class 4.1
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 3 - ≥100 and <500 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 500 Hazard statements Physical H228 Flammable solid. Health H302 Harmful if swallowed. H351 Suspected of causing cancer. Environmental H410 Very toxic to aquatic life with long lasting effects. Precautionary statements Prevention P202 Do not handle until all safety precautions have been read and understood. P234 Keep only in original container. P270 Do no eat, drink or smoke when using this product. P273 Avoid release to the environment. P281 Use personal protective equipment as required. Response P301 + P330 + P331 IF SWALLOWED: rinse mouth. Do NOT induce vomiting. P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P308 + P313 IF exposed or concerned: Get medical advice/attention. P370 + P378 In case of fire: Use ... for extinction. Disposal P501 Dispose of contents/container to ... TLV-TWA 10 TEEL-1 (mg/m3) 15 ppm TEEL-2 (mg/m3) 15 ppm TEEL-3 (mg/m3) 250 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 2.96 Lowest median lethal concentration (LC50) on crustacean (mg/l) 0.8 Lowest median lethal concentration (LC50) on fishes (mg/l) 1.6 Highest no observed effect concentration (NOEC) on algae (mg/l) > 4.3 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.5 Highest no observed effect concentration (NOEC) on fishes (mg/l) 0.12 Assessment factor (AF) 100 on the Short term 100 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 8 [µg/l] on the Short term 1.2 [µg/l] on the Long term
# NAPHTHENIC ACIDS
UN Number: 3082 - CAS Number: 1338-24-5 Also known as: ACIDES NAPHTHENIQUES
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082 CAS number 1338-24-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 982 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 200 Boiling Point (°C) 140-370 Melting Point (°C) -35 Flash Point (°C) 149
### Behaviour at sea
### Additional data
Colour gold to black Odour odourless
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Interference with coastal amenities (E2) FD - Floater/Dissolver
### Human toxicity threshold
### Ecotoxicity
# NEODECANOIC ACID
CAS Number: 26896-20-8 Also known as: ACIDE NEODECANOIQUE, 2,2-DIMETHYLOCTANOIC ACID
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 26896-20-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 920 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 172.27 Density of gas (kg/m3) 7.74 Boiling Point (°C) 250/257 Melting Point (°C) < 40 Flash Point (°C) 94
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Temperature (°C) ambient Family name organic acids
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 40 TEEL-2 (mg/m3) 300 TEEL-3 (mg/m3) 500
### Ecotoxicity
# NICKEL CYANIDE
UN Number: 1653 - CAS Number: 98-95-3 Also known as: CYANURE DE NICKEL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1653 CAS number 98-95-3
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2400 [Kg/m³] at a temperature of 20°C
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour light green, yellow-brown Odour weak almond odour Marine pollutant P Standard behavior classification D, SD, S
### Transportation data
Package group II State solid Temperature (°C) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 4 - Very high Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 1.13 TEEL-2 (mg/m3) 9.44 TEEL-3 (mg/m3) 18.9
### Ecotoxicity
# Nitric Acid
CAS Number: 7697-37-2 Also known as: Hydrogen Nitrate, Aqua Fortis, Nitric Acid, Acide Nitrique
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 7697-37-2 Formula HNO 3
### Physical chemical data
Physical State (25°C) Liquid Molar mass (g/mol) 63.012 Solubility (g/L) 10000000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 83 Melting Point (°C) -41.6 Vapor enthalpy (J/Kg) 620517 [J/Kg] at a temperature of 25°C Specific heat capacity (J/(Kg·K)) 1744
### Behaviour at sea
Log kow 0.21 Log koc 1.21
### Additional data
MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
### Reactivity data
Abilities Miscible in water.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
Hazard statements Physical H272 May intensify fire, oxidiser. H290 May be corrosive to metals. Health H314 Causes severe skin burns and eye damage. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P220 Keep/Store away from clothing/.../combustible materials. P221 Take any precaution to avoid mixing with combustibles... P234 Keep only in original container. P260 Do not breathe dust/fume/gas/mist/vapours/spray. P264 Wash ... thoroughly after handling. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P310 Immediately call a POISON CENTER or doctor/physician. P363 Wash contaminated clothing before reuse. P390 Absorb spillage to prevent material damage. Storage P404 Store in a closed container. P406 Store in corrosive resistant/... container with a resistant inner liner. Disposal P501 Dispose of contents/container to ...
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 180
# NITRIC ACID (all concentrations up 70% acid)
UN Number: 2031 Also known as: ACIDE NITRIQUE (contenant plus de 70% d'acide nitrique), AQUAFORTIS, AZOTIC ACID
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2031
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1490 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 63 Density of gas (kg/m3) 2.838 Boiling Point (°C) 121 Melting Point (°C) -42 Vapour Pressure (Pa) 6400 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless to light brown Odour choking odour
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name nitric acid
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 4 - High Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 100 ERPG-3 (ppm) 78
### Ecotoxicity
# NITRILOTRIACETIC ACID AND SALTS
CAS Number: 5094-31-3 Also known as: ACIDE NITRILOTRIACETIQUE ET SELS
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 5094-31-3
### Physical chemical data
Physical State (20°C) Solid Molar mass (g/mol) 191
### Behaviour at sea
### Additional data
Colour white Odour odourless
### Transportation data
State solid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 100 TEEL-2 (mg/m3) 500 TEEL-3 (mg/m3) 500
### Ecotoxicity
# NITROBENZENE
UN Number: 1662 - CAS Number: 98-95-3 Also known as: Nitrobenzol, Oil Of Mirbane, Nitrobenzene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1662 CAS number 98-95-3 Formula C 6 H 5 NO 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1204 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 1.6865 [cSt] at a temperature of 20°C 1.5477 [cSt] at a temperature of 25°C Molar mass (g/mol) 123.11 Density of gas (kg/m3) 7.74 Solubility (g/L) 2090 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 211.1 Melting Point (°C) 5.7 Critical temperature (°C) 720 Critical pressure (Pa) 405300 Surface tension (mN/m) 46.34 [mN/m] at a temperature of 20°C Vapour Pressure (Pa) 27 [Pa] at a temperature of 20°C 32.7 [Pa] at a temperature of 25°C Ignition Temperature (°C) 480 Flash Point (°C) 88 Flash Point (Pensky- Martens closed cup) (°C) 88 Lower explosivity limit (LEL) (volume %) 1.8 Upper explosivity limit (UEL) (volume %) 40 Vapor enthalpy (J/Kg) 352700 [J/Kg] at a temperature of 210.8°C 446755 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 24250000 Specific heat capacity (J/(Kg·K)) 1509 Henry's constant (mol/(m³·Pa)) 2.43
### Behaviour at sea
Persistence (days) 2.7 Log kow 1.85 Log koc 2.35 Aqueous photolysis (Half-life) 133 Bioconcentration factor (BCF) 24
### Additional data
Colour light yellow to brown Odour almond, shoe polish odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification SD
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 43 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name miscell. water solut. IMO class 6.1
### Reactivity data
Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 200 Hazard statements Health H301 Toxic if swallowed. H311 Toxic in contact with skin. H331 Toxic if inhaled. H351 Suspected of causing cancer. H361 Suspected of damaging fertility or the unborn child. H372 Causes damage to organs through prolonged or repeated exposure, exposure cause the hazard: Environmental H411 Toxic to aquatic life with long lasting effects. Precautionary statements Prevention P260 Do not breathe dust/fume/gas/mist/vapours/spray. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P308 + P313 IF exposed or concerned: Get medical advice/attention. Disposal P501 Dispose of contents/container to ... TEEL-1 (mg/m3) 3 ppm TEEL-2 (mg/m3) 19.9 ppm TEEL-3 (mg/m3) 200 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 6.68 Lowest median lethal concentration (LC50) on fishes (mg/l) 24.25 Highest no observed effect concentration (NOEC) on algae (mg/l) 3.2 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 2.6
# NITROETHANE
UN Number: 2842 - CAS Number: 79-24-3
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2842 CAS number 79-24-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1100 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 75.07 Density of gas (kg/m3) 3.35 Boiling Point (°C) 114 Melting Point (°C) -90 Vapour Pressure (Pa) 2100 [Pa] at a temperature of 20°C Ignition Temperature (°C) 360 Flash Point (°C) 28 Lower explosivity limit (LEL) (volume %) 3.4 Upper explosivity limit (UEL) (volume %) 40
### Behaviour at sea
### Additional data
Colour colourless Odour mild fruity Standard behavior classification S/SD
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 42 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name nitro compounds IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 1000 TLV-TWA 100 TEEL-1 (mg/m3) 100 ppm TEEL-2 (mg/m3) 200 ppm TEEL-3 (mg/m3) 1000 ppm
### Ecotoxicity
# NITROGEN (compressed gas)
UN Number: 1066 Also known as: AZOTE (gaz comprimé)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1066
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 1.161 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 28 Density of gas (kg/m3) 1.161 Boiling Point (°C) -195.4 Melting Point (°C) -210 Vapour Pressure (Pa) 25000000 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Transport mode Gas,Packaged Ship type 3G State liq.compr.gas Temperature (°C) -196� Pressure (Pa) ambient IMO class 2(2.2)
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 65000 ppm TEEL-2 (mg/m3) 230000 ppm TEEL-3 (mg/m3) 400000 ppm
### Ecotoxicity
# NITROGEN (refrigerated liquid)
UN Number: 1977 Also known as: AZOTE (liquide réfrigéré)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1977
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 1.161 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 28 Density of gas (kg/m3) 1.161 Boiling Point (°C) -195.4 Melting Point (°C) -210 Vapour Pressure (Pa) 25000000 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Transport mode Gas,Packaged Ship type 3G State liquefied gas Temperature (°C) < -196� Pressure (Pa) ambient IMO class 2(2.2)
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 65000 ppm TEEL-2 (mg/m3) 230000 ppm TEEL-3 (mg/m3) 400000 ppm
### Ecotoxicity
# NITROMETHANE
UN Number: 1261
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1261
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1139 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 61.04 Density of gas (kg/m3) 2.709 Boiling Point (°C) 101.4 Melting Point (°C) -29 Vapour Pressure (Pa) 3600 [Pa] at a temperature of 20°C Ignition Temperature (°C) 415 Flash Point (°C) 36 Lower explosivity limit (LEL) (volume %) 7.3
### Behaviour at sea
### Additional data
Colour colourless Odour strong odour
### Transportation data
Package group II Cargo group 43 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name miscell. water solut. IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 1000 TLV-TWA 100 TEEL-1 (mg/m3) 60 ppm TEEL-2 (mg/m3) 750 ppm TEEL-3 (mg/m3) 750 ppm
### Ecotoxicity
# NITROPHENOL
UN Number: 1663
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1663
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1280 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 139.1 Boiling Point (°C) 214 Melting Point (°C) 45 Ignition Temperature (°C) 550 Flash Point (°C) 108
### Behaviour at sea
### Additional data
Colour yellow Odour peculiar, aromatic odour Standard behavior classification SD
### Transportation data
Package group III State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 2.5 TEEL-2 (mg/m3) 15 TEEL-3 (mg/m3) 75
### Ecotoxicity
# NITROTOLUENES mix
UN Number: 1664
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1664
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1100/1200 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 137.13 Density of gas (kg/m3) 6.06 Boiling Point (°C) 220/238 Melting Point (°C) -0.192307692 Vapour Pressure (Pa) 34 [Pa] at a temperature of 20°C Flash Point (°C) 95/100
### Behaviour at sea
### Additional data
Colour yellow Odour characteristic
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 42 State liquid/solid Temperature (°C) ambient Family name nitro compounds IMO class 6.1
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Reducing agents Yes Combustibles Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 200
### Ecotoxicity
# NONANE
UN Number: 1920 - CAS Number: 111-84-2
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1920 CAS number 111-84-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 718 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 128.3 Density of gas (kg/m3) 5.69 Boiling Point (°C) 150.7 Melting Point (°C) -54 Vapour Pressure (Pa) 430 [Pa] at a temperature of 20°C Ignition Temperature (°C) 205 Flash Point (°C) 30 Lower explosivity limit (LEL) (volume %) 0.87 Upper explosivity limit (UEL) (volume %) 2.9
### Behaviour at sea
### Additional data
Colour colourless Odour gasoline odour Standard behavior classification FE
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 31 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name paraffins IMO class 3.3
### Reactivity data
Water No Static electricity Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Specific Health Concern (D3) A - Aspiration Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TLV-TWA 200 TEEL-1 (mg/m3) 600 ppm TEEL-2 (mg/m3) 1000 ppm TEEL-3 (mg/m3) 1250 ppm
### Ecotoxicity
# NONANOIC ACID
CAS Number: 112-05-0 Also known as: ACIDE NONANOIQUE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 112-05-0
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 900 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 158.2 Boiling Point (°C) 255 Melting Point (°C) 12 Vapour Pressure (Pa) < 10 [Pa] at a temperature of 20°C Ignition Temperature (°C) 405 Flash Point (°C) 114
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification FD
### Transportation data
Family name organic acids
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# NONENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 739 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 126.2 Density of gas (kg/m3) 5.676 Boiling Point (°C) 135 Melting Point (°C) -81 Vapour Pressure (Pa) 543 [Pa] at a temperature of 20°C Flash Point (°C) 83 Lower explosivity limit (LEL) (volume %) 0.7 Upper explosivity limit (UEL) (volume %) 3.9
### Behaviour at sea
### Additional data
Colour colourless Odour gasoline odour Standard behavior classification FE
### Transportation data
Cargo group 30 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name olefins
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# NONYL PHENOL POLY(4-12)ETHOXYLATES
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid/Solid Density (kg/m3) 1070 [Kg/m³] at a temperature of 20°C Melting Point (°C) -0.714285714 Flash Point (°C) > 205
### Behaviour at sea
### Additional data
Colour colourless Odour mild Standard behavior classification D/DE
### Transportation data
### Reactivity data
Metal(s) and alloys Yes (Al, Cu, Zn, Brass)
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# NONYLPHENOL
UN Number: 3082 - CAS Number: 25154-52-3 Also known as: 2,6-DIMETHYL-4-HEPTYL PHENOL, Monononylphenol, Phenol, Nonyl, Nonylphenol, N-Nonylphenol (Mixed Isomers), Nonylphenols
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082 CAS number 25154-52-3 Formula C 1 5 H 2 4 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 949.4 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 2630 [cSt] at a temperature of 20°C Molar mass (g/mol) 220.36 Density of gas (kg/m3) 9.804 Solubility (g/L) 6 [g/L] at a temperature of 20°C and salinity of 0‰ 4 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 304 Melting Point (°C) 140 Interfacial tension (mN/m) 30 [mN/m] at a temperature of 20°C and salinity of 0‰ Vapour Pressure (Pa) 50 [Pa] at a temperature of 20°C 0.3 [Pa] at a temperature of 25°C Ignition Temperature (°C) 370 Flash Point (°C) 140 Flash Point (Pensky-Martens closed cup) (°C) 141 Flash Point (Cleveland open cup) (°C) 141 Combus enthalpy (J/Kg) 38200000 Combustion efficiency (%) 70 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.036 Rad fraction (%) 30 Henry's constant (mol/(m³·Pa)) 11.02
### Behaviour at sea
Log kow 4.48 Log koc 3.7 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 150 Bioconcentration factor (BCF) 1280
### Additional data
Colour light yellow, straw colour Odour medicine odour MARPOL pollution category Category Description X Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a major hazard to either marine resources or human health and, therefore, justify the prohibition of the discharge into the marine environment.
### Transportation data
Package group II Cargo group 40 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name glycol ethers
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 5 - Very highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 3 - High Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 20 TEEL-2 (mg/m3) 125 TEEL-3 (mg/m3) 500
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 0.027 Lowest median lethal concentration (LC50) on crustacean (mg/l) 0.021 Lowest median lethal concentration (LC50) on fishes (mg/l) 0.017 Highest no observed effect concentration (NOEC) on algae (mg/l) 0.0251 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.0039 Highest no observed effect concentration (NOEC) on fishes (mg/l) 0.006 Assessment factor (AF) 10 on the Short term 10 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 1.7 [µg/l] on the Short term 0.39 [µg/l] on the Long term
# Nonylphenol Poly (4+)Ethoxylate
CAS Number: 9016-45-9 Also known as: Nonylphenoxypoly(Ethyleneoxy)Ethanol, Alpha-(Nonylphenyl)-Omega-Hydroxypoly(Oxy-1,2-Ethanediyl, Nonylphenol Poly (4+)Ethoxylate, Poly (4+) Ethoxylate De Nonylphenol
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 9016-45-9 Formula C 9 H 1 9 -C 6 H 4 O(CH 2 CH 2 O)nH
### Physical chemical data
Physical State (25°C) Liquid
### Behaviour at sea
Bioconcentration factor (BCF) 10
### Additional data
MARPOL pollution category Category Description Other Substances Substances which have been evaluated and found to fall outside Category X, Y or Z because they are considered to present no harm to marine resources, human health, amenities or other legitimate uses of the sea when discharged into the sea from tank cleaning of deballasting operations. The discharge of bilge or ballast water or other residues or mixtures containing these substances are not subject to any requirements of MARPOL Annex II.
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Interference with coastal amenities (E2) G - Gas
### Human toxicity threshold
Hazard statements Health H315 Causes skin irritation. H319 Causes serious eye irritation. Environmental H411 Toxic to aquatic life with long lasting effects. Precautionary statements Prevention P264 Wash ... thoroughly after handling. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P302 + P352 IF ON SKIN: Wash with plenty of soap and water. P321 Specific treatment (see ... on this label). P332 + P313 If skin irritation occurs: Get medical advice/attention. P337 + P313 If eye irritation persists: Get medical advice/attention. P362 Take off contaminated clothing and wash before reuse. P391 Collect spillage.
### Ecotoxicity
# o-CHLORONITROBENZENE
UN Number: 1578 - CAS Number: 25167-93-5 Also known as: 1-CHLORO-2-NITROBENZENE, 2-CHLORONITROBENZENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1578 CAS number 25167-93-5
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1400 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 157.56 Density of gas (kg/m3) 6.97 Boiling Point (°C) 246 Melting Point (°C) 32.5 Vapour Pressure (Pa) 600 [Pa] at a temperature of 20°C Flash Point (°C) 124
### Behaviour at sea
### Additional data
Colour yellow-green Odour aromatic
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 42 State solid Temperature (°C) cool Family name nitrocompounds IMO class 6.1
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Reducing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# o-CHLOROTOLUENE
UN Number: 2338 - CAS Number: 95-49-8 Also known as: 2-CHLORO-1-METHYLBENZENE, 2-CHLOROTOLUENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2338 CAS number 95-49-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1080 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 126.59 Boiling Point (°C) 157/159 Melting Point (°C) 1.058823529 Vapour Pressure (Pa) 359 [Pa] at a temperature of 20°C Flash Point (°C) 46/47
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 36 State liquid Family name halogenated hydrocarbons IMO class 3.3
### Reactivity data
Water No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 3 - ≥100 and <500 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
### Ecotoxicity
# o-ETHYLPHENOL
CAS Number: 90-00-6
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 90-00-6
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1037 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 122.17 Density of gas (kg/m3) 5.43 Boiling Point (°C) 195/197 Melting Point (°C) -18 Vapour Pressure (Pa) < 130 [Pa] at a temperature of 20°C Flash Point (°C) 78
### Behaviour at sea
### Additional data
Colour yellow Odour odourless
### Transportation data
Cargo group 21 State liquid Temperature (°C) ambient Family name phenols, cresols
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly
### Human toxicity threshold
### Ecotoxicity
# OCTANE
UN Number: 1262 - CAS Number: 111-65-9 Also known as: N-Octane, Octane
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1262 CAS number 111-65-9 Formula C 8 H 1 8
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 703 [Kg/m³] at a temperature of 20°C 698.6 [Kg/m³] at a temperature of 25°C Molar mass (g/mol) 114.2 Density of gas (kg/m3) 5.792 Solubility (g/L) 0.66 [g/L] at a temperature of 20°C and salinity of 0‰ 0.66 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 125.9 Melting Point (°C) -16 Critical molar volume (m³/mol) 0.000492 Critical temperature (°C) 568.7 Critical pressure (Pa) 2490000 Surface tension (mN/m) 21.62 [mN/m] at a temperature of 20°C 21.14 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 1306 [Pa] at a temperature of 20°C Ignition Temperature (°C) 210 Flash Point (°C) 81 Flash Point (Pensky-Martens closed cup) (°C) 13 Flash Point (Cleveland open cup) (°C) 22 Lower explosivity limit (LEL) (volume %) 1 Upper explosivity limit (UEL) (volume %) 6.5 Vapor enthalpy (J/Kg) 301237 [J/Kg] at a temperature of 126°C 363310 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 47715549 Specific heat capacity (J/(Kg·K)) 2229 Henry's constant (mol/(m³·Pa)) 324240
### Behaviour at sea
Log kow 5.18 Log koc 2.64 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 1200
### Additional data
Colour colourless Odour gasoline odour MARPOL pollution category Category Description X Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a major hazard to either marine resources or human health and, therefore, justify the prohibition of the discharge into the marine environment. Standard behavior classification FE
### Transportation data
Package group II Cargo group 31 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name paraffins IMO class 3.2
### Reactivity data
Water No Static electricity Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 0 - Not irritating Specific Health Concern (D3) A - Aspiration Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 5000 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H304 May be fatal if swallowed and enters airways. H315 Causes skin irritation. H336 May cause drowsiness or dizziness. Environmental H410 Very toxic to aquatic life with long lasting effects. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P241 Use explosion- proof electrical/ventilating/lighting/.../equipment. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. Storage P405 Store locked up. Disposal P501 Dispose of contents/container to ... TLV-TWA 300 TEEL-1 (mg/m3) 300 ppm TEEL-2 (mg/m3) 385 ppm TEEL-3 (mg/m3) 1000 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 0.38 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.17 Assessment factor (AF) 1 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 10 [µg/l] on the Short term
# OCTANOIC ACID
CAS Number: 134-07-2 Also known as: C-8 ACID, ACIDE OCTANOIQUE, n-CAPRYLIC ACID
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 134-07-2
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 910 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 144.21 Density of gas (kg/m3) 6.45 Boiling Point (°C) 237 Melting Point (°C) 16 Flash Point (°C) 110
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Temperature (°C) ambient Family name organic acids
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# OCTANOL
UN Number: 3082 - CAS Number: 111-87-5 Also known as: ALCOHOL C-8, ALFOL 8, CAPRYL ALCOHOL, n-CAPRYLIC ALCOHOL, DYTOL M-83
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082 CAS number 111-87-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 829 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 130.23 Density of gas (kg/m3) 5.805 Boiling Point (°C) 195 Melting Point (°C) -16 Vapour Pressure (Pa) 20260 [Pa] at a temperature of 20°C Ignition Temperature (°C) 270 Flash Point (°C) 81 Lower explosivity limit (LEL) (volume %) 1.1 Upper explosivity limit (UEL) (volume %) 7.4
### Behaviour at sea
### Additional data
Colour colourless Odour sweet odour
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# OCTYL ACETATE
Also known as: ACETATE D'OCTYLE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Density (kg/m3) 868 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 172.26 Boiling Point (°C) 211 Flash Point (°C) 86
### Behaviour at sea
### Additional data
### Transportation data
Cargo group 34
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
### Ecotoxicity
# OCTYL ALDEHYDES
UN Number: 1191 Also known as: ALDEHYDES OCTYLIQUES
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1191
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 825 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 128.22 Boiling Point (°C) 163 Melting Point (°C) -85 Vapour Pressure (Pa) 200000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 180 Flash Point (°C) 52 Lower explosivity limit (LEL) (volume %) 0.85 Upper explosivity limit (UEL) (volume %) 7.2
### Behaviour at sea
### Additional data
Colour colourless Odour strong fruity
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 19 Temperature (°C) ambient Family name aldehydes IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 60 TEEL-2 (mg/m3) 500 TEEL-3 (mg/m3) 500
### Ecotoxicity
# OLEIC ACID
CAS Number: 112-80-1 Also known as: ACIDE OLEIQUE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 112-80-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 890 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 277 Boiling Point (°C) 222 Melting Point (°C) 13.4 Ignition Temperature (°C) 363 Flash Point (°C) 189
### Behaviour at sea
### Additional data
Colour colourless to pale yellow Odour mild odour
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 0.05 TEEL-2 (mg/m3) 0.4 TEEL-3 (mg/m3) 500
### Ecotoxicity
# OLEUM (20-65% free SO3)
UN Number: 1831
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1831
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1920/1990 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 80.1 (pure) Density of gas (kg/m3) 3.48 Boiling Point (°C) 55/139 Vapour Pressure (Pa) 900 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless to brown Odour pungent, sharp, choking
### Transportation data
Transport mode Bulk,Packaged State liquid Temperature (°C) ambient
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes (cast iron) Oxidizing agents Yes Reducing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Skin irritation/corrosivity (D1) 3C - Corrosive
### Human toxicity threshold
IDHL 15 mg/m3 TLV-TWA 1 mg/m3 ERPG-2 (ppm) 10 ERPG-3 (ppm) 30
### Ecotoxicity
# OXALIC ACID
Also known as: ACIDE OXALIQUE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1700 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 126.07 Density of gas (kg/m3) 5.676 Boiling Point (°C) 157 Melting Point (°C) 102
### Behaviour at sea
### Additional data
Colour white Odour odourless
### Transportation data
State solid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 90 TLV-TWA 0.2 TEEL-2 (mg/m3) 40 TEEL-3 (mg/m3) 500
### Ecotoxicity
# Palm Oil
CAS Number: 8002-75-3 Also known as: Palm Oil, Huile De Palme
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 8002-75-3
### Physical chemical data
Physical State (25°C) Solid Mixed Yes Solubility (g/L) 0 [g/L] at a temperature of 20°C and salinity of 0‰ 0 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 338 Melting Point (°C) 27 Flash Point (Pensky-Martens closed cup) (°C) 162
### Behaviour at sea
Log kow 22.52 Log koc 10 Biodegradation in estuary environment (Half- life) (days) 552
### Additional data
MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# PARAFFIN WAX
CAS Number: 8002-74-2 Also known as: CIRE DE PARAFFINE, CIRES DE PARAFFINES
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 8002-74-2
### Physical chemical data
Physical State (20°C) Liquid/Solid Density (kg/m3) 850/900 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 410 Density of gas (kg/m3) 51.85 Boiling Point (°C) 370 Melting Point (°C) 15/90 Vapour Pressure (Pa) < 100 [Pa] at a temperature of 20°C Ignition Temperature (°C) > 245 Flash Point (°C) 110
### Behaviour at sea
### Additional data
Colour white to yellow Odour waxy
### Transportation data
Package group III Cargo group 31 State liquid/solid Temperature (°C) ambient Family name paraffins IMO class 3.3
### Reactivity data
Water No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# PARALDEHYDE
UN Number: 1264 - CAS Number: 123-63-7 Also known as: p-ACETALDEHYDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1264 CAS number 123-63-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 990 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 132.16 Density of gas (kg/m3) 5.93 Boiling Point (°C) 124 Melting Point (°C) 12 Vapour Pressure (Pa) 3330 [Pa] at a temperature of 20°C Ignition Temperature (°C) 235 Flash Point (°C) 17 Lower explosivity limit (LEL) (volume %) 1.3
### Behaviour at sea
### Additional data
Colour colourless Odour aromatic
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 19 State liquid Temperature (°C) ambient Family name aldehydes IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 30 TEEL-2 (mg/m3) 50 TEEL-3 (mg/m3) 500
### Ecotoxicity
# PARATHION liquid
UN Number: 3018 Also known as: APHAMITE, BLADAN, COROTHION, DANATHION, DNTP
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3018
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1269 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 291.3 Boiling Point (°C) 375 Flash Point (°C) 120
### Behaviour at sea
Persistence (days) 3.1
### Additional data
Colour light to dark brown Odour characteristic odour Marine pollutant P
### Transportation data
Transport mode Bulk,Packaged State liquid Temperature (°C) ambient Pressure (Pa) under pressure IMO class 6.1
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 1.5 TLV-TWA 0.008 TEEL-1 (mg/m3) 0.15 TEEL-3 (mg/m3) 10
### Ecotoxicity
# PENTACHLOROETHANE
UN Number: 1669 - CAS Number: 76-01-7
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1669 CAS number 76-01-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1673 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 202.3 Density of gas (kg/m3) 9.03 Boiling Point (°C) 160.5 Melting Point (°C) -22 Vapour Pressure (Pa) 453 (25C) [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless Odour sweet, chloroform-like
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 36 State liquid Family name halogenated hydrocarbons IMO class 6.1
### Reactivity data
Water No Base(s) Yes Metal(s) and alloys Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 30 TEEL-2 (mg/m3) 500 TEEL-3 (mg/m3) 500
### Ecotoxicity
# PENTACHLOROPHENOL
UN Number: 3155
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3155
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1980 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 266.35 Boiling Point (°C) 310 Melting Point (°C) 188 Vapour Pressure (Pa) 20 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour white to light brown Odour odourless Marine pollutant P
### Transportation data
Package group II State solid Temperature (°C) ambient IMO class 6.1
### Reactivity data
Water No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 0.225 TLV-TWA 0.045 TEEL-1 (mg/m3) 2.5 TEEL-2 (mg/m3) 2.5 TEEL-3 (mg/m3) 2.5
### Ecotoxicity
# PENTAETHYLENEHEXAMINE
CAS Number: 4067-16-7
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 4067-16-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1000 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 232.38 Boiling Point (°C) 350/390 Ignition Temperature (°C) 360 Flash Point (°C) 175/207
### Behaviour at sea
### Additional data
Colour yellowish Odour ammonia-like Standard behavior classification D/DE
### Transportation data
Temperature (°C) ambient Family name aliphatic amines
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# PENTANOIC ACID
CAS Number: 109-52-4 Also known as: ACIDE PENTANOIQUE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 109-52-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 939 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 102.13 Boiling Point (°C) 185 Melting Point (°C) -18 Vapour Pressure (Pa) 21 [Pa] at a temperature of 20°C Ignition Temperature (°C) 400 Flash Point (°C) 96 Lower explosivity limit (LEL) (volume %) 1.6 Upper explosivity limit (UEL) (volume %) 7.6
### Behaviour at sea
### Additional data
Colour colourless Odour unpleasant
### Transportation data
State liquid Temperature (°C) ambient Family name organic acids
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# PERCHLOROETHYLENE
UN Number: 1897 - CAS Number: 127-18-4 Also known as: Ethylene Tetrachloride, Pce, Perc, Perchlor, Perchlorethylene, Perchloroethylene, Perk, Tetrachloroethene, Tetrachlorethylene, 1,1,2,2-Tetrachloroethylene, Tetrachloroethylene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1897 CAS number 127-18-4 Formula C 2 Cl 4
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1620 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.54 [cSt] at a temperature of 20°C 0.52 [cSt] at a temperature of 25°C Molar mass (g/mol) 165.83 Density of gas (kg/m3) 7.4 Solubility (g/L) 149 [g/L] at a temperature of 20°C and salinity of 0‰ 209 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 121 Melting Point (°C) -23 Surface tension (mN/m) 32.1 [mN/m] at a temperature of 20°C Interfacial tension (mN/m) 44.4 [mN/m] at a temperature of 25°C and salinity of 0‰ Vapour Pressure (Pa) 1900 [Pa] at a temperature of 20°C 2481 [Pa] at a temperature of 25°C Vapor enthalpy (J/Kg) 209105 [J/Kg] at a temperature of 121.2°C 23952 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 4440000 Specific heat capacity (J/(Kg·K)) 864.64 Combustion efficiency (%) 50 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.03 Rad fraction (%) 40 Henry's constant (mol/(m³·Pa)) 2114
### Behaviour at sea
Log kow 2.53 Log koc 1.98 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) 270 Biodegradation in marine environment (Half-life) (days) Not biodegradable Bioconcentration factor (BCF) 103
### Additional data
Colour colourless Odour sweet MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 36 State liquid Family name halogenated hydrocarbons IMO class 6.1
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 150 Hazard statements Health H335 May cause respiratory irritation. Environmental H411 Toxic to aquatic life with long lasting effects. Precautionary statements Prevention P202 Do not handle until all safety precautions have been read and understood. P273 Avoid release to the environment. P281 Use personal protective equipment as required. Response P308 + P313 IF exposed or concerned: Get medical advice/attention. P391 Collect spillage. Storage P405 Store locked up. Disposal P501 Dispose of contents/container to ... TLV-TWA 50 ERPG-1 (ppm) 100 ERPG-2 (ppm) 200 ERPG-3 (ppm) 1000
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 3.64 Lowest median lethal concentration (LC50) on crustacean (mg/l) 8.5 Lowest median lethal concentration (LC50) on fishes (mg/l) 5 Highest no observed effect concentration (NOEC) on algae (mg/l) 1.77 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.51 Highest no observed effect concentration (NOEC) on fishes (mg/l) 1.99 Assessment factor (AF) 100 on the Short term 100 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 36.4 [µg/l] on the Short term 5.1 [µg/l] on the Long term
# PERMETHRIN
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1920 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 391.28 Boiling Point (°C) 200 (1.33 Pa) Melting Point (°C) 34/35 Vapour Pressure (Pa) 0.000045 [Pa] at a temperature of 20°C Flash Point (°C) > 100
### Behaviour at sea
### Additional data
Colour pale brown
### Transportation data
### Reactivity data
Water No
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# PETROLATUM
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 900 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 302 Melting Point (°C) 36-60 Vapour Pressure (Pa) <1.3 [Pa] at a temperature of 20°C Ignition Temperature (°C) >290 Flash Point (°C) 182/221 Lower explosivity limit (LEL) (volume %) 0.9
### Behaviour at sea
### Additional data
Colour green, dark brown Odour odourless Standard behavior classification F/FE/E
### Transportation data
Cargo group 33 State solid Family name miscell. hydroc. mixt
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 50 TEEL-2 (mg/m3) 350 TEEL-3 (mg/m3) 500
### Ecotoxicity
# PETROLEUM DISTILLATES (flashed feed stocks)
UN Number: 1268
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1268
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 760 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 75 Vapour Pressure (Pa) 400 [Pa] at a temperature of 20°C Flash Point (°C) -18
### Behaviour at sea
### Additional data
Colour colourless Odour gasoline odour
### Transportation data
Transport mode Bulk,Packaged Cargo group 33 State liquid Temperature (°C) ambient Family name miscell. hydroc. mixt IMO class 3.1/3.2/3.
### Reactivity data
Acid(s) Yes Static electricity Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 10000 TLV-TWA 400
### Ecotoxicity
# PETROLEUM OIL
UN Number: 1270
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1270
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 841 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 288 Vapour Pressure (Pa) 400 [Pa] at a temperature of 20°C Flash Point (°C) -18 Lower explosivity limit (LEL) (volume %) 1.3
### Behaviour at sea
### Additional data
Colour yellow-brown Odour gasoline odour Standard behavior classification E, FE, F
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 33 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name miscell. hydroc. mixt IMO class 3.1/3.2/3.
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# PHENOL
UN Number: 1671 - CAS Number: 108-95-2 Also known as: ACID CARBOLIC, BAKER P & S LIQUID OINTMENT, BENZENOL, CARBOLIC ACID, CARBOLSÄURE, Hydroxybenzene, Monohydroxybenzene, Oxybenzene, Phenic Acid, Phenyl Alcohol, Phenylic Acid, Phenylic Alcohol, Phenyl Hydrate, Phenyl Hydroxide, Acide Carbolique, Phenol
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1671 CAS number 108-95-2 Formula C 6 H 6 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Solid Density (kg/m3) 1058 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 3.26 [cSt] at a temperature of 20°C Molar mass (g/mol) 94.11 Density of gas (kg/m3) 4.18 Solubility (g/L) 84000 [g/L] at a temperature of 20°C and salinity of 0‰ 86600 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 182 Melting Point (°C) 41 Vapour Pressure (Pa) 35455 [Pa] at a temperature of 20°C 46.6 [Pa] at a temperature of 25°C Ignition Temperature (°C) 605 Flash Point (°C) 79 Flash Point (Pensky-Martens closed cup) (°C) 79 Flash Point (Cleveland open cup) (°C) 85 Lower explosivity limit (LEL) (volume %) 1.7 Upper explosivity limit (UEL) (volume %) 8.6 Vapor enthalpy (J/Kg) 485496 [J/Kg] at a temperature of 181.8°C 614387 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 31000000 Specific heat capacity (J/(Kg·K)) 2123 Combustion efficiency (%) 89 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.04 Rad fraction (%) 33 Henry's constant (mol/(m³·Pa)) 0.02
### Behaviour at sea
Log kow 1.47 Log koc 1.59 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 50 Bioconcentration factor (BCF) 17.5
### Additional data
Colour white, light pink Odour sweet, tar odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification DE
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 21 State solid Temperature (°C) ambient Pressure (Pa) under pressure Family name phenols, cresols IMO class 6.1
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 250 Hazard statements Health H301 Toxic if swallowed. H311 Toxic in contact with skin. H314 Causes severe skin burns and eye damage. H331 Toxic if inhaled. H341 Suspected of causing genetic defects. H373 May cause damage to organs through prolonged or repeated exposure, exposure cause the hazard: Precautionary statements Prevention P201 Obtain special instructions before use. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P308 + P313 IF exposed or concerned: Get medical advice/attention. P331 Do NOT induce vomiting. ERPG-1 (ppm) 10 ERPG-2 (ppm) 50 ERPG-3 (ppm) 200
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 49.6 Lowest median lethal concentration (LC50) on crustacean (mg/l) 3.1 Lowest median lethal concentration (LC50) on fishes (mg/l) 5 Highest no observed effect concentration (NOEC) on algae (mg/l) 13 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.46 Highest no observed effect concentration (NOEC) on fishes (mg/l) 0.077 Assessment factor (AF) 100 on the Short term 100 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 31 [µg/l] on the Short term 0.77 [µg/l] on the Long term
# PHENOL molten
UN Number: 2312 - CAS Number: 108-95-2 Also known as: CARBOLIC ACID
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2312 CAS number 108-95-2
### Physical chemical data
Physical State (20°C) Liquid/Solid Density (kg/m3) 1070 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 94.11 Density of gas (kg/m3) 4.21 Boiling Point (°C) 182 Melting Point (°C) 15/41 Vapour Pressure (Pa) 100 [Pa] at a temperature of 20°C Ignition Temperature (°C) 605 Flash Point (°C) 79 Lower explosivity limit (LEL) (volume %) 1.4 Upper explosivity limit (UEL) (volume %) 8.6
### Behaviour at sea
### Additional data
Colour white to pink Odour sweet, tarry
### Transportation data
Package group II Cargo group 21 Family name phenols, cresols IMO class 6.1
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Combustibles Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 250 ERPG-1 (ppm) 10 ERPG-2 (ppm) 50 ERPG-3 (ppm) 200
### Ecotoxicity
# PHOSGENE
UN Number: 1076 Also known as: CARBONIC CHLORIDE, CARBON OXYCHLORIDE, CARBONYL CHLORIDE, CHLOROFORMYL CHLORIDE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1076
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 4.4 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 98.9 Melting Point (°C) -13 Vapour Pressure (Pa) 160000 [Pa] at a temperature of 20°C Flash Point (°C) 999
### Behaviour at sea
### Additional data
### Transportation data
IMO class 2(2.3)
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.1 ERPG-2 (ppm) 0.2 10 min 30 min 60 min 4 hrs 8 hrs AEGL-2 (ppm) 0.6 0.6 0.3 0.08 0.04 AEGL-3 (ppm) 3.6 1.5 0.75 0.2 0.09
### Ecotoxicity
# PHOSPHINE
UN Number: 2199
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2199
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 1.5 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 34 Boiling Point (°C) -87.7 Melting Point (°C) -133 Vapour Pressure (Pa) 4200000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 38 Flash Point (°C) 999 Lower explosivity limit (LEL) (volume %) 1.8
### Behaviour at sea
### Additional data
### Transportation data
IMO class 2(2.3)
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 200 TLV-TWA 0.3 ERPG-2 (ppm) 0.5 10 min 30 min 60 min 4 hrs 8 hrs AEGL-2 (ppm) 0.5 0.25 AEGL-3 (ppm) 7.2 7.2 3.6 0.9 0.45
### Ecotoxicity
# PHOSPHORIC ACID liquid
UN Number: 1805 - CAS Number: 7664-38-2 Also known as: ACIDE PHOSPHORIQUE liquide, Orthophosphoric Acid, O-Phosphoric Acid, White Phosphoric Acid, Phosphoric Acid, Hydrogen Phosphate, Acide Phosphorique
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1805 CAS number 7664-38-2 Formula H 3 PO 4
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1892 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 140 [cSt] at a temperature of 20°C 100 [cSt] at a temperature of 25°C Molar mass (g/mol) 98 Solubility (g/L) 1863000 [g/L] at a temperature of 20°C and salinity of 0‰ 1863000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 130 Melting Point (°C) 42 Specific heat capacity (J/(Kg·K)) 1480 Henry's constant (mol/(m³·Pa)) 0
### Behaviour at sea
Log kow 0.21 Log koc 1.21 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) 1 Biodegradation in marine environment (Half-life) (days) Not biodegradable
### Additional data
Colour colourless Odour odourless MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name non-oxid. min. acids
### Reactivity data
Water Yes Abilities Miscible in water. Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes Notable risks Reacts to heat Reacts with other compouds.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 2500 Hazard statements Health H314 Causes severe skin burns and eye damage. Precautionary statements Prevention P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. TLV-TWA 0.25 TEEL-2 (mg/m3) 500 TEEL-3 (mg/m3) 500
### Ecotoxicity
Highest no observed effect concentration (NOEC) on algae (mg/l) 100 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 56
# PHOSPHORUS (white, molten)
UN Number: 2447 - CAS Number: 7732-14-0
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2447 CAS number 7732-14-0
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1800 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 123.89 Density of gas (kg/m3) 5.676 Boiling Point (°C) 279.9 Melting Point (°C) 44 Vapour Pressure (Pa) 130 [Pa] at a temperature of 20°C Ignition Temperature (°C) 30 Flash Point (°C) 30
### Behaviour at sea
### Additional data
Colour light yellow Odour garlic odour Marine pollutant P
### Transportation data
Transport mode Bulk,Packaged State liquid, wax Temperature (°C) elevated Pressure (Pa) under pressure IMO class 4.2
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 3 - ≥100 and <500 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 6 - Extremely toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 4 - Very high Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TLV-TWA 0.02 TEEL-1 (mg/m3) 0.125 TEEL-2 (mg/m3) 0.75
### Ecotoxicity
# PHOSPHORUS OXYCHLORIDE
UN Number: 1810
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1810
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1675 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 153.33 Density of gas (kg/m3) 6.837 Boiling Point (°C) 107 Vapour Pressure (Pa) 3700 [Pa] at a temperature of 20°C Upper explosivity limit (UEL) (volume %) 12.4
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour colourless to light yellow Odour musty odour Standard behavior classification D, SD
### Transportation data
Package group II State liquid Temperature (°C) > 2� Pressure (Pa) under pressure
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.5 TEEL-1 (mg/m3) 0.479 ppm TEEL-2 (mg/m3) 0.479 ppm TEEL-3 (mg/m3) 0.85
### Ecotoxicity
# PHOSPHORUS TRICHLORIDE
UN Number: 1809 Also known as: CHLORIDE OF PHOSPHORUS
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1809
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1575 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 137.33 Density of gas (kg/m3) 6.192 Boiling Point (°C) 76 Melting Point (°C) -91 Vapour Pressure (Pa) 12700 [Pa] at a temperature of 20°C
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour colourless to light yellow Odour sharp, irritating odour Standard behavior classification DE, SD
### Transportation data
Package group II State liquid Temperature (°C) ambient Pressure (Pa) under pressure IMO class 6.1
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 50 TLV-TWA 0.2 ERPG-1 (ppm) 0.5 ERPG-3 (ppm) 15
### Ecotoxicity
# PHTHALIC ANHYDRIDE molten
UN Number: 2214 - CAS Number: 85-44-9 Also known as: ANHYDRIDE PHTALIQUE fondu, 1,2-BENZENE DICARBOXYLIC ACID ANHYDRIDE, 1,3-DIOXOPHTHALAN
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2214 CAS number 85-44-9
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1500 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 148.12 Density of gas (kg/m3) 6.708 Boiling Point (°C) 284.4 Melting Point (°C) 132 Ignition Temperature (°C) 580 Flash Point (°C) 140 Lower explosivity limit (LEL) (volume %) 1.7 Upper explosivity limit (UEL) (volume %) 10.4
### Behaviour at sea
Persistence (days) 1.9
### Additional data
Colour colourless to pale yellow Odour choking odour
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 11 State liquid Temperature (°C) 131� - 160� Pressure (Pa) ambient Family name organic anhydrides
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 1600 TEEL-1 (mg/m3) 12 TEEL-2 (mg/m3) 40 TEEL-3 (mg/m3) 60
### Ecotoxicity
# POLYBUTENE
CAS Number: 9003-29-6
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 9003-29-6
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 960 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 225 Vapour Pressure (Pa) 400 [Pa] at a temperature of 20°C Flash Point (°C) 215
### Behaviour at sea
### Additional data
Standard behavior classification E, FE, F
### Transportation data
Cargo group 30 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name olefins
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# POLYCHLORINATED BIPHENYLS
UN Number: 2315 Also known as: AROCHLOR, BIPHENYLES POLYCHLORES, CHLOPHREN (T), CHLOREXTOL (T), DYKANOL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2315
### Physical chemical data
Physical State (20°C) Solid/Liquid Density (kg/m3) 1300/1800 (liq) [Kg/m³] at a temperature of 20°C Boiling Point (°C) very high Flash Point (°C) > 141
### Behaviour at sea
### Additional data
Colour white (S), yellow (L) Odour weak Marine pollutant P
### Transportation data
Package group II State liquid/solid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water No
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# POLYMETHYLENE POLYPHENYL ISOCYANATE
UN Number: 2206 - CAS Number: 9016-87-9 Also known as: 4,4'-Mdi, 1,1'- Methylenebis(4-Isocyanatobenzene), Methylene Bis (4-Phenyl Isocyanate), Diphenylmethane Diisocyanate, 4,4'- Diisocyanate De Diphenylmethane, Polymethylene Polyphenyl Isocyanate, Polyphenyl Isocyanates De Polymethylene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2206 CAS number 9016-87-9 Formula [C 6 H 3 (NCO)CH 2 ]n
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1200 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 400 Boiling Point (°C) 200 Melting Point (°C) 41 Vapour Pressure (Pa) 10100 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour dark brown Odour weak odour MARPOL pollution category Category Description Other Substances Substances which have been evaluated and found to fall outside Category X, Y or Z because they are considered to present no harm to marine resources, human health, amenities or other legitimate uses of the sea when discharged into the sea from tank cleaning of deballasting operations. The discharge of bilge or ballast water or other residues or mixtures containing these substances are not subject to any requirements of MARPOL Annex II. Standard behavior classification D, DE, SD
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 12 State liquid Temperature (°C) 2� - 52� Pressure (Pa) under pressure Family name isocyanates IMO class 6.1
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non- toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
Hazard statements Health H315 Causes skin irritation. H317 May cause an allergic skin reaction. H319 Causes serious eye irritation. H332 Harmful if inhaled. H334 May cause allergy or asthma symptoms or breathing difficulties if inhaled. H335 May cause respiratory irritation. H351 Suspected of causing cancer. H373 May cause damage to organs through prolonged or repeated exposure, exposure cause the hazard: Precautionary statements Prevention P280 Wear protective gloves/protective clothing/eye protection/face protection. P285 In case of inadequate ventilation wear respiratory protection. Response P302 + P352 IF ON SKIN: Wash with plenty of soap and water. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P309 + P311 IF exposed or if you feel unwell: Call a POISON CENTER or doctor/physician. TEEL-2 (mg/m3) 40 TEEL-3 (mg/m3) 200
### Ecotoxicity
# POLYPROPYLENE GLYCOL
CAS Number: 25322-69-4
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 25322-69-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1012 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 200 Flash Point (°C) 390
### Behaviour at sea
### Additional data
Colour colourless Odour odourless, mild sweet odor
### Transportation data
Cargo group 30 State liquid Temperature (°C) < 60� Pressure (Pa) ambient Family name olefins
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
TEEL-1 (mg/m3) 30 TEEL-2 (mg/m3) 200 TEEL-3 (mg/m3) 500
### Ecotoxicity
# POTASSIUM ARSENATE
UN Number: 1677 Also known as: ARSENIATE DE POTASSIUM
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1677
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2800 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 180 Melting Point (°C) 288
### Behaviour at sea
### Additional data
Colour white Odour odourless Standard behavior classification SD
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.07 (As) TEEL-1 (mg/m3) 0.072 TEEL-2 (mg/m3) 2.5 TEEL-3 (mg/m3) 12
### Ecotoxicity
# POTASSIUM BROMATE
UN Number: 1484 Also known as: BROMATE DE POTASSIUM
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1484
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 3300 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 167 Boiling Point (°C) 370 Melting Point (°C) 350
### Behaviour at sea
### Additional data
Colour white Odour odourless
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 5.1
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents Yes Combustibles Yes Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 0.3 TEEL-2 (mg/m3) 60 TEEL-3 (mg/m3) 60
### Ecotoxicity
# POTASSIUM CHLORIDE
CAS Number: 7447-40-7 Also known as: CHLORURE DE POTASSIUM
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 7447-40-7
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1980 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 74.55 Boiling Point (°C) 1500 Melting Point (°C) 770 Vapour Pressure (Pa) 2000 (sol. [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour white
### Transportation data
Transport mode Bulk (sol.) Ship type 3 (sol.) State solid
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 0 - Is not a floater; and does not pose any known health hazards
### Human toxicity threshold
TEEL-2 (mg/m3) 15 TEEL-3 (mg/m3) 15
### Ecotoxicity
# POTASSIUM CYANIDE
UN Number: 1680 Also known as: CYANURE DE POTASSIUM
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1680
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1500 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 65.12 Boiling Point (°C) 1625 Melting Point (°C) 635
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour white Odour almond odour Standard behavior classification SD
### Transportation data
State solid Temperature (°C) ambient IMO class 6.1
### Reactivity data
Water Yes Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 20 TLV-TWA 4.5 (CN) TEEL-3 (mg/m3) 62.6
### Ecotoxicity
# POTASSIUM HYDROXIDE solution
UN Number: 1813 Also known as: CAUSTIC POTASH
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1813
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2040 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 56.11 Boiling Point (°C) 1320 Melting Point (°C) 410
### Behaviour at sea
### Additional data
Colour colourless, white Odour odourless
### Transportation data
Transport mode Bulk,Packaged Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.8 TEEL-1 (mg/m3) 0.3 TEEL-3 (mg/m3) 125
### Ecotoxicity
# Potassium Hydroxide Solution (50%)
UN Number: 1814 - CAS Number: 1310-58-3 Also known as: Caustic Potash, Potassium Hydrate, Potash, Potassa, Potassium Hydroxide Solution, Potash Lye, Potassium Hydroxide (K(Oh)), Potassium Hydroxide Solid, Caustic Potash Solid, Caustic Potash Solution, Potassium Hydrate Solution, Potassium Hydrate Solid, Potassium Hydroxide, Potassium Hydroxide Solution (50%), Hydroxyde De Potassium (Solution)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1814 CAS number 1310-58-3 Formula KOH(H 2 O)
### Physical chemical data
Physical State (25°C) Liquid Kinematic viscosity (cSt) 5.25 [cSt] at a temperature of 20°C Solubility (g/L) 10000000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 145 Melting Point (°C) -43
### Behaviour at sea
### Additional data
MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
### Reactivity data
Abilities Solution.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
Hazard statements Physical H290 May be corrosive to metals. Health H302 Harmful if swallowed. H314 Causes severe skin burns and eye damage. Precautionary statements Prevention P260 Do not breathe dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P310 Immediately call a POISON CENTER or doctor/physician.
### Ecotoxicity
# POTASSIUM OLEATE
CAS Number: 143-18-0
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 143-18-0
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1000 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 320.57
### Behaviour at sea
### Additional data
Colour clear to hazy amber Odour soap-like
### Transportation data
Cargo group 34 Temperature (°C) ambient Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
### Ecotoxicity
# PROPANE
UN Number: 1978 - CAS Number: 74-98-6 Also known as: Dimethylmethane, Propyl Hydride, Propane
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1978 CAS number 74-98-6 Formula C 3 H 8
### Physical chemical data
Physical State (20°C) Gas Physical State (25°C) Gas Density (kg/m3) 2.012 [Kg/m³] at a temperature of 20°C 493 [Kg/m³] at a temperature of 25°C Molar mass (g/mol) 44.09 Density of gas (kg/m3) 2.012 Solubility (g/L) 70 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) -41.9 Melting Point (°C) -186 Critical temperature (°C) 369.89 Critical pressure (Pa) 4215000 Surface tension (mN/m) 16 [mN/m] at a temperature of -47°C Interfacial tension (mN/m) 50 [mN/m] at a temperature of -50°C and salinity of 0‰ Vapour Pressure (Pa) 861050 [Pa] at a temperature of 20°C 953260 [Pa] at a temperature of 25°C Vapour pressure at 70% of critical temperature (Pa) 299030 Ignition Temperature (°C) 470 Flash Point (°C) -42 Flash Point (Pensky-Martens closed cup) (°C) -104 Lower explosivity limit (LEL) (volume %) 2.2 Upper explosivity limit (UEL) (volume %) 9.5 Vapor enthalpy (J/Kg) 3353741 [J/Kg] at a temperature of 25°C Henry's constant (mol/(m³·Pa)) 71636.775
### Behaviour at sea
Log kow 2.36 Log koc 1.33 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 13
### Additional data
Colour colourless Odour odourless MARPOL pollution category Category Description Other Substances Substances which have been evaluated and found to fall outside Category X, Y or Z because they are considered to present no harm to marine resources, human health, amenities or other legitimate uses of the sea when discharged into the sea from tank cleaning of deballasting operations. The discharge of bilge or ballast water or other residues or mixtures containing these substances are not subject to any requirements of MARPOL Annex II.
### Transportation data
Transport mode Gas,Packaged Ship type 2G,2PG Cargo group 31 State liq.compr.gas Temperature (°C) ambient Pressure (Pa) under pressure Family name paraffins IMO class 2(2.1)
### Reactivity data
Water No Static electricity Yes
### GESAMP Hazard profile
Interference with coastal amenities (E2) G - Gas
### Human toxicity threshold
IDHL 20000 Hazard statements Physical H220 Extremely flammable gas. TLV-TWA 1000 TEEL-1 (mg/m3) 5500 ppm TEEL-2 (mg/m3) 17000 ppm TEEL-3 (mg/m3) 33000 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 69.43 Lowest median lethal concentration (LC50) on fishes (mg/l) 49.9
# PROPANOL
UN Number: 1274 - CAS Number: 71-23-8
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1274 CAS number 71-23-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 803 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 60.1 Density of gas (kg/m3) 3.48 Boiling Point (°C) 97.4 Melting Point (°C) -126 Vapour Pressure (Pa) 1933 [Pa] at a temperature of 20°C Ignition Temperature (°C) 405 Flash Point (°C) 15 Upper explosivity limit (UEL) (volume %) 13.5
### Behaviour at sea
### Additional data
Colour colourless Odour alcohol odour
### Transportation data
Package group II Cargo group 20 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alcohols, glycols IMO class 3.2/3.3
### Reactivity data
Acid(s) Yes Base(s) Yes Static electricity Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Specific Health Concern (D3) R - Reprotoxicity Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 4000 TLV-TWA 200 TEEL-1 (mg/m3) 250 ppm TEEL-2 (mg/m3) 250 ppm TEEL-3 (mg/m3) 800 ppm
### Ecotoxicity
# PROPIONALDEHYDE
UN Number: 1275 Also known as: ALDEHYDE PROPIONIQUE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1275
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 805 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 58.08 Density of gas (kg/m3) 2.59 Boiling Point (°C) 48 Melting Point (°C) -81 Vapour Pressure (Pa) 30000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 207 Flash Point (°C) -20 Lower explosivity limit (LEL) (volume %) 2.9 Upper explosivity limit (UEL) (volume %) 17
### Behaviour at sea
### Additional data
Colour colourless Odour choking, unpleasant odour Standard behavior classification DE
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 19 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aldehydes IMO class 3.1
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 45 ppm TEEL-2 (mg/m3) 260 ppm TEEL-3 (mg/m3) 840 ppm
### Ecotoxicity
# PROPIONIC ACID solution (with >80% acid)
UN Number: 1848 - CAS Number: 598-78-7 Also known as: ACIDE PROPIONIQUE en solution (avec plus de 80% d'acide), Propanoic Acid, Methylacetic Acid, Ethanecarboxylic Acid, Ethylformic Acid, Carboxyethane, Propionic Acid, Acide Propionique
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1848 CAS number 598-78-7 Formula C 3 H 6 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 995 [Kg/m³] at a temperature of 20°C 988.2 [Kg/m³] at a temperature of 25°C Kinematic viscosity (cSt) 1.03 [cSt] at a temperature of 25°C Molar mass (g/mol) 74.08 Density of gas (kg/m3) 3.302 Solubility (g/L) 100000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 141 Melting Point (°C) -22 Critical molar volume (m³/mol) 0.000233 Critical temperature (°C) 598.5 Critical pressure (Pa) 4670000 Surface tension (mN/m) 26.2 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 1291 [Pa] at a temperature of 20°C 470 [Pa] at a temperature of 25°C Ignition Temperature (°C) 485 Flash Point (°C) 50 Flash Point (Pensky-Martens closed cup) (°C) 52 Flash Point (Cleveland open cup) (°C) 57 Lower explosivity limit (LEL) (volume %) 2.9 Upper explosivity limit (UEL) (volume %) 14.8 Vapor enthalpy (J/Kg) 433861 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 20630678 Specific heat capacity (J/(Kg·K)) 2063 Henry's constant (mol/(m³·Pa)) 0.045
### Behaviour at sea
Log kow 0.3 Log koc 0.16 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 3.2
### Additional data
Colour colourless Odour sharp, rancid odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name organic acids
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
Hazard statements Health H314 Causes severe skin burns and eye damage. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. Storage P403 + P235 Store in a well-ventilated place. Keep cool. TLV-TWA 10 TEEL-1 (mg/m3) 10 ppm TEEL-2 (mg/m3) 15 ppm TEEL-3 (mg/m3) 350 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 50 Lowest median lethal concentration (LC50) on fishes (mg/l) 51 Highest no observed effect concentration (NOEC) on fishes (mg/l) 188 Assessment factor (AF) 10000 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 50 [µg/l] on the Short term
# PROPIONIC ANHYDRIDE
UN Number: 2496 - CAS Number: 123-62-6 Also known as: ANHYDRIDE PROPIONIQUE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2496 CAS number 123-62-6
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1010 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 130.1 Density of gas (kg/m3) 5.805 Boiling Point (°C) 169 Melting Point (°C) -45 Vapour Pressure (Pa) 130 [Pa] at a temperature of 20°C Flash Point (°C) 74 Lower explosivity limit (LEL) (volume %) 1.48 Upper explosivity limit (UEL) (volume %) 11.9
### Behaviour at sea
Persistence (days) 0.8
### Additional data
Colour colourless Odour sharp odour Standard behavior classification D, FD
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 11 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name organic anhydrides
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 30 TEEL-2 (mg/m3) 200 TEEL-3 (mg/m3) 500
### Ecotoxicity
# PROPIONITRILE
UN Number: 2404 Also known as: CYANOETHANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2404
### Physical chemical data
Physical State (20°C) Liquid Molar mass (g/mol) 55.08 Density of gas (kg/m3) 2.45 Boiling Point (°C) 97.3 Melting Point (°C) -92.8 Vapour Pressure (Pa) 5200 [Pa] at a temperature of 20°C Lower explosivity limit (LEL) (volume %) 3.1
### Behaviour at sea
### Additional data
Colour colourless Odour ethereal
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 37 State liquid Family name nitriles IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 4 - High Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Specific Health Concern (D3) R - Reprotoxicity Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 6 ppm TEEL-2 (mg/m3) 7 ppm TEEL-3 (mg/m3) 37 ppm
### Ecotoxicity
# PROPYLENE
UN Number: 1077
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1077
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 1.935 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 42.08 Density of gas (kg/m3) 1.935 Boiling Point (°C) -47.5 Melting Point (°C) -185 Vapour Pressure (Pa) 1053520 [Pa] at a temperature of 20°C Ignition Temperature (°C) 455 Flash Point (°C) -48 Upper explosivity limit (UEL) (volume %) 11
### Behaviour at sea
### Additional data
Colour colourless Odour mild odour
### Transportation data
Transport mode Gas,Packaged Ship type 2G,2PG Cargo group 30 State liquefied gas Temperature (°C) ambient Pressure (Pa) under pressure Family name olefins IMO class 2(2.1)
### Reactivity data
Acid(s) Yes Static electricity Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 1500 ppm TEEL-2 (mg/m3) 10000 ppm TEEL-3 (mg/m3) 20000 ppm
### Ecotoxicity
# PROPYLENE BUTYLENE COPOLYMER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Boiling Point (°C) very high
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Cargo group 30 Family name olefins
### Reactivity data
Water No
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# PROPYLENE GLYCOL
CAS Number: 57-55-6 Also known as: 1,2-DIHYDROXYPROPANE, 2-Hydroxypropanol, 1,2-Propanediol, Alpha-Propylene Glycol, Monopropylene Glycol, Methylethylene Glycol, Methyl Glycol, Propylene Glycol, Pg 12, Propane-1,2-Diol, Propanediol, Methylethyl Glycol, 1,2-Propylene Glycol, α-Propylene Glycol
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 57-55-6 Formula C 3 H 8 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1040 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 54.05 [cSt] at a temperature of 20°C 39 [cSt] at a temperature of 25°C Molar mass (g/mol) 76.09 Density of gas (kg/m3) 3.39 Solubility (g/L) 1040000 [g/L] at a temperature of 20°C and salinity of 0‰ 1040000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 187 Melting Point (°C) -59 Critical temperature (°C) 676.4 Critical pressure (Pa) 5941000 Surface tension (mN/m) 38 [mN/m] at a temperature of 20°C 36.51 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 10.4 [Pa] at a temperature of 20°C 17 [Pa] at a temperature of 25°C Ignition Temperature (°C) 420 Flash Point (°C) 99 Flash Point (Pensky-Martens closed cup) (°C) 99 Flash Point (Cleveland open cup) (°C) 107.2 Lower explosivity limit (LEL) (volume %) 2.5 Upper explosivity limit (UEL) (volume %) 12.6 Vapor enthalpy (J/Kg) 688000 [J/Kg] at a temperature of 187.6°C 486366 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 21700000 Specific heat capacity (J/(Kg·K)) 2507.55 Combustion efficiency (%) 99 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.02 Rad fraction (%) 28 Henry's constant (mol/(m³·Pa)) 0.01
### Behaviour at sea
Log kow -0.92 Log koc 0.65 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 10 Bioconcentration factor (BCF) 1
### Additional data
Colour colourless Odour odourless MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment.
### Transportation data
Cargo group 20 State liquid Temperature (°C) ambient Family name alcohols, glycols
### Reactivity data
Water No Abilities Miscible in water.. Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes (light metals) Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
TLV-TWA 25 TEEL-1 (mg/m3) 10 TEEL-2 (mg/m3) 10 TEEL-3 (mg/m3) 500
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 19000 Lowest median lethal concentration (LC50) on crustacean (mg/l) 18340 Lowest median lethal concentration (LC50) on fishes (mg/l) 46500 Highest no observed effect concentration (NOEC) on algae (mg/l) > 5300 Assessment factor (AF) 1000 on the Short term 10000 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 18340 [µg/l] on the Short term 1834 [µg/l] on the Long term
# PROPYLENE GLYCOL METHYL ETHER
UN Number: 3092 - CAS Number: 107-98-2 Also known as: 1,2-Propylene Glycol Monomethyl Ether, 1-Methoxy-2-Propanol, Propylene Glycol Methyl Ether, Ether Methylique De Propylene Glycol
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3092 CAS number 107-98-2 Formula C 4 H 1 0 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 924 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 1.88 [cSt] at a temperature of 20°C 1.86 [cSt] at a temperature of 25°C Molar mass (g/mol) 90.12 Density of gas (kg/m3) 3.999 Solubility (g/L) 10000000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 121 Melting Point (°C) -97 Critical temperature (°C) 579.8 Critical pressure (Pa) 4113000 Surface tension (mN/m) 27.27 [mN/m] at a temperature of 20°C Vapour Pressure (Pa) 1460 [Pa] at a temperature of 20°C 1665 [Pa] at a temperature of 25°C Flash Point (°C) 38 Flash Point (Pensky-Martens closed cup) (°C) 32 Flash Point (Cleveland open cup) (°C) 36 Combus enthalpy (J/Kg) 25857120 Specific heat capacity (J/(Kg·K)) 2426 Henry's constant (mol/(m³·Pa)) 0.09
### Behaviour at sea
Log kow -0.49 Log koc 0 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 3.2
### Additional data
Colour colourless Odour mild odour MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment.
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Abilities Miscible in water.
### GESAMP Hazard profile
Interference with coastal amenities (E2) G - Gas
### Human toxicity threshold
Hazard statements Physical H226 Flammable liquid and vapour. Health H336 May cause drowsiness or dizziness. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P233 Keep container tightly closed. P240 Ground/bond container and receiving equipment. Response P370 + P378 In case of fire: Use ... for extinction. Storage P403 + P235 Store in a well- ventilated place. Keep cool. Disposal P501 Dispose of contents/container to ... TLV-TWA 100 TEEL-1 (mg/m3) 150 ppm TEEL-2 (mg/m3) 300 ppm TEEL-3 (mg/m3) 750 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 23300 Assessment factor (AF) 100 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 208000 [µg/l] on the Short term
# PROPYLENE GLYCOL METHYL ETHER ACETATE
UN Number: 3271 - CAS Number: 108-65-6 Also known as: ACETATE DE L'ETHER METHYLIQUE DU PROPYLENEGLYCOL, 1,2-Propylene Glycol Monomethyl Ether Acetate, 2-Acetoxy-1-Methoxypropane, Propylene Glycol Methyl Ether Acetate, Acetate D'Ether Methylique De Propylene Glycol
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3271 CAS number 108-65-6 Formula C 6 H 1 2 O 3
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 969 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 132.16 Solubility (g/L) 160 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 150 Melting Point (°C) -96.7 Critical molar volume (m³/mol) 0.000432 Critical temperature (°C) 597.8 Critical pressure (Pa) 3010000 Vapour Pressure (Pa) 496 [Pa] at a temperature of 20°C 517 [Pa] at a temperature of 25°C Ignition Temperature (°C) 354 Flash Point (°C) 46 Flash Point (Pensky-Martens closed cup) (°C) 42 Lower explosivity limit (LEL) (volume %) 1.3 (78�C) Upper explosivity limit (UEL) (volume %) 13.1 (140� Henry's constant (mol/(m³·Pa)) 40.5
### Behaviour at sea
Log kow 0.43 Log koc 1.8
### Additional data
Colour colourless Odour sweet, ether-like MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment.
### Transportation data
Temperature (°C) ambient Family name esters
### Reactivity data
Water No Oxidizing agents Yes Combustibles No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
Hazard statements Physical H226 Flammable liquid and vapour. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking.
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) > 1000 Lowest median lethal concentration (LC50) on crustacean (mg/l) > 500 Lowest median lethal concentration (LC50) on fishes (mg/l) 100 Highest no observed effect concentration (NOEC) on algae (mg/l) > 1000 Highest no observed effect concentration (NOEC) on fishes (mg/l) 100 Assessment factor (AF) 100 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 635 [µg/l] on the Long term
# PROPYLENE OXIDE
UN Number: 1280 - CAS Number: 75-56-9 Also known as: 1,2-Epoxypropane, 2-Methyloxirane, Propene Oxide, Epoxypropane, Methyloxirane, Propylene Oxide, Oxyde De Propylene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1280 CAS number 75-56-9 Formula C 3 H 6 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 830 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 58.08 Density of gas (kg/m3) 2.58 Boiling Point (°C) 34.5 Melting Point (°C) -112 Critical molar volume (m³/mol) 0.00019 Vapour Pressure (Pa) 59851 [Pa] at a temperature of 20°C Ignition Temperature (°C) 430 Flash Point (°C) -37 Lower explosivity limit (LEL) (volume %) 1.8 Upper explosivity limit (UEL) (volume %) 38.5
### Behaviour at sea
Log kow 0.03 Log koc 0.72 Biodegradation in estuary environment (Half- life) (days) 11.6 Bioconcentration factor (BCF) 3
### Additional data
Colour colourless Odour sweet, alcohol odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification DE
### Transportation data
Transport mode Bulk,Gas,Packaged Ship type 2G,2PG Cargo group 16 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name alkylene oxides IMO class 3.1
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Static electricity Yes Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 2000 Hazard statements Physical H224 Extremely flammable liquid and vapour. Health H312 Harmful in contact with skin. H319 Causes serious eye irritation. H332 Harmful if inhaled. H335 May cause respiratory irritation. H340 May cause genetic defects. Exposure cause the hazard: H350 May cause cancer. Precautionary statements Prevention P201 Obtain special instructions before use. P202 Do not handle until all safety precautions have been read and understood. P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P233 Keep container tightly closed. P240 Ground/bond container and receiving equipment. P241 Use explosion-proof electrical/ventilating/lighting/.../equipment. P242 Use only non- sparking tools. P243 Take precautionary measures against static discharge. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Disposal P501 Dispose of contents/container to ... TLV-TWA 20 ERPG-1 (ppm) 50 ERPG-2 (ppm) 250 ERPG-3 (ppm) 750
### Ecotoxicity
Lowest median lethal concentration (LC50) on fishes (mg/l) 52 Highest no observed effect concentration (NOEC) on fishes (mg/l) 141 Assessment factor (AF) 1000 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 52 [µg/l] on the Short term
# PROPYLENE TETRAMER
UN Number: 2850
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2850
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 760 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 168.31 Density of gas (kg/m3) 7.482 Boiling Point (°C) 185 Vapour Pressure (Pa) 400 [Pa] at a temperature of 20°C Flash Point (°C) 42 Lower explosivity limit (LEL) (volume %) 0.6
### Behaviour at sea
### Additional data
Colour colourless Standard behavior classification E, FE, F
### Transportation data
Package group III Cargo group 30 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name olefins IMO class 3.3
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
### Ecotoxicity
# PROPYLENE trimer
UN Number: 2057 - CAS Number: 13987-01-4
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2057 CAS number 13987-01-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 738 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 126.24 Density of gas (kg/m3) 5.61 Boiling Point (°C) 133/142 Flash Point (°C) 24
### Behaviour at sea
### Additional data
Odour odourless Standard behavior classification F/FE/E
### Transportation data
Transport mode Bulk,Packaged Package group II/III Cargo group 30 Temperature (°C) ambient Family name olefins IMO class 3.2/3.3
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 2 - Moderate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# PYRIDINE
UN Number: 1282 - CAS Number: 110-86-1 Also known as: AZABENZENE, AZINE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1282 CAS number 110-86-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 983 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 79.1 Density of gas (kg/m3) 3.483 Boiling Point (°C) 115.1 Melting Point (°C) -42 Vapour Pressure (Pa) 1500 [Pa] at a temperature of 20°C Ignition Temperature (°C) 550 Flash Point (°C) 17 Lower explosivity limit (LEL) (volume %) 1.8 Upper explosivity limit (UEL) (volume %) 12.4
### Behaviour at sea
### Additional data
Colour colourless to yellow Odour sharp, nauseating odour
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name aromatic amines IMO class 3.2
### Reactivity data
Acid(s) Yes Static electricity Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 3600 TEEL-1 (mg/m3) 15 ppm TEEL-2 (mg/m3) 200 ppm TEEL-3 (mg/m3) 1000 ppm
### Ecotoxicity
# ROSIN
UN Number: 1286 - CAS Number: 8050-09-7 Also known as: CODOIL, COLLOPHANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1286 CAS number 8050-09-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1020 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 300/400 Melting Point (°C) 100-150 Vapour Pressure (Pa) 290 [Pa] at a temperature of 20°C Ignition Temperature (°C) 342 Flash Point (°C) 124/199
### Behaviour at sea
### Additional data
Colour light amber to red to black Odour pinetree pitch
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 33 Temperature (°C) ambient Family name miscell. hydroc. mixt IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Specific Health Concern (D3) Ss - Skin Sensitization Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# Sec-BUTYL ACETATE
UN Number: 1123 - CAS Number: 123-86-4 Also known as: ACETATES DE BUTYLE, Sec-BUTYL ACETATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1123 CAS number 123-86-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 872 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 116.16 Density of gas (kg/m3) 5.173 Boiling Point (°C) 112 Melting Point (°C) -73 Vapour Pressure (Pa) 1500 [Pa] at a temperature of 20°C Ignition Temperature (°C) 480 Flash Point (°C) 19 Lower explosivity limit (LEL) (volume %) 1.7 Upper explosivity limit (UEL) (volume %) 9.8
### Behaviour at sea
Persistence (days) 0.8
### Additional data
Colour colourless Odour pleasant, fruit odour Standard behavior classification FED
### Transportation data
Package group II/III Cargo group 34 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name esters IMO class 3.2/3.3
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) FED - Floater/Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 10000 TLV-TWA 200 TEEL-1 (mg/m3) 200 ppm TEEL-2 (mg/m3) 350ppm TEEL-3 (mg/m3) 1700 ppm
### Ecotoxicity
# SEC-BUTYL ALCOHOL
UN Number: 1120 Also known as: ALCOOL BUTYLIQUE SECONDAIRE, Sec-BUTANOL, 2-BUTANOL, BUTYLENE HYDRATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1120
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 810 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 74.12 Density of gas (kg/m3) 3.3 Boiling Point (°C) 99.5 Melting Point (°C) -115 Vapour Pressure (Pa) 1300 [Pa] at a temperature of 20°C Ignition Temperature (°C) 406 Flash Point (°C) 24 Lower explosivity limit (LEL) (volume %) 1.7
### Behaviour at sea
### Additional data
Colour colourless Odour strong pleasant alcohol odour
### Transportation data
Package group II Cargo group 20 State liquid Temperature (°C) ambient Family name alcohols, glycols IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 2000 TLV-TWA 100 TEEL-1 (mg/m3) 50 ppm TEEL-2 (mg/m3) 50 ppm TEEL-3 (mg/m3) 1400 ppm
### Ecotoxicity
# SILICON TETRACHLORIDE
UN Number: 1818
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1818
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1480 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 169.9 Density of gas (kg/m3) 7.611 Boiling Point (°C) 57.8 Melting Point (°C) -68 Vapour Pressure (Pa) 25900 [Pa] at a temperature of 20°C
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour colourless to light yellow Odour choking odour Standard behavior classification DE, SD
### Transportation data
Package group II State liquid Temperature (°C) ambient Pressure (Pa) under pressure
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 15 TLV-TWA 0.03 ERPG-1 (ppm) 0.75 ERPG-3 (ppm) 37
### Ecotoxicity
# SODIUM ALUMINATE solutions
UN Number: 1819 - CAS Number: 11138-49-1 Also known as: ALUMINATE DE SODIUM en solution
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1819 CAS number 11138-49-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1550 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 81.97 Boiling Point (°C) 115 Melting Point (°C) 1650
### Behaviour at sea
### Additional data
Colour colourless to amber Odour odourless
### Transportation data
Transport mode Bulk,Packaged Package group II/III State liquid Temperature (°C) ambient Family name caustics
### Reactivity data
Water No Acid(s) Yes Metal(s) and alloys Yes (Al, Cu, Sn, Zn) Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 8.75 TEEL-2 (mg/m3) 8.75 TEEL-3 (mg/m3) 8.75
### Ecotoxicity
# SODIUM ARSENATE
UN Number: 1685 Also known as: ARSENIATE DE SODIUM
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1685
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1900 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 312 Boiling Point (°C) 180 Melting Point (°C) 130
### Behaviour at sea
### Additional data
Colour white Odour odourless
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.16 (As) TEEL-1 (mg/m3) 7.5 TEEL-2 (mg/m3) 13.5 TEEL-3 (mg/m3) 13.5
### Ecotoxicity
# SODIUM ARSENITE
UN Number: 1686 Also known as: ARSENIOUS ACID MONOSODIUM SALT, ARSENITE DE SODIUM, ATLAS A (T), CHEM PELS (T)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1686
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1870 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 129.9 Melting Point (°C) 615
### Behaviour at sea
### Additional data
Colour white to grey Odour odourless Standard behavior classification D, SD, S
### Transportation data
State solid Temperature (°C) ambient Pressure (Pa) under pressure IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 0.16 (As) TEEL-1 (mg/m3) 0.075 TEEL-2 (mg/m3) 0.6 TEEL-3 (mg/m3) 8.67
### Ecotoxicity
# SODIUM BENZOATE
CAS Number: 532-32-1 Also known as: BENZOATE DE SODIUM
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 532-32-1
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1440 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 144.11 Melting Point (°C) 300 Ignition Temperature (°C) >500 Flash Point (°C) >100
### Behaviour at sea
### Additional data
Colour white
### Transportation data
### Reactivity data
Water No Acid(s) Yes Base(s) Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
### Ecotoxicity
# SODIUM CACODYLATE
UN Number: 1688 Also known as: CACODYLATE DE SODIUM
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1688
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1100 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 160
### Behaviour at sea
### Additional data
Colour colourless to light yellow Odour odourless Standard behavior classification SD
### Transportation data
Package group II State solid, solut. Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 3.2 TEEL-2 (mg/m3) 40 TEEL-3 (mg/m3) 500
### Ecotoxicity
# SODIUM CHLORATE
UN Number: 1495 - CAS Number: 7775-09-9 Also known as: CHLORATE DE SODIUM, CHLORATE OF SODA
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1495 CAS number 7775-09-9
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2200 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 106.45 Boiling Point (°C) 1413 Melting Point (°C) 255
### Behaviour at sea
### Additional data
Colour colourless to pale yellow Odour odourless Standard behavior classification SD
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 5.1
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents Yes Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 0.4 TEEL-3 (mg/m3) 75
### Ecotoxicity
# SODIUM CHLORATE solutions (50% or less)
UN Number: 2428 - CAS Number: 7775-09-9 Also known as: CHLORATE OF SODA, CHLORATE DE SODIUM en solution (< 50%)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2428 CAS number 7775-09-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 2500 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 106.4 Boiling Point (°C) decomp Melting Point (°C) 248
### Behaviour at sea
### Additional data
Colour colourless to pale yellow Odour odourless Standard behavior classification D/DE
### Transportation data
Transport mode Bulk,Packaged Package group II/III State liquid Temperature (°C) ambient IMO class 5.1
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Reducing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 0.4 TEEL-3 (mg/m3) 75
### Ecotoxicity
# SODIUM CYANIDE solid
UN Number: 1689 Also known as: CYANIDE OF SODIUM, CYANURE DE SODIUM solide
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1689
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1600 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 49.01 Boiling Point (°C) 1496 Melting Point (°C) 563
### Behaviour at sea
### Additional data
Colour white Odour odourless
### Transportation data
State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 45 TLV-TWA 4.5 (CN) TEEL-3 (mg/m3) 47.1
### Ecotoxicity
# SODIUM DICHROMATE
CAS Number: 10588-01-9 Also known as: BICHROMATE OF SODA, DICHROMATE DE SODIUM
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 10588-01-9
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2350 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 262.01 Boiling Point (°C) decomp. Melting Point (°C) 357
### Behaviour at sea
### Additional data
Colour red to orange Odour almond odour Standard behavior classification SD
### Transportation data
State solid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 4 - High Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 115 TLV-TWA 0.02 (Cr) TEEL-1 (mg/m3) 20 TEEL-2 (mg/m3) 37.8 TEEL-3 (mg/m3) 37.8
### Ecotoxicity
# SODIUM HYDROGEN SULPHITE solutions (45% or less)
UN Number: 2693 - CAS Number: 7631-90-5
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2693 CAS number 7631-90-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1360 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 104.06 Density of gas (kg/m3) 2.84 Boiling Point (°C) > 100 Melting Point (°C) < 0
### Behaviour at sea
### Additional data
Colour pale yellow Odour pungent, sulphur dioxide-like Standard behavior classification D/DE
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 43 State liquid Temperature (°C) ambient Family name miscell. water solut.
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 0 - Is not a floater; and does not pose any known health hazards
### Human toxicity threshold
TLV-TWA 1.08
### Ecotoxicity
# SODIUM HYDROSULPHIDE (<25% water of crystallization)
UN Number: 2318
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2318
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1300 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 64 Vapour Pressure (Pa) 2261 [Pa] at a temperature of 20°C Lower explosivity limit (LEL) (volume %) 4.3 Upper explosivity limit (UEL) (volume %) 45.5
### Behaviour at sea
### Additional data
Colour light yellow to red Odour odourless
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) > 17� Pressure (Pa) under pressure Family name caustics IMO class 4.2
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 0.15 TEEL-2 (mg/m3) 1.25
### Ecotoxicity
# SODIUM HYDROSULPHIDE solutions (45% or less)
UN Number: 2949 - CAS Number: 16721-80-5
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2949 CAS number 16721-80-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) < 1300 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 100 Melting Point (°C) 17
### Behaviour at sea
### Additional data
Colour light yellow to red Odour rotten egg
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) > 17 �C Family name caustics
### Reactivity data
Water No Acid(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# SODIUM HYDROXIDE solid
UN Number: 1823 - CAS Number: 1310-73-2 Also known as: CAUSTIC SODA, Lye, Soda Lye, Sodium Hydrate, White Caustic, Sodium Hydroxide Solution, Caustic Soda Solution, Sodium Hydroxide (Na(Oh)), Sodium Hydrate Solution, Sodium Hydroxide Solid, Caustic Soda Solid, Sodium Hydrate Solid, Sodium Hydroxide, Sodium Hydroxide Solution (40%), Solution D'Hydroxyde De Sodium (40%)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1823 CAS number 1310-73-2 Formula NaOH
### Physical chemical data
Physical State (20°C) Solid Physical State (25°C) Liquid Density (kg/m3) 2100 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 25.35 [cSt] at a temperature of 20°C Molar mass (g/mol) 40 Solubility (g/L) 10000000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 1390 Melting Point (°C) 318
### Behaviour at sea
### Additional data
Colour white Odour rotten egg odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water No Abilities Solution. Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No Notable risks Reacts with many compounds.
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 150 Hazard statements Physical H290 May be corrosive to metals. Health H314 Causes severe skin burns and eye damage. H315 Causes skin irritation. H319 Causes serious eye irritation. Precautionary statements Prevention P260 Do not breathe dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P310 Immediately call a POISON CENTER or doctor/physician. TLV-TWA 1.2 ERPG-1 (ppm) 0.5 mg ERPG-2 (ppm) 5 mg ERPG-3 (ppm) 50 mg
### Ecotoxicity
# SODIUM HYDROXIDE solutions (33%)
UN Number: 1824 - CAS Number: 1310-73-2 Also known as: CAUSTIC SODA
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1824 CAS number 1310-73-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1480 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 40 Density of gas (kg/m3) 1.78 Boiling Point (°C) 140 Vapour Pressure (Pa) 900 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Transport mode Bulk,Packaged Package group II/III State liquid Family name caustics
### Reactivity data
Water Yes Acid(s) Yes Base(s) No Metal(s) and alloys Yes Oxidizing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 250 ERPG-1 (ppm) 0.5 ERPG-3 (ppm) 50
### Ecotoxicity
# SODIUM HYPOCHLORITE solution (>5% avail. chlorine)
UN Number: 1791 - CAS Number: 7681-52-9
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1791 CAS number 7681-52-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1060 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 74.4 Melting Point (°C) 27
### Behaviour at sea
### Additional data
Colour green to yellow Odour odourless
### Transportation data
Package group II State liquid Temperature (°C) ambient Pressure (Pa) under pressure
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-2 (mg/m3) 50 TEEL-3 (mg/m3) 500
### Ecotoxicity
# SODIUM metal
UN Number: 1428
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1428
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 971 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 22.49 Boiling Point (°C) 883 Melting Point (°C) 97.8 Ignition Temperature (°C) 121
### Behaviour at sea
### Additional data
Colour silver to greyish-white Odour weak odour Standard behavior classification D, FD
### Transportation data
State liquid, solid Temperature (°C) 110� - 121�,ambient Pressure (Pa) under pressure IMO class 4.3
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 0.5 TEEL-3 (mg/m3) 50
### Ecotoxicity
# SODIUM NITRITE
UN Number: 1500 - CAS Number: 7632-00-0 Also known as: ANTI-RUST
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1500 CAS number 7632-00-0
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2200 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 69 Boiling Point (°C) 320 Melting Point (°C) 271
### Behaviour at sea
### Additional data
Colour white Odour bleaching liquid odour Standard behavior classification SD
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 5.1
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 0.15 TEEL-3 (mg/m3) 60
### Ecotoxicity
# SODIUM PENTACHLOROPHENATE
UN Number: 2567
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2567
### Physical chemical data
Physical State (20°C) Solid Molar mass (g/mol) 288.35 Boiling Point (°C) decomp.
### Behaviour at sea
### Additional data
Colour buff coloured Odour phenolic Marine pollutant P Standard behavior classification SD/D
### Transportation data
Package group II State solid Temperature (°C) ambient IMO class 6.1
### Reactivity data
Water No Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 3.5 TEEL-2 (mg/m3) 24 TEEL-3 (mg/m3) 75
### Ecotoxicity
# SODIUM PEROXIDE
UN Number: 1504
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1504
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2800 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 78 Boiling Point (°C) 657 Melting Point (°C) 460
### Behaviour at sea
### Additional data
Colour pale yellow
### Transportation data
State solid Temperature (°C) ambiant IMO class 5.1
### Reactivity data
Water Yes Metal(s) and alloys Yes (light metals) Reducing agents Yes Combustibles Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 10 TEEL-2 (mg/m3) 10 TEEL-3 (mg/m3) 10
### Ecotoxicity
# SODIUM PETROLEUM SULPHONATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1050 [Kg/m³] at a temperature of 20°C Melting Point (°C) -5 Vapour Pressure (Pa) < 100 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# SODIUM SILICATE
CAS Number: 1344-09-8
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 1344-09-8
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1700 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 122.1 Melting Point (°C) 1088
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification SD
### Transportation data
State visc. liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 25 TEEL-2 (mg/m3) 150 TEEL-3 (mg/m3) 500
### Ecotoxicity
# SODIUM SULPHATE solutions
CAS Number: 7757-82-6
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 7757-82-6
### Physical chemical data
Physical State (20°C) Liquid Vapour Pressure (Pa) 2000 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
### Transportation data
Cargo group 43 State liquid
### Reactivity data
Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
### Ecotoxicity
# SODIUM SULPHIDE (<30% water of cristallization)
UN Number: 1385 - CAS Number: 1313-82-2
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1385 CAS number 1313-82-2
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2470 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 78.4
### Behaviour at sea
### Additional data
Colour yellow to red Odour odourless
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 4.2
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 2.5 TEEL-2 (mg/m3) 15 TEEL-3 (mg/m3) 75
### Ecotoxicity
# SODIUM SULPHITE
CAS Number: 7757-83-7 Also known as: DISODIUM SULPHITE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 7757-83-7
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2600 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 126.04 Melting Point (°C) >500
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification SD
### Transportation data
State solid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
TEEL-1 (mg/m3) 30 TEEL-2 (mg/m3) 50 TEEL-3 (mg/m3) 100
### Ecotoxicity
# SODIUM THIOCYANATE solutions (56% or less)
CAS Number: 540-72-7
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 540-72-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) > 1000 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 81.08 Melting Point (°C) < 0 Vapour Pressure (Pa) 2000 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour clear to pale yellow Odour odourless
### Transportation data
State liquid Temperature (°C) ambient
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
TEEL-1 (mg/m3) 0.75 TEEL-3 (mg/m3) 100
### Ecotoxicity
# SORBITOL solution
CAS Number: 50-70-4 Also known as: CHOLAXINE, DI AKARMON
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 50-70-4
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1490 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 182.17 Density of gas (kg/m3) 4.128 Melting Point (°C) 100 Flash Point (°C) 918
### Behaviour at sea
### Additional data
Colour colourless Odour rotten egg odour Standard behavior classification D, SD, S
### Transportation data
Cargo group 20 State liquid Temperature (°C) elevated Pressure (Pa) ambient Family name alcohols, glycols
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 0 - Is not a floater; and does not pose any known health hazards
### Human toxicity threshold
TEEL-1 (mg/m3) 125 TEEL-2 (mg/m3) 500 TEEL-3 (mg/m3) 500
### Ecotoxicity
# STYRENE MONOMER inhibited
UN Number: 2055 - CAS Number: 100-42-5 Also known as: CINNAMENE, CINNAMENOL, DIAREX HF 77, Ethenylbenzene, Phenylethene, Phenethylene, Phenylethylene, Styrene Monomer, Styrol, Styrolene, Vinylbenzene, Vinylbenzol, Vinyl Benzene, Styrene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2055 CAS number 100-42-5 Formula C 8 H 8
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 906 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.83 [cSt] at a temperature of 20°C 0.75 [cSt] at a temperature of 25°C Molar mass (g/mol) 104.15 Density of gas (kg/m3) 4.631 Solubility (g/L) 300 [g/L] at a temperature of 20°C and salinity of 0‰ 310 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 145.4 Melting Point (°C) -31 Surface tension (mN/m) 32.14 [mN/m] at a temperature of 20°C Interfacial tension (mN/m) 35.48 [mN/m] at a temperature of 20°C and salinity of 0‰ Vapour Pressure (Pa) 600 [Pa] at a temperature of 20°C 810 [Pa] at a temperature of 25°C Ignition Temperature (°C) 490 Flash Point (°C) 32 Flash Point (Pensky-Martens closed cup) (°C) 31 Flash Point (Cleveland open cup) (°C) 34.4 Lower explosivity limit (LEL) (volume %) 1.1 Upper explosivity limit (UEL) (volume %) 6.1 Vapor enthalpy (J/Kg) 371579 [J/Kg] at a temperature of 145.2°C Combus enthalpy (J/Kg) 40500000 Specific heat capacity (J/(Kg·K)) 1747.5 Combustion efficiency (%) 70 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.07 Rad fraction (%) 60 Henry's constant (mol/(m³·Pa)) 278
### Behaviour at sea
Log kow 3.02 Log koc 2.96 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 50 Bioconcentration factor (BCF) 74
### Additional data
Colour colourless to light yellow Odour odourless MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification FE
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 30 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name olefins IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Static electricity Yes Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes Notable risks Polymerization.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 5000 Hazard statements Health H317 May cause an allergic skin reaction. Environmental H400 Very toxic to aquatic life. H410 Very toxic to aquatic life with long lasting effects. Precautionary statements Prevention P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P272 Contaminated work clothing should not be allowed out of the workplace. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P321 Specific treatment (see ... on this label). P333 + P313 If skin irritation or rash occurs: Get medical advice/attention. P363 Wash contaminated clothing before reuse. P391 Collect spillage. Disposal P501 Dispose of contents/container to ... TLV-TWA 50 ERPG-1 (ppm) 50 ERPG-2 (ppm) 250 ERPG-3 (ppm) 1000
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 4.9 Lowest median lethal concentration (LC50) on crustacean (mg/l) 4.7 Lowest median lethal concentration (LC50) on fishes (mg/l) 4.02 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 1.01 Assessment factor (AF) 100 on the Short term 1000 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 40.2 [µg/l] on the Short term 4.02 [µg/l] on the Long term
# SULPHOHYDROCARBON LONG CHAIN (18+) ALKYLAMINE mixture
Also known as: ALKYLAMINES A LONGUES CHAINES SULFOHYDROCARBONEES mélanges (C18+)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1000/1100 [Kg/m³] at a temperature of 20°C Boiling Point (°C) > 100 Melting Point (°C) < 0 Vapour Pressure (Pa) < 1300 [Pa] at a temperature of 20°C Ignition Temperature (°C) 260/370 Flash Point (°C) 80
### Behaviour at sea
### Additional data
Colour yellow-brown Odour lub oil
### Transportation data
Cargo group 33 State liquid Family name miscell. hydroc. mixt
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# SULPHOLANE
CAS Number: 126-33-0
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 126-33-0
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) > 1260 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 120.17 Boiling Point (°C) 285 Melting Point (°C) 26 Vapour Pressure (Pa) 10 [Pa] at a temperature of 20°C Flash Point (°C) 166
### Behaviour at sea
### Additional data
Colour colourless Odour weak oily
### Transportation data
Cargo group 39 Temperature (°C) ambient Family name sulpholane
### Reactivity data
Water No Acid(s) Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# SULPHUR DIOXIDE liquefied
UN Number: 1079 Also known as: DIOXYDE DE SOUFRE liquefié
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1079
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 2.967 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 64.06 Density of gas (kg/m3) 2.967 Boiling Point (°C) -10 Melting Point (°C) -75 Vapour Pressure (Pa) 324160 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless Odour weak rotten egg odour Standard behavior classification GD, G
### Transportation data
Transport mode Gas,Packaged Ship type 1G State liquefied gas Temperature (°C) < 54� Pressure (Pa) under pressure IMO class 2(2.3)
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 100 ERPG-1 (ppm) 0.3 ERPG-3 (ppm) 15
### Ecotoxicity
# SULPHUR HEXAFLUORIDE
UN Number: 1080
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1080
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 6.579 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 146.1 Density of gas (kg/m3) 6.579 Boiling Point (°C) -64 Melting Point (°C) -51 Vapour Pressure (Pa) 2100000 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Odour sharp, irritating odour
### Transportation data
State liq.compr.gas IMO class 2(2.2)
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TLV-TWA 1000 TEEL-1 (mg/m3) 3000 ppm TEEL-2 (mg/m3) 5000 ppm TEEL-3 (mg/m3) 5000 ppm
### Ecotoxicity
# SULPHUR molten
UN Number: 2448 - CAS Number: 7704-34-9 Also known as: Sulphur (Commercially Formed, Solid), Souffre (Solide), Sulphur (Molten), Souffre (Fondu)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2448 CAS number 7704-34-9 Formula S
### Physical chemical data
Physical State (20°C) Solid Physical State (25°C) Liquid Density (kg/m3) 1800 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 256.51 Density of gas (kg/m3) 11.48 Solubility (g/L) 0 [g/L] at a temperature of 20°C and salinity of 0‰ 0 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 444.8 Melting Point (°C) 113 Vapour Pressure (Pa) 10 [Pa] at a temperature of 20°C 5e-07 [Pa] at a temperature of 25°C Ignition Temperature (°C) 260 Flash Point (°C) 168 Lower explosivity limit (LEL) (volume %) 0.3 Upper explosivity limit (UEL) (volume %) 12.1
### Behaviour at sea
### Additional data
Colour yellow,orange,brown,grey Odour sweet, pleasant odour MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) 132� Pressure (Pa) under pressure IMO class 4.1
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
Hazard statements Health H315 Causes skin irritation. TEEL-1 (mg/m3) 0.4 TEEL-2 (mg/m3) 2.5 TEEL-3 (mg/m3) 12.5
### Ecotoxicity
# SULPHURIC ACID (fuming)
UN Number: 1831 - CAS Number: 7664-93-9 Also known as: ACIDE SULFURIQUE (fumant)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1831 CAS number 7664-93-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1920 [Kg/m³] at a temperature of 20°C Density of gas (kg/m3) 3.483 Boiling Point (°C) 139 Vapour Pressure (Pa) 900 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless to cloudy Odour odourless
### Transportation data
Transport mode Bulk,Packaged State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles Yes Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 4 - High Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
ERPG-1 (ppm) 2 mg ERPG-2 (ppm) 10 mg ERPG-3 (ppm) 30 mg
### Ecotoxicity
# SULPHURIC ACID (spent)
UN Number: 1832 - CAS Number: 7664-93-9 Also known as: ACIDE SULPHURIQUE (résiduaire)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1832 CAS number 7664-93-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1390 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 98.1 Density of gas (kg/m3) 4.386 Boiling Point (°C) 100 Melting Point (°C) -32 Vapour Pressure (Pa) 10100 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless to dark brown Standard behavior classification DE, D
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name sulfuric acid
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 4 - High Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 20 TLV-TWA 0.25 ERPG-1 (ppm) 2 mg ERPG-2 (ppm) 10 mg ERPG-3 (ppm) 30 mg
### Ecotoxicity
# SULPHURIC ACID (with more than 51% acid)
UN Number: 1830 - CAS Number: 7664-93-9 Also known as: ACIDE SULFURIQUE (avec plus de 51% d'acide), Battery Acid, Dihydrogen Sulfate++, Electrolyte Acid, Hydrogen Sulfate, Mattling Acid, Oil Of Vitriol, Spirit Of Sulfur, Sulphuric Acid, Dipping Acid, Sulfuric Acid, Acide Sulfurique
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1830 CAS number 7664-93-9 Formula H 2 SO 4
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1840 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 21 [cSt] at a temperature of 25°C Molar mass (g/mol) 98.08 Density of gas (kg/m3) 4.386 Solubility (g/L) 1840000 [g/L] at a temperature of 20°C and salinity of 0‰ 1840000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 340 Melting Point (°C) -35 Surface tension (mN/m) 5.51 [mN/m] at a temperature of 20°C Vapour Pressure (Pa) 10100 [Pa] at a temperature of 20°C Specific heat capacity (J/(Kg·K)) 1416 Henry's constant (mol/(m³·Pa)) 20.1
### Behaviour at sea
Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) 1 Biodegradation in marine environment (Half-life) (days) Not biodegradable Bioconcentration factor (BCF) 0
### Additional data
Colour colourless to dark brown Odour odourless.When hot, choking MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification DE, D
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name sulfuric acid
### Reactivity data
Water Yes Abilities Miscible in water. Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Reducing agents No Combustibles Yes Organic substance Yes Notable risks Reacts with water. Reacts to heat Oxidizer Reacts with other compounds.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 4 - High Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 12.5 Hazard statements Health H314 Causes severe skin burns and eye damage. Precautionary statements Prevention P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. ERPG-1 (ppm) 2 mg ERPG-2 (ppm) 10 mg ERPG-3 (ppm) 30 mg
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 0.13 Lowest median lethal concentration (LC50) on crustacean (mg/l) 29 Lowest median lethal concentration (LC50) on fishes (mg/l) 16 Highest no observed effect concentration (NOEC) on algae (mg/l) 0.13 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.15 Highest no observed effect concentration (NOEC) on fishes (mg/l) 0.025 Assessment factor (AF) 1000 on the Short term 500 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 0.13 [µg/l] on the Short term 0.05 [µg/l] on the Long term
# Tall Oil
CAS Number: 8002-26-4 Also known as: Tall Oil, Huile De Tall
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 8002-26-4
### Physical chemical data
Physical State (25°C) Liquid Solubility (g/L) 0 [g/L] at a temperature of 20°C and salinity of 0‰ 0 [g/L] at a temperature of 25°C and salinity of 0‰ Flash Point (Pensky-Martens closed cup) (°C) 182.2
### Behaviour at sea
Log kow 6.91 Log koc 5.429 Biodegradation in estuary environment (Half-life) (days) 1.844
### Additional data
MARPOL pollution category Category Description Other Substances Substances which have been evaluated and found to fall outside Category X, Y or Z because they are considered to present no harm to marine resources, human health, amenities or other legitimate uses of the sea when discharged into the sea from tank cleaning of deballasting operations. The discharge of bilge or ballast water or other residues or mixtures containing these substances are not subject to any requirements of MARPOL Annex II.
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# TALL OIL SOAP (disproportionated solution)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1040 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 100 Vapour Pressure (Pa) 2400 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# TALLOW
CAS Number: 61789-97-7 Also known as: Tallow, Suif
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 61789-97-7
### Physical chemical data
Physical State (20°C) Solid Physical State (25°C) Solid Density (kg/m3) 870 [Kg/m³] at a temperature of 20°C Solubility (g/L) 0 [g/L] at a temperature of 20°C and salinity of 0‰ 0 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 829 Melting Point (°C) 31 Vapour Pressure (Pa) 266 [Pa] at a temperature of 20°C Flash Point (Pensky-Martens closed cup) (°C) 265 Henry's constant (mol/(m³·Pa)) 1.49
### Behaviour at sea
Persistence (days) 1.9 Log kow 23.3 Log koc 10 Biodegradation in estuary environment (Half-life) (days) 552
### Additional data
Colour dark yellow MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Cargo group 34 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name esters
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# TALLOW FATTY ACID
Also known as: ACIDE GRAS DE SUIF
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Vapour Pressure (Pa) 100 [Pa] at a temperature of 20°C Ignition Temperature (°C) > 200 (E) Flash Point (°C) 200 (E)
### Behaviour at sea
### Additional data
### Transportation data
Family name esters
### Reactivity data
Base(s) Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# TANNIC ACID
Also known as: ACIDE TANNIQUE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Solid Molar mass (g/mol) 1701
### Behaviour at sea
### Additional data
Colour light yellow to tan Odour wax odour
### Transportation data
State solid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# Tert-AMYL ALCOHOL
UN Number: 1105 Also known as: ALCOOL AMYLIQUE TERTIAIRE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1105
### Physical chemical data
Physical State (20°C) Liquid Molar mass (g/mol) 88.14 Boiling Point (°C) 102 Melting Point (°C) -12 Flash Point (°C) 20
### Behaviour at sea
### Additional data
### Transportation data
Package group III Cargo group 20 State liquid IMO class 3.3
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 100 ppm TEEL-2 (mg/m3) 100 ppm TEEL-3 (mg/m3) 100 ppm
### Ecotoxicity
# Tert-Amyl Methyl Ether
CAS Number: 994-05-8 Also known as: 2-Methoxy-2-Methyl-Butane, Methyl-Tert-Pentyl Ether, 1,1-Dimethylpropyl Methyl Ether, Tame, Tert-Amyl Methyl Ether, Tertioamymethylether
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 994-05-8 Formula C 6 H 1 4 O
### Physical chemical data
Physical State (25°C) Liquid Molar mass (g/mol) 102.174 Solubility (g/L) 2640 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 86.1 Melting Point (°C) -80 Critical molar volume (m³/mol) 0.000374 Critical temperature (°C) 535 Critical pressure (Pa) 3200000 Flash Point (Pensky-Martens closed cup) (°C) -7 Lower explosivity limit (LEL) (volume %) 1.1 Upper explosivity limit (UEL) (volume %) 7.4 Specific heat capacity (J/(Kg·K)) 2949 Henry's constant (mol/(m³·Pa)) 133.7
### Behaviour at sea
Log kow 1.92 Log koc 1.36 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) Not biodegradable Bioconcentration factor (BCF) 5
### Additional data
MARPOL pollution category Category Description X Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a major hazard to either marine resources or human health and, therefore, justify the prohibition of the discharge into the marine environment.
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
Hazard statements Physical H225 Highly flammable liquid and vapour. Health H302 Harmful if swallowed. H336 May cause drowsiness or dizziness. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P243 Take precautionary measures against static discharge. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P271 Use only outdoors or in a well- ventilated area. Response P301 + P312 IF SWALLOWED: Call a POISON CENTER or doctor/physician if you feel unwell. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. Storage P403 + P235 Store in a well-ventilated place. Keep cool.
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 14 Lowest median lethal concentration (LC50) on fishes (mg/l) 580 Highest no observed effect concentration (NOEC) on algae (mg/l) 77 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 51 Highest no observed effect concentration (NOEC) on fishes (mg/l) 63.9 Assessment factor (AF) 50 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 68 [µg/l] on the Long term
# TERT-BUTYL ALCOHOL
UN Number: 1120 - CAS Number: 75-65-0 Also known as: ALCOOL BUTYLIQUE TERTIAIRE, Tert-BUTANOL, Tert-Butanol, 2-Methyl-2-Propanol, 2-Methylpropan-2-Ol, Trimethylcarbinol, Tert- Butyl Alcohol, Alcool Tert-Butylique
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1120 CAS number 75-65-0 Formula C 4 H 1 0 O
### Physical chemical data
Physical State (20°C) Liquid/Solid Physical State (25°C) Solid Density (kg/m3) 800 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 5.4647 [cSt] at a temperature of 25°C Molar mass (g/mol) 74.12 Density of gas (kg/m3) 3.35 Solubility (g/L) 1000000 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 83 Melting Point (°C) 25 Critical molar volume (m³/mol) 0.000275 Critical temperature (°C) 506.2 Critical pressure (Pa) 3972000 Vapour Pressure (Pa) 4000 [Pa] at a temperature of 20°C 5600 [Pa] at a temperature of 25°C Ignition Temperature (°C) 470 Flash Point (°C) 10 Flash Point (Pensky-Martens closed cup) (°C) 11 Lower explosivity limit (LEL) (volume %) 2.3 Upper explosivity limit (UEL) (volume %) 8 Vapor enthalpy (J/Kg) 527111 [J/Kg] at a temperature of 82.4°C 629916 [J/Kg] at a temperature of 25°C Specific heat capacity (J/(Kg·K)) 2949 Henry's constant (mol/(m³·Pa)) 0.92
### Behaviour at sea
Log kow 0.37 Log koc 0.32 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 5
### Additional data
Colour white crystals if solid Odour sharp alcohol odour MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment.
### Transportation data
Package group II Cargo group 20 Temperature (°C) ambient Family name alcohols, glycols IMO class 3.2
### Reactivity data
Water No Abilities Miscible in water. Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Combustibles Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 1600 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H319 Causes serious eye irritation. H332 Harmful if inhaled. H335 May cause respiratory irritation. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P233 Keep container tightly closed. P240 Ground/bond container and receiving equipment. P241 Use explosion- proof electrical/ventilating/lighting/.../equipment. P242 Use only non-sparking tools. P243 Take precautionary measures against static discharge. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P312 Call a POISON CENTER or doctor/physician if you feel unwell. P337 + P313 If eye irritation persists: Get medical advice/attention. P370 + P378 In case of fire: Use ... for extinction. Storage P403 + P233 Store in a well-ventilated place. Keep container tightly closed. P403 + P235 Store in a well-ventilated place. Keep cool. P405 Store locked up. Disposal P501 Dispose of contents/container to ... TLV-TWA 100 TEEL-1 (mg/m3) 150 ppm TEEL-2 (mg/m3) 1600 ppm TEEL-3 (mg/m3) 1600 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on fishes (mg/l) 3550 Highest no observed effect concentration (NOEC) on algae (mg/l) 976 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 100 Highest no observed effect concentration (NOEC) on fishes (mg/l) 332 Assessment factor (AF) 500 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 200 [µg/l] on the Short term
# TETRACHLOROETHANE
UN Number: 1702 - CAS Number: 79-34-5 Also known as: ACETYLENE TETRACHLORIDE, BONOFORM, CELLON
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1702 CAS number 79-34-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1595 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 167.85 Density of gas (kg/m3) 7.482 Boiling Point (°C) 146.5 Melting Point (°C) -44 Vapour Pressure (Pa) 12100 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless to pale yellow Odour weak odour
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 36 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name halogenated hydrocarb IMO class 6.1
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 150 TEEL-2 (mg/m3) 30 TEEL-3 (mg/m3) 100
### Ecotoxicity
# TETRAETHYL DITHIOPYROPHOSPHATE (dry, liquid or mixtures)
UN Number: 1704 Also known as: DITHIOPYROPHOSPHATE DE TETRAETHYLE (solide, liquide ou en mélange)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1704
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1190 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 322.3
### Behaviour at sea
### Additional data
Colour colourless Odour sweet odour
### Transportation data
Package group II State liquid Temperature (°C) ambient Pressure (Pa) under pressure IMO class 6.1
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 0.5 TEEL-2 (mg/m3) 3.5 TEEL-3 (mg/m3) 10
### Ecotoxicity
# TETRAETHYL LEAD
UN Number: 1649 - CAS Number: 78-00-2
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1649 CAS number 78-00-2
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1633 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 322.44 Density of gas (kg/m3) 14.45 Boiling Point (°C) 180 Melting Point (°C) -28 Vapour Pressure (Pa) 27 [Pa] at a temperature of 20°C Ignition Temperature (°C) 320 Flash Point (°C) 80 Lower explosivity limit (LEL) (volume %) 1.8
### Behaviour at sea
Persistence (days) 3.1
### Additional data
Colour dyed distinctive colour Marine pollutant P
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) under pressure IMO class 6.1
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation in BCF (A1B) 5 - ≥ 4000 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 5 - Very highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 3 - Moderately high Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 4 - High Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TLV-TWA 0.005 TEEL-1 (mg/m3) 0.468 TEEL-2 (mg/m3) 0.781 TEEL-3 (mg/m3) 62.4
### Ecotoxicity
# TETRAETHYL PYROPHOSPHATE
Also known as: BLADAN
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1180 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 290.2 Vapour Pressure (Pa) 10100 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless to yellow Odour sweet odour Standard behavior classification DE, D, SD
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 0.15
### Ecotoxicity
# TETRAETHYLENE GLYCOL
CAS Number: 112-60-7 Also known as: BIS-k2-(2-HYDROXYETHOXY)ETHYL ETHER
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 112-60-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1120 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 194,23 Boiling Point (°C) 327 Melting Point (°C) -6 Vapour Pressure (Pa) 10 [Pa] at a temperature of 20°C Flash Point (°C) 182
### Behaviour at sea
### Additional data
Colour colourless to straw Odour mild
### Transportation data
Cargo group 40 State liquid Temperature (°C) ambient Family name glycol ethers
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
TEEL-1 (mg/m3) 350 TEEL-2 (mg/m3) 500 TEEL-3 (mg/m3) 500
### Ecotoxicity
# TETRAETHYLENEPENTAMINE
UN Number: 2320
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2320
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 998 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 189 Density of gas (kg/m3) 8.386 Boiling Point (°C) 340 Melting Point (°C) -30 Ignition Temperature (°C) 321 Flash Point (°C) 163 Lower explosivity limit (LEL) (volume %) 0.8 Upper explosivity limit (UEL) (volume %) 4.6
### Behaviour at sea
### Additional data
Colour yellow Odour weak fruit odour
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aliphatic amines
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 15 TEEL-2 (mg/m3) 350 TEEL-3 (mg/m3) 500
### Ecotoxicity
# TETRAHYDROFURAN
UN Number: 2056 - CAS Number: 109-99-9 Also known as: Thf, Diethylneoxide, Tetramethyleneoxide, Tetrahydrofuran, Tetrahydrofurane
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2056 CAS number 109-99-9 Formula C 4 H 8 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 888 [Kg/m³] at a temperature of 20°C 883.3 [Kg/m³] at a temperature of 25°C Kinematic viscosity (cSt) 0.6 [cSt] at a temperature of 20°C Molar mass (g/mol) 72.1 Density of gas (kg/m3) 3.225 Solubility (g/L) 10000000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 66 Melting Point (°C) -108 Critical molar volume (m³/mol) 0.000224 Critical temperature (°C) 540.5 Critical pressure (Pa) 5190000 Surface tension (mN/m) 26.4 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 20260 [Pa] at a temperature of 20°C Ignition Temperature (°C) 260 Flash Point (°C) -17 Flash Point (Pensky-Martens closed cup) (°C) -14.5 Flash Point (Cleveland open cup) (°C) -20 Lower explosivity limit (LEL) (volume %) 2 Upper explosivity limit (UEL) (volume %) 11.8 Vapor enthalpy (J/Kg) 413419 [J/Kg] at a temperature of 65°C 443452 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 34880000 Specific heat capacity (J/(Kg·K)) 1720 Henry's constant (mol/(m³·Pa)) 7.09
### Behaviour at sea
Log kow 0.46 Log koc 1.03 Biodegradation in estuary environment (Half- life) (days) Not hydrolysable Bioconcentration factor (BCF) 3
### Additional data
Colour colourless Odour ammonia odour MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment. Standard behavior classification DE
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 41 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name ethers
### Reactivity data
Water No Abilities Miscible in water. Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No Notable risks May form explosive peroxides.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 20000 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H302 Harmful if swallowed. H319 Causes serious eye irritation. H335 May cause respiratory irritation. H351 Suspected of causing cancer. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P233 Keep container tightly closed. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P370 + P378 In case of fire: Use ... for extinction. Disposal P501 Dispose of contents/container to ... TLV-TWA 200 ERPG-1 (ppm) 100 ERPG-2 (ppm) 500 ERPG-3 (ppm) 5000
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 5930 Lowest median lethal concentration (LC50) on fishes (mg/l) 2160 Highest no observed effect concentration (NOEC) on fishes (mg/l) 216 Assessment factor (AF) 500 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 432 [µg/l] on the Short term
# TETRAHYDRONAPHTHALENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 974 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 132.21 Boiling Point (°C) 208 Melting Point (°C) -35 Vapour Pressure (Pa) 133 [Pa] at a temperature of 20°C Flash Point (°C) 284 Lower explosivity limit (LEL) (volume %) 0.8
### Behaviour at sea
### Additional data
Colour colourless Odour weak fruit odour
### Transportation data
Cargo group 32 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aromatic hydrocarbons
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 3 - ≥100 and <500 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 0.6 ppm TEEL-2 (mg/m3) 5 ppm TEEL-3 (mg/m3) 20 ppm
### Ecotoxicity
# TETRAMETHYL LEAD
UN Number: 1649
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1649
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1999 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 267.33 Density of gas (kg/m3) 11.87 Boiling Point (°C) 110 Melting Point (°C) -136 Vapour Pressure (Pa) 3332 [Pa] at a temperature of 20°C Ignition Temperature (°C) 320 Lower explosivity limit (LEL) (volume %) 1.8
### Behaviour at sea
Persistence (days) 3.1
### Additional data
Colour dyed distinctive colour Odour musty, turpentine odour
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) under pressure IMO class 6.1
### Reactivity data
Water No Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 3.5 TLV-TWA 0.007 TEEL-1 (mg/m3) 0.581 TEEL-3 (mg/m3) 51.6
### Ecotoxicity
# TETRAZOL-1-ACETIC ACID
UN Number: 407 Also known as: ACIDE TETRAZOL-1-ACETIQUE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 407
### Physical chemical data
Physical State (20°C) Solid
### Behaviour at sea
### Additional data
Odour fruit odour
### Transportation data
State solid Temperature (°C) ambient Pressure (Pa) ambient Family name nitric acid IMO class 1.4 C
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# THORIUM NITRATE
UN Number: 2976
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2976
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 990 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 555.2 Radioactivity (mrems/hr) 5.3
### Behaviour at sea
### Additional data
Colour white Odour odourless
### Transportation data
State solid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys Yes Static electricity Yes Oxidizing agents No Reducing agents Yes Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-2 (mg/m3) 15 TEEL-3 (mg/m3) 25
### Ecotoxicity
# TITANIUM TETRACHLORIDE
UN Number: 1838
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1838
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1726 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 189.71 Boiling Point (°C) 136 Melting Point (°C) -24.1 Vapour Pressure (Pa) 1300 [Pa] at a temperature of 20°C
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour colourless to light yellow Odour odourless Standard behavior classification D, SD
### Transportation data
Package group II State liquid Temperature (°C) ambient Pressure (Pa) under pressure
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
ERPG-1 (ppm) 5 mg ERPG-2 (ppm) 20 mg ERPG-3 (ppm) 100 mg
### Ecotoxicity
# TOLUENE
UN Number: 1294 - CAS Number: 108-88-3 Also known as: ANTISAL LA, BENZENE METHYL, Methylbenzene, Methylbenzol, Phenylmethane, Toluol, Toluene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1294 CAS number 108-88-3 Formula C 7 H 8
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 867 [Kg/m³] at a temperature of 20°C 880.9 [Kg/m³] at a temperature of 5°C 875.7 [Kg/m³] at a temperature of 10°C 868.3 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.68 [cSt] at a temperature of 20°C 0.64 [cSt] at a temperature of 25°C 2.2477 [cSt] at a temperature of 5°C 2.0669 [cSt] at a temperature of 10°C 2.0845 [cSt] at a temperature of 20°C Molar mass (g/mol) 92.14 Density of gas (kg/m3) 4.1 Solubility (g/L) 515 [g/L] at a temperature of 20°C and salinity of 0‰ 535 [g/L] at a temperature of 25°C and salinity of 0‰ 387 [g/L] at a temperature of 25°C and salinity of 35‰ 160 [g/L] at a temperature of 20°C and salinity of 0‰ 150 [g/L] at a temperature of 20°C and salinity of 5‰ 110 [g/L] at a temperature of 20°C and salinity of 30‰ Boiling Point (°C) 110.8 Melting Point (°C) -95 Surface tension (mN/m) 28.52 [mN/m] at a temperature of 20°C 27.93 [mN/m] at a temperature of 25°C 29.8 [mN/m] at a temperature of 5.6°C 28.66 [mN/m] at a temperature of 11.6°C 28.01 [mN/m] at a temperature of 18.1°C Interfacial tension (mN/m) 36.1 [mN/m] at a temperature of 25°C and salinity of 0‰ Vapour Pressure (Pa) 2932 [Pa] at a temperature of 20°C 3800 [Pa] at a temperature of 25°C Ignition Temperature (°C) 535 Flash Point (Pensky-Martens closed cup) (°C) 4 Flash Point (Cleveland open cup) (°C) 12.8 Lower explosivity limit (LEL) (volume %) 1.27 Upper explosivity limit (UEL) (volume %) 7.1 Vapor enthalpy (J/Kg) 360065 [J/Kg] at a temperature of 110.6°C 412480 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 40500000 Specific heat capacity (J/(Kg·K)) 1707 Combustion efficiency (%) 71 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.11 Rad fraction (%) 60 Henry's constant (mol/(m³·Pa)) 673
### Behaviour at sea
Persistence (days) 1.6 Log kow 2.65 Log koc 2.25 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 30 Bioconcentration factor (BCF) 90
### Additional data
Colour colourless Odour irritating odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification FE
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 32 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aromatic hydrocarbons IMO class 3.2
### Reactivity data
Acid(s) Yes Static electricity Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 2000 Hazard statements Physical H225 Highly flammable liquid and vapour. Health H304 May be fatal if swallowed and enters airways. H315 Causes skin irritation. H336 May cause drowsiness or dizziness. H361 Suspected of damaging fertility or the unborn child. H373 May cause damage to organs through prolonged or repeated exposure, exposure cause the hazard: Precautionary statements Prevention P202 Do not handle until all safety precautions have been read and understood. P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P243 Take precautionary measures against static discharge. P260 Do not breathe dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P308 + P313 IF exposed or concerned: Get medical advice/attention. P331 Do NOT induce vomiting. TLV-TWA 100 ERPG-1 (ppm) 50 ERPG-2 (ppm) 300 ERPG-3 (ppm) 1000
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 9.4 Lowest median lethal concentration (LC50) on crustacean (mg/l) 3.5 Lowest median lethal concentration (LC50) on fishes (mg/l) 5.4 Highest no observed effect concentration (NOEC) on algae (mg/l) 1.2 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.74 Highest no observed effect concentration (NOEC) on fishes (mg/l) 1.4 Assessment factor (AF) 100 on the Short term 100 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 35 [µg/l] on the Short term 7.4 [µg/l] on the Long term
# TOLUENE DIISOCYANATE
UN Number: 2078 - CAS Number: 584-84-9 Also known as: DIISOCYANATE DE TOLUENE, Toluene-2,4-Diisocyanate, 2,4-Diisocyanate-1-Methylbenzene, Toluene Diisocyanate
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2078 CAS number 584-84-9 Formula C 9 H 6 N 2 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1220 [Kg/m³] at a temperature of 20°C 1224.4 [Kg/m³] at a temperature of 25°C Molar mass (g/mol) 174.16 Density of gas (kg/m3) 7.74 Solubility (g/L) 37.6 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 250 Melting Point (°C) 14 Surface tension (mN/m) 25 [mN/m] at a temperature of 25°C Vapour Pressure (Pa) 3998 [Pa] at a temperature of 20°C 3 [Pa] at a temperature of 25°C Ignition Temperature (°C) 620 Flash Point (°C) 135 Flash Point (Pensky-Martens closed cup) (°C) 127 Flash Point (Cleveland open cup) (°C) 132 Lower explosivity limit (LEL) (volume %) 0.9 Upper explosivity limit (UEL) (volume %) 9.5 Combus enthalpy (J/Kg) 23900000 Specific heat capacity (J/(Kg·K)) 1653 Henry's constant (mol/(m³·Pa)) 1.11
### Behaviour at sea
Persistence (days) 2.7 Log kow 3.74 Log koc 3.87 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) 1
### Additional data
Colour colourless to light yellow Odour pleasant odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification D, SD
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 12 State liquid Temperature (°C) 24� - 38� Pressure (Pa) under pressure Family name isocyanates IMO class 6.1
### Reactivity data
Water Yes Abilities Reacts with water. Acid(s) Yes Base(s) Yes Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 4 - High Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 10 Hazard statements Health H315 Causes skin irritation. H317 May cause an allergic skin reaction. H319 Causes serious eye irritation. H330 Fatal if inhaled. H334 May cause allergy or asthma symptoms or breathing difficulties if inhaled. H335 May cause respiratory irritation. H351 Suspected of causing cancer. Environmental H412 Harmful to aquatic life with long lasting effects. Precautionary statements Prevention P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. P284 Wear respiratory protection. Response P308 + P313 IF exposed or concerned: Get medical advice/attention. Storage P403 + P233 Store in a well-ventilated place. Keep container tightly closed. Disposal P501 Dispose of contents/container to ... TLV-TWA 0.005 TEEL-1 (mg/m3) 0.75 ppm TEEL-2 (mg/m3) 2 ppm TEEL-3 (mg/m3) 2 ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on fishes (mg/l) 164 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 1.1
# TOLUENEDIAMINE
Also known as: 2,4-DIAMINOTOLUENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1000 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 122,17 Boiling Point (°C) 280 Melting Point (°C) 88/96 Vapour Pressure (Pa) 10 [Pa] at a temperature of 20°C Ignition Temperature (°C) 450 Flash Point (°C) 210
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Package group III State solid Family name aromatic amines
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# TOLUIDINES
UN Number: 1708
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1708
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 998 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 107.2 Density of gas (kg/m3) 5.031 Boiling Point (°C) 200 Melting Point (°C) -16 Vapour Pressure (Pa) 26793 [Pa] at a temperature of 20°C Ignition Temperature (°C) 480 Flash Point (°C) 85
### Behaviour at sea
### Additional data
Colour colourless to yellow-brown Odour sharp, sweet, fruit odour
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 2 - Moderate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 100 TEEL-1 (mg/m3) 5 ppm TEEL-2 (mg/m3) 5ppm TEEL-3 (mg/m3) 50 ppm
### Ecotoxicity
# TRIBUTYL PHOSPHATE
CAS Number: 126-73-8
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 126-73-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 980 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 266.3 Density of gas (kg/m3) 11.87 Boiling Point (°C) 289 (decomp.) Melting Point (°C) < -80 Vapour Pressure (Pa) 10 [Pa] at a temperature of 20°C Ignition Temperature (°C) 410 Flash Point (°C) 146 Lower explosivity limit (LEL) (volume %) 1.3 Upper explosivity limit (UEL) (volume %) 7.1
### Behaviour at sea
### Additional data
Colour colourless to pale yellow Odour odourless
### Transportation data
Cargo group 34 State liquid Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 30 TLV-TWA 0.2 TEEL-1 (mg/m3) 2 ppm TEEL-2 (mg/m3) 15 ppm TEEL-3 (mg/m3) 30 ppm
### Ecotoxicity
# TRICHLOROETHYLENE
UN Number: 1710 - CAS Number: 79-01-6 Also known as: ACETYLENE TRICHLORIDE, CHLORO ETHANE, CHLOROTEN, CHLORO THANE NU, CHLORO THENE INHIBITED, CHLORO THENE NU, CHLORO THENE VG, CHLORYLEA, CHLORYLEN, CIRCOSOLV, CRAWHASPOL, DAKERON, DENSINFLUAT, DOW-TRI, Trichloroethene, 1,1,2-Trichloroethene, Trichloroethylene
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1710 CAS number 79-01-6 Formula C 2 HCl 3
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 1460 [Kg/m³] at a temperature of 20°C 1464.2 [Kg/m³] at a temperature of 25°C Kinematic viscosity (cSt) 0.38 [cSt] at a temperature of 25°C Molar mass (g/mol) 131.39 Density of gas (kg/m3) 5.805 Solubility (g/L) 1100 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 87 Melting Point (°C) -86 Critical temperature (°C) 544.2 Critical pressure (Pa) 5020000 Surface tension (mN/m) 29.3 [mN/m] at a temperature of 20°C Vapour Pressure (Pa) 133330 [Pa] at a temperature of 20°C Ignition Temperature (°C) 410 Flash Point (°C) 32 Flash Point (Pensky-Martens closed cup) (°C) 90 Lower explosivity limit (LEL) (volume %) 8 Upper explosivity limit (UEL) (volume %) 10.5 Vapor enthalpy (J/Kg) 238987 [J/Kg] at a temperature of 87.21°C 260830 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 6560000 Specific heat capacity (J/(Kg·K)) 947 Henry's constant (mol/(m³·Pa)) 998
### Behaviour at sea
Log kow 2.42 Log koc 1.78 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Bioconcentration factor (BCF) 39
### Additional data
Colour colourless Odour sweet odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 36 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name halogenated hydrocarb IMO class 6.1
### Reactivity data
Base(s) Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 2 - ≥10 and <100 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 1000 Hazard statements Health H319 Causes serious eye irritation. H336 May cause drowsiness or dizziness. H341 Suspected of causing genetic defects. H350 May cause cancer. Environmental H412 Harmful to aquatic life with long lasting effects. Precautionary statements Prevention P202 Do not handle until all safety precautions have been read and understood. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P273 Avoid release to the environment. P281 Use personal protective equipment as required. Response P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P308 + P313 IF exposed or concerned: Get medical advice/attention. P391 Collect spillage. Storage P405 Store locked up. Disposal P501 Dispose of contents/container to ... TLV-TWA 50 ERPG-1 (ppm) 100 ERPG-2 (ppm) 500 ERPG-3 (ppm) 5000
### Ecotoxicity
Lowest median lethal concentration (LC50) on fishes (mg/l) 28.3 Highest no observed effect concentration (NOEC) on algae (mg/l) 63 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.15 Highest no observed effect concentration (NOEC) on fishes (mg/l) 5.76 Assessment factor (AF) 500 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 11 [µg/l] on the Short term
# TRICRESYL PHOSPHATE (1% ortho isomer or more)
UN Number: 2574 - CAS Number: 1330-78-5 Also known as: o-CRESYLPHOSPHATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2574 CAS number 1330-78-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1200 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 368.4 Density of gas (kg/m3) 16.38 Boiling Point (°C) 410 Melting Point (°C) -25 Vapour Pressure (Pa) 10 [Pa] at a temperature of 20°C Ignition Temperature (°C) 385 Flash Point (°C) 223
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Marine pollutant P
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 34 State liquid Temperature (°C) ambient Family name esters IMO class 6.1
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation in BCF (A1B) 3 - ≥100 and <500 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 4 - Very high Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TLV-TWA 0.0065 TEEL-1 (mg/m3) 0.3 ppm TEEL-2 (mg/m3) 0.6 ppm TEEL-3 (mg/m3) 40 ppm
### Ecotoxicity
# TRICRESYLPHOSPHATE (>3% ortho-isomer)
UN Number: 2574 Also known as: DURAD (T)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2574
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1160 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 368 Density of gas (kg/m3) 16.77 Boiling Point (°C) 410 Melting Point (°C) -30 Vapour Pressure (Pa) 1333 [Pa] at a temperature of 20°C Ignition Temperature (°C) 400 Flash Point (°C) 210
### Behaviour at sea
Persistence (days) 3.1
### Additional data
Colour colourless Odour sweet odour Marine pollutant P
### Transportation data
Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 0.3 ppm TEEL-2 (mg/m3) 0.6 ppm TEEL-3 (mg/m3) 40 ppm
### Ecotoxicity
# TRIDECANOIC ACID
CAS Number: 638-53-9 Also known as: ACIDE TRIDECANOIQUE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 638-53-9
### Physical chemical data
Physical State (20°C) Solid Melting Point (°C) 41/42 Flash Point (°C) > 110
### Behaviour at sea
### Additional data
Colour white
### Transportation data
Family name organic acids
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Reducing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# TRIDECANOL
Also known as: ALCOHOLS C13+
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 846 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 200.37 Density of gas (kg/m3) 8.9 Boiling Point (°C) 274 Melting Point (°C) 33 Vapour Pressure (Pa) 1300 [Pa] at a temperature of 20°C Flash Point (°C) 121
### Behaviour at sea
### Additional data
Colour white Odour mild, pleasant Standard behavior classification FE
### Transportation data
Cargo group 20 Temperature (°C) ambient Family name alcohols, glycols
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes Oxidizing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# TRIETHANOLAMINE
CAS Number: 102-71-6 Also known as: DALTOGEN
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 102-71-6
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1130 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 149.19 Density of gas (kg/m3) 6.579 Boiling Point (°C) 360 Melting Point (°C) 21 Ignition Temperature (°C) 324 Flash Point (°C) 179 Lower explosivity limit (LEL) (volume %) 3.6 Upper explosivity limit (UEL) (volume %) 7.2
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name alkanolamines
### Reactivity data
Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# TRIETHYL PHOSPHATE
CAS Number: 78-40-0
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 78-40-0
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1070 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 182.16 Density of gas (kg/m3) 8.1 Boiling Point (°C) 209 Melting Point (°C) -56.4 Vapour Pressure (Pa) 34 [Pa] at a temperature of 20°C Ignition Temperature (°C) 452 Flash Point (°C) 116 Lower explosivity limit (LEL) (volume %) 1.7 Upper explosivity limit (UEL) (volume %) 10
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Cargo group 34 State liquid Temperature (°C) ambient Family name esters
### Reactivity data
Water Yes Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 200 TEEL-2 (mg/m3) 500 TEEL-3 (mg/m3) 500
### Ecotoxicity
# TRIETHYL PHOSPHITE
UN Number: 2323 - CAS Number: 122-52-1
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2323 CAS number 122-52-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 970 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 166.16 Density of gas (kg/m3) 7.39 Boiling Point (°C) 155 Vapour Pressure (Pa) 131 [Pa] at a temperature of 20°C Flash Point (°C) 44
### Behaviour at sea
### Additional data
Colour colourless Odour odourless Standard behavior classification F/FD
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 34 State liquid Temperature (°C) ambient Family name esters IMO class 3.3
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Specific Health Concern (D3) Ss - Skin Sensitization Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 6 ppm TEEL-2 (mg/m3) 40 ppm TEEL-3 (mg/m3) 200 ppm
### Ecotoxicity
# TRIETHYLAMINE
UN Number: 1296 - CAS Number: 121-44-8
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1296 CAS number 121-44-8
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 729 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 101.19 Density of gas (kg/m3) 4.515 Boiling Point (°C) 89.7 Melting Point (°C) -115 Vapour Pressure (Pa) 7198 [Pa] at a temperature of 20°C Ignition Temperature (°C) 230 Flash Point (°C) -17 Lower explosivity limit (LEL) (volume %) 1.2
### Behaviour at sea
### Additional data
Colour colourless Odour mild ammonia odour
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aliphatic amines IMO class 3.2
### Reactivity data
Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 1000 TLV-TWA 10 TEEL-1 (mg/m3) 3 ppm TEEL-2 (mg/m3) 3 ppm TEEL-3 (mg/m3) 200 ppm
### Ecotoxicity
# TRIETHYLBENZENE
CAS Number: 25340-18-5
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 25340-18-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 861 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 162.27 Density of gas (kg/m3) 5.354 Boiling Point (°C) 216
### Behaviour at sea
### Additional data
Colour colourless Odour fish odour Standard behavior classification FD
### Transportation data
Cargo group 32 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aromatic hydrocarbons
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TEEL-1 (mg/m3) 15 ppm TEEL-2 (mg/m3) 125 ppm TEEL-3 (mg/m3) 600 ppm
### Ecotoxicity
# TRIETHYLENE GLYCOL
CAS Number: 112-27-6
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 112-27-6
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1125 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 150.17 Density of gas (kg/m3) 6.68 Boiling Point (°C) 288 Melting Point (°C) -4 Vapour Pressure (Pa) 1299 [Pa] at a temperature of 20°C Ignition Temperature (°C) 370 Flash Point (°C) 177 Lower explosivity limit (LEL) (volume %) 0.9 Upper explosivity limit (UEL) (volume %) 9.2
### Behaviour at sea
### Additional data
Colour colourless Odour weak chemical odour
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 0 - Is not a floater; and does not pose any known health hazards
### Human toxicity threshold
TEEL-1 (mg/m3) 500 TEEL-2 (mg/m3) 500 TEEL-3 (mg/m3) 500
### Ecotoxicity
# TRIETHYLENETETRAMINE
UN Number: 2259 - CAS Number: 112-24-3
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2259 CAS number 112-24-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 982 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 146.24 Density of gas (kg/m3) 6.579 Boiling Point (°C) 277.6 Melting Point (°C) -35 Ignition Temperature (°C) 338 Flash Point (°C) 135 Lower explosivity limit (LEL) (volume %) 1.1
### Behaviour at sea
### Additional data
Colour light straw to amber Odour mild odour
### Transportation data
Transport mode Bulk,Packaged Package group II State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aliphatic amines
### Reactivity data
Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Specific Health Concern (D3) Ss - Skin Sensitization Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TEEL-1 (mg/m3) 7.5 ppm TEEL-2 (mg/m3) 60 ppm TEEL-3 (mg/m3) 150 ppm
### Ecotoxicity
# TRIISOPROPANOLAMINE
CAS Number: 122-20-3
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 122-20-3
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 1020 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 191.27 Density of gas (kg/m3) 8.51 Boiling Point (°C) 300/305 Melting Point (°C) 58 Vapour Pressure (Pa) < 500 [Pa] at a temperature of 20°C Ignition Temperature (°C) 320 Flash Point (°C) 160 Lower explosivity limit (LEL) (volume %) 0.8 (E) Upper explosivity limit (UEL) (volume %) 5.1 (E)
### Behaviour at sea
### Additional data
Colour white Odour slight ammonia Standard behavior classification FD
### Transportation data
State solid Family name alkanolamines
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) FD - Floater/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# TRIISOPROPYLATED PHENYL PHOSPHATES
UN Number: 3082 - CAS Number: 68937-41-7
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082 CAS number 68937-41-7
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1100 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 220/270 Melting Point (°C) -26 Vapour Pressure (Pa) 10 [Pa] at a temperature of 20°C Ignition Temperature (°C) 510/550 Flash Point (°C) 200/245
### Behaviour at sea
### Additional data
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 34 State liquid
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation in BCF (A1B) 5 - ≥ 4000 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 0 - Is not a floater; and does not pose any known health hazards
### Human toxicity threshold
### Ecotoxicity
# TRIMETHYL HEXAMETHYLENE DIAMINE (2,2,4 and 2,4,4)
UN Number: 2327 - CAS Number: 26520-58-0 Also known as: 1,6-DIAMINO-2,2,4(2,4,4)-TRIMETHYLHEXANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2327 CAS number 26520-58-0
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 867 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 158.29 Density of gas (kg/m3) 7.06 Boiling Point (°C) 232 Melting Point (°C) -80 Vapour Pressure (Pa) < 7 [Pa] at a temperature of 20°C Ignition Temperature (°C) 350 Flash Point (°C) 127 Lower explosivity limit (LEL) (volume %) 1.2
### Behaviour at sea
### Additional data
Colour colourless Odour faint amine
### Transportation data
Transport mode Bulk,Packaged Package group III State liquid Family name aliphatic amines
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# TRIMETHYL HEXAMETHYLENE DIISOCYANATE (2,2,4 and 2,4,4)
UN Number: 2328 - CAS Number: 28679-16-5 Also known as: DIISOCYANATE DE TRIMETHYLHEXAMETHYLENE (2,2,4 et 2,4,4), 1,6-DIISOCYANATO-2,2,4(2,4,4)-TRIMETHYLHEXANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2328 CAS number 28679-16-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1010 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 210.27 Density of gas (kg/m3) 9.42 Boiling Point (°C) 291 Melting Point (°C) -80 Vapour Pressure (Pa) 10 [Pa] at a temperature of 20°C Ignition Temperature (°C) 440 Flash Point (°C) > 200 (E) Lower explosivity limit (LEL) (volume %) 1.1
### Behaviour at sea
### Additional data
Colour colourless or yellowish Odour odourless
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 12 State liquid Family name isocyanates IMO class 6.1
### Reactivity data
Water Yes Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# TRIMETHYL PHOSPHATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1197 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 140.07 Boiling Point (°C) 197 Melting Point (°C) -46 Vapour Pressure (Pa) 110 [Pa] at a temperature of 20°C Flash Point (°C) 107
### Behaviour at sea
### Additional data
### Transportation data
State liquid
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 15 ppm TEEL-2 (mg/m3) 60 ppm TEEL-3 (mg/m3) 60 ppm
### Ecotoxicity
# TRIMETHYL PHOSPHITE
UN Number: 2329 - CAS Number: 121-45-9
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2329 CAS number 121-45-9
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1046 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 124.08 Density of gas (kg/m3) 5.55 Boiling Point (°C) 111 Melting Point (°C) -78 Vapour Pressure (Pa) 3200 (25C) [Pa] at a temperature of 20°C Ignition Temperature (°C) 250 Flash Point (°C) 28
### Behaviour at sea
### Additional data
Colour colourless Odour pungent, pyridine-like
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 34 State liquid Family name esters IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Combustibles Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly
### Human toxicity threshold
TEEL-1 (mg/m3) 60 ppm TEEL-2 (mg/m3) 500 ppm TEEL-3 (mg/m3) 750 ppm
### Ecotoxicity
# TRIMETHYLACETIC ACID
CAS Number: 75-98-9 Also known as: ACIDE TRIMETHYLACETIQUE, alpha,alpha-DIMETHYLPROPIONIC ACID
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 75-98-9
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 900 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 102.13 Density of gas (kg/m3) 4.50 (E) Boiling Point (°C) 164 Melting Point (°C) 36 Vapour Pressure (Pa) 10 [Pa] at a temperature of 20°C Flash Point (°C) 63
### Behaviour at sea
### Additional data
Colour coloured Odour odourless
### Transportation data
Family name organic acids
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# TRIMETHYLAMINE (40% solution in water)
UN Number: 1297 - CAS Number: 75-50-3 Also known as: N,N-DIMETHYLMETHANAMINE Solution
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1297 CAS number 75-50-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 900 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 59.1 Density of gas (kg/m3) 2.58 Boiling Point (°C) 30 Melting Point (°C) -3 Vapour Pressure (Pa) 62000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 190 Upper explosivity limit (UEL) (volume %) 11.6
### Behaviour at sea
### Additional data
Colour colourless Odour pungent Standard behavior classification DE
### Transportation data
Transport mode Bulk,Packaged Ship type 2 (sol. < 30%) Package group I/II Family name miscell. water solut. IMO class 3.1
### Reactivity data
Water No Acid(s) Yes Metal(s) and alloys Yes (Al, Zn) Oxidizing agents Yes Reducing agents Yes Combustibles Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
ERPG-1 (ppm) 0.1 ERPG-2 (ppm) 100 ERPG-3 (ppm) 500
### Ecotoxicity
# TRIMETHYLAMINE anhydrous
UN Number: 1083 - CAS Number: 75-50-3
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1083 CAS number 75-50-3
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 2.58 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 59.11 Density of gas (kg/m3) 2.58 Boiling Point (°C) 3.1 Melting Point (°C) -117 Vapour Pressure (Pa) 62000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 190 Upper explosivity limit (UEL) (volume %) 12
### Behaviour at sea
### Additional data
Colour colourless Odour ammonia odour Standard behavior classification GD
### Transportation data
State liq.compr.gas Temperature (°C) ambient Pressure (Pa) under pressure IMO class 2(2.1)
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) DE - Dissolver/Evaporator Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TLV-TWA 10 ERPG-1 (ppm) 0.1 ERPG-2 (ppm) 100 ERPG-3 (ppm) 500
### Ecotoxicity
# TRIMETHYLCHLOROSILANE
UN Number: 1298 Also known as: CHLOROTRIMETHYLSILANE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1298
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 846 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 108.7 Density of gas (kg/m3) 4.77 Boiling Point (°C) 57 Melting Point (°C) -58 Vapour Pressure (Pa) 7360 [Pa] at a temperature of 20°C Ignition Temperature (°C) 395 Flash Point (°C) -28 Lower explosivity limit (LEL) (volume %) 1.8
### Behaviour at sea
### Additional data
Colour colourless Odour sharp irritating
### Transportation data
Package group II State liquid Temperature (°C) ambient IMO class 3.1
### Reactivity data
Water Yes
### GESAMP Hazard profile
### Human toxicity threshold
ERPG-2 (ppm) 20 ERPG-3 (ppm) 150
### Ecotoxicity
# TRIMETHYLENE DIAMINE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 888 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 74.12 Melting Point (°C) -12 Flash Point (°C) 48
### Behaviour at sea
### Additional data
### Transportation data
State liquid
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# TRIMETHYLOL PROPANE POLYETHOXYLATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Vapour Pressure (Pa) 10 [Pa] at a temperature of 20°C Flash Point (°C) 183
### Behaviour at sea
### Additional data
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible
### Human toxicity threshold
### Ecotoxicity
# TRINITROANISOLE
UN Number: 213
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 213
### Physical chemical data
Physical State (20°C) Solid
### Behaviour at sea
### Additional data
Odour perceptible odour
### Transportation data
State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 1.1 D
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# TRIPROPYLENE GLYCOL
CAS Number: 24800-44-0
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 24800-44-0
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1020 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 192.3 Density of gas (kg/m3) 8.51 Boiling Point (°C) 273 Melting Point (°C) -45 Vapour Pressure (Pa) 130 (96�C) [Pa] at a temperature of 20°C Flash Point (°C) 140 Lower explosivity limit (LEL) (volume %) 0.8
### Behaviour at sea
### Additional data
Colour colourless Odour characteristic
### Transportation data
Cargo group 40 State liquid Temperature (°C) ambient Family name glycol ethers
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 0 - Not irritating Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 0 - Is not a floater; and does not pose any known health hazards
### Human toxicity threshold
TEEL-1 (mg/m3) 5 ppm TEEL-2 (mg/m3) 35 ppm TEEL-3 (mg/m3) 150 ppm
### Ecotoxicity
# TRIXYLYL PHOSPHATE
UN Number: 3082 - CAS Number: 25155-23-1 Also known as: COALITE NTP, DIMETHYLPHENOL PHOSPHATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082 CAS number 25155-23-1
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1130/1155 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 410.4 Density of gas (kg/m3) 18.32 Boiling Point (°C) 248/265 Melting Point (°C) -20 Ignition Temperature (°C) 343 Flash Point (°C) 199
### Behaviour at sea
### Additional data
Colour slightly coloured Odour slight odour
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 34 State liquid Temperature (°C) ambient Family name esters
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# TURPENTINE
UN Number: 1299
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1299
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 860 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 136 Density of gas (kg/m3) 6.063 Boiling Point (°C) 155.3 Melting Point (°C) -55 Vapour Pressure (Pa) 500 [Pa] at a temperature of 20°C Ignition Temperature (°C) 220 Flash Point (°C) 33 Lower explosivity limit (LEL) (volume %) 0.8
### Behaviour at sea
Persistence (days) 1.6
### Additional data
Colour colourless Standard behavior classification FE
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 30 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name olefins IMO class 3.3
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 1500 TLV-TWA 100 TEEL-1 (mg/m3) 20 ppm TEEL-2 (mg/m3) 20 ppm TEEL-3 (mg/m3) 800 ppm
### Ecotoxicity
# TURPENTINE SUBSTITUTE
UN Number: 1300
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1300
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 780 [Kg/m³] at a temperature of 20°C Density of gas (kg/m3) 5.35 Boiling Point (°C) 155 Vapour Pressure (Pa) 5865 [Pa] at a temperature of 20°C Flash Point (°C) 42 Lower explosivity limit (LEL) (volume %) 0.8
### Behaviour at sea
### Additional data
Colour colourless Odour penetrat. unpleasant odour
### Transportation data
Transport mode Bulk,Packaged Package group II/III Cargo group 33 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name miscell. hydroc. mixt IMO class 3.2/3.3
### Reactivity data
Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 60 ppm TEEL-2 (mg/m3) 400 ppm TEEL-3 (mg/m3) 2000 ppm
### Ecotoxicity
# UNDECANOIC ACID
CAS Number: 112-37-8 Also known as: ACIDE UNDECANOIQUE, 1-DECANECARBOXYLIC ACID
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 112-37-8
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 891 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 186.3 Density of gas (kg/m3) 8.28 Boiling Point (°C) 228 Melting Point (°C) 28.5 Flash Point (°C) > 110
### Behaviour at sea
### Additional data
Colour white Odour odourless Standard behavior classification F/FE/E
### Transportation data
State solid Temperature (°C) ambient Family name organic acids
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes (common metals) Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# UNDECYL ALCOHOL
UN Number: 3082 - CAS Number: 112-42-5 Also known as: ALCOHOL C-11(UNDECYLIC)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 3082 CAS number 112-42-5
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 835 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 172.3 Boiling Point (°C) 245 Melting Point (°C) 15.9 Flash Point (°C) 93
### Behaviour at sea
### Additional data
Colour colourless Odour mild Standard behavior classification F/FE/E
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 20 Temperature (°C) ambient Family name alcohols, glycols
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# Undecylbenzene
CAS Number: 67774-74-7 Also known as: Benzene, C10-C13 Alkyl Derivs, Undecylbenzene, Benzene, Derives En Alkyle C10-13
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 67774-74-7 Formula C 6 H 5 CnH 2 n+ 1 (n= 1 0 - 1 3 )
### Physical chemical data
Physical State (25°C) Liquid Molar mass (g/mol) 239 Solubility (g/L) 0 [g/L] at a temperature of 25°C and salinity of 0‰ Boiling Point (°C) 298 Melting Point (°C) -70 Henry's constant (mol/(m³·Pa)) 95
### Behaviour at sea
Log kow 7.5 Log koc 4.34 Bioconcentration factor (BCF) 35
### Additional data
MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment.
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Interference with coastal amenities (E2) G - Gas
### Human toxicity threshold
Hazard statements Health H304 May be fatal if swallowed and enters airways. Precautionary statements Response P301 + P310 IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. P331 Do NOT induce vomiting. Storage P405 Store locked up. Disposal P501 Dispose of contents/container to ...
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 0.01 Lowest median lethal concentration (LC50) on fishes (mg/l) > 1000 Highest no observed effect concentration (NOEC) on algae (mg/l) > 1000 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 0.01
# URANIUM HEXAFLUORIDE
UN Number: 2977
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2977
### Physical chemical data
Physical State (20°C) Liquid Molar mass (g/mol) 352 Boiling Point (°C) 56 Vapour Pressure (Pa) 14200 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Odour mild odour
### Transportation data
State liquid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
ERPG-1 (ppm) 5 mg ERPG-2 (ppm) 15 mg ERPG-3 (ppm) 30 mg 10 min 30 min 60 min 4 hrs 8 hrs AEGL-1 (ppm) 3.6 3.6 3.6 AEGL-2 (ppm) 28 19 9.6 2.4 1.2 AEGL-3 (ppm) 216 72 36 4.5
### Ecotoxicity
# URANYL NITRATE
UN Number: 2981
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2981
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2807 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 502.13 Melting Point (°C) 59 Radioactivity (mrems/hr) 5.3
### Behaviour at sea
### Additional data
Colour light yellow
### Transportation data
State solid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys Yes Oxidizing agents No Reducing agents Yes Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 2 (as U) TLV-TWA 0.02 (U) TEEL-1 (mg/m3) 0.993 TEEL-2 (mg/m3) 0.993 TEEL-3 (mg/m3) 16.6
### Ecotoxicity
# URANYL SULFATE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Solid Molar mass (g/mol) 420.2
### Behaviour at sea
### Additional data
Colour yellow Odour odourless
### Transportation data
State solid Temperature (°C) ambient Pressure (Pa) ambient
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
IDHL 2 (as U) TLV-TWA 0.02 (U)
### Ecotoxicity
# UREA ammonium nitrate solution
CAS Number: 57-13-6
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 57-13-6
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1330 [Kg/m³] at a temperature of 20°C Boiling Point (°C) 107 Vapour Pressure (Pa) 2000 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless Odour slight ammonia
### Transportation data
State liquid Temperature (°C) ambient Family name ammonia
### Reactivity data
Water No Acid(s) Yes Metal(s) and alloys Yes (Cu) Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
TEEL-1 (mg/m3) 10 TEEL-2 (mg/m3) 10 TEEL-3 (mg/m3) 500
### Ecotoxicity
# UREA ammonium phosphate solution
CAS Number: 57-13-6 Also known as: Amide Of Carbonic Acid, Carbamide, Carbamimidic Acid, Carbonyl Diamide, Carbonyldiamide, Carbonyldiamine, Isourea, Urea, Uree
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 57-13-6 Formula CH 4 N 2 O
### Physical chemical data
Physical State (25°C) Solid Kinematic viscosity (cSt) 1.49 [cSt] at a temperature of 20°C Molar mass (g/mol) 60.06 Solubility (g/L) 1080000 [g/L] at a temperature of 20°C and salinity of 0‰ 1230000 [g/L] at a temperature of 25°C and salinity of 0‰ Melting Point (°C) 132.7 Combus enthalpy (J/Kg) 9050000 Combustion efficiency (%) 95 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.01 Rad fraction (%) 22 Henry's constant (mol/(m³·Pa)) 0
### Behaviour at sea
Log kow 0 Log koc 0.9 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 50 Bioconcentration factor (BCF) 1.1
### Additional data
MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment.
### Transportation data
### Reactivity data
Abilities Miscible in water. Notable risks Reacts with some compounds.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation in BCF (A1B) 0 - No measurable BCF Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 1 - Slight Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 1 - Is a floater; and/or is slightly acutely toxic; and/or is mildly irritant to skin and/or eyes
### Human toxicity threshold
### Ecotoxicity
Lowest median lethal concentration (LC50) on crustacean (mg/l) 3910 Lowest median lethal concentration (LC50) on fishes (mg/l) 67 Highest no observed effect concentration (NOEC) on algae (mg/l) 1050 Assessment factor (AF) 47 on the Short term Predicted No Effect Concentration (PNEC) (µg/l) 1000 [µg/l] on the Short term
# VALERALDEHYDE
UN Number: 2058 - CAS Number: 590-86-3
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2058 CAS number 590-86-3
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 811 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 86.13 Density of gas (kg/m3) 3.87 Boiling Point (°C) 103.2 Melting Point (°C) -91 Vapour Pressure (Pa) 6665 [Pa] at a temperature of 20°C Ignition Temperature (°C) 222 Flash Point (°C) 12 Lower explosivity limit (LEL) (volume %) 1.4 Upper explosivity limit (UEL) (volume %) 7.2
### Behaviour at sea
### Additional data
Colour colourless Odour odourless
### Transportation data
Package group II Cargo group 19 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name aldehydes IMO class 3.2
### Reactivity data
Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
TLV-TWA 50
### Ecotoxicity
# VEGETABLE PROTEIN solution (hydrolised)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) > 1000 [Kg/m³] at a temperature of 20°C Vapour Pressure (Pa) 2000 [Pa] at a temperature of 20°C
### Behaviour at sea
### Additional data
Colour colourless to yellowish
### Transportation data
Cargo group 43
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 0 - Non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 0 - Is not a floater; and does not pose any known health hazards
### Human toxicity threshold
### Ecotoxicity
# VINYL ACETATE inhibited
UN Number: 1301 - CAS Number: 108-05-4 Also known as: ACETATE DE VINYLE, ACETIC ACID ETHENYL ESTER, ACETIC ACID VINYL ESTER, 1-ACETOXY ETHYLENE, Acetic Acid, Ethylene Ester, 1-Acetoxyethylene, Ethenyl Acetate, Ethenyl Ethanoate, Vinyl A Monomer, Vinyl Acetate Monomer, Vinyl Ethanoate, Vinyl Acetate
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1301 CAS number 108-05-4 Formula C 4 H 6 O 2
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 934 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 0.46 [cSt] at a temperature of 20°C Molar mass (g/mol) 86.09 Density of gas (kg/m3) 3.844 Solubility (g/L) 20000 [g/L] at a temperature of 20°C and salinity of 0‰ Boiling Point (°C) 73.1 Melting Point (°C) -100 Surface tension (mN/m) 24 [mN/m] at a temperature of 20°C Interfacial tension (mN/m) 30 [mN/m] at a temperature of 20°C and salinity of 0‰ Vapour Pressure (Pa) 11997 [Pa] at a temperature of 20°C 15300 [Pa] at a temperature of 25°C Ignition Temperature (°C) 425 Flash Point (°C) -8 Flash Point (Pensky-Martens closed cup) (°C) -8 Flash Point (Cleveland open cup) (°C) -5 Lower explosivity limit (LEL) (volume %) 2.6 Upper explosivity limit (UEL) (volume %) 13.4 Vapor enthalpy (J/Kg) 379000 [J/Kg] at a temperature of 72.7°C Combus enthalpy (J/Kg) 22700000 Specific heat capacity (J/(Kg·K)) 1969 Combustion efficiency (%) 98 Mass flow rate of the combustion surface (Kg/(m²·s)) 0.14 Rad fraction (%) 23 Henry's constant (mol/(m³·Pa)) 51.6
### Behaviour at sea
Log kow 0.7 Log koc 1.4 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) 50 Bioconcentration factor (BCF) 0.16
### Additional data
Colour colourless Odour weak fat odour MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification ED
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 13 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name vinyl acetate IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys No Static electricity Yes Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) ED - Evaporator/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
Hazard statements Physical H225 Highly flammable liquid and vapour. Health H332 Harmful if inhaled. H335 May cause respiratory irritation. H351 Suspected of causing cancer. Environmental H412 Harmful to aquatic life with long lasting effects. Precautionary statements Prevention P201 Obtain special instructions before use. P202 Do not handle until all safety precautions have been read and understood. P233 Keep container tightly closed. P240 Ground/bond container and receiving equipment. P241 Use explosion-proof electrical/ventilating/lighting/.../equipment. P242 Use only non- sparking tools. P243 Take precautionary measures against static discharge. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. P271 Use only outdoors or in a well-ventilated area. P273 Avoid release to the environment. P280 Wear protective gloves/protective clothing/eye protection/face protection. P281 Use personal protective equipment as required. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P304 + P340 IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. P308 + P313 IF exposed or concerned: Get medical advice/attention. P312 Call a POISON CENTER or doctor/physician if you feel unwell. P370 + P378 In case of fire: Use ... for extinction. Storage P403 + P233 Store in a well- ventilated place. Keep container tightly closed. P403 + P235 Store in a well-ventilated place. Keep cool. P405 Store locked up. Disposal P501 Dispose of contents/container to ... TLV-TWA 10 ERPG-1 (ppm) 575 ERPG-2 (ppm) 500
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 12.7 Lowest median lethal concentration (LC50) on crustacean (mg/l) 12.6 Lowest median lethal concentration (LC50) on fishes (mg/l) 14 Highest no observed effect concentration (NOEC) on algae (mg/l) 6 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 45 Highest no observed effect concentration (NOEC) on fishes (mg/l) 0.6 Assessment factor (AF) 5000 on the Short term 500 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 2.52 [µg/l] on the Short term 1.1 [µg/l] on the Long term
# VINYL CHLORIDE inhibited or stabilized
UN Number: 1086 Also known as: CHLORETHENE, CHLOROETHYLENE, CHLORURE DE VINYLE stabilisé
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1086
### Physical chemical data
Physical State (20°C) Gas Density (kg/m3) 2.786 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 62.5 Density of gas (kg/m3) 2.786 Boiling Point (°C) -13.6 Melting Point (°C) -154 Vapour Pressure (Pa) 340000 [Pa] at a temperature of 20°C Ignition Temperature (°C) 473 Flash Point (°C) -77 Lower explosivity limit (LEL) (volume %) 3.6 Upper explosivity limit (UEL) (volume %) 33
### Behaviour at sea
### Additional data
Colour colourless Odour pleasant, fruit odour Standard behavior classification GD, G
### Transportation data
Transport mode Gas,Packaged Ship type 2G,2PG Cargo group 35 State liquefied gas Temperature (°C) ambient Pressure (Pa) ambient Family name vinyl halides IMO class 2(2.1)
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Static electricity Yes Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
ERPG-1 (ppm) 500 ERPG-2 (ppm) 5000 ERPG-3 (ppm) 20000
### Ecotoxicity
# VINYL ETHYL ETHER inhibited
UN Number: 1302 - CAS Number: 109-92-2 Also known as: Ethoxyethylene, Ethyl Vinyl Ether, Vinyl Ethyl Ether, Ether Etyhlique De Vinyle
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1302 CAS number 109-92-2 Formula C 4 H 8 O
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 759 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 72.1 Density of gas (kg/m3) 3.225 Solubility (g/L) 10000 [g/L] at a temperature of 37°C and salinity of 0‰ Boiling Point (°C) 35.6 Melting Point (°C) -115 Vapour Pressure (Pa) 58900 [Pa] at a temperature of 20°C 68128 [Pa] at a temperature of 25°C Ignition Temperature (°C) 201 Flash Point (°C) < 10 Lower explosivity limit (LEL) (volume %) 1.7 Upper explosivity limit (UEL) (volume %) 28 Henry's constant (mol/(m³·Pa)) 547
### Behaviour at sea
Log kow 1.04 Log koc 0.99
### Additional data
Colour colourless Odour characteristic, disagreable MARPOL pollution category Category Description Z Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a minor hazard to either marine resources or human health and therefore justify less stringent restrictions on the quality and quantity of the discharge into the marine environment.
### Transportation data
Transport mode Bulk,Packaged State liquid Family name ethers IMO class 3.1
### Reactivity data
Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 1 - ≥1 and <2 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 1 - Practically non-toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 1 - Mildly irritating Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) E - Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
Hazard statements Environmental H412 Harmful to aquatic life with long lasting effects. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P261 Avoid breathing dust/fume/gas/mist/vapours/spray. Response P305 + P351 + P338 IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. TEEL-1 (mg/m3) 50 ppm TEEL-2 (mg/m3) 350 ppm TEEL-3 (mg/m3) 1500 ppm
### Ecotoxicity
# VINYL NEODECANOATE
CAS Number: 45115-34-2
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
CAS number 45115-34-2
### Physical chemical data
Physical State (20°C) Liquid Molar mass (g/mol) 198.3 Density of gas (kg/m3) 14.33 Melting Point (°C) -20 Ignition Temperature (°C) 309 Flash Point (°C) > 79
### Behaviour at sea
### Additional data
Colour colourless Odour pleasant
### Transportation data
Cargo group 13 State liquid Temperature (°C) ambient Family name vinyl acetate
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Metal(s) and alloys Yes (Cu, Zn) Oxidizing agents Yes Organic substance Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Skin irritation/corrosivity (D1) 3 - Corrosive Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# VINYL TOLUENES inhibited (mixed isomers)
UN Number: 2618 - CAS Number: 25013-15-4
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2618 CAS number 25013-15-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 897 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 118.18 Density of gas (kg/m3) 5.289 Boiling Point (°C) 167.9 Melting Point (°C) -77 Vapour Pressure (Pa) 339908 [Pa] at a temperature of 20°C Ignition Temperature (°C) 494 Flash Point (°C) 53 Lower explosivity limit (LEL) (volume %) 0.8 Upper explosivity limit (UEL) (volume %) 11
### Behaviour at sea
### Additional data
Colour colourless Odour sweet odour
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 30 State liquid Temperature (°C) ambient Pressure (Pa) ambient Family name olefins IMO class 3.3
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation in BCF (A1B) 3 - ≥100 and <500 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 1 - Mildly irritating Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 5000 TLV-TWA 50
### Ecotoxicity
# VINYLIDENE CHLORIDE inhibited
UN Number: 1303 - CAS Number: 75-35-4 Also known as: CHLORURE DE VINYLIDENE
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1303 CAS number 75-35-4
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1210 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 96.95 Density of gas (kg/m3) 4.322 Boiling Point (°C) 31.8 Melting Point (°C) -122 Vapour Pressure (Pa) 66500 [Pa] at a temperature of 20°C Ignition Temperature (°C) 440 Flash Point (°C) -10 Lower explosivity limit (LEL) (volume %) 5.6 Upper explosivity limit (UEL) (volume %) 16
### Behaviour at sea
### Additional data
Colour colourless Odour unpleasant odour
### Transportation data
Transport mode Bulk,Gas,Packaged Cargo group 35 State liquid Temperature (°C) ambient Pressure (Pa) under pressure Family name vinyl halides IMO class 3.1
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents Yes Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation in BCF (A1B) 1 - ≥1 and <10 Bioaccumulation (A1) 1 - Very low potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 2 - Slightly toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) SD - Sinker/Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
TLV-TWA 10 ERPG-2 (ppm) 500 ERPG-3 (ppm) 1000
### Ecotoxicity
# WHITE SPIRIT aromatic low (15-20%)
UN Number: 2319
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2319
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 970 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 132.2 Density of gas (kg/m3) 5.9 Boiling Point (°C) 150/190 Melting Point (°C) 1.194444444 Vapour Pressure (Pa) 200 [Pa] at a temperature of 20°C Ignition Temperature (°C) 210 Flash Point (°C) -0.782608696 Lower explosivity limit (LEL) (volume %) 0.6 Upper explosivity limit (UEL) (volume %) 6.5
### Behaviour at sea
### Additional data
Colour colourless Odour characteristic
### Transportation data
Transport mode Bulk,Packaged Package group III Cargo group 33 State liquid Temperature (°C) ambient Family name miscell. hydroc. mixt IMO class 3.2
### Reactivity data
Water No Acid(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 4 - ≥4 and <5 Bioaccumulation (A1) 4 - High potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 2 - Moderate Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) F - Floating substance, not likely to evaporate or to dissolve quickly Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# XYLENES meta
UN Number: 1307 - CAS Number: 133-20-7 Also known as: CHROMAR, DIMETHYLBENZENES, Dimethylbenzene, Methyltoluene, Xylol, Xylene, Xylene, Mixed Isomers, Xylenes (Mixed), Total Xylenes, Xylenes, Total, Mixed Xylene, Xylene (Mixed Isomers), Xylenes (Mixture)
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1307 CAS number 133-20-7 Formula C 8 H 1 0
### Physical chemical data
Physical State (20°C) Liquid Physical State (25°C) Liquid Density (kg/m3) 864 [Kg/m³] at a temperature of 20°C 879 [Kg/m³] at a temperature of 5°C 874.3 [Kg/m³] at a temperature of 10°C 867.7 [Kg/m³] at a temperature of 20°C Kinematic viscosity (cSt) 4.8 [cSt] at a temperature of 20°C 2.3891 [cSt] at a temperature of 5°C 2.3219 [cSt] at a temperature of 10°C 2.2012 [cSt] at a temperature of 20°C Molar mass (g/mol) 106.16 Solubility (g/L) 175 [g/L] at a temperature of 20°C and salinity of 0‰ 130 [g/L] at a temperature of 20°C and salinity of 0‰ 120 [g/L] at a temperature of 20°C and salinity of 5‰ 100 [g/L] at a temperature of 20°C and salinity of 30‰ Boiling Point (°C) 139 Melting Point (°C) -48 Critical temperature (°C) 619.9 Critical pressure (Pa) 3540000 Surface tension (mN/m) 29.8 [mN/m] at a temperature of 25°C 29.04 [mN/m] at a temperature of 5.3°C 27.88 [mN/m] at a temperature of 10°C 26.96 [mN/m] at a temperature of 17.9°C Vapour Pressure (Pa) 1330 [Pa] at a temperature of 20°C 1070 [Pa] at a temperature of 25°C Ignition Temperature (°C) 527 Flash Point (°C) 28 Flash Point (Pensky-Martens closed cup) (°C) 25 Flash Point (Cleveland open cup) (°C) 25 Lower explosivity limit (LEL) (volume %) 1.1 Upper explosivity limit (UEL) (volume %) 7 Vapor enthalpy (J/Kg) 335892 [J/Kg] at a temperature of 140°C 401733 [J/Kg] at a temperature of 25°C Combus enthalpy (J/Kg) 40831000 Henry's constant (mol/(m³·Pa)) 7
### Behaviour at sea
Persistence (days) 0.8 Log kow 3.12 Log koc 2.58 Aqueous photolysis (Half-life) Not photolysable Biodegradation in estuary environment (Half-life) (days) Not hydrolysable Biodegradation in marine environment (Half-life) (days) Not biodegradable Bioconcentration factor (BCF) 15
### Additional data
MARPOL pollution category Category Description Y Noxious Liquid Substances which, if discharged into the sea from tank cleaning or deballasting operations, are deemed to present a hazard to either marine resources or human health or cause harm to amenities or other legitimate uses of the sea and therefore justify a limitation on the quality and quantity of the discharge into the marine environment. Standard behavior classification FE
### Transportation data
Package group II IMO class 3.2/3.3
### Reactivity data
Notable risks Reacts with oxidizers Reacts with other compounds.
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 3 - ≥3 and <4 Bioaccumulation (A1) 3 - Moderate potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 0 - Negligible Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Skin irritation/corrosivity (D1) 2 - Irritating Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) FE - Floater/Evaporator Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
IDHL 1000 Hazard statements Physical H226 Flammable liquid and vapour. Health H312 Harmful in contact with skin. H315 Causes skin irritation. H332 Harmful if inhaled. Precautionary statements Prevention P210 Keep away from heat/sparks/open flames/hot surfaces. No smoking. P243 Take precautionary measures against static discharge. P260 Do not breathe dust/fume/gas/mist/vapours/spray. P280 Wear protective gloves/protective clothing/eye protection/face protection. Response P303 + P361 + P353 IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. P332 + P313 If skin irritation occurs: Get medical advice/attention. TLV-TWA 100 TEEL-1 (mg/m3) 150 ppm TEEL-2 (mg/m3) 200 ppm TEEL-3 (mg/m3) 900ppm
### Ecotoxicity
Lowest median lethal concentration (LC50) on algae (mg/l) 3.2 Lowest median lethal concentration (LC50) on crustacean (mg/l) 1.3 Lowest median lethal concentration (LC50) on fishes (mg/l) 2.6 Highest no observed effect concentration (NOEC) on algae (mg/l) 0.7 Highest no observed effect concentration (NOEC) on crustacean (mg/l) 1.2 Highest no observed effect concentration (NOEC) on fishes (mg/l) > 1.3 Assessment factor (AF) 1000 on the Short term 10000 on the Long term Predicted No Effect Concentration (PNEC) (µg/l) 1 [µg/l] on the Short term 0.1 [µg/l] on the Long term
# XYLENOL
UN Number: 2261 - CAS Number: 1300-71-6 Also known as: CRESYLIC ACID, DIMETHYLPHENOL
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2261 CAS number 1300-71-6
### Physical chemical data
Physical State (20°C) Liquid/Solid Density (kg/m3) 1010 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 122.2 Boiling Point (°C) 212 Melting Point (°C) -0.571428571 Vapour Pressure (Pa) 100 [Pa] at a temperature of 20°C Ignition Temperature (°C) 599 Flash Point (°C) 80/95 Lower explosivity limit (LEL) (volume %) 1.4
### Behaviour at sea
### Additional data
Colour light yellowish brown Odour sweet tarry
### Transportation data
Transport mode Bulk,Packaged Package group II Cargo group 21 Temperature (°C) ambient Family name phenols, cresols IMO class 6.1
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 2 - ≥2 and <3 Bioaccumulation (A1) 2 - Low potential to bioaccumulate Biodegradation (A2) R - Readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 2 - Moderate Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
### Ecotoxicity
# ZINC ALKARYL DITHIOPHOSPHATE (C7-C16)
Also known as: ALKARYLDITHIOPHOSPHATES (C7-C16) DE ZINC
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1000 [Kg/m³] at a temperature of 20°C Vapour Pressure (Pa) 100 [Pa] at a temperature of 20°C Flash Point (°C) 150/210
### Behaviour at sea
### Additional data
### Transportation data
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 0 - e <1, or > ca.7, or Mol. Wt. > 1000 Bioaccumulation (A1) 0 - No potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 0 - Not irritating Interference with coastal amenities (E2) Fp - Persistent slick forming substance Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# ZINC ALKYL DITHIOPHOSPHATE (C3-C14)
Also known as: ALKYLDITHIOPHOSPHATES (C3-C14) DE ZINC
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
### Physical chemical data
Physical State (20°C) Liquid Density (kg/m3) 1000/1100 [Kg/m³] at a temperature of 20°C Boiling Point (°C) > 100 Melting Point (°C) < 0 Vapour Pressure (Pa) < 100 [Pa] at a temperature of 20°C Ignition Temperature (°C) 260/370 Flash Point (°C) 150
### Behaviour at sea
### Additional data
Colour yellow-brown Odour lub oil
### Transportation data
Cargo group 34 State liquid
### Reactivity data
Water No Acid(s) Yes Base(s) Yes Oxidizing agents Yes
### GESAMP Hazard profile
Bioaccumulation in logPow (A1A) 5 - ≥5 and ≤ ca.7 Bioaccumulation (A1) 5 - Very high potential to bioaccumulate Biodegradation (A2) NR - Not readily biodegradable Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 3 - Moderately toxic Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 0 - Negligible Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 0 - Negligible Eye irritation/corrosivity (D2) 2 - Irritating Interference with coastal amenities (E2) S - Sinking substance that would deposit on the seabed, not likely to dissolve quickly Effects on wildlife and bottom habitats (E3) 2 - Is a persistent floater; and/or is moderately acutely toxic; and/or is irritating to skin and/or eyes; and/or has long-term health effects other than carcinogenicity, mutagenicity or reprotoxicity; and/or is highly flammable; and/or is flammable and is a floater with evaporative properties
### Human toxicity threshold
### Ecotoxicity
# ZINC ARSENATE
UN Number: 1712 Also known as: ARSENIATE DE ZINC
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1712
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 3309 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 866
### Behaviour at sea
### Additional data
Colour colourless Odour sweet odour Standard behavior classification D, SD, S
### Transportation data
Package group II State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 6.1
### Reactivity data
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# ZINC CHLORIDE anhydrous
UN Number: 2331 - CAS Number: 7646-85-7 Also known as: CHLORURE DE ZINC anhydre
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 2331 CAS number 7646-85-7
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 2900 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 136.28 Boiling Point (°C) 732 Melting Point (°C) 285
### Behaviour at sea
### Additional data
Colour white Odour odourless Standard behavior classification SD
### Transportation data
Package group III State solid Temperature (°C) ambient
### Reactivity data
### GESAMP Hazard profile
Bioaccumulation in BCF (A1B) 4 - ≥500 and <4000 Bioaccumulation (A1) 4 - High potential to bioaccumulate Acute aquatic toxicity (B1) (LC/EC/IC50 (mg/l)) 4 - Highly toxic Chronic aquatic toxicity (B2) (NOEC (mg/l)) 1 - Low Acute mammalian toxicity by swallowing (C1) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by skin penetration (C2) (LD50 (mg/kg)) 1 - Slight Acute mammalian toxicity by inhalation (C3) (LC50 (mg/l)) 3 - Moderately high Eye irritation/corrosivity (D2) 3 - Severely irritating, with irreversible corneal injury Interference with coastal amenities (E2) D - Dissolver Effects on wildlife and bottom habitats (E3) 3 - Is highly acutely toxic; and/or is severely irritant or corrosive to skin or eyes; and/or is carcinogenic, mutagenic or reprotoxic; and/or is a floater or persistent floater with associated health effects
### Human toxicity threshold
IDHL 850 TLV-TWA 0.2 TEEL-2 (mg/m3) 50 TEEL-3 (mg/m3) 50
### Ecotoxicity
# ZINC HYDROSULPHITE
UN Number: 1931
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1931
### Physical chemical data
Physical State (20°C) Solid
### Behaviour at sea
### Additional data
Odour odourless
### Transportation data
Package group III State solid Temperature (°C) ambient Pressure (Pa) ambient IMO class 4.2
### Reactivity data
Water No Acid(s) Yes Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
### Ecotoxicity
# ZINC PHOSPHIDE
UN Number: 1714
## Information on chemical
### External resources
CAMEO Chemical Database WISER Substance List
### Description
UN number 1714
### Physical chemical data
Physical State (20°C) Solid Density (kg/m3) 4600 [Kg/m³] at a temperature of 20°C Molar mass (g/mol) 258.1 Boiling Point (°C) 1100 Melting Point (°C) 420
### Behaviour at sea
### Additional data
Colour grey to black Standard behavior classification SD
### Transportation data
State solid Temperature (°C) ambient Pressure (Pa) under pressure IMO class 4.3
### Reactivity data
Water Yes Acid(s) No Base(s) No Metal(s) and alloys No Oxidizing agents No Reducing agents No Combustibles No Organic substance No
### GESAMP Hazard profile
### Human toxicity threshold
TEEL-1 (mg/m3) 0.15 ppm TEEL-2 (mg/m3) 1 ppm TEEL-3 (mg/m3) 1.8 ppm
### Ecotoxicity